## Slide 1: Magnetized Electron Beam Source for the Jefferson Lab Electron-Ion Collider Re-circulator Cooler Ring
P. Adderley, B. Bullard, J. Benesch, J. Grames, F. Hannon, J. Hansknecht, C. Hernandez-Garcia, R. Kazimi, G. A. Krafft, M. A. Mamun, G. Palacios-Serrano, M. Poelker, M. Stutzman, R. Suleiman, M. Tiefenback, C.A. Valerio Lizarraga, Y. Wang, S. Wijethunga, J. Yoskovitz and S. Zhang.
Supported in part by DoE and JLab LDRD
High Brightness Beams Workshop, Crete, Greece, April 8 - 12, 2019
Graduate students, Old Dominion University
I know, it’s Ghost beam but it looks really cool and kind of spiraling

## Slide 2: The proposed JLEIC High Energy Electron Cooler is based on magnetized bunched electron beam generated in an Energy Recover Linac
High Energy Electron Cooler
Circulator Cooler Ring
Energy Recover Linac Ring
Magnetized e-beam injection
100 meters
Why does the cooler go here?

## Slide 3: Magnetized bunched-beam electron cooling of the ion beam
Ion beam cooling in the presence of a magnetic field is much more efficient than cooling in a drift (no magnetic field):
  Electron beam helical motion in strong magnetic field increases electron-ion interaction time, thereby significantly improving cooling efficiency
  Electron-ion collisions that occur over many cyclotron oscillations and at distances larger than cyclotron radius are insensitive to electrons transverse velocity
Long cooling solenoid provides desired cooling effect:
  Counteracting emittance degradation induced by intra-beam scattering
  Maintaining ion beam emittance during collisions and extending luminosity lifetime
  Suppressing electron-ion recombination
  Putting the electron beam into the cooling solenoid represents a challenge
What is the challenge?
Generating the ebeam? Transporting the beam to the cooling solenoid?, or passing the cooling beam through the cooling solenoid? Or all 3?

## Slide 4: Magnetized cooling schematics
Electron beam suffers an azimuthal kick at entrance of the cooling solenoid. But this kick can be cancelled by an earlier kick at exit of photogun. That is the purpose of cathode solenoid.
Upon exit of Cathode Solenoid
Upon entering Cooling Solenoid
Electrons born in strong uniform Bz
v
Bz
v
Bz
v
Br
v
Br
What is this formula?
What is re?
Should we differentiate between the two Vs?

## Slide 5: JLEIC magnetized source beam requirements have never been generated simultaneously by any electron gun
Parameter | Magnetized Source Parameters
Bunch length – Flat-top | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Peak current | 53.9 A
Average current | 140 mA (400 kV)
Transverse normalized emittance | <19 microns
Normalized drift emittance | 36 microns
Cathode spot radius – Flat-top () | 3.14 mm
Solenoid field at cathode (Bz) | 0.50 kG
Parameter | Magnetized Source Parameters
Bunch length – Flat-top | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Peak current | 53.9 A
Average current | 140 mA (400 kV)
Transverse normalized emittance | <19 microns
Normalized drift emittance | 36 microns
 | 3.14 mm
Solenoid field at cathode (Bz) | 0.50 kG

## Slide 6: The JLab magnetized source test stand is utilized to develop the technology for achieving the JLEC magnetized source requirements
Prototype magnetized source was funded by the Jefferson Lab LDRD program that aimed to operate up to 30 mA average current. This three-year project concluded in October 2018
Goals of the project:
  Generate magnetized electron beam from dc high voltage photogun and measure its properties
  Explore impact of cathode solenoid on photogun operation
  Perform simulations and measurements to provide insights on ways to optimize JLEIC electron cooler and help design appropriate source
  Provide JLab with direct experience on magnetizing electron beams at high current
Gun high voltage: 200 – 300 kV
Average beam currents up to 30 mA CW
= 0.1 - 1.0 mm rms
Laser pulse length: 50 ps FWHM
Laser wavelength 532 nm
Laser operating frequency: 1-15 Hz , or 100-500 MHz
Longitudinal magnetic field at cathode Bz = 0 - 1.5 kG
Target Bunch charge: 3 nC

## Slide 7: The magnetized source consists of a 300 kV inverted electron gun with KxCsySb photocathode and a cathode solenoid magnetization coil
Is based on doped-alumina inverted insulator and triple point junction shield for max gradient of 10 MV/m at 350 kV
Has been high voltage conditioned to 360 kV in 70 hours
Nominal vacuum levels ~5x10-12 Torr after vacuum bake and high voltage conditioning
The cathode solenoid provides magnetic field up to 1.5 kG at the cathode using a 400 A, 80 VDC power supply
We learned how to energize solenoid without exciting new field emitters
Photogun operated at 300 kV with gun solenoid at 400 A
Chart: z, m
Magnetic Field with coil at 400 A
Beamline
Focusing
Solenoid 1
Beamline
Focusing
Solenoid 2
Electrostatic Accelerating Field at 300 kV
The photogun

## Slide 8: KxCsySb photocathode films are grown on substrates in a vacuum chamber connected to the photogun
KxCsySb grown with a mask – limit photocathode active area (3 and 5 mm diameter) to reduce beam halo and prolong quantum efficiency operating lifetime
Active area can be offset from electrostatic center to minimize damaging on the emission area from ion back bombardment and micro-arcing events during high current run
Moly substrate to reduce laser induced thermal desorption of chemicals during high current run
Consistently fabricated photocathodes with 5-9% QE
Rotary
Fork
Manipulator
Photo
cathode
puck facing down for activation
Activation mask
Effusion Cs-K source
Sb
pellets crucible
Chart: Bialkali activation on 60 min Sb on GaAs
What makes the change in slope at these two inflection points?

## Slide 9: A diagnostic beamline for magnetized electron beam source characterization
Cathode Solenoid
Photocathode
Preparation
Chamber
Photogun
Slit
Viewer Screen
Shield Tube
Viewer 3 Screen
Beam Dump
The slit crops the magnetized beam into a beamlette that appears rotated when imaged in a downstream viewer screen
: beam size on i -th viewer
φ: rotation (sheering) angle
Slit at first viewer screen

## Slide 10: Magnetized beam characterization
Magnetic field at photocathode = 0 G
Magnetic field at photocathode = 1514 G
Photocathode preparation chamber
Photogun
Cathode solenoid
No slit
Through slit
No slit
Through slit
Slit
Beam and beamlet are observed on viewer YAG screens
What is the reason for the curvature?

## Slide 11: Characterizing beam magnetization
Chart: Bz@cathode, G
| 0 | 7.57 | 18.925000000000001 | 30.28 | 37.85 | 56.775000000000006 | 75.7 | 94.625 | 113.55000000000001 | 151.4 | 189.25 | 227.10000000000002 | 264.95 | 302.8 | 340.65000000000003 | 378.5 | 416.35 | 454.20000000000005 | 492.05 | 529.9 | 567.75 | 605.6 | 643.45000000000005 | 662.375 | 681.30000000000007 | 719.15 | 757 | 794.85 | 832.7 | 870.55000000000007 | 908.40000000000009 | 946.25 | 984.1 | 1021.95 | 1059.8 | 1097.6500000000001 | 1135.5 | 1230.125 | 1324.75 | 1419.375 | 1514
σ (V2 data) | 4.5925 | 4.8449 | 4.8867 | 4.613 | 4.1973 | 3.6337 | 2.3706 | 1.3047 | 1.2439 | 4.0026 | 5.2902 | 4.5872 | 2.183 | 3.1807 | 5.1196 | 4.9853 | 2.8309 | 2.1399 | 2.9657 | 2.5657 | 1.3029 | 1.5463 | 1.7464 | 1.6518 | 1.9049 | 3.163 | 4.3091 | 4.5513 | 6.1355 | 7.5073 | 8.7252 | 8.3367 | 9.8913 | 12.6293 | 12.5157 | 12.7635 | 11.6239 | 14.0262 | 13.1802 | 11.6409 | 10.425
θ for S1-V2 (data) | 0 | -0.29794 | -0.60752 | -0.13751 | -0.27502 | -0.022918 | 0.32659 | 5.4775 | 10.3648 | 0.45837 | -0.68182 | -0.060349 | 4.8472 | 2.1601 | -0.911 | -1.1516 | 2.3205 | 9.3908 | 3.0997 | 6.2567 | 45.9397 | 45.9398 | 36.9271 | 55.8976 | 58.3384 | 18.2831 | 6.3885 | 3.5753 | -0.18259 | -2.4637 | -3.4377 | -3.7529 | -4.8071 | -5.7697 | -6.039 | -6.0603 | -5.8843 | -7.775 | -9.0413 | -9.3621 | -9.3335
Gun voltage 300 kV and laser spot size 0.2 mm rms on photocathode center
Beam size and Rotation: Experiment vs ASTRA simulation
A non-uniform cathode magnetic field causes mismatch oscillations
repeated focusing inside the solenoid field affects the beam size at the exit of the solenoid field
resulting in varying beam expansion rate in the field free region.
Observed and simulated oscillating beam profiles and corresponding beam rotation
RMS beam size (data)
RMS beam size (sim)
Rotation angle (data)
Rotation angle (sim)

## Slide 12: Magnetized beam emittance measurements for two laser spot sizes at 200kV
GPT simulation and experimental results show encouraging agreement
Chart: Bz@cathode, G
| 0 | 94.462500000000006 | 226.71 | 358.95750000000004 | 453.42 | 566.77499999999998 | 755.7 | 944.625 | 1133.55 | 1322.4750000000001 | 1511.4
0.44 mm | 0 | 0.3648 | 0.9 | 1.4729 | 1.8618 | 2.4096 | 3.3562 | 4.2718 | 5.0409 | 5.8738 | 6.5317
0.90 mm | 0.63065 | 1.885 | 4.3202 | 6.9325 | 11.3036 | 14.9175 | 19.3278
 | 26.7548
0.44 mm (GPT simulation) | 0.2811 | 0.51773 | 1.12 | 1.7092 | 2.1322 | 2.6533 | 3.3238 | 4.4138 | 5.0737 | 6.0372 | 6.5514
0.90 mm (GPT simulation) | 0.58128 | 2.0574 | 4.6321 | 7.2702 | 9.9725 | 12.025 | 14.128
Beam size too large to transport cleanly

## Slide 13: Magnetized beam bunch charge measurements
We encountered space-charge-limited regime within 0.3 nC for different magnetized conditions
Need longer laser pulses, higher gun voltage and better beamline optics to get nC bunches
Chart: Pulse energy, nJ
| 0.80600000000000005 | 2.88 | 6.18 | 10.46 | 15.34 | 21 | 27 | 33.4 | 40.4 | 48 | 88 | 92 | 108 | 120 | 128.80000000000001 | 136.6 | 143 | 148.6 | 186.4 | 218 | 264 | 318.00000000000006 | 380 | 450 | 530
 | 0.0218 | 0.078 | 0.16 | 0.22 | 0.252 | 0.27 | 0.28 | 0.288 | 0.292 | 0.296 | 0.316 | 0.334 | 0.35 | 0.366 | 0.378 | 0.392 | 0.4 | 0.412 | 0.53 | 0.58 | 0.596 | 0.604 | 0.654 | 0.66 | 0.72
 | 6.3042 | 6.3127 | 6.0345 | 4.9023 | 3.829 | 2.9968 | 2.4172 | 2.0098 | 1.6847 | 1.4373 | 0.83698 | 0.84619 | 0.75536 | 0.7109 | 0.68405 | 0.66888 | 0.65198 | 0.64623 | 0.66274 | 0.62013 | 0.5262 | 0.44271 | 0.40115 | 0.34185 | 0.31664
Gun voltage 225 kV, Magnetic field at cathode 757 Gauss, laser pulse width 75ps (FWHM)
Irregular pattern due to beam-loss
Why this set of parameters?
What is laser pulse energy on cathode?
I thought high bunch charge studies where done with 300kV

## Slide 14: Initial attempts to run high current magnetized beam where limited by gun current surges tripping off the high voltage power supply damaging the photocathode at 1 mA CW
Physical damage on photocathode every time there is a surge in gun HVPS current
Sudden drop in beam current
Gun vacuum pressure surge

## Slide 15: Biasing the gun anode to +1 kVDC was essential to achieve high current magnetized beam for extended periods of time without gun current trip offs
Laser rms = 1.4 mm, 374.25 MHz, 50 ps (FWHM)
Cathode magnetic field = 568 Gauss
Gun HV = 100 kV
Anode = + 1 kV
KxCsySb photocathode on molybdenum
Gun Vacuum: 5 X 10-12 Torr (background) increased to 5 X 10-11 Torr during 28 mA beam current run
Bunch charge 75 X 10-12 Coulombs
Limited lifetime might be a result of photocathode heating and associated bandgap shift, or ion back bombardment
Approval for higher current obtained
Elapsed run time (hours)
Cumulative Charge (Coulombs)
Beam current (mA)
1/e charge lifetime

## Slide 16: Simulations of ions generated by the high current electron beam suggest that:
Ions in the beamline (red) are attracted to the potential well formed by the electron beam
These trapped ions are then accelerated towards the negatively biased photocathode where they generate secondary electrons (yellow) upon impact which in turn strike the anode and generate secondary ions (pink).
High density ‘channels’ could form leading to arcing between the photocathode and the anode
Biasing the anode repels beamline ions permitting to run high current without gun current trip offs (photocathode arcing)

## Slide 17: JLEIC magnetized source beam requirements compared to parameters achieved in this work
Parameter | JLEIC | Gun Test Stand Demonstrated
Bunch length – Flat-top | 60 ps (2 cm) | 25 – 60 ps
Repetition rate | 43.3 MHz | 100 Hz – 374.3 MHz
Bunch charge | 3.2 nC | 0.7 nC (75 ps FWHM, 25 kHz, 225 kV, 0.76 kG)
Peak current | 53.9 A | 9.3 A
Average current | 140 mA (400 kV) | 28 mA (50 ps FWHM, 74.8 pC, 374.25 MHz, 100 kV, 0.57 kG)
Transverse normalized emittance | <19 microns | <2 microns
Normalized drift emittance | 36 microns | 26 microns
Cathode spot radius – Flat-top () | 3.14 mm | 1.70 mm
Solenoid field at cathode (Bz) | 0.50 kG | 1.51 kG
Parameter | JLEIC | Gun Test Stand Demonstrated
Bunch length – Flat-top | 60 ps (2 cm) | 25 – 60 ps
Repetition rate | 43.3 MHz | 100 Hz – 374.3 MHz
Bunch charge | 3.2 nC | 0.7 nC (75 ps FWHM, 25 kHz, 225 kV, 0.76 kG)
Peak current | 53.9 A | 9.3 A
Average current | 140 mA (400 kV) | 28 mA (50 ps FWHM, 74.8 pC, 374.25 MHz, 100 kV, 0.57 kG)
Transverse normalized emittance | <19 microns | <2 microns
Normalized drift emittance | 36 microns | 26 microns
 | 3.14 mm | 1.70 mm
Solenoid field at cathode (Bz) | 0.50 kG | 1.51 kG
The beam current was limited by the gun the high voltage
power supply (30 mA/225 kV Spellman power supply with 3 kW max power)
What is DRIFT emittance? Where in the machine is this parameter important?
What makes DRIFT emittance so large? The magnetizing coil?
We do not know this, we never measured bunch length, so we cannot say GTS demonstrated, sane with oeak current, we just infer it assuming the laser pulse width
Did you guys ever ran magnetized beam with that high field?

## Slide 18: Future Plans
Swap the photogun for the RF-pulsed thermionic gun built by Xelera Research LLC to demonstrate 65 mA magnetized beam (307 G, 500 MHz, 130 pC, 90 ps rms, 125 kV): an SBIR II funded project
Install non-invasive magnetometers - TE011 Cavity and “Brock” Cavity from Electrodynamic to measure beam magnetization and electron bunch-length for high bunch charge beam: another SBIR II funded project
Reinstall photogun, now with Xelera’s power supply and BNL laser, the setup will enable high average current AND high bunch charge, simultaneously (65 mA, 3 nC)
Characterize space-charge effects of high bunch charge and high average current beam as a function of beam magnetization
Collaborate with Xelera, Electrodynamic, BNL and others on follow-up projects

## Slide 19: THANK YOU!!!
On behalf of the JLab magnetized source team!
Team picture goes hes

## Slide 20: Backup Slides

## Slide 21: High Current Magnetized Beam: 20 mA at 568 G for 20 h
14 mA, 725 G, 90 h run
Laser rms =0.9 mm, 303 MHz, 60 ps
Gun Sol=200 A, HV=200 kV
No QE degradation over 20 hour run
Positive anode bias (+1 kV) effectively prevented ions in beamline from reaching the gun that causes micro-arcs and sudden QE degradation
20 mA, 568 G, 20 h run
Laser rms = 0.9 mm, 303 MHz, 60 ps (FWHM)
Gun HV = 100 kV, Gun Solenoid = 150 A, Anode at + 1 kV
KxCsySb photocathode on molybdenum
Gun Vacuum: 2.7 – 4.2 X 10-12 Torr = 3.6 – 5.6 X 10-10 Pa
(2.0 – 3.2 nA on ion pump)

## Slide 22: High Current Magnetized Beam: 14 mA at 757 G for 90 h
14 mA, 757 G, 90 h run
Laser rms = 0.9 mm, 303 MHz, 60 ps (FWHM)
Gun HV = 200 kV, Gun Solenoid = 200 A, Anode at + 1 kV
KxCsySb photocathode on molybdenum
Gun Vacuum: 2.0 – 2.9 X 10-12 Torr = 2.7 – 3.9 X 10-10 Pa
(1.6 – 2.2 nA on ion pump)
No QE degradation over 90 hour run
Positive anode bias (+1 kV) effectively prevented ions in beamline from reaching the gun that causes micro-arcs and sudden QE degradation

## Slide 23: Modeling beam magnetization in GPT
Larmor frequency increases with magnetic field at cathode
Focusing by cathode magnetic field causes mismatch oscillations resulting in repeated focusing inside cathode solenoid field which affects beam size at exit of solenoid field and resulted in varying beam expansion rate in field free region
Rotation angles are influenced by focusing in cathode solenoid
What is this?
Do you want this with the main slides?
Why is it important?

## Slide 24: Gun high voltage conditioning took ~70 hours with the magnetization coil off
With the magnetization solenoid energized, the gun had to be high voltage re-conditioned.
Vacuum and radiation levels indistinguishable from bkgd at 350kV
Max gradient 10 MV/m at 350 kV

## Slide 25: Summary
KxCsySb photocathode preparation chamber, gun, solenoid and beamline - all operational
Photogun operated reliably up to 300 kV for >1000 h
Cathode solenoid can trigger field emission but we have learned how to prevent this
Have successfully magnetized electron beams and measured rotation angle and drift emittance
Demonstrated high bunch charge up to 0.7 nC
Delivered 28 mA magnetized beam (568 G at photocathode) with RF structure (a gain-switched drive laser, 374.25 MHz, 50 ps FWHM) at 100 kV using 30 mA/225 kV Spellman power supply (3 kW power limit)
Successfully fabricated bialkali antimonide photocathode with QE ~ 9% on molybdenum substrate that provided longer charge lifetime
Positive bias on anode helps to prevent sudden QE loss from ion-induced micro-arcing events
Thanks to those involved in this team work:
P. Adderley, J. Benesch, B. Bullard, J. Delayen , J. Grames, J. Guo, F. Hannon, J. Hansknecht, C. Hernandez-Garcia, R. Kazimi, G. Krafft, M. Poelker, R. Suleiman, M. Tiefenback, Y. Wang, S. Wijiethunga, S. Zhang.
ODU Graduate Students

## Slide 26: Photocathode Preparation by Co-deposition
Co-deposition of alkalis (K and Cs) on Sb layer using an effusion alkali source to grow bialkali antimonide photocathode
Deposition chamber was initially baked at 200 °C for >180 h
Vacuum with NEG pumps and an ion pump, Vacuum ~10 nA (~10-10 Pa)
Sb (99.9999%) , K (99.95%), and Cs (99.9+%)
Working distance: 2 cm, – 280 V bias, low power (4 mW) laser (532 nm) and wavelength tunable light source
Substrate temperatures: 120 °C (for Sb), dropping from 120 °C to 80 °C (for alkalis)
Sb heater current supply from 25 A for 10-20 minutes
RGA as a control to monitor evaporation rate
Temperature kept stable at effusion source and adjusted to control alkali evaporation rate: hot air inlet tube (381 – 462 °C), dispensing tube (232 – 294 °C), and reservoir tube (153 – 281 °C)
Chamber pressure: during bialkali deposition > 1x10-6 Pa and post-deposition to ~10-7 – 10-8 Pa
H2O partial pressure < 2x10-9 Pa

## Slide 27: Anode-cathode potential when anode is biased to +1kVDC

## Slide 28: Centrifugal Barrel Polishing to Rescue
Months to hours !!!
  From machine shop
30 min. plastic cones
30 min. crushed corncob
  Barrel polishing machine at JLab SRF

## Slide 29: Excellent Surface Finish
Diamond paste polishing Ra 30 nm*
* M. BastaniNejad, A. A. Elmustafa, E. Forman, S. Covert, J. Hansknecht, C. Hernandez-Garcia, M. Poelker, L. Das, M. Kelley, P. Williams, “Evaluation of electropolished stainless steel electrodes for use in DC high voltage photoelectron guns,” J. Vac. Sci. Technol. A, Vol. 33, No. 4, Jul/Aug 2015
similar to traditional hand polishing with sand paper and diamond grit