## Slide 1: Desirable BCM Performance
Vashek Vylet
UITF BCM discussion, October 21, 2016

## Slide 2: Radiation Exposure Constraints
Normal operation (per Shielding Policy)
  < 250 mrem/y in occupied RCAs
  < 100 mrem/y in other occupied areas (< 50 mrem/h)
  < 10 mrem/y at site boundary
Max. credible accident: <15 rem per incident

## Slide 3: Layout
CAVE 2
CAVE 1

## Slide 4: Shielding Design – Phase 1
CAVE 2
  – HDIce operation at 10 MeV for 900 h/y
  Iav = 5 nA for 80% of time
  Iav = 100 nA for 20% of time (180 h)
  concrete shielding: 4 ft lateral and 1.75 ft roof
CAVE 1
  Iav = 100 mA when not running HDIce, beam terminated in FC before Cave 2
  55”/27” lateral and 30” roof shielding

## Slide 5: Cave 2
If total losses above are very unlikely, how can we justify a lower loss assumption?
A loss of 200 nA may be tollerated, considering HDIce will run only 900 h/y
BCM should reliably catch Iav > 200 nA within ≤ 2 minutes
TOTAL BEAM LOSS | D [mrem/h] | Note
Cave 2, 1 uA, side | 0.44 | RCA
Cave 2, 1 uA, roof | 55.21 | RA
Cave 2, 100 nA, side | 0.044 | just < RCA
Cave 2, 100 nA, roof | 5.52 | RA

## Slide 6: Cave 1
Cave 1 shielding as is; Iav = 100 mA is desired in cave 1
Cave 2 has 4 ft forward and lateral concrete shielding, with a 1.75 ft thick roof
Beam ends in a well shielded FARC at 42” beam height

## Slide 7: Cave 1 at 100 mA
CAVE 1 | Dose rate | 
 | [mrem/h] | Note
Side 100% loss | 41 | RA
Side 1% loss | 0.4 | RCA
High Side 1% loss | 26 | RA
28”
27”
30”
Thinner wall may be an issue for stairs (and ground due to skyshine).
Cable penetrations under
west wall must be filled
with grout or similar

## Slide 8: Cave 1 at 100 mA
CAVE 1 | Dose rate | 
 | [mrem/h] | 
Roof 100% loss | 2973 | 
Roof 1% | 30 | 
Penet* 100% | 40621 | 
Penet* 1% | 406 | 
* with current 3.25" Fe shield |  | 
Penetrations are above the beamline – about 8” of steel is needed for same attenuation as the 30” concrete slab. Roof will have to be inaccessible; Depending on results of measurements, full 100 mA may not be feasible at 10 MeV;
Existing BCM would catch a 1% loss (1mA)
3” steel
7.8” steel
30” concrete

## Slide 9: Summary
Side shielding can (just) handle a full 100 nA loss continuously, if we forget skyshine
Short episodes of higher beam loss can be tolerated as mis-stearing, providing they are reliably terminated in < 2 min
Recommendation: BCM should reliably detect beam loss of 200 nA at most