## Slide 1: GPT Simulations: Interaction of FA and Chopper 1
A. Hofler and R. Kazimi

## Slide 2: Model
130 keV beam
  Single particle
  36 particles separated by 10 degrees at 499 MHz
Chopper settings fixed
Solenoid setting
  Installed MFA0I03 setting 1298.57 mA (used November 2016-July 2018)
    Corresponds to focal length 0.37 m for beam at r=3 mm
  Jay solenoids set to produce the same focal length for beam at r=3 mm

## Slide 3: MFA abutting CH1
Solenoid | r (mm)
RF Only | 17.13
Installed FA | 17.09
32 mm | 16.91
38 mm | 16.80
45 mm | 16.67
57 mm | 16.36

## Slide 4: MFA abutting CH1 2X setting
Solenoid | r (mm)
RF Only | 17.13
Installed FA | 17.06
32 mm | 16.68
38 mm | 16.47
45 mm | 16.21
57 mm | 15.59

## Slide 5: MFA abutting CH1
Solenoid | r (mm)
RF Only | 17.13
Installed FA | 17.09
32 mm | 16.91
38 mm | 16.80
45 mm | 16.67
57 mm | 16.36

## Slide 6: MFA center shifted to 10 cm upstream CH1
Solenoid | r (mm)
RF Only | 17.13
Installed FA | 17.13
32 mm | 17.10
38 mm | 17.08
45 mm | 17.04
57 mm | 16.94

## Slide 7: MFA center shifted to 15 cm upstream CH1
Solenoid | r (mm)
RF Only | 17.13
Installed FA | 17.13
32 mm | 17.12
38 mm | 17.11
45 mm | 17.10
57 mm | 17.07

## Slide 8: MFA center shifted to 20 cm upstream CH1
Solenoid | r (mm)
RF Only | 17.13
Installed FA | 17.13
32 mm | 17.13
38 mm | 17.12
45 mm | 17.12
57 mm | 17.10

## Slide 9: MFA center shifted so Bz=1% Peak Bz at entrance to CH1
Solenoid | Z extent (cm) | Z shift abutting (cm) | Z shift 1% Peak (cm)
Installed | 6.5 | 3.25 | 6.4
32 mm | 10.16 | 5.08 | 13.8
38 mm | 10.16 | 5.08 | 15.9
45 mm | 10.16 | 5.08 | 18.1
57 mm | 10.16 | 5.08 | 22.3
Solenoid | r (mm)
RF Only | 17.13
Installed FA | 17.13
32 mm | 17.12
38 mm | 17.12
45 mm | 17.11
57 mm | 17.11