## Slide 1: Polarized Positrons for NP & HEP
US-Japan Collaboration Meeting
February 25, 2019
Polarized Electrons for Polarized Positrons (PEPPo)
Why not PEPPo for HEP (ILC, CLIC, LHeC) ?
R&D Topics
Joseph Grames, Carlos Hernandez-Garcia, Matt Poelker
Center for Injectors and Sources

## Slide 2: CEBAF @ 12 GeV
Users: 1500 (230 Institutions/30 Countries)
Multiplicity: 4 Halls (simultaneously)
Beam Polarization: >85% (as high as 90%)
Beam Energy: 11 GeV (ABC) / 12 GeV (D)
Beam Power: 1 MW (85 mA @ 11 GeV)
Cryogenics: Two 4.5 kW plants @ 2.1 K

## Slide 3: High Impact Physics
Polarized electron beams have supported some of the highest impact results from the JLab program:
  The strangeness distribution in the nucleon (HAPPEX and G0)
  Precision Tests of the Standard Model (QWeak)
  Measurement of the neutron skin in 208Pb
  GE/GM of the proton
High-P photocathode development in US motivated by HEP (SLAC) and NP (JLab) resulted from successful DOE SBIR program grants.

## Slide 4: Polarized Positron Beams at Jefferson Lab ?
Unpolarized positron beams offer greater precision
  Comparison of e- with e+ tests our understanding of two photon effects
Polarized positron beams provide a key tool
  Unraveling nucleon structure through the measurement of charge-sensitive General Parton Distributions
  Expand the nature of these tests (e.g. for GE/GM via polarization transfer)
Jefferson Lab Positron Working Group (formed 2016)
  120 members (>90% are Users), and growing…
  39 institutions
“Physics Program with Positron Beams at CEBAF 12 GeV “ (July 2018)
PAC Response: “These measurements all have significant physics interest. The proposers should carefully evaluate feasibility and present the best case possible in a future proposal.”

## Slide 5: PEPPo : Exploit Spin Transfer of Electromagnetic Shower
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
Polarized Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Polarized Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)
Longitudinal spin polarization passes from incident electron beam to bremsstrahlung to outgoing pair-produced positrons in the electromagnetic shower.

## Slide 6: PEPPo : Principle of Operation
1. BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
e+
2. PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
3. Phase Space Definition
The emittance of the positron beam is defined by slits and magnetic fields
S1
D
D
S2
Positron Transverse and Longitudinal Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
4. COMPTON TRANSMISSION POLARIMETER
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
6

## Slide 7: PEPPo : Demo Experiment @ CEBAF Injector
J. Grames, E. Voutier et al., JLab Experiment E12-11-105 (2011)
Demonstrate feasibility to produce highly spin polarized positrons from GaAs/GaAsP spin polarized electron source at low beam energy and with low power target.
CEBAF Injector (8 MeV, 1mA, 85% polarization
Production Target
(W 1mm)
PEPPo possible due to support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and the Jefferson Science Associates.

## Slide 8: PEPPo : Production of Highly Spin Polarized Positrons
Phys. Rev. Lett. 116 (2016) 214801
electron beam polarization
85.2 ± 0.6 ± 0.7 %
Whenever producing e+ from e-, polarization is coming for free, if initial electrons are polarized.

## Slide 9: PEPPo : (Polarization, Yield) vs. Energy
R. Dollan, K. Laihem, A. Schälicke, NIM A 559 (2006) 185,
J. Dumas, J. Grames, E. Voutier, JPos09, AIP 1160 (2009) 120
J. Dumas, Doctorate Thesis (2011)
Optimum energy
Optimum
FoM
The polarization distribution of generated positrons is dominated by low-energy events.
The positron energy at the optimum FoM (P2I) is about half of the electron beam energy.

## Slide 10: CEBAF: Positron scheme using the 123 MeV injector
Positrons would be created at the CEBAF injector, using the 123 MeV electron beam.
60 MeV positrons maximizes FoM (P > 60%, I < 100 nA)
6 MeV positrons maximizes flux (P < 10%, I > 1 mA)
Positron source should have tunability
to optimize for Intensity or Polarization
Sz

## Slide 11: ILC : Positron Polarization from the Tune Up Source?
What is expected (w/o any cuts) for a 3 GeV spin polarized electron beam over range of target thickness (5mm – 16 mm)
Thicker targets improve yield of lowest energy positrons, and provide a degree of spin filtering.
Thinner targets conversely improve yield of highest energy positrons, and with less impact by spin filtering.
E(e+) | N(e+)/N(e-) | <Sz> | P (%)
150 MeV | 0.436 | 0.23 | 21
350 MeV | 0.056 | 0.41 | 37
E(e-)=3 GeV
W=16mm

## Slide 12
What is expected (w/o any cuts) if the electron drive beam energy were reduced to 1 GeV and 10 mm respectively.
Small reduction in target thickness has the effect of increasing yield (at this lower electron beam energy).
Target thickness has less impact when positron energy large fraction of electron energy.
E (e-) | Target | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 16 mm | 0.436 | 0.23 | 21
1 GeV | 10 mm | 0.178 | 0.39 | 35
E (e-) | Target | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 16 mm | 0.056 | 0.41 | 37
1 GeV | 10 mm | 0.018 | 0.69 | 62
E(e+)=150 MeV
E(e+)=350 MeV
ILC : Positron Polarization from the Tune Up Source?

## Slide 13: GaAs Electron Sources : Machine Parameters
Parameter \ Machine => | CEBAF | SLC | JLab/FEL | Cornell ERL | LHeC | eRHIC | CLIC | ILC | JLEIC(e+) | CEBAF (e+)
Polarization | Yes | Yes | No | No | Yes | Yes | Yes | Yes | Yes | Yes
Number electrons/microbunch | 2.5 x 106 | 1 x 1011 | 8.3 x 108 | 4.8 x 108 | 1 x 109 | 2.2 x 1010 | 6 x 109 | 3 x 1010 | 1.2 x 1010 | 2.5 x 108
Number of microbunches | CW | 2 | CW | CW | CW | CW | 312 | 3000 | 900 | CW
Width of microbunch | 50 ps | 2 ns | 35 ps | 2 ps | 100 ps | ~ 100 ps | ~ 100 ps | ~ 1 ns | 100 ps | 50 ps
Time between microbunches | 2 ns | 61.6 ns | 13 ns | 0.77 ns | 25 ns | 71.4 ns | 0.5002 ns | 337 ns | 1.33 ns | 4 ns
Microbunch rep rate | 499 MHz | 16 MHz | 75 MHz | 1300 MHz | 40MHz | 14MHz | 1999 MHz | 3 MHz | 750 MHz | 250 MHz
Width of macropulse | - | 64 ns | - | - | - | - | 156 ns | 1 ms | 1.1 ms | -
Macropulse repetition rate | - | 120 Hz | - | - | - | - | 50 Hz | 5 Hz | 50 Hz | -
Charge per micropulse | 0.4 pC | 16 nC | 133 pC | 77 pC | 500 pC | 3.6 nC | 0.96 nC | 4.8 nC | 2 nC | 40 pC
Charge per macropulse | - | 32 nC | - | - | - | - | 300 nC | 14420 nC | 1800 nC | -
Average current from gun | 200 uA | 2 uA | 10 mA | 100 mA | 20 mA | 50 mA | 15 uA | 72 uA | 88 uA | 10 mA
Average current in macropulse | - | 0.064 A | - | - | - | - | 1.9 A | 0.0144 A | 0.034 A | -
Duty Factor | 2.5 x 10-2 | 2.8 x 10-7 | 2.6 x 10-3 | 2.6 x 10-3 | 4 x 10-3 | 1.4 x 10-3 | 0.2 | 3x10-3 | 2.6 x 10-3 | 1.2 x 10-2
Peak current of micropulse | 8 mA | 8 A | 3.8 A | 38.5 A | 5 A | 35.7 A | 9.6 A | 4.8 A | 20 A | 0.8 A
Current density* | 4 A/cm2 | 10 A/cm2 | 19 A/cm2 | 500 A/cm2 | 100 A/cm2 | 182 A/cm2 | 12 A/cm2 | 6 A/cm2 | 20 A/cm2 | 16 A/cm2
Laser Spot Size* | 0.05 cm | 1 cm | 0.5 cm | 0.3 cm | 0.5 cm | 0.5 cm | 1 cm | 1 cm | 1 cm | 0.10 cm
Demonstrated
Proposed (excuse outdated values)
* Loose estimates
My Speculations

## Slide 14: R&D Topics
PEPPo Option for High Energy Physics Colliders
  Collaborating with KEK to evaluate the PEPPo concept as applied to ILC design parameters.
High Voltage Polarized Electron Source (>400kV)
  Extending the capability for reliably applying very high voltage w/o field emission or breakdown to a GaAs polarized source for high bunch charge (nC) operation (R&D activity of Carlos Hernandez-Garcia, CIS)
High Current Polarized Electron Source (>10 mA)
  Mitigating the QE degradation of GaAs in high voltage photogun to achieve >1000C charge lifetime at mA current (PhD thesis work of Josh Yoskowitz, Old Dominion University)
  Evaluating DBR/GaAs photocathodes that exhibit very high quantum efficiency (>5%)
Polarized Positron Collection Experiment (PEPPo II)
  Designing, building and testing a positron beam collection system to optimized to achieve a new metric of spin polarized source luminosity.
  Collaborating with P3 (IN2P3, CERN, Orsay, Mainz) to develop low energy high power polarized production system.
  Developing proposal for new PhD student on this topic.
14

## Slide 15: Traditional Vent-Bake Photogun
The 350 kV FEL vent-bake gun is based on large bore insulators
Large areas at high voltage (field emission, polishing)
Requires large HVPS SF6 tank connected directly to electrode
Takes 4 weeks to replace a photocathode (no load-lock)
Challenging to achieve 10^-12 Torr needed for high-P photocathodes
Electrodes
Vacuum chamber
Ceramic stand-offs
Corona shield
High voltage feed
(3) 1000 l/s NEG pumps
RGA, extractor gauge
and leak valve
Photocathode
Photocathode retractor mechanism
80 cm
End flange
End flange
Anode
15

## Slide 16: Inverted High Voltage Photogun Approach
High peak current means managing the required high voltage inside/outside of the gun
  Vacuum side (triple point, shed, beam effects)
  Air side (linearity, breakdown, charging)
  Cathode-Anode Gap (FE, gas desorption, x-rays)

## Slide 17: 350 kV Inverted Insulator Photogun
Optimized triple point shields and mildly conductive insulators.
Maintain maximum field strength < 10 MV/m

## Slide 18: Jefferson Lab : High Voltage (200-350 kV) Inverted Insulator Photoguns
CEBAF 200 kV
Installed June 2018
(operates at 130kV until an upgrade in 2020)
UITF 350 kV
Polarized Gun
Under assembly
GTS 350 kV
In operation since Nov 2016 with CsK2Sb photocathode

## Slide 19: Metric of Success: High Voltage without Field Emission
Reached
360 kV in 70 hours
Vacuum and radiation levels indistinguishable from background at 350kV
10 MV/m at 350 kV

## Slide 20: Application: Magnetized Beam from 350 kV Photogun at the Gun Test Stand
Load-lock inverted insulator photo-gun (multiple photocathodes), like CEBAF geometry.
Cable connection from HVPS to gun.
Over 1000 hours operating >300kV; HV conditioning about 1 week.
Operating with CsKSb photocathodes at >10 mA average current, and 0.7nC bunch charge.
Magnetized Beam LDRD, PI's: R. Suleiman and M. Poelker

## Slide 21: R&D : >400 kV load-lock polarized photogun with cable interface to HVPS
CEBAF 200 kV Gun
350 kV GTS Gun
R28 200kV
R30 300kV
R350, 400kV ?
12"
CONCEPT !
The next step:
400 kV R&D !

## Slide 22: 2019-2020 : our 400kV R&D plan
Can the commercial plugs and receptacles be operated and sustained >400kV for days?
What is the highest voltage limit before breakdown?
Design coupling between large insulator and R350 cable plug
  (spinoff: partner with industry to design new conical insulator to mate with commercial R350 cable plug as done now for 200kV and 300kV)
Test this configuration first in an SF6-filled chamber
Design electrode and triple junction shields
Build and test in vacuum, likely will need larger chamber to keep gradient < 10 MV/m at 450kV
Success? Then:
Our HV chamber
22

## Slide 23: Summary
Jefferson Lab Users are making the physics case for both high energy polarized and unpolarized positron beams at CEBAF 12 GeV.
PEPPo demonstrated high positron polarization from polarized electrons at low energy w/ small footprint (cost, energy, radioactivity), extensible to high energy.
We are exploring concepts to produce positron beams for both CEBAF (CW, pC, mA) and JLEIC (pulsed, nC, mA) with tunability on intensity and polarization.
Recent progress is promising to develop a 400 kV polarized source based on the inverted insulator geometry necessary for >nC bunch charge.
Can the PEPPo concept applied to the ILC electron driven positron source turn a “no polarization” scheme into a “polarization scheme”, even for a later upgrade?

## Slide 24
Backup Slides

## Slide 25: Areas of Interest
Polarized Photocathodes – generation of high peak current and limitations
Surface Charge Limit (Surface Photovoltage Effect), reduces NEA of GaAs: Photoelectrons trapped near GaAs surface produce opposing field that reduces NEA resulting in QE reduction at high laser power (LP).
Higher Gun HV suppresses SCL!

## Slide 26: Areas of Interest
Lasers – high peak power short pulse rf-synchronized lasers
Beam – managing every electron counts for photocathode lifetime
Accounting for loss at the ppm level is significant, and becomes increasingly challenging with bunch charge
Digital gain switching provided CEBAF with 250 MHz and 32 MHz rep rate beam; the lower rep rate can be exploited for UITF and phase locking can be investigated to have option at CEBAF for many rep rates

## Slide 27: CEBAF: High Energy (11 GeV) with Low Current + Low Bunch Charge
27

## Slide 28: Polarized Positrons at the Jefferson Lab Electron Ion Collider
A polarized positron injector suitable for the Jefferson Lab Electron Ion Collider (JLEIC) has also been considered.
L ≥1033cm-2s-1 Pe+≥40%
Iave > 10 nA (~1010 e+/s)
Ipeak > 4 mA (~1013 e+/s)
e+
Challenge is accumulating positron bunch charge with JLEIC bunch pattern.

## Slide 29: JLEIC: Low Energy (50 MeV) with Low Current + High Bunch Charge
200 keV polarized e-
8 pC @ 748.5 MHz
(DF=100%)
50 MeV polarized e-
4 nC bunches @ 748.5 MHz
Accumulator Ring (36m)
500-turn
phase-space painting
Bunch
Management
50 MeV polarized e-
4 nC @ 17 MHz
Positron Conversion/Collection Efficiency ~ 5 x 10-4
60% in polarization
25 MeV Polarized e+
0.2 pC @ 17 MHz
(DF=0.26%)
to CEBAF
Harmonic kicker
Extraction
Polarized Electron
50 MeV Injector
Power on target
3.4 MW peak power
0.6 kW average
350 keV polarized e-
2 nC @ 17 MHz
(DF=0.26%)
Polarized Electron Source

## Slide 30: ILC : Spin Polarized Electron Driven Source ?
What is expected (w/o any cuts) if the electron beam energy were lowered, for the same target thickness (16mm).
Lower electron beam energy results in lower yield, expectedly, preferentially at low positron energy.
Lower electron beam energy results in high spin polarization at same positron energy
E (e-) | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 0.436 | 0.23 | 21
1 GeV | 0.091 | 0.44 | 40
E (e-) | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 0.056 | 0.41 | 37
1 GeV | 0.007 | 0.71 | 64
E(e+)=150 MeV
W=16mm
E(e+)=350 MeV
W=16mm