## Slide 1: Polarized Injector Update
Riad Suleiman
Center for Injectors and Sources
QWeak Collaboration Meeting
July 17-18, 2009

## Slide 2: Outline
Higher Gun Voltage & Inverted Gun
Two Wien Slow Helicity Reversal
Fast Helicity Reversal
Other Improvements

## Slide 3: Upcoming Parity Experiments
Experiment | Hall | Start | Energy (GeV) | Current (µA) | Target | Apv (ppm) | Maximum Charge Asym (ppm) | Maximum Position Diff (nm)
HAPPEx-III | A | Aug 09 | 3.484 | 85 | 1H (25 cm) | 16.9±0.4 | 1 | 10
PVDIS | A | Oct 09 | 6.068 | 85 | 2H (25 cm) | 63±3 | 1 | 10
PREx | A | March 10 | 1.056 | 50 | 208Pb (0.5 mm) | 0.500±0.015 | 0.100±0.010 | 2
QWeak | C | May 10 | 1.162 | 180 | 1H (35 cm) | 0.234±0.005 | 0.100±0.010 | 2
Achieved |  |  |  |  |  |  | 0.4 | 1

## Slide 4: Higher Voltage & Inverted Gun
Increase gun voltage up to 150 kV to reduce space charge emittance growth at higher bunch charge (higher current)
  Beam quality including transmission improves
  Problem: Field emission at higher voltage degrades lifetime → solution: Inverted Gun
Chart: Transmission vs Gun Voltage
| 11.7 | 26 | 51.4 | 74.8 | 98.2 | 122.2 | 148 | 170.5 | 198
115kV | 96.5812 | 92.6923 | 82.4903 | 73.262 | 67.0061 | 61.784 | 57.6351 | 54.8974 | 51.3131
100kV | 99.0099 | 92.7419 | 77.8431 | 66.7553 | 59.2 | 52.7911 | 47.451 | 44.2153 | 40.5941
85kV | 93.8931 | 83.274 | 67.2761 | 56.2421 | 47.6465 | 40.9161 | 35.0449 | 30.9244 | 27.2059
70kV | 77.2727 | 61.6327 | 45.2479 | 35.9712 | 29.0608 | 23.7197 | 19.8027 | 17.2973 | 14.5238
Chart: Electron Bunchlength vs Gun Voltage
| 0.8 | 12 | 51 | 98 | 148 | 198
115kV | 43.771 | 60.6061 | 104.3771 | 138.0471 | 161.6162 | 188.5522
100kV | 43.8596 | 70.1754 | 96.4912 | 125.731 | 149.1228 | 152.0468 | 181.2865 | 198.8304 | 213.4503 | 233.9181
85kV | 53.8721 | 77.4411 | 107.7441 | 144.7811 | 158.2492 | 181.8182 | 208.7542 | 232.3232 | 255.8923 | 269.3603
70kV | 50.8547 | 77.7778 | 113.6752 | 152.5641 | 173.5043 | 203.4188 | 227.3504 | 245.2991 | 260.2564 | 278.2051

## Slide 5
Move away from “conventional” insulator used on all GaAs photo-guns today: expensive, months to build, prone to damage from field emission.

## Slide 6
e-
Medical x-ray technology
Present Ceramic
Exposed to field emission
Large area
Expensive ($50k)
e-
Inverted Gun
New Ceramic
Compact
$5k

## Slide 8
Inverted Gun installed on July 14, 2009, beam in two weeks

## Slide 9: Two Wien Slow Helicity Reversal
Insertable Half Wave Plate (IHWP) provides slow helicity reversal of laser polarization:
  Cancels Electronic cross talk and Pockels Cell Steering
  Residual Linear polarization effects do not cancel
  Spot size asymmetry, which we cannot measure, does not cancel
New: Slow helicity reversal of electron polarization using two Wien Filters and solenoid:
  Wien settings constant
  Solenoid rotates spin by ±90° with ±B but focuses beam as B2
    Maintain constant Injector and Accelerator configuration
  Cancels all helicity-correlated beam asymmetries from the Injector including spot size
  Can be used up to maximum Gun voltage of 140 kV
  Will be installed in January 2010

## Slide 10
“Spin Flipper”
Vertical Wien = 90°
Azimuthal Solenoid = ± 90°
“Long. Pol. for Halls”
Horizontal Wien = -90° → +90°
+ Solenoid current
- Solenoid current

## Slide 11: Fast Helicity Reversal
We have been using 30 Hz helicity reversal:
  Power line 60 Hz frequency is major source of noise in parity experiments
  For 30 Hz reversal, T_Stable (= 33.333 ms) contains exactly two cycles of 60 Hz line noise → this reversal cancels line noise
Problem:
  There are other sources of noise at low frequencies, i.e., target density fluctuations, beam current fluctuations
  → Cause larger widths of helicity correlated distributions, double-horned distributions
Solution: Use fast helicity reversal (faster than 30 Hz)
Studied beam properties at 1 kHz (Oct 2008 – April 2009)
    Fast reversal of helicity Pockels Cell was possible using new optically-driven fast high voltage switch designed by J. Hansknecht

## Slide 12
30 Hz, T_Stable = 33.333 ms, T_Settle = 500 µs
1 kHz, T_Stable = 0.980 ms, T_Settle = 60 µs

## Slide 13
Summary of Fast Helicity Reversal Studies
  Fast Helicity Reversal is needed:
    Huge reduction of noise from target density fluctuations
    Reduces noise on beam current by factor of 4
    Reasonable reduction in beam position noise
  Achieved Pockels Cell T_Settle of 60 µs
  Future Parity Experiment:
  New Helicity Board to be installed in July 2009
Experiment | Frequency | Clock | Pattern
HAPPEx III & PVDIS | 30 Hz | Line-Locked | Quartet
PREx | 240 Hz | Line-Locked | Octet
QWeak | 1 kHz | Free | Quartet

## Slide 14: Other Developments
Charge Feedback: Ability to do Charge Feedback using either Pockels Cell or Intensity Attenuator without or with the option to correct for Pockels Cell hysteresis
Helicity Magnets: Ability to do Position Feedback using the newly commissioned helicity magnets located in the 5 MeV region of the Injector
Pockels Cell Motion: Pockels Cell is equipped with remote controlled x & y translational stage for minimizing position differences while measuring the position differences of electron beam
Photocathode Rotation: With Load-Locked Gun, now we can zero the offset term in the charge asymmetry caused by the vacuum window birefringence by rotating the photocathode