## Slide 1: UITF Gun through 2-7 Quarter Optimization
Alicia Hofler
March 18, 2016
UITF Internal Review

## Slide 2: Outline
Optimization setup
Optimization results
Conclusion

## Slide 3: Optimization Setup
Multi-objective optimization using genetic algorithm (GA)
  Non-Sorting Genetic Algorithm II (K. Deb et al., 2002) and Differential Evolution (K. Price and R. Storn, 1996) based tool: gdfmgo from Pulsar Physics (http://www.pulsar.nl/gpt)
  Population size: 96 individuals
  Generations: 398 over 5 chained runs
Beamline simulation with General Particle Tracer (also from Pulsar Physics)
Beamline model
  Follows drawing layout from cathode to valve at exit of quarter cryomodule (2-cell 7-cell)
    15o dipole, RF choppers, beam diagnostics, Wien , apertures, etc. omitted
    Straight beamline
  200 kV D.C. gun
  Field maps for solenoids and RF elements
    Field map radial extent between 1.2 cm (3D solenoid field maps from Jay Benesch, JLAB-TN-14-022) and 15 cm (2D solenoid field maps from CIS)
    2.5D field map fr Buncher
    1D field profiles gor gun, 2-cell, and 7-cell cavities
1 nA beam current at 750 MHz (no space charge)
  GaAs cathode
    Thermal electron energy 0.025 eV
    Thermal emittance 0.061 mm mrad
    Gaussian transverse momentum distributions
  21.3 ps bunchlength
    Gaussian temporal distribution
  213 μm beam size
    Gaussian spatial distributions
  10k macro-particles
Macro-particles removed
  Backward traveling
  Outside defined fieldmap regions

## Slide 4: Optimization Setup
Optimization Variables (14)
  3 phases (degrees) and 3 peak amplitudes (V/m) of buncher, 2-cell, and 7-cell cavities
    Rough guess for amplitude limits
    Buncher phase ±50o around zero-crossing
    2-cell and 7-cell phases ±180o
  6 solenoid currents
    CEBAF control system limits
    MFD3K20B = -MFD3K02A
  2 quadrupole integrated field (Gauss)
    CEBAF control system limits
Element positions fixed and bunch characteristics at cathode fixed
Optimization goals
  At exit of quarter minimize
    Standard deviation of kinetic energy
    Transverse beam size
    Bunchlength (σt)
Additional constraints
  No lost macro-particles
  Average kinetic energy ranges at exit of cavities
  Maximum standard deviation for kinetic energy at exit of buncher and 7-cell
  Maximum beam size and bunchlength (σt) at exit of 7-cell
  Transverse emittance below 1 mm mrad at exit of 7-cell

## Slide 5: Qualifying Final Front Solutions

## Slide 6: Kinetic Energy and Energy Spread

## Slide 7: Sample Solutions (Ek, bunchlength, and beam size)

## Slide 8: Sample Solutions (Courant-Snyder parameters)

## Slide 9: Sample Solutions (transverse normalized emittances)

## Slide 10: Conclusion
Simple model optimization suggests UITF can support HDIce
Further improvement possible
  Some variables have head room
  Constraints imposed to ensure “reasonable” beam quality can be relaxed
  Add constraints to produce more standard optics in lenses and quadrupoles
Future work
  Verify performance with more realistic model that includes 15o dipole, RF choppers, MeV line, apertures, and more macro-particles
  Consider performing optimizations with 15o dipole and RF choppers
  Optimizations needed for 100 μA (space charge) to support quarter commissioning