## Slide 1
Production of Highly Polarized Positrons Using Polarized Electrons at MeV Energies
(…or why PEPPo is like the Red-Billed Oxpecker)
Joe Grames
Jefferson Laboratory

## Slide 2
Acknowledgments

## Slide 3
Outline
Motivation
PEPPo Experiment
Polarized Positron R&D Efforts
Summary
Jefferson Lab Positron Working Group

## Slide 4
4
Jefferson Lab’s CEBAF Accelerator
CW electron beam to 3 halls
Electron Polarization 85-90%
Max Energy: 11 GeV(ABC) / 12GeV(D)
Max Current: 200 uA
The charge and polarization of the probe beam provide degrees of freedom which constrain physical observables.
Jefferson Lab physics that would benefit a polarized positron beam:
  Interference (Two Photon, GPD’s)
  Standard Model Test (Dark Matter, C3q)
Proposed physics that may benefit investigation:
  Electron Ion Collider (spin EMC, Strange/Charm GPD)
  Materials Science (spintronic devices, ferromagnetics)
Polarized Positron Beam Applications

## Slide 5
M.P. Rekalo, E. Tomasi Gustafsson, NPA 742 (2004) 322 C. Carlson, M. Vanderhaeghen, ARNPS 57 (2007) 171
Combining Polarized electrons and positrons allows a model independent separation of the electromagnetic form factors of the nucleon.
Unpolarized e± elastic scattering and polarization transfer observables from the nucleon involve up to 5 unknown quantities.
5 unknown contributions for 6 independent observables
Cross Section
Polarization
Transfer
Electromagnetic Form Factors

## Slide 6
P(e+) = 73 ± 15(stat) ± 19(syst) %
Compton Backscattering (KEK)
T. Omori et al, PRL 96 (2006) 114801
Helical Undulator (SLAC E166)
G. Alexander et al, PRL 100 (2008) 210801
P(e+) = 80 ± 7(stat) ± 9(syst) %
47.7GeV
Polarized b+ Decay
L.A. Page & M. Heinberg. Phys. Rev.
106(6):1220-1224 (1957)
Polarized due to parity non-conservation in the weak interaction
P(e+) ~ 40 %
Sokolov-Ternov Effect
D. Barber , AIP Conf. Proc. 588, 338 (2001)
HERA 27.5 GeV e+/e-
P(e+) ~ 70 %
Polarized Positron Options

## Slide 7
7
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
E.G. Bessonov, A.A. Mikhailichenko, EPAC (1996) A.P. Potylitsin, NIM A398 (1997) 395
Polarized Bremmstrahlung
Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)

## Slide 8
100nA – 1mA useful for CEBAF NP
Positron Yield
Photon energy k up to electron energy T1
Cross section decreases as 1/k
Positron energy T1 to photon energy k-2mc2
Cross section essentially energy independent
Bremsstrahlung
Pair Production

## Slide 9
QE ~ 5%, 30 μA/mW
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 μA/mW
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 μA/mW
Pol ~ 85% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
Timeline of Polarized Source at CEBAF
Spin Polarized program at JLab (particularly our PV Users) have
driven the need for improved performance over last 20+ years
GaAs Photocathode Evolution

## Slide 10
Polarized Electron Source Intensity
Year
Intensity (mA)
First GaAs photogun
Low-P Bulk GaAs
High-P GaAs/GaAsP
Parameter | Value | Value
Laser Rep Rate | 499 MHz | 1500 MHz
Laser Pulse Length | 30 ps | 50 ps
Laser Wavelength | 780 nm | 780 nm
Laser Spot Size | 0.45 mm | 0.35 mm
Photocathode | GaAs/GaAsP | GaAs/GaAsP
Gun Voltage | 100 kV | 200 kV
Beam Current | 1 mA | 4 mA
Run Duration | 8.25 hr | 1.4 hr
Extracted Charge | 30.3 C | 20 C
Charge Lifetime | 210 C | 80 C
Fluence Lifetime | 132 kC/cm2 | 83 kC/cm2
Bunch Charge | 2.0 pC | 2.7 pC
Peak Current | 67 mA | 53 mA
Peak Current Density | 42 A/cm2 | 55 A/cm2
J. Grames et al., PAC07, THPMS064
R. Suleiman et al., PAC11, WEODS3

## Slide 11
BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
COMPTON TRANSMISSION
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
S1
D
D
S2
Pe+
Positron Transverse and Momentum Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
Ee = 6.3 MeV
Ie = 1 µA
T1 = 1 mm W
Geant4
PEPPo
J. Dumas, PhD Thesis (2011)
PEPPo measured the longitudinal polarization transfer from 8.25 MeV/c e- to e+ in the 3.07-6.25 MeV/c momentum range.
PEPPo - Principle of Operation

## Slide 12
PEPPo @ CEBAF Injector
Compton
Polarimeter
(DESY/Cornell)
Positron Collection
Magnets
(Princeton/SLAC)
Pair
Creation
Target
Mott
Polarimeter

## Slide 13
T1
T2
S1
S2
D
D
e+
e-
Positron Collection
Na22
Two NaI detectors measured coincidence of back-to-back photons emitted by annihilation of positrons in a viewscreen.
13
pe-= 8.2 MeV/c
4 MeV/c e+
Viewscreen 0.011 thick @ 45 deg to beam line
99.5% aluminum oxide Al2O3
0.5% chromium doped Al2O3/Al2O3Cr2O3
Positron Detection

## Slide 14
14
Detected e+ rate (1 e+ per 109 e-)
Solid Angle (0.1 sr)
GEANT annihilation probability (1/400)
Coincidence detector efficiency (0.49 @ 511keV)
1 e+ per 105 e-
Positron Yield

## Slide 15
Electrons or Positrons radiate polarized photons by Bremmstrahlung in reconversion target. Energy dependent Compton scattering of photons transmitted through polarized target correspond to polarization of incoming Electrons or Positrons (aligned or anti-aligned).
μ1 - Compton absorption coefficient
L - target length
P3 - photon polarization (long.)
Pe - electron/positron polarization
PT - target polarization
Ae - analyzing power
g
Target (Densimet D17K)
90.5% W, 7%, 2.5% Cu
e-
Pe-
e+
Pe+
Compton Transmission Polarimetry

## Slide 16
C
A
L
O
R
I
M
E
T
E
R
e+
g
Trigger Scintillator
10mil Al window
Reconversion
Target
Positrons are detected in coincidence between a thin trigger scintillator placed prior to the reconversion target and the central crystal (PMT5) and tagged by e- helicity.
Trigger Scintillator
Coincidence
Calorimeter
Energy Integrated Asymmetry
WITHOUT
Coincidence
WITH
Coincidence

## Slide 17
511 keV from e+ annihilation at rest
Bremsstrahlung
end-point
Energy (FADC units)
Energy Integrated Asymmetry

## Slide 18
Summary of Positron Asymmetries

## Slide 19
Positron Analyzing Power
GEANT4 simulations allow to link the measured electron analyzing power to the expected positron analyzing power of the PEPPo Compton transmission polarimeter.
See A. Adeyemi talk

## Slide 20
Demonstrated efficient polarization transfer from 8.2 MeV/c electrons to positrons, expanding polarized positron capabilities from GeV to MeV accelerators.
e- beam polarization
85.2 ± 0.6 ± 0.7 %
Positron Polarization Results
(PEPPo Collaboration) D. Abbott et al., Phys. Rev. Lett. 116 (2016) 214801
Whenever producing e+ from e-, polarization is coming for free
if initial electrons are polarized.

## Slide 21
P. Aderley1, A. Adeyemi4, P. Aguilera1, M. Ali1, H. Areti1, M. Baylac2, J. Benesch1,
G. Bosson2, B. Cade1, A. Camsonne1, L. Cardman1, J. Clark1, P. Cole5, S. Covert1,
C. Cuevas1, O. Dadoun3, D. Dale5, J. Dumas1,2, E. Fanchini2, T. Forest5, E. Forman1,
Freyberger1, E. Froidefond2, S. Golge6, J. Grames1, P. Guèye4, J. Hansknecht1,
P. Harrell1, J. Hoskins8, C. Hyde7, R. Kazimi1, Y. Kim1,5, D. Machie1, K. Mahoney1,
R. Mammei1, M. Marton2, J. McCarter9, M. McCaughan1, M. McHugh10, D. McNulty5, T. Michaelides1, R. Michaels1, C. Muñoz Camacho11, J.-F. Muraz2, K. Myers12,
Opper10, M. Poelker1, J.-S. Réal2, L. Richardson1, S. Setiniyazi5, M. Stutzman1,
R. Suleiman1, C. Tennant1, C.-Y. Tsai13, D. Turner1, A. Variola3, E. Voutier2,11,
Y. Wang1, Y. Zhang12
1 Jefferson Lab, Newport News, VA, US 2 LPSC, Grenoble, France 3 LAL, Orsay, France
4 Hampton University, Hampton, VA, USA 5 Idaho State University & IAC, Pocatello, ID, USA
6 North Carolina University, Durham, NC, USA 7 Old Dominion University, Norfolk, VA, US
8 The College of William & Mary, Williamsburg, VA, USA 9 University of Virginia, Charlottesville, VA, USA 10 George Washington University, Washington, DC, USA 11 IPN, Orsay, France
12 Rutgers University, Piscataway, NJ, USA 13 Virginia Tech, Blacksburg, VA, USA
PEPPo Collaboration
Many thanks for advice, equipment loan, GEANT4 modeling support, and funding to
SLAC E-166 Collaboration
International Linear Collider Project
Jefferson Science Association Initiatives Award
Orsay, September 14-16, 2016
13/19

## Slide 22
Positrons at JLEIC
A pulsed beam with low average current (~10 nA) but significant bunch charge (~2pC) and high macro-pulse peak current (~50µA) is required for injection into JLEIC.
20 times CEBAF
A group (J. Grames, J. Guo, F. Lin, V. Morozov, E. Voutier) is exploring a polarized positron injector suitable for JLEIC.
L ≥1033cm-2s-1 Pe+≥40%

## Slide 23: JLEIC Positron Production Scheme
10 MeV polarized e-
1.33 pC @ 1500 MHz
= 2 mA
10 MeV pol e-
0.67 nC bunches
@ 1500 MHz
= 1 A
22 m accumulator ring
with 500 turn phase-space painting
bunch focusing
and compression
if needed
10 MeV polarized e-
0.67 nC @ 68.1 MHz
= 46 mA
1 mm W
target
x 10-3
0-9.5 MeV polarized e+
0.67 pC @ 68.1 MHz
= 46 uA
e+ collection
system
x 10-2
5-7 MeV Polarized e+
6.7 fC @ 68.1 MHz
= 460 nA
to CEBAF
22 m
extraction ring
Machine | Electron Source | Storage Ring | Extractor Ring | Positron Source
JLEIC | Ave = 2 mA 1500 MHz DF = 0.8% | Ave = 1 A 1500 MHz DF = 0.8% | Ave = 46 mA 68.1 MHz DF = 0.8% | Ave = 460 nA 68.1 MHz DF = 0.8%
CEBAF (cw) | Ave = 1-10 mA 499 or 250 Mhz DF = 100% | n/a | n/a | Ave = 0.01 - 0.1 uA 499 or 250 Mhz DF = 100%
Accelerator R&D
High-P photocathodes
High bunch charge gun
Electron accumulator
Electron extractor
High power 10kW target

## Slide 24: High Polarization Photocathode R&D
6.4% QE & 84% polarization at 776 nm from strained GaAs/GaAsP superlattice photocathode with GaAsP/AlAsP Distributed Bragg Reflector (DBR)
The highest QE & FOM of any reported high polarization photocathode
Possible to improve both QE & Pol
SBIR partnership
Paper ready for SPIN and APL submission: W. Liu, S. Zhang, M. Stutzman, M. Poelker, Y. Chen, W. Lu, and A. Moy
DBR
Substrate
Photo-cathode
See W. Liu talk

## Slide 25
Higher Voltage (300 kV) Inverted Photo Gun
8 MV/m
11 MV/m
First insulator commissioned to 325 kV
New insulator, getting installed now, supports higher voltage operation
CsK2Sb 1mA

## Slide 26: Multi-Turn Injection
Concept: an orbit bump created near a septum and then slowly reduced as beam being injected (phase-space painting)
A number of painting schemes has been developed
Process can also be simultaneously occurring in vertical and longitudinal dimensions
CERN’s LEIR has a design for 75-turn injection of Pb54+, we plan to push this number to a few hundred to a thousand using low electron emittance
Main injection system components
  Magnetic or electrostatic septum
  Four bumper magnets with ~1 s rise time, reasonably fast fall-off time and ~10 mrad maximum deflection
Injected beam
Accumulator ring
x
x
> Septum thickness + bunch width

## Slide 27
Harmonic Kicker Extraction
Port 1/2
Port3/4, to matched load
Chart: Example: Waveform that kicks 1 in every 10 bunches bunch reprate 476MHz Synthesized with 9 RF harmonics and 1 DC mode
Two technology options for the kicker
Stripline kicker, faster rise time, can synthesize 10s of modes with single device. Consumes more RF power, but power level might be acceptable for low energy 10MeV beam
J. Guo et al. COOL15 TUPF10
Harmonic cavity kicker designed to kick 1 in every 10 bunches using 4 cavities (Y. Huang et al, accepted by PRSTAB). The 5 harmonics prototype was built as shown.
More efficient than stripline, but needs 5 cavities to kick 1 in every 22 bunches, or 7 cavities to kick every 66 /88bunches
Slow rise time, need a 2nd ring., so the kicker can be turned on before bunch train arrives
Harmonic kicker that kicks every 3rd bunch
Empty ring buckets already kicked out to linac
Ring buckets still occupied by bunches
Empty linac buckets
Linac buckets occupied by extracted bunches
JLEIC e+/e- injection requires CEBAF to operate at a reduced bunch reprate of 68MHz (1/22 of 1.497GHz in CEBAF) or its subharmonics to match the 476MHz RF system in JLEIC.
An example is that we use a ring with Nh=89 at 1.497GHz (~18.9m circumference), and kicks out 1 in every 88 bunches with the harmonic kicker, generating a bunch train with ~60 bunches and ~1050m long, leaving a ~19ns gap in the ring to accommodate the rise time for the kickers..
A ring using harmonic kickers to extract bunch train 3 times longer

## Slide 28
High Power Target R&D

## Slide 29
High Power Target R&D

## Slide 30
Summary
The PEPPo technique provides an efficient, reliable, radioactive-less, and low cost method opening access to polarized positron beam to a wide community.
Next steps in low energy scheme of e+ source R&D is optimizing for beam intensity and beam quality.
An experimental program in context of CEBAF 12 GeV, JLEIC and LERF is being explored. If you would like to participate in the newly formed Jefferson Lab Positron Working Group please visit: wiki.jlab.org/pwg

## Slide 31
Synergy
The Hippopotamus and Red-Billed Oxpecker share a positive and synergistic relationship.