## Slide 1
Chart: Magnetic field map including metal shielding near solenoids
Beam gets off axis quickly with the currents, should use correctors to bring it on axis.
ASTRA simulation results cont’d
Chart: 300 kV 0.106 mm viewer 1
| 0 | 2 | 5 | 8 | 10 | 15 | 20 | 25 | 30 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 175 | 180 | 190 | 200 | 205 | 210 | 215 | 220 | 225 | 230 | 235 | 240 | 245 | 250 | 260 | 270 | 275 | 280 | 290 | 300 | 305 | 310 | 325 | 335 | 345 | 350 | 375 | 385 | 390 | 400
ASTRA | 1.6532 | 1.6693 | 1.6067 | 1.4516 | 1.3119 | 0.9273 | 0.6127 | 0.3718 | 0.3403 | 1.0491 | 1.2304 | 1.2373 | 1.1061 | 0.6862 | 0.504 | 0.9325 | 1.1574 | 0.9383 | 0.487 | 0.5337 | 0.7188 | 0.5724 | 0.312 | 0.3028 | 0.3299 | 0.3271 | 0.3338 | 0.5161 | 0.5871 | 0.6366 | 0.6752 | 0.7266 | 0.8224 | 0.965 | 1.1182 | 1.2459 | 1.3372 | 1.3919 | 1.4166 | 1.5431 | 1.6897 | 1.8631 | 2.168 | 2.2133 | 2.1621 | 2.1313 | 2.3903 | 2.5546 | 2.4551 | 2.3667 | 1.9521 | 1.6206 | 1.4428 | 1.06
Measured values | 1.7714 | 1.7775 | 1.7704 | 1.7626 | 1.7071 | 1.6955 | 1.6802 | 1.6048 | 1.5353 | 1.5437 | 1.4785 | 1.1003 | 0.659 | 0.25374 | 0.43979 | 0.84338 | 1.1792 | 1.4508 | 1.4479 | 1.1094 | 0.38868 | 0.42047 | 0.74867 | 1.1531 | 1.0345 | 0.54079 | 0.45355 | 0.58938 | 0.65869 | 0.55215 | 0.32189 | 0.49159 | 0.68473 | 0.86909 | 1.0323 | 1.0938 | 0.47539 | 0.49614 | 0.54158 | 0.63396 | 0.79357 | 0.91425 | 1.0069 | 1.045 | 1.0617 | 1.064 | 1.1167 | 1.4647 | 1.7154 | 1.7361 | 1.6907 | 1.7376 | 1.8783 | 2.1166 | 2.1719 | 2.0662 | 1.6395
Simulation results massively depend on the field maps.
Chart: Magnetic field map without including metal shielding near solenoids
Simulation Study of the Magnetized Electron Beam
Introduction
Electron cooling of ion beam plays an important role in electron ion colliders to obtain the required high luminosity. This cooling can be enhanced using a magnetized electron beam, where the cooling process occurs inside a solenoid field. This presentation provides a comparison between the beam-based magnetization measurements conducted from the magnetized electron beam generated from a DC high voltage photo-gun and simulations from ASTRA and GPT software, as a function of beam size and rotation angle variations along the beamline, for different solenoid currents and ASTRA simulation studies on the magnetic field map dependence on mismatch oscillations.
Sajini A. K. Wijethunga1, J. R. Delayen1, G. A. Krafft2, F. E. Hannon2, R. Suleiman2,
M. Poelker2, J. Benesch2, M. A. Mamun2
1Department of Physics, Old Dominion University, Norfolk, Virginia 23529, USA
2Thomas Jefferson National Accelerator Facility, Newport News, Virginia 23606, USA
Acknowledgement: This work is supported by the Department of Energy, Laboratory Directed Research and Development funding, under contract DE-AC05-06OR23177
Beam Line
Modelling
sajini@jlab.org
Green
Laser
Cathode
Anode
K2CsSb
Photocathode
Cathode
Solenoid
Diagnostic Cross 1
(Slit + YAG Screen)
Diagnostic Cross 2
(Slit + YAG Screen)
Diagnostic Cross 3
(YAG Screen)
Injector Focusing
Solenoid
ASTRA simulation results
Summary and Outlook
Measurements vs Simulations (ASTRA & GPT)
Beam Profile
GPT
ASTRA
Max Bz at the cathode | 0.1511 T
xy_rms, Gaussian | 0.301 mm
t_rms, Uniform | 24 ps
Gun voltage | 300 kV
x_off | 0 mm
y_off | 0.5 mm
Emittance | 0.56 mm mrad/ mm
Rotation angle variation of a diverging beam- 180 A
Rotation angle variation of a converging and diverging beam – 100A
Simulation Parameters
Beam line is mainly consists of a K2CsSb photocathode preparation chamber, DC high-voltage photo-gun operating at 300 kV, cathode solenoid magnet with maximum 400 A, two YAG screen-slit combinations at 0.5 m and 2.0 m, a YAG-screen at 3.75 m, three focusing solenoids, correctors, harp, vacuum pump and dump .
4 m
1D Electric and Magnetic Field maps
Beam line is modeled using ASTRA (A Space Charge Tracking Algorithm) and GPT (General Particle Tracer) software separately.
ASTRA used 1D electric field map and GPT used 2D electric field map.
Magnetic field map is distorted by the steel covers of the focusing solenoids.
MATLAB is used to do the post-processing and calculate the beam sizes and rotation angles.
Measurements:
Beam at 0 A on 1st Screen
ASTRA: Beam at 0 A on 1st Screen
ASTRA: Beam rotation
ASTRA: Energy profile
General formula to find the rotation angle
Converging
At waist 0
Diverging 0
Magnetic field is not uniform in z.
Thus, no transverse equilibrium occurs and unbalanced forces inside the magnetic field cause the mismatch oscillations.
Larmor frequency increases with the B field.
Slit 1-Viewer 2
Slit 1-Viewer 3
Slit 2-Viewer 3
Mismatch Oscillations
Chart: 300 kV 0.106 mm viewer 1
Measured values | 1.7714 | 1.7775 | 1.7704 | 1.7626 | 1.7071 | 1.6955 | 1.6802 | 1.6048 | 1.5353 | 1.5437 | 1.4785 | 1.1003 | 0.659 | 0.25374 | 0.43979 | 0.84338 | 1.1792 | 1.4508 | 1.4479 | 1.1094 | 0.38868 | 0.42047 | 0.74867 | 1.1531 | 1.0345 | 0.54079 | 0.45355 | 0.58938 | 0.65869 | 0.55215 | 0.32189 | 0.49159 | 0.68473 | 0.86909 | 1.0323 | 1.0938 | 0.47539 | 0.49614 | 0.54158 | 0.63396 | 0.79357 | 0.91425 | 1.0069 | 1.045 | 1.0617 | 1.064 | 1.1167 | 1.4647 | 1.7154 | 1.7361 | 1.6907 | 1.7376 | 1.8783 | 2.1166 | 2.1719 | 2.0662 | 1.6395
GPT and ASTRA shows same variations with the measurements.
Gun solenoid magnetizes the beam but also focuses the beam.
Rotation angle influenced by Larmor oscillations in the gun solenoid.
Negative angles occurs due to the beam convergence.
Other slit –viewer combinations showed the same pattern.
-rotation from magnetization, z- drift length, - velocity in z direction, f- focal length
Chart: Beam Size vs Gun Solenoid Current on Two Viewers
| 0 | 2 | 5 | 8 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 175 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 325 | 350 | 375 | 400
σ (V1) | 4.2187 | 4.1365 | 4.0356 | 3.5672 | 3.4484 | 2.7941 | 1.9864 | 1.1014 | 0.85912 | 2.7442 | 3.9267 | 3.3982 | 1.8134 | 2.1099 | 3.6258 | 3.7659 | 2.3538 | 1.7027 | 2.4811 | 2.3046 | 1.4525 | 1.0398 | 1.191 | 0.99283 | 0.88574 | 1.3713 | 1.9517 | 2.3174 | 3.1994 | 4.0307 | 4.4818 | 4.7415 | 5.8149 | 6.6285 | 7.398 | 7.0897 | 6.9298 | 8.3442 | 8.2379 | 8.4421 | 7.8597
σ (V2) | 4.5925 | 4.8449 | 4.8867 | 4.613 | 4.1973 | 3.6337 | 2.3706 | 1.3047 | 1.2439 | 4.0026 | 5.2902 | 4.5872 | 2.183 | 3.1807 | 5.1196 | 4.9853 | 2.8309 | 2.1399 | 2.9657 | 2.5657 | 1.3029 | 1.5463 | 1.7464 | 1.6518 | 1.9049 | 3.163 | 4.3091 | 4.5513 | 6.1355 | 7.5073 | 8.7252 | 8.3367 | 9.8913 | 12.6293 | 12.5157 | 12.7635 | 11.6239 | 14.0262 | 13.1802 | 11.6409 | 10.425
Chart: Rotation Angle vs Gun Solenoid Current for slit 1 - viewer 2 combination
| 0 | 2 | 5 | 8 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 175 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 325 | 350 | 375 | 400
Slit1-v2 | 0 | -0.29794 | -0.60752 | -0.13751 | -0.27502 | -0.022918 | 0.32659 | 5.4775 | 10.3648 | 0.45837 | -0.68182 | -0.060349 | 4.8472 | 2.1601 | -0.911 | -1.1516 | 2.3205 | 9.3908 | 3.0997 | 6.2567 | 45.9397 | 45.9398 | 36.9271 | 55.8976 | 58.3384 | 18.2831 | 6.3885 | 3.5753 | -0.18259 | -2.4637 | -3.4377 | -3.7529 | -4.8071 | -5.7697 | -6.039 | 3.9821 | -5.8843 | -7.775 | -9.0413 | -9.3621 | -9.3335
Chart: Beam Size vs Gun Solenoid Current on Two Viewers
| 0 | 2 | 5 | 8 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 175 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 325 | 350 | 375 | 400
σ (V1) | 4.2187 | 4.1365 | 4.0356 | 3.5672 | 3.4484 | 2.7941 | 1.9864 | 1.1014 | 0.85912 | 2.7442 | 3.9267 | 3.3982 | 1.8134 | 2.1099 | 3.6258 | 3.7659 | 2.3538 | 1.7027 | 2.4811 | 2.3046 | 1.4525 | 1.0398 | 1.191 | 0.99283 | 0.88574 | 1.3713 | 1.9517 | 2.3174 | 3.1994 | 4.0307 | 4.4818 | 4.7415 | 5.8149 | 6.6285 | 7.398 | 7.0897 | 6.9298 | 8.3442 | 8.2379 | 8.4421 | 7.8597
σ (V2) | 4.5925 | 4.8449 | 4.8867 | 4.613 | 4.1973 | 3.6337 | 2.3706 | 1.3047 | 1.2439 | 4.0026 | 5.2902 | 4.5872 | 2.183 | 3.1807 | 5.1196 | 4.9853 | 2.8309 | 2.1399 | 2.9657 | 2.5657 | 1.3029 | 1.5463 | 1.7464 | 1.6518 | 1.9049 | 3.163 | 4.3091 | 4.5513 | 6.1355 | 7.5073 | 8.7252 | 8.3367 | 9.8913 | 12.6293 | 12.5157 | 12.7635 | 11.6239 | 14.0262 | 13.1802 | 11.6409 | 10.425
σ (V1)_Sim | 2.0005 | 1.998 | 1.9832 | 1.9482 | 1.9087 | 1.7305 | 1.4197 | 1.022 | 0.81119 | 1.7936 | 2.3842 | 2.7895 | 2.7652 | 1.7747 | 1.5407 | 2.6527 | 3.0539 | 2.4058 | 1.5439 | 1.7104 | 1.9383 | 1.5177 | 0.95919 | 0.91955 | 0.86285 | 1.4798 | 1.8584 | 2.1714 | 2.9138 | 2.4891 | 3.7195 | 4.0438 | 4.1642 | 4.8299 | 5.7999 | 6.2813 | 6.2252 | 6.2108 | 6.3247 | 7.1753 | 7.4565 | 7.3968 | 7.3508 | 7.2155 | 7.0058 | 6.9078 | 6.7007
σ (V2)_Sim | 2.7173 | 2.7132 | 2.6892 | 2.6345 | 2.5742 | 2.3106 | 1.8654 | 1.327 | 1.1461 | 2.6377 | 3.4383 | 3.9567 | 3.7951 | 2.3482 | 2.2329 | 3.7417 | 4.0997 | 3.0393 | 1.9333 | 2.2674 | 2.3519 | 1.5881 | 1.1649 | 1.4672 | 1.5491 | 3.1979 | 3.7131 | 4.2265 | 5.4967 | 4.7844 | 6.7338 | 7.091 | 7.169 | 8.1876 | 9.612 | 10.1771 | 9.9086 | 9.8138 | 9.9187 | 10.9346 | 11.1299 | 10.8296 | 10.6589 | 9.8795 | 9.3295 | 9.0568 | 8.4706
Chart: Rotation Angle vs Gun Solenoid Current for slit 1 viewer 2 combination
| 0 | 2 | 5 | 8 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 175 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 325 | 350 | 375 | 400
Slit1-v2 | 0 | -0.29794 | -0.60752 | -0.13751 | -0.27502 | -0.022918 | 0.32659 | 5.4775 | 10.3648 | 0.45837 | -0.68182 | -0.060349 | 4.8472 | 2.1601 | -0.911 | -1.1516 | 2.3205 | 9.3908 | 3.0997 | 6.2567 | 45.9397 | 45.9398 | 36.9271 | 55.8976 | 58.3384 | 18.2831 | 6.3885 | 3.5753 | -0.18259 | -2.4637 | -3.4377 | -3.7529 | -4.8071 | -5.7697 | -6.039 | 3.9821 | -5.8843 | -7.775 | -9.0413 | -9.3621 | -9.3335
Slit1-v2 _Sim | -0.0012879 | 0.010486 | 0.17496 | 1.1833 | 6.444 | 0.80288 | -0.53944 | -0.60551 | 1.5671 | 2.9244 | -0.74434 | -1.5331 | -0.50312 | 5.0943 | 3.4854 | 1.9362 | 8.1059 | 30.9637 | 27.146 | 29.6958 | 18.8194 | 5.8982 | 2.4036 | 0.47786 | -2.2178 | -3.8248 | -4.4786 | -4.8823 | -5.7005 | -6.5655 | -7.0993 | -7.4292 | -8.6526 | -9.7495 | -10.9921 | -12.3931
Successfully simulated the magnetized beam using ASTRA and GPT software and they are in good agreement with the measurements.
Beam sizes and rotation angles oscillates rapidly due to the focusing and de-focusing effects.
Mismatch oscillations occurred due to the non-uniform magnetic field map which results to unbalance the forces inside the magnetic field.
Convergence of the beam caused in negative rotation angle values.
Accuracy of the field maps greatly affect the simulation results.
3D field maps give more reliable results on simulations than 2D or 1D field maps.
Increase the bunch charge and continue simulations on space charge effect of the magnetized beam.
Simulate the emittance vs laser size for maximum gun solenoid current.