## Slide 1: Development of Beam Polarimeter for BNL SRF Gun
NP Accelerator R&D + Data Science AI/ML virtual PI Exchange meeting on November 30, 2021
Riad Suleiman

## Slide 2: Goals, Timeline, and Budget
Co-Principal Investigator: Riad Suleiman, with Joe Grames and Matt Poelker (Jefferson Lab), and Eric Voutier (IJCLab, Orsay, France)
Jefferson Lab’s contribution to this project is to provide a Compton Transmission Polarimeter, which will be used to measure beam polarization when SRF photogun employs a GaAs photocathode. IJCLab is contributing to Jefferson Lab’s effort.
Goals:
  Year 1: Design and build electron beam polarimeter
  Year 2: Install and commission polarimeter at CeC accelerator
Current Status:
  Design of polarimeter and new portable data acquisition system (DAQ) is completed
  NCE for one more year was approved
 | FY20 ($k) | FY21 ($k) | Totals ($k)
a) Funds allocated | 200.1 | 200.1 | 400.2
b) Actual costs to date | 10.9 |  | 

## Slide 3: Compton Transmission Polarimeter
Longitudinally Polarized Electron Beam,
Radiator
Polarized Iron (Longitudinally polarized Electrons, )
Detector
PMT
(Compton Transmission Asymmetry, )
Polarized Compton Scattering
( Analyzing Power, )
Circularly Polarized Gammas
Calculated
GEANT4 Simulation
from
Calibration at JLab
Measured

## Slide 4: An Example of Polarimeter at Jefferson Lab CEBAF – Summer 2018

## Slide 5: Polarimeter Parameters
CEBAF Injector can deliver electron beam with 5 – 9 MeV kinetic energy
CEBAF Mott polarimeter ideally works at 5 MeV kinetic energy
At BNL, electron beam kinetic energy will be 5.0 MeV (total energy 5.5 MeV)
  Minimum radiation levels and no risk of activation
Compton Transmission Polarimeter will be installed in place of Low Power Beam Dump
Maximum average current is limited to 2.5 µA by Low Power Dump

## Slide 6: Polarimeter Schematics at BNL
Pockels Cell is synchronized to laser
Helicity board will just provide a gate to determine which voltage (helicity) Pockels Cell gets set to
GaAs
Photocathode
IHWP
Pockels
Cell
Delayed
Helicity
PMT
T-Settle
BCM
DAQ
Helicity Generator
Compton Transmission Polarimeter
Laser
Helicity TTL 5V Signal
Synchronized
Pattern Sync

## Slide 7: New Portable Data Acquisition System (DAQ)
DAQ Readout:
  Delayed Helicity, T_Settle and Pattern Sync
  PMT, BCM
  Battery
Remote controllable IHWP
DAC
Mini VME Crate
Battery (1 V)
Magnet
Portable Rack
Magnet Power Supply, ±10 Amps
Computer
HV Power Supply, -5kV
PMT
Delayed
Helicity Fiber
Pattern Sync
Helicity TTL 5V Signal to
Pockels Cell
FADC
Helicity
Generator
PMT Signal
Beam Current Monitor (1 V)
T-Settle Fiber

## Slide 8: Polarimeter Design Optimization
Student Benjamin Fernandes Neres (from France)
https://wiki.jlab.org/ciswiki/images/8/82/CompPol_Optimization_B.Fernandes-Neres.pdf
GEANT4 simulation model of Compton transmission polarimeter was successfully implemented
Optimization of polarimeter:
  Radiator length = 7.0 mm, magnet iron core length = 8.0 cm, crystal detector radius = 3.5 cm and length larger than 18.0 cm
Evaluated of performance within BNL beam conditions (duration of a measurement, radiation damage to crystal detector)

## Slide 9: Achievements, Milestones and New Timeline
Year 1:
  Agreed upon basic operational parameters of polarized electron beam and polarimeter
  Portable DAQ design completed and implementation started
  Jefferson Lab Fast Electronics Group has finished programming of flash analog-to-digital convertor (FADC) and now working on user interface of DAQ
  Polarimeter (radiator, magnet, and detector) design was optimized using GEANT4
Year 2:
  Magnet engineer started design of electro-magnet with iron core
  Build two polarimeters (radiator, magnet, and detector) and one portable DAQ – one polarimeter will stay at CEBAF
Year 3:
  Calibrate polarimeter at CEBAF with portable DAQ
  Install and commission polarimeter at CeC accelerator
When SRF photogun employs a GaAs photocathode: Measure electron beam polarization