## Slide 1
Positron Production Conceptual Design
10 MeV, 100 kW CW Superconducting Electron Linac
flowing liquid metal target
positron-electron pair production
positron separation and capture
solenoid magnets
flow

## Slide 2: 10 MeV Accelerator with Positron Target
Electron Source
  350 MHz, 100 kV normal-conducting resonant cavity
  integrated, gated thermionic cathode
10 MV superconducting cryomodule
  3-cell, 350 MHz niobium resonator
  thermal and magnetic shields
Proof of concept test successfully complete with simplified LBE target

## Slide 3
Liquid Metal Target Design
Input electron beam passes through:
0.25 mm SS
2 mm LBE, for highest rate of production of e+
0.25 mm SS
Prototype target expected to handle >10 kW
Stainless Steel
Thin layer of lead-bismuth eutectic
Input (e-)
Output (e-,e+,γ)

## Slide 4
Positron System Hardware
Liquid Metal
Converter
Capture Solenoid
Separation
Dipole
Positron Solenoids
Electron Dump
Positron Target
Converter Solenoid