## Slide 1: Extreme High Vacuum: why and how Marcy L. Stutzman Jefferson Lab Center for Injectors and Sources
Notes: Title Page Design 3

## Slide 2: What is vacuum?
Vacuums are nothings. We only mention them to let them know we know they're there.
Middle school student’s answer on a science test

## Slide 3: Modern Vacuum History
‘Ultimate’ Vacuum vs. Time
Improvements with pumps
Improvements with gauges
P.A. Redhead Vacuum 53 (1999) 137
10-14
Ultimate Vacuum (Torr)
10-6
10-12
10-10
10-8
1900
1920
1940
1960
1980
2000

## Slide 4: Vacuum level definitions
Vacuum | Pressure (Torr) | Molecules/m^3 (bottom of range) | Mean free path
Atomsphere | 760 | 2.7x1025 | 68 nm
Low vacuum | 300 – 1 Torr | 1022 | 100 µm
Medium vacuum | 1 Torr – 1 mTorr | 1019 | 100 mm
High vacuum | 1 mTorr – 1x10-7 | 1015 | 1 km
Ultra High vacuum | 1x10-7 – 1x10-12 | 1010 | 105 km
Extreme high vacuum | <1x10-12 | <1010 | >105 km

## Slide 5
Atmosphere
Medium Vacuum
Vacuum Level | Where found | If people were molecules, you could move __ without hitting someone
Atmosphere | This room | About 1 foot away
Medium Vacuum | Bell jar, scattering chambers | Near the Newport News airport, almost 3 miles
High Vacuum | Low earth orbit, beamline | At the moon, 240,000 miles
Ultra High Vacuum (UHV) | Lunar atmosphere, Electron gun | Near Pluto, 4 billion miles
Extreme High Vacuum (XHV) | Interstellar space, Cryomodules | At the nearest star, Alpha Centauri, 25,000 billion miles
High Vacuum
UHV
XHV

## Slide 7: Beam required at Jefferson Lab
24 Hours
High polarization for 3 (4) experimental halls simultaneously
24/7 beam operation
Beam Current: 200 µA
Charge Delivered: 16 Coulombs polarized electrons / day
Outline
How do we emit polarized electrons?
What is required to keep the electron source working for the duration of experiments?
How do we achieve and maintain the required vacuum

## Slide 8: Photoemission Source
-130 kV DC (vs. RF) electrode bias
x-ray standard “inverted” insulator
Pumps with NEG modules and ion pump
Base pressure approaching XHV ≡ P < 1x10-12 Torr
-130kV
light in
electrons out
photocathode

## Slide 9: Metals, Insulators and Semiconductors
gap
filled
unfilled
unfilled
Metal:
Unfilled valance band
Insulator:
Large band gap
Semiconductor:
Small band gap
gap
filled
unfilled
gap
filled
unfilled
EF
EF
EF
Fermi
Level, EF

## Slide 10: Photoelectric effect
No emission below cutoff wavelength
Increase in photocurrent with increase in intensity of light above cutoff wavelength
Metallic emission: typically UV wavelengths
Particle nature of light
The Nobel Prize in Physics 1921 was awarded to Albert Einstein "for his services to Theoretical Physics, and especially for his discovery of the law of the photoelectric effect".

## Slide 11: Photoemission from GaAs
Bare GaAs surface
Large Work Function
Positive Electron Affinity (PEA)
PEA=4.07 eV
Egap=1.4 eV
Conduction
Band
Valence
Band
GaAs
Vacuum
Dipole layers of Cs + NF3 or Oxygen
Reduces Work Function
Negative Electron Affinity (NEA)
+
-
-
χNEA ~ 0.2 eV
GaAs
Vacuum
Light
NEA Surface Activation
GaAs Spin Polarized Electron Source, D.T. Pierce, R.J. Celotta, G.-C. Wang, W.N. Unertl, A. Galejs, C.E. Kuyatt, and S.R. Mielczarek, Review of Scientific Instruments 51(4), 478 (1980).

## Slide 12
  Any gas in chamber can be ionized by electron beam, accelerated back toward the photocathode and
  limit photocathode operational lifetime

## Slide 13: Photocathode Lifetime
Ion bombardment – with characteristic QE “trench” from laser spot to electrostatic center of photocathode – damages NEA of GaAs
High energy ions are focused to electrostatic center: create QE “hole”
  Don’t run beam from electrostatic center.
QE can be restored, but takes about 8 hours to heat and reactivate

## Slide 14: Operational Lifetime Limitations
Static vacuum approaching XHV (1x10-12 Torr)
  Baked, leak free, all metal vacuum systems
    Ceramic insulators, glass windows bonded to metal
    No machining oil, no fingerprints
    Bake for 30 hours 250°C to largely eliminate water vapor
  Hydrogen outgassing reduction
  Pumping for nearly XHV
Dynamic vacuum issues
  Eliminate field emission from electrodes
  Eliminate beam halo, scraping

## Slide 15
How to reach XHV ≡ P < 1x10-12 Torr?
Pump gas away
Less gas in
Measure pressure

## Slide 16: Vacuum Pumps – Rough Pumps
Low, Medium Vacuum (>10-5 Torr)
Mechanical (Oil Seal) Pump
Backs Turbo, Roots in
systems where oil isn’t
to detrimental

## Slide 17: Dry pumps
Molecular Drag pump
Used to rough down systems that will go to UHV – no oil contamination
Rotating fan blades, like a turbo, but more robust blade design for higher pressure use
Typically backed with a diaphragm pump

## Slide 18: Generation of High, Very High Vacuum
Turbo pumps
  High speed, precisely tuned fan blades
  Backed with mechanical pump
System must be roughed down to medium vacuum before starting
Must be operated with a backing rough pump at all times
Can have some backstreaming of gasses from atmosphere into the system

## Slide 19: Generation of High, Very High Vacuum
Ion pumps
  High voltage to ionize gas
  Magnetic field to direct ionized gas into plates to trap gasses
System must be roughed down to medium vacuum before starting
Capture pump – requires no backing pump during operation

## Slide 20: Ultra-High Vacuum: Bake and Add Getter Pumps
Getter Pumps
  Chemically active surface
    Titanium sublimed from hot filament
    Non-Evaporative Getters
  Molecules stick when they hit
    Does not work for inert gasses such as Argon, Helium

## Slide 21: Extreme High Vacuum Generation
Typically a combination of Getter pumps and cryo or ion pumps is used to achieve Extreme High Vacuum (XHV)
At room temperature, materials selection and processing, pumping, and gauging are huge issues
Calculations tell us that pressure is very, very good (<10-14 Torr or better)
XHV in room temperature chambers harder!

## Slide 22: A novel system: Leybold XHV Cryopump
LN2 chill circuit
  cools cryosorber panels and compressor
  allows bake of cryopump body
Operation
  10K pumping surface
  30K baffles
Presented at AVS 55 by Dieter Mueller

## Slide 23: Effectiveness of adding a cryopump
Chart: Time (hours)
dummy secondary y axis | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30

## Slide 24: Even more novel: Nanomaterial Cryopump
Typical cryopumps glue charcoal to cold surface
  Large surface area allows cryosorption rather than cryocondensation
  Lower pressure
Requires Low temperature adhesives
  Can’t bake system well
Boron-Nitride Nanotubes have
  Huge surface area
  Good thermal
  Are freestanding
  Are manufactured across street (JLab spin-off)
Can we use these for cryosorber material?

## Slide 25: First and second tries
1 g BNNT material
Copper grid
~4 g BNNT material
“sewn on” with wires
Veronica

## Slide 26: First BNNT cryopump: cooldown
Baked 48 hours at or below 150°C
Coldhead temperature: 15.5K (14K before BNNT)
39K: pressure drop – Cryopumping!
Chart: Hours

## Slide 27: Can we model this cryopump system?
Modeled geometry, temperature distribution of cryopump
Compare BNNT vs. charcoal
Predicting behavior of version 2
For more info: See Veronica’s poster

## Slide 28
How to reach XHV ≡ P < 1x10-12 Torr?
Pump gas away
Less gas in
Measure pressure

## Slide 29: High/Ultra High Gauges
Lowest pressures:
  10-8 Torr – 10-11 Torr
  up to $4,000
Bayard-Alpert Gauges
Stabil-Ion gauge
Cold Cathode gauge
A
filament
+V
collector
+

## Slide 30
True gas ionization
  Positive current
Cathode
Anode
1
+
3
e-
2
e-
X-ray effect
  e- on anode -> photons emitted
  Photons on collector -> electrons emitted
  Extra positive current
Inverse X-ray effect
  e- on anode -> photons
  Photons on walls -> electrons
  Electrons to collector
  Extra negative current
4
+
Electron stimulated desorption
  e- strike gas molecules on anode
  Gas ionized and reaches collector
    can be distinguished with energy analysis
  Neutral atom desorbed
    Ionized within grid
    Indistinguishable from real gas
    Must eliminate souce
Measure Pressure:
Hot cathode gauge operation and errors

## Slide 31: XHV gauges
Extractor gauge
  available commercially for decades
  x-ray limit reduced through geometry
  x-ray limit quote: 7.5x10-13 Torr
  $4,300
Axtran gauge
  Bessel box energy discrimination
  electron multiplier to assist in low current measurements
  Quoted limit: 3.75x10-13 Torr
  $7,500
Watanabe BBB (Bent Belt Beam) gauge
  Uses Leybold IE540 controller
  230° deflector BeCu housing
  JVSTA 28, 486 (2010)
  Quoted limit: 4x10-14 Torr
  $13,000 + Ext. controller ($2,600)
extractor
BBB
Axtran
Hot filament

## Slide 32
How to reach XHV ≡ P < 1x10-12 Torr?
Pump gas away
Less gas in
Measure pressure

## Slide 33: Less gas in: reduce outgassing
Primary source in stainless system: hydrogen outgassing
To reduce outgassing
  reduce thick flange area
  heat treatment
    400°C bake
    10+ days
thin dome replaces thick flanges

## Slide 34: Outgassing rates vs. heat processing and coatings
Identical 304L chambers
Bare steel
TiN coating (9 µm)
a-Si (SilcoGuard-1000®~900 nm)
Outgassing rates
Spinning Rotor Gauge
Accumulation technique
Multiple bakes
Q(Troom) after each bake

## Slide 35: Outgassing rates: bare and coated chambers
Chart: Outgassing Rate (Torr L s-1 cm-2)
| First Bake 90°C, 30h | Second Bake 150°C, 30h | Third Bake 250°C, 30h | Fourth Bake 400°C, 100h | Fifth Bake 150°C, 30h | Sixth Bake 250°C, 30h | Seventh Bake 150°C, 30h | Eighth Bake 360°C, 150h
SilcoII | 1e-12 | 1.3e-13 | 1.5e-13
SS | 4e-12 | 1.7e-13 | 1e-13 | 2.8e-13 | 2.2e-13 | 9.9e-14
Silco | 2.4e-12 | 2.1e-12 | 1.6e-12 | 3.6e-12 | 2.8e-12 | 1.9e-12
All data at Troom = 20°C
Notes: Steel:
Expected reduction
with 400°C heat
treatment
Silco:
Little variation with
heat treatment
Silco on heated SS:
Retains prior
outgassing rate
TiN coating:
Very low outgassing
rates, consistent with
literature, elemental
Ti pumping?

## Slide 36
Remember: Better Vacuum, longer lifetime
System Leak
~5x10-11 Torr
~2.5x10-11 Torr

## Slide 37: Summary
High polarization strained superlattice GaAs-GaAsP photocathodes susceptible to ion damage, gun vacuum level
Outgassing reduction, pumping combinations and measurements to verify improvements are being optimized
Vacuum improvements required for future proposed higher current polarized electron sources

## Slide 38: Thank you for your attention
(L-R) Matt Poelker, Joe Grames, Bubba Bullard
Marcy Stutzman, John Hansknecht, Shukui Zhang
Carlos Hernandez Garcia, Phil Adderley, Riad Suleiman