## Slide 1
Production of Highly Polarized Positrons Using Polarized Electrons at MeV Energies
(…or why polarized positrons are like Red-Billed Oxpeckers)
Joe Grames
Center for Injectors & Sources, Jefferson Laboratory
On behalf of PEPPo Collaboration

## Slide 2
Outline
Motivation
PEPPo Experiment
Polarized Positron Accelerator R&D
Summary
Jefferson Lab Positron Working Group

## Slide 3
3
Jefferson Lab’s CEBAF Accelerator
CW electron beams to 4 Halls
Electron Polarization 85-90%
Max Energy: 11 GeV(ABC) / 12GeV(D)
Max Current: 200 mA
The charge and polarization of the probe beam provide degrees of freedom which isolate physical observables of great interest.
Jefferson Lab physics that would benefit a polarized positron beam:
  Interference (Two Photon, GPD’s, WNC)
  Standard Model Test (Dark Matter, C3q)
Proposed physics that may benefit investigation:
  Electron Ion Collider (spin EMC, Strange/Charm GPD’s)
  Materials Science (spintronic devices, ferromagnetics)
Polarized Positron Beam Applications
Quantity | User Interest
Intensity | > 10 nA
Duty Factor | 100 % (cw)
Bunch Frequency | 499 MHz (or sub-harmonic)
Polarization | > 50 %
Helicity | Rapid reversal (> 30 Hz)

## Slide 4
P(e+) = 73 ± 15(stat) ± 19(syst) %
Compton Backscattering (KEK)
T. Omori et al, PRL 96 (2006) 114801
Helical Undulator (SLAC E166)
G. Alexander et al, PRL 100 (2008) 210801
P(e+) = 80 ± 7(stat) ± 9(syst) %
47.7GeV
Polarized b+ Decay
L.A. Page & M. Heinberg. Phys. Rev.
106(6):1220-1224 (1957)
Polarized due to parity non-conservation in the weak interaction
P(e+) ~ 40 %
Sokolov-Ternov Effect
D. Barber , AIP Conf. Proc. 588, 338 (2001)
HERA 27.5 GeV e+/e-
P(e+) ~ 70 %
Polarized Positron Options

## Slide 5
5
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
E.G. Bessonov, A.A. Mikhailichenko, EPAC (1996) A.P. Potylitsin, NIM A398 (1997) 395
Polarized Electrons for Polarized Positrons
Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)

## Slide 6
>10nA useful for CEBAF NP
Positron Yield
Photon energy k up to electron energy T1
Cross section decreases as 1/k
Yield scales with electron energy T1
Positron energy T1 to photon energy k-2mc2
Cross section essentially energy independent
Bremsstrahlung
Pair Production

## Slide 7
QE ~ 5%, 30 μA/mW
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 μA/mW
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 μA/mW
Pol ~ 85% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
GaAs Photocathode Evolution
Spin Polarized program at JLab (particularly our PV Users) have
driven the need for improved performance over last 20+ years
Pe- 35% 35% 75% 75% 85% 89%
Ie- 30mA 100mA 50mA 100mA 150mA 200mA
1995 1998 1999 2000 2004 2012 2016

## Slide 8
Polarized Electron Source Intensity Frontier
Year
Intensity (mA)
SLAC: First GaAs photogun
JLAB: Low-P Bulk GaAs
JLAB: High-P GaAs/GaAsP
Parameter | Value | Value
Laser Rep Rate | 499 MHz | 1500 MHz
Laser Pulse Length | 30 ps | 50 ps
Laser Wavelength | 780 nm | 780 nm
Laser Spot Size | 0.45 mm | 0.35 mm
Photocathode | GaAs/GaAsP | GaAs/GaAsP
Gun Voltage | 100 kV | 200 kV
Beam Current | 1 mA | 4 mA
Run Duration | 8.25 hr | 1.4 hr
Extracted Charge | 30.3 C | 20 C
Charge Lifetime | 210 C | 80 C
Fluence Lifetime | 132 kC/cm2 | 83 kC/cm2
Bunch Charge | 2.0 pC | 2.7 pC
Peak Current | 67 mA | 53 mA
Peak Current Density | 42 A/cm2 | 55 A/cm2
J. Grames et al., PAC07, THPMS064
R. Suleiman et al., PAC11, WEODS3
Sustained operation (e.g. 1 mA ~ 86 C/day) requires improving charge lifetime.

## Slide 9
BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
COMPTON TRANSMISSION
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
S1
D
D
S2
Pe+
Positron Transverse and Momentum Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
Ee = 6.3 MeV
Ie = 1 µA
T1 = 1 mm W
Geant4
PEPPo
J. Dumas, PhD Thesis (2011)
PEPPo measured the longitudinal polarization transfer from 8.25 MeV/c e- to e+ in the 3.07-6.25 MeV/c momentum range.
Measuring Polarization Transfer <10 MeV

## Slide 10
PEPPo @ CEBAF Injector
Compton
Polarimeter
(DESY/Cornell)
Positron Collection
Magnets
(Princeton/SLAC)
Pair
Creation
Target
Mott
Polarimeter

## Slide 11
T1
T2
S1
S2
D
D
e+
e-
Positron Collection
Na22
Two NaI detectors measured coincidence of back-to-back photons emitted by annihilation of positrons in a viewscreen.
11
pe-= 8.2 MeV/c
4 MeV/c e+
Viewscreen 0.011 thick @ 45 deg to beam line
99.5% aluminum oxide Al2O3
0.5% chromium doped Al2O3/Al2O3Cr2O3
Positron Detection
e+

## Slide 12
12
Detected e+ rate (1 e+ per 109 e-)
Solid Angle (0.1 sr)
GEANT annihilation probability (1/400)
Coincidence detector efficiency (0.49 @ 511keV)
1 e+ per 105 e-
Positron Yield

## Slide 13
Electrons or Positrons radiate polarized photons by Bremmstrahlung in reconversion target. Energy dependent Compton scattering of photons transmitted through polarized target correspond to polarization of incoming Electrons or Positrons (aligned or anti-aligned).
μ1 - Compton absorption coefficient
L - target length
P3 - photon polarization (long.)
Pe - electron/positron polarization
PT - target polarization
Ae - analyzing power
g
Target (Densimet D17K) 90.5% W, 7%, 2.5% Cu
e-
Pe-
e+
Pe+
Compton Transmission Polarimetry
PT = 7.06% ± 0.05% (sys1) ± 0.07% (sys2)

## Slide 14
C
A
L
O
R
I
M
E
T
E
R
e+
g
Trigger Scintillator
10mil Al window
Reconversion
Target
Positrons are detected in coincidence between a thin trigger scintillator placed prior to the reconversion target and the central crystal and tagged by e- helicity.
Trigger Scintillator
Coincidence
Calorimeter
Positron Identification
WITHOUT
Coincidence
WITH
Coincidence

## Slide 15
511 keV from e+ annihilation at rest
Bremsstrahlung
end-point
Energy (FADC units)
Positron Energy Integrated Asymmetry
Accidentals
Time (TDC units)

## Slide 16
Electron/Positron Analyzing Power
Experimental measurements of electron analyzing power allows us to benchmark GEANT4 model of the PEPPo Compton transmission polarimeter for the purpose of simulating the positron analyzing power.
Electron calibration performed with precisely known electron beam energy/polarization, and target polarization:
See A. Adeyemi talk for calibration of the Compton transmission polarimeter
Pe – e-/e+ polarization
PT - target polarization
Ae - analyzing power
Electron beam polarization
Pe- = 83.7% ± 0.6% (stat) ± 0.7% (sys)
Target polarization
PT = 7.06% ± 0.05% (sys1) ± 0.07% (sys2)

## Slide 17
Electron polarization (~85%) efficiently transferred from 8.2 MeV/c electron beam to positrons (measured 3.2 – 6.7 MeV/c).
e- beam polarization
85.2 ± 0.6 ± 0.7 %
Positron Polarization Results
(PEPPo Collaboration) D. Abbott et al., Phys. Rev. Lett. 116 (2016) 214801
Whenever producing e+ from e-, polarization is coming for free
if initial electrons are polarized.

## Slide 18
P. Aderley1, A. Adeyemi4, P. Aguilera1, M. Ali1, H. Areti1, M. Baylac2, J. Benesch1,
G. Bosson2, B. Cade1, A. Camsonne1, L. Cardman1, J. Clark1, P. Cole5, S. Covert1,
C. Cuevas1, O. Dadoun3, D. Dale5, J. Dumas1,2, E. Fanchini2, T. Forest5, E. Forman1,
Freyberger1, E. Froidefond2, S. Golge6, J. Grames1, P. Guèye4, J. Hansknecht1,
P. Harrell1, J. Hoskins8, C. Hyde7, R. Kazimi1, Y. Kim1,5, D. Machie1, K. Mahoney1,
R. Mammei1, M. Marton2, J. McCarter9, M. McCaughan1, M. McHugh10, D. McNulty5, T. Michaelides1, R. Michaels1, C. Muñoz Camacho11, J.-F. Muraz2, K. Myers12,
Opper10, M. Poelker1, J.-S. Réal2, L. Richardson1, S. Setiniyazi5, M. Stutzman1,
R. Suleiman1, C. Tennant1, C.-Y. Tsai13, D. Turner1, A. Variola3, E. Voutier2,11,
Y. Wang1, Y. Zhang12
1 Jefferson Lab, Newport News, VA, US 2 LPSC, Grenoble, France 3 LAL, Orsay, France
4 Hampton University, Hampton, VA, USA 5 Idaho State University & IAC, Pocatello, ID, USA
6 North Carolina University, Durham, NC, USA 7 Old Dominion University, Norfolk, VA, US
8 The College of William & Mary, Williamsburg, VA, USA 9 University of Virginia, Charlottesville, VA, USA 10 George Washington University, Washington, DC, USA 11 IPN, Orsay, France
12 Rutgers University, Piscataway, NJ, USA 13 Virginia Tech, Blacksburg, VA, USA
PEPPo Collaboration
Many thanks for support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and Jefferson Science Associates
Orsay, September 14-16, 2016
13/19

## Slide 19: Polarized Positrons at JLEIC
A pulsed positron beam with low average current (~10 nA) is required for injection into JLEIC with a reasonably short injection time (minutes) and reasonably high equilibrium polarization (>40%).
A group (J. Grames, J. Guo, F. Lin, V. Morozov, E. Voutier) is exploring a polarized positron injector suitable for Jefferson Lab Electron Ion Collider (JLEIC).
L ≥1033cm-2s-1 Pe+≥40%
(An Early Career Award proposal will be submitted.)
35 s
68.1 MHz bunch train, 1.6 us
110 bunches (I = 4.6 uA)
67 fC
1.05 ms
20 ms
~ 50 Hz, Iave= 10.5 nA
…
×30
Bunch structure from the injector:
See F. Lin’s talk: Spin dynamics at Jefferson Lab Electron Ion Collider (JLEIC)

## Slide 20: JLEIC/CEBAF Positron Injector
10 MeV polarized e-
1.33 pC @ 1500 MHz
10 MeV pol e-
0.67 nC bunches
@ 1500 MHz
500-Turn
Accumulator Ring
(22m)
Bunch
Management
10 MeV polarized e-
0.67 nC @ 68.1 MHz
Positron Conversion/Collection Efficiency ~ 10-4
5-7 MeV Polarized e+
67 fC @ 68.1 MHz
to 12 GeV CEBAF
Harmonic
Extraction Ring
(22m)
 | Polarized Electron Source | Accumulator/ Extractor Rings | Electrons at Converter | Polarized Positron Source | R&D Challenge
JLEIC | Ave = 100 uA 1.33 pC @ 1500 MHz 2 mA w/ DF=5% | Ave = 1 A 1500 MHz | Ave = 100 uA 68.1 MHz 44 mA @ DF=0.23% | Ave = 10 nA 68.1 MHz 4.4 uA @ DF = 0.23% | Electron accumulator Harmonic extraction Target: 440kW peak
CEBAF | Ave = 1-10 mA 4-40 pc @ 250 MHz (cw) | Not Necessary | Ave = 1-10 mA 250 MHz (cw) | Ave = 100nA - 1 uA 250 MHz (cw) | High-QE photocathode High voltage gun Target: 10-100 kW ave
Polarized
Electron
10 MeV Injector

## Slide 21: High Polarization Photocathode R&D
6.4% QE & 84% polarization at 776 nm from strained GaAs/GaAsP superlattice photocathode with GaAsP/AlAsP Distributed Bragg Reflector (DBR)
The highest QE & FOM of any reported high polarization photocathode
Possible to improve both QE & Pol
SBIR partnership
Paper ready for SPIN and APL submission: W. Liu, S. Zhang, M. Stutzman, M. Poelker, Y. Chen, W. Lu, and A. Moy
DBR
Substrate
Photo-cathode
See talk by W. Liu talk

## Slide 22
Higher Voltage (300 kV) Inverted Photo Gun
8 MV/m
11 MV/m
First insulator commissioned to 325 kV
New insulator, getting installed now, supports higher voltage operation
CsK2Sb 1mA

## Slide 23: Multi-Turn Injection
Concept: an orbit bump created near a septum and then slowly reduced as beam being injected (phase-space painting)
A number of painting schemes has been developed
Process can also be simultaneously occurring in vertical and longitudinal dimensions
CERN’s LEIR has a design for 75-turn injection of Pb54+, we plan to push this number to a few hundred to a thousand using low electron emittance
Main injection system components
  Magnetic or electrostatic septum
  Four bumper magnets with ~1 s rise time, reasonably fast fall-off time and ~10 mrad maximum deflection
Injected beam
Accumulator ring
x
x
> Septum thickness + bunch width

## Slide 24
Harmonic Kicker Extraction
Chart: Waveform kicks 1 in 10 bunches w/ bunch = 476MHz Synthesized with 9 RF harmonics and 1 DC mode
Harmonic kicker that kicks every 3rd bunch
Empty ring buckets already kicked out to linac
Ring buckets still occupied by bunches
Empty linac buckets
Linac buckets occupied by extracted bunches
Y. Huang et al, accepted by PRSTAB

## Slide 25
High Power Target R&D
Stainless Steel Windows (0.25mm)
LBE (2mm)
Input (e-)
Output (e-,e+,γ)
Liquid Metal Target - lead-bismuth eutectic (LBE)
  High Z = 82, 83
  Low melting point: 124°C
  High boiling point: 1670 °C
Multiple LBE targets tested on various accelerators
  Natural Circulation
  Mechanical Pumping
  Electromagnetic Pumping
Approaching 10 kW power level, CW
Courtesy J. McCarter, Niowave

## Slide 26
Summary
The PEPPo technique provides an efficient, reliable, radioactive-less, and low cost method opening access to polarized positron beam to a wide community.
Next steps in low energy scheme of e+ source R&D is optimizing for beam intensity and beam quality.
An experimental program in context of CEBAF 12 GeV, JLEIC and LERF is being explored. If you would like to participate in the newly formed Jefferson Lab Positron Working Group please visit: wiki.jlab.org/pwg

## Slide 27
Synergy
The Hippopotamus and Red-Billed Oxpecker share a positive and synergistic relationship.

## Slide 28
Backup Slides

## Slide 29
M.P. Rekalo, E. Tomasi Gustafsson, NPA 742 (2004) 322 C. Carlson, M. Vanderhaeghen, ARNPS 57 (2007) 171
Combining Polarized electrons and positrons allows a model independent separation of the electromagnetic form factors of the nucleon.
Unpolarized e± elastic scattering and polarization transfer observables from the nucleon involve up to 5 unknown quantities.
5 unknown contributions for 6 independent observables
Cross Section
Polarization
Transfer
Electromagnetic Form Factors

## Slide 30
Summary of Positron Asymmetries

## Slide 31: 10 MeV Accelerator with Positron Target
Electron Source
  350 MHz, 100 kV normal-conducting resonant cavity
  integrated, gated thermionic cathode
10 MV superconducting cryomodule
  3-cell, 350 MHz niobium resonator
  thermal and magnetic shields
Proof of concept test successfully complete with simplified LBE target

## Slide 32
Liquid Metal Target Design
Input electron beam passes through:
0.25 mm SS
2 mm LBE, for highest rate of production of e+
0.25 mm SS
Prototype target expected to handle >10 kW
Stainless Steel
Thin layer of lead-bismuth eutectic
Input (e-)
Output (e-,e+,γ)
Lead-bismuth eutectic (LBE)
  Low melting point: 124°C
  High boiling point: 1670 °C
  Z = 82, 83

## Slide 33
Liquid Metal Target Testing
~1 m
Successfully tested LBE target systems based on:
Natural Circulation
  Multiple targets tested on various accelerators
  Approaching 10 kW power level, CW
Mechanical Pumping
  Submerged impellor
Electromagnetic Pumping
  Current through LBE in magnetic field

## Slide 34
Positron System Hardware
Liquid Metal
Converter
Capture Solenoid
Separation
Dipole
Positron Solenoids
Electron Dump
Positron Target
Converter Solenoid