## Slide 1
Experiment | Energy (GeV) | Pol (%) | I (µA) | Target | Apv (ppb) | Maximum Charge Asym (ppb) | Maximum Position Diff (nm) | Maximum Angle Diff (nrad) | Maximum Size Diff (δσ/σ)
HAPPEx-I (Achieved) | 3.3 | 38.8 | 40 | 1H (15 cm) | 15,050 | 200 | 12 | 12 | 
G0-Forward (Achieved) | 3.0 | 73.7 | 40 | 1H (20 cm) | 3,000-40,000 | 300±300 | 7±4 | 3±1 | 
HAPPEx-II (Achieved) | 3.0 | 87.1 | 55 | 1H (20 cm) | 1400 | 400 | 1 | 0.2 | 
HAPPEx-III (Achieved) | 3.484 | 89.4 | 100 | 1H (25 cm) | 16900 | 200±100 | 3±3 | 0.5±0.1 | 10-3
PREx-I (Achieved) | 1.056 | 89.2 | 100 | 208Pb (0.5 mm) | 657±60 | 100±130 | 2±3 | 1 | 10-4
QWeak-I (Achieved) | 1.155 | 89.0 | 180 | 1H (35 cm) | 281±46 | 8±15 | 5±1 | 0.1±0.02 | 10-4
QWeak | 1.162 | 90 | 180 | 1H (35 cm) | 234±5 | 100±10 | 2±1 | 30±3 | 10-4
PREx-II | 1.0 | 90 | 70 | 208Pb (0.5mm) | 500±15 | 100±10 | 1±1 | 0.3±0.1 | 10-4
Møller | 11.0 | 90 | 85 | 1H (150 cm) | 35.6±0.74 | 10±10 | 0.5±0.5 | 0.05±0.05 | 10-4

## Slide 2
Experiment | Energy (GeV) | Pol (%) | I (µA) | Target | Apv (ppb) | Maximum Charge Asym (ppb) | Maximum Position Diff (nm) | Maximum Angle Diff (nrad) | Maximum Size Diff (δσ/σ)
HAPPEx-I (Achieved) | 3.3 | 38.8 | 40 | 1H (15 cm) | 15,050 | 200 | 12 | 12 | 
G0-Forward (Achieved) | 3.0 | 73.7 | 40 | 1H (20 cm) | 3,000-40,000 | 300±300 | 7±4 | 3±1 | 
HAPPEx-II (Achieved) | 3.0 | 87.1 | 55 | 1H (20 cm) | 1400 | 400 | 1 | 0.2 | 
HAPPEx-III (Achieved) | 3.484 | 89.4 | 100 | 1H (25 cm) | 16900 | 200±100 | 3±3 | 0.5±0.1 | 10-3
PREx-I (Achieved) | 1.056 | 89.2 | 100 | 208Pb (0.5 mm) | 657±60 | 100±130 | 2±3 | 1 | 10-4
QWeak-I (Achieved) | 1.155 | 89.0 | 180 | 1H (35 cm) | 281±46 | 8±15 | 5±1 | 0.1±0.02 | 10-4
QWeak | 1.162 | 90 | 180 | 1H (35 cm) | 234±5 | 100±10 | 2±1 | 30±3 | 10-4
PREx-II | 1.0 | 90 | 70 | 208Pb (0.5mm) | 500±15 | 100±10 | 1±1 | 0.3±0.1 | 10-4
Møller | 11.0 | 90 | 85 | 1H (150 cm) | 35.6±0.74 | 10±10 | 0.5±0.5 | 0.05±0.05 | 10-4

## Slide 3: Always Tweaking the Design
Endless (?) quest for perfection
1
2
3
4
The photogun works well,
No anticipated near-term changes

## Slide 4
Higher Voltage = Better Transmission = Better Beam Quality
(and maybe longer lifetime)
130 kV Inverted Gun
Prebuncher operating at modest power takes care of the rest

## Slide 5: Improve Lifetime with Large Laser Spot?
(Best Solution – Improve Vacuum, but not easy)
Bigger laser spot, same # electrons, same # ions
Ionized residual gas
strikes photocathode
Ion damage distributed
over larger area

## Slide 6: Enhanced lifetime for Qweak
“Charge and fluence lifetime measurements of a DC high voltage GaAs photogun at high average current.,” J. Grames, R. Suleiman, et al., Phys. Rev. ST Accel. Beams 14, 043501 (2011)
Can we use ~ cm size laser beams? Not in today’s CEBAF photogun.
How far can we extrapolate? Need a better cathode/anode optic
Increase size of laser beam from ~ 0.35 mm to ~ 0.7 mm dia.

## Slide 7: 4p Electron Spin Manipulation
Two Solenoids
Horizontal Wien Filter
Vertical Wien Filter
Harder to flip spin than we imagined, more “things” change than just spin direction
Beam orbit downstream of HWien sensitive to laser/prebuncher (mis-)phasing
Don’t know what to do about this….

## Slide 8: Electron Spin Reversal for PV
“Spin Reversal”
Vertical Wien = 90 deg
Two Solenoids = ±90 deg
“Longitudinal Polarization”
Horizontal Wien = {-90…+90}
LEFT
RIGHT
From Gun
Pondering a new beamline, but will it behave differently? Reluctant to move prebuncher. Modification would provide an opportunity to improve beamline vacuum….

## Slide 9: Two Wien Improvements
Do a better job characterizing optics, and compensate asymmetric focusing using quads, to achieve “perfect” spin flip
Mis-matched E and B fields create mini-chicane, with e-beam displaced from zero potential, which introduces a time delay…

## Slide 10
Gain-switched Diode Laser and Fiber Amplifier
Attenuator
PC WP LP
Shutter
Rotatable GaAs
Photocathode
V-Wien Filter
Vacuum
Window
15° Dipole
PZT
Mirror
IHWP
RHWP
Pockels
Cell
Delayed
Helicity Fiber
HV Supply
(0 – 4 kV)
HV Supply
(0 – 90 V)
CEBAF
Hall
T-Settle
Fiber
Charge Feedback (PITA)
Electron
Beam
Helicity Fiber
Charge Feedback (IA)
LP HWP LP
IA
Target
BCM
BPMs
5 MeV
Helicity Magnets
Parity
DAQ
nHelicity
Fiber
Position
Feedback
Helicity Generator
H-Wien Filter
Spin Solenoids
All of the same knobs exist today….

## Slide 11
Stewart Platform: complete RC of PC alignment
LINUX-based software/freeware from hobbyists who build flight simulators
X, Y, pitch, roll and yaw

## Slide 12
Initial attempts and problems encountered
Two commercial high-speed / high-voltage transistor (~$8000)
This approach needed big capacitors…. lots of current
Exaggeration of voltage droop on cell and subsequent re-charge after a helicity flip. Droop causes a serious problem when helicity flip rate was changed from a toggle to a pseudo-random pattern: pockels cell “memory”
high-voltage switch (~$10,000) All-in-one commercial bipolar
Charge droop was greatly improved, but high speed ringing of the cell was a problem for the settling time. In addition, the large high-speed switching currents created a noise induced helicity pickup on sensitive helicity DAQ components.
Work of John Hansknecht

## Slide 13
Encapsulated Opto-diode $67 each
Solution: Opto-diode
I = CΔV/ Charge time
+/- quarter wave voltage = 5120V
Cell capacitance = 6pf
Desired charge time = 100us
Calculated current is only 307uA !!
Work of John Hansknecht

## Slide 14
Pockels cell λ/2 transition optical result. ~70us with no ringing.
Pockels cell λ/2 flipping at 1kHz.
Perfect symmetry and no voltage droop over time.
The old switch was limited to 30 Hz helicity flip rates due to power handling limitations. Now we flip at 1kHz for ~ 400$.
Pockels cell “memory” not an issue anymore….
Push-Pull Circuit
New Opto Diode Pockels Cell Switch
1
2
3
4
Work of John Hansknecht

## Slide 15
Mott Polarimeter at CEBAF

## Slide 16
M. Steigerwald first reported MeV Mott Polarimeter at SPIN 2000, with accuracy 1.1%
Still that accurate? Can it be more accurate ??? => motivates a new “campaign” to study 5 MeV Mott

## Slide 17: Accurate Mott Polarimetry
List of improvements and tasks:
Reduce background using time of flight analysis, laser at 31 MHz
Reduce background using Be dump plate
Upgrade DAQ to operate at higher data rates, higher beam currents (i.e., measure polarization at your current)
Exhaustive studies of systematic errors
GEANT modeling and assistance from theorists to help pin down the Sherman function at zero foil thickness
Different Zs, different energies
Planned Summer 2014 tests using 1/4CM at 4K…..
M. McHugh, Joe Grames, Riad Suleiman

## Slide 18
Role of Beam Dump Background
Gold
0.1 um
Gold
1.0 um
Gold
10 um
12 ns round trip time
499 MHz (2ns)
M. McHugh
Joe Grames
Riad Suleiman

## Slide 19
Dipole Suppression
Dipole deflects primary and secondary electrons
OFF
+5 A

## Slide 20
Time Of Flight Separation
TARGET
STRAGGLERS
DUMP
TARGET
STRAGGLERS
DUMP
fbeam = 31.1875MHz
16 ns repetition rate > 12 ns “clearing time”

## Slide 21
Be Dump Design
Kalrez™ high temp (240C) o-ring
Dump should work fine to 1 kW (200uA @ 5MeV) so limitation will be deadtime.
Number of Electrons
Total Momentum [MeV/c]
Cu
Al
C
Be
M. McHugh, Joe Grames, Riad Suleiman

## Slide 22: TMONO Harmonic Resonant Cavity
…..a cavity sensitive to each mode = bunchlength monitor (Brock Roberts)
I(t) = a0 + a1 cos (wot + q1) + a2 cos (2wot + q2) + a3 cos(3wot + q3) + …
Bunched electron beam can be described as Fourier series….

## Slide 23
“antenna/radiator” placed where the e-beam would travel. The antenna was driven with a 20 dBm,1556 MHz signal through a step recovery diode. Yes, cavity resonates at many harmonic modes.
On the bench

## Slide 24
Installed at ITS
With beam delivered to dump, spectrum analysis shows harmonics visible to 18.396GHz, the 12th harmonic of 1533MHz (measurement made at 150kV, 25uA, superlattice cathode)

## Slide 25: Bandwidth determines Resolution

## Slide 26
500 kV spectrometer line
Brock Roberts will use RF model of cavity to see if it is sensitive to transverse beam motion and beam size variation…. helicity correlated beam size monitor? Lower noise floor for current monitoring?
At CEBAF 500 kV spectrometer line
(a)
(b)
(c)
Laser optical pulse
O-scope Brock cavity
Electron bunch

## Slide 27
Load-locked photogun
and baked beamline:
Pressure ~ 4 e-12Torr

## Slide 30: 350kV Inverted Gun
Longer insulator
Spherical electrode
Thin NEG sheet to move ground plane further away
200kV Inverted Gun

## Slide 31: To do list
Stewart Platform for Pockels cell: complete remote control of all alignment parameters
2 kHz Pockels cell switch, stable voltage and minimum transition time between helicity states
Improve 2-Wien Spin Flipper optics
Beam envelope matching to maximize adiabatic damping
Accurate Mott measurements at Injector
Re-wire 5MeV helicity magnets to provide HC focusing, and evaluate experimental sensitivity to HC spot size variation
Use POISSON and genetic algorithm to improve the field uniformity of pockel cell
Helicity correlated beam size monitor?
Beam current monitor with low noise floor?

## Slide 32
Chart: Bunchlength vs Gun Voltage
| 50 | 100 | 150 | 200
200KeV | 51.5 | 56.2 | 60.2 | 64.1
115KeV | 55.7 | 68.4 | 78.7 | 87.5
100KeV | 58.4 | 73.7 | 85.7 | 95.7
85KeV | 62.7 | 81.1 | 95.2 | 99.8
70KeV | 68.2 | 91.7 | 103.4 | 105.5
Chart: Bunchlength vs Gun Voltage
| 0.8 | 12 | 51 | 98 | 148 | 198
115kV | 43.771 | 60.6061 | 104.3771 | 138.0471 | 161.6162 | 188.5522
100kV | 43.8596 | 70.1754 | 96.4912 | 125.731 | 149.1228 | 152.0468 | 181.2865 | 198.8304 | 213.4503 | 233.9181
85kV | 53.8721 | 77.4411 | 107.7441 | 144.7811 | 158.2492 | 181.8182 | 208.7542 | 232.3232 | 255.8923 | 269.3603
70kV | 50.8547 | 77.7778 | 113.6752 | 152.5641 | 173.5043 | 203.4188 | 227.3504 | 245.2991 | 260.2564 | 278.2051
Measurements at CEBAF/JLab
PARMELA Simulation Results
Benchmarking PARMELA Simulation Results Against Beam-Based Measurements at CEBAF/Jefferson Lab – work of Ashwini Jayaprakash, JLab
Message: Beam quality, including transmission, improves at higher gun voltage
Chart: Transmission vs Gun Voltage
| 50 | 100 | 150 | 200
200KeV | 97.9 | 97.7 | 97 | 96.6
115KeV | 93.7 | 86.6 | 77.8 | 69.9
100KeV | 92.6 | 78.4 | 67.4 | 60.3
85KeV | 85.6 | 66.7 | 57.3 | 50.9
70KeV | 72.5 | 54.5 | 46.2 | 39.6
Chart: Transmission vs Gun Voltage
| 11.7 | 26 | 51.4 | 74.8 | 98.2 | 122.2 | 148 | 170.5 | 198
115kV | 96.5812 | 92.6923 | 82.4903 | 73.262 | 67.0061 | 61.784 | 57.6351 | 54.8974 | 51.3131
100kV | 99.0099 | 92.7419 | 77.8431 | 66.7553 | 59.2 | 52.7911 | 47.451 | 44.2153 | 40.5941
85kV | 93.8931 | 83.274 | 67.2761 | 56.2421 | 47.6465 | 40.9161 | 35.0449 | 30.9244 | 27.2059
70kV | 77.2727 | 61.6327 | 45.2479 | 35.9712 | 29.0608 | 23.7197 | 19.8027 | 17.2973 | 14.5238
Similar Trends