## Slide 1
Example : 7 MeV e- on 1 mm W
Concept for JLab-EPIC ?
Test Idea for UITF ?
Parts !
LDRD Brainstorming Session
Joe Grames
April 8, 2016

## Slide 2
W
1 mm
N = 10M
E = 7 MeV
P = 100% long.
(mm)
(MeV/c)
KE (MeV)

## Slide 3
Electrons
f = 22.7 MHz
DF=100%
Qb = 36 pC
10 MeV
Accumulations = 20 ms / 3.23 us = 6192
Accumulated Positrons
f = 22.7 MHz
DF= 3.23us / 20ms
Qb = 2.2 pC
5 MeV?
CW Positrons
f = 22.7 MHz
DF=100%
“Qb” = 0.28 fC
5 MeV?
Step 1:
Produce 817uA polarized e- and accelerator to 10 MeV
Step 2:
Collide 8kW of beam power in 1.2 mm W target (1e+/1250e-)
Step 3:
Collect e+ beam in accumulator (1e+/100,000e-) for 6192 revol.
Step 4:
Dump 3.23 us train of 2.2pC e+ bunches (73) every 20 ms with frequency 22.7 MHz
Dare to dream !!!!
But 3.23us is lengthy=962m (150m), maybe do this 10x @ 0.323us (R=15m)???

## Slide 4
But think small first !!!
Electrons
f = 750 MHz
Qb = 14 fC
<I>=10 uA
10 MeV
Accumulated Positrons
Bunch space = 1.33 ns = 0.4 m
10 bunches => C=4 m (D=1.3m) = 13.3 ns
Accumulate for 100 ms => 7.5E6
Qe+ = 14E-15 / 1E5 * 7.5E6 = 1.0 pC
CW Positrons
f = 750 MHz
DF=100%
Qb Tot = 11E-18 C
5 MeV?
Diagnostic Line
Sing : 110 pA : 11E-18C @ 750 MHz (DF=100%)
Accu: <110 pA> : 1E-12C @ 750 MHz (DF=13.3ns/100ms)

## Slide 5
Production target
  (1) PEPPo Low-Power (100W) cooled target ladder; need to find W targets (0.1, 1, 2? mm)
  Niowave stretch plan - lead bismuth eutectic target (100kW, 125 kW/cm2)
  Lead – Estimate ~80 sq.ft. of 2” thickness in CEBAF injector
Post target collection
  (1) High field solenoid – assembled (at MMF?); needs PS
  (1) High field solenoid – coil (Test Lab); needs steel & PS
  (2) tungsten beam scrapers w/ linear actuators
Diagnostics
  (2) Viewers
  (2) Linear motion actuators
  (2) annihilation detectors and cross; needs DAQ and target
  RF cavity?
  Wire scanner
Accumulator
  Design and build : dipoles, RF cavity?
Parts for experiment