## Slide 1: UITF MPS system requirements
MPS = a combination of hardware configuration and CEBAF-style FSD protection
FSD trips will mostly turn OFF the laser, vacuum excursions will shutter laser and close valves
GUN HV will not trip often

## Slide 2
Protect the ¼ CM
Protect against beam loss and burn-through, maintain UHV
Protect viewers (this is a software interlock – Not FSD)
Protect magnets, ensure proper field for beam transport: comparator interlock, water flow or klixon interlocks
Protect RF beamline components: vacuum and water flow interlocks
Protect cups, apertures and dumps: water flow interlocks
Protect HDIce (mostly, this means putting the beam where it is supposed to go, protect against mis-steered beam)
UITF MPS – what will it protect?

## Slide 3: Hardware configuration
Valves OPEN only when vacuum good
Current limiting resistors in series with magnets
Water flow interlocks at cups, dumps and apertures
Window comparators on dipoles and gun HV
Viewers inserted only when laser in pulsed-mode
Water flow interlocks at buncher and chopper cavities, RF can be applied to chopper and buncher only when vacuum reads “good”
Helium liquid level interlocked to klystron high power RF

## Slide 4: FSD Input Signals
FSD trips will shutter laser and sometimes close all valves
BLMs will shutter laser: CEBAF-style BLM modules (x2)
LLRF control boards with CEBAF-style FSD signals
Vacuum FSD signals from ¼ CM. Helium liquid level interlocked to klystron control panel
All beamline ion pumps ganged together, close laser shutter and close all pneumatic valves when pressure exceeds a setpoint
Window comparators using 16 bit ADC cards designed by EES
HDice “off target” detector (qty 1, suspect it will look like a BLM)

## Slide 5: Similar to CEBAF
SSG BLM chassis, x2 units
New LLRF control boards
Cryo and SRF signals from ¼ CM
Window comparators using 16 bit ADC cards designed by EES
FSD signals summed using VME boards with 12 input channels each
FSD signals transmitted via fiber at 5 MHz
SCAM to create low duty factor modes
CEBAF style pockel cell tune mode generator: RTP cell with <250ns response time, backed by shutter that closes 5-10ms later

## Slide 6: MPS timing requirements
All inputs should be processed to create an output within 10 micro-seconds (that’s are goal, what we would work towards)

## Slide 7: MPS system communications
All inputs are visible to EPICS
All outputs are shown on EPICS
First fault detection is desirable and the first fault should be visible on EPICS
EPICS should have the ability to mask or clear any input