## Slide 1
Polarized Positron Beams at JLab
Joe Grames
Center for Injectors & Sources
Jefferson Laboratory

## Slide 2
  Physics Motivation for CEBAF 12 GeV
  CEBAF Injector PEPPo Experiment
  Proposed Polarized Positron Beam R&D
  Outlook
Outline

## Slide 3
Polarized Electrons have supported some of the highest impact results from the JLab program:
  The strangeness distribution in the nucleon (HAPPEX and G0)
  Precision Tests of the Standard Model (QWeak)
  Measurement of the neutron skin in 208Pb
  Polarization transfer measurement of GE/GM for the proton
Unpolarized positron beams provide a key tool for further pushing the precision of electron scattering experiments
  Comparison of e- with e+ tests our understanding of two photon effects
Polarized positrons beams provide essential tool
  Unraveling nucleon structure through the measurement of charge-sensitive General Parton Distributions
  Expand the nature of these tests (e.g. for GE/GM via polarization transfer)
Why Polarized Positrons at JLab?
Beam Quality | Electron Beam (Delivered) | Positron Beam (Desired)
Average Intensity | > 200 mA | > 100 nA (5 x 1011 e+/s)
Duty Factor | 100% (cw) | 100% (cw)
Bunch Frequency | 499 MHz (or sub-harmonic) | 499 MHz (or sub-harmonic)
Polarization (orientation) | > 85% (4p control) | > 50% (4p control)
Helicity Control | Rapid reversal (> 30 Hz) | Rapid reversal (> 30 Hz)

## Slide 4
Letter of Intent (LOI12-18-004) to PAC-46
Jefferson Lab Positron Working Group (JLAB-PWG) formed in the summer 2016
  120 members, and growing
  39 institutions
Letter of Intent submitted to PAC-46 (July 2018) motivating a discussion by our Users for a Physics Program with Positron Beams at CEBAF 12 GeV
“Summary: These measurements all have significant physics interest. The proposers should carefully evaluate feasibility and present the best case possible in a future proposal. The justification must be very strong to enable the significant changes needed in the accelerator, both in equipment and in schedule. Any proposal should have a section on the linkage between a realistic plan for beam and the way the measurement is made.”

## Slide 5
A polarized positron injector suitable for the Jefferson Lab Electron Ion Collider (JLEIC) has also been considered.
L ≥1033cm-2s-1 Pe+≥40%
Iave > 10 nA (~1010 e+/s)
Ipeak > 4 mA (~1013 e+/s)
e+
Polarized Positrons at an Electron Ion Collider
Challenge is accumulating high positron bunch charge with high rep rate.

## Slide 6
P(e+) = 73 ± 15(stat) ± 19(syst) %
Compton Backscattering (KEK)
T. Omori et al, PRL 96 (2006) 114801
Helical Undulator (SLAC E166)
G. Alexander et al, PRL 100 (2008) 210801
P(e+) = 80 ± 7(stat) ± 9(syst) %
SLAC 47.7GeV
Polarized b+ Decay
L.A. Page & M. Heinberg. Phys. Rev.
106(6):1220-1224 (1957)
Polarized due to parity non-conservation in the weak interaction
P(e+) ~ 40 %
Sokolov-Ternov Effect
D. Barber , AIP Conf. Proc. 588, 338 (2001)
P(e+) ~ 70 %
HERA 27.5 GeV e+/e-
Methods for Generating Polarized Positrons
KEK 1.28 GeV

## Slide 7
QE ~ 5%, 30 mA/W
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 mA/W
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Strained Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 mA/W
Pol ~ 89% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
Figure-of-Merit (P2I) has improved by a factor of 43
over the span of the CEBAF “6 GeV era”
Pe- 35% 35% 75% 75% 85% 89%
Ie- 30mA 100mA 50mA 100mA 150mA 200mA
1995 1998 1999 2000 2004 2012 2018
JLab’s e- Beams Provide the Basis for e+ Beams

## Slide 8
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
E.G. Bessonov, A.A. Mikhailichenko, EPAC (1996) A.P. Potylitsin, NIM A398 (1997) 395
Polarized Electrons for Polarized Positrons
Polarized Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Polarized Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)

## Slide 9
P. Adderley1, A. Adeyemi4, P. Aguilera1, M. Ali1, H. Areti1, M. Baylac2, J. Benesch1, G. Bosson2,
B. Cade1, A. Camsonne1, L. Cardman1, J. Clark1, P. Cole5, S. Covert1, C. Cuevas1, O. Dadoun3,
D. Dale5, J. Dumas1,2, E. Fanchini2, T. Forest5, E. Forman1, A. Freyberger1, E. Froidefond2,
S. Golge6, J. Grames1, P. Guèye4, J. Hansknecht1, P. Harrell1, J. Hoskins8, C. Hyde7, R. Kazimi1,
Y. Kim1,5, D. Machie1, K. Mahoney1, R. Mammei1, M. Marton2, J. McCarter9, M. McCaughan1,
M. McHugh10, D. McNulty5, T. Michaelides1, R. Michaels1, C. Muñoz Camacho11, J.-F. Muraz2,
K. Myers12, A. Opper10, M. Poelker1, J.-S. Réal2, L. Richardson1, S. Setiniyazi5, M. Stutzman1,
R. Suleiman1, C. Tennant1, C.-Y. Tsai13, D. Turner1, A. Variola3, E. Voutier2,11, Y. Wang1, Y. Zhang12
1Jefferson Lab, Newport News, VA, US, 2 LPSC, Grenoble, France, 3LAL, Orsay, France
4 Hampton University, Hampton, VA, USA 5 Idaho State University & IAC, Pocatello, ID, USA
6 North Carolina University, Durham, NC, USA 7 Old Dominion University, Norfolk, VA, US
8 The College of William & Mary, Williamsburg, VA, USA 9 University of Virginia, Charlottesville, VA, USA 10 George Washington University, Washington, DC, USA 11 IPN, Orsay, France
12 Rutgers University, Piscataway, NJ, USA 13 Virginia Tech, Blacksburg, VA, USA
PEPPo possible due to support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and the Jefferson Science Associates
The PEPPo Collaboration

## Slide 10
J. Grames, E. Voutier et al., JLab Experiment E12-11-105 (2011)
The purpose of the PEPPo (Polarized Electrons for Polarized Positrons) experiment at the CEBAF Injector was to demonstrate the feasibility of using bremsstrahlung radiation of MeV energy Polarized Electrons for the efficient production of Polarized Positrons.
PEPPo Demonstrated Efficient e+ Production

## Slide 11
1. BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
e+
2. PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
3. Phase Space Definition
The emittance of the positron beam is defined by slits and magnetic fields
S1
D
D
S2
Positron Transverse and Longitudinal Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
4. COMPTON TRANSMISSION POLARIMETER
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
PEPPo: Principle of Operation

## Slide 12
Polarized positrons incident on a target produce polarized bremsstrahlung, which is then analyzed via the Compton scattering transmission asymmetry through a magnetized target.
Pe - electron/positron polarization
PT - target polarization
Ae - analyzing power
Compton Transmission Polarimeter
PT = 7.06% ± 0.05% (sys1) ± 0.07% (sys2)
C
A
L
O
R
I
M
E
T
E
R
e+
g
Trigger Scintillator
10mil Al window
Reconversion
Target
Trigger Scintillator
Coincidence
Calorimeter
Background

## Slide 13
PEPPo demonstrated efficient polarization transfer of 8.2 MeV/c polarized electrons to positrons, expanding polarized positron production using MeV electron beam energies.
(PEPPo Collaboration) D. Abbott et al. , Phys. Rev. Lett. 116 (2016) 214801
electron beam polarization
85.2 ± 0.6 ± 0.7 %
Whenever producing e+ from e-, polarization is coming for free, if initial electrons are polarized.
PEPPo Experiment Result

## Slide 14
Two NaI detectors measured coincidence of back-to-back photons emitted by annihilation of positrons in a viewscreen.
Positron Yield at MeV Energies
T1
T2
S1
S2
D
D
e+
e-
pe-= 8.2 MeV/c
e+
For these data we had a yield of ~10-5 e+/e-
A3
A1
A3
A1
Viewscreen 0.011 thick @ 45 deg to beam line
99.5% aluminum oxide Al2O3
0.5% chromium doped Al2O3/Al2O3Cr2O3
pe+= 4 MeV/c

## Slide 15
R. Dollan, K. Laihem, A. Schälicke, NIM A 559 (2006) 185,
J. Dumas, J. Grames, E. Voutier, JPos09, AIP 1160 (2009) 120
J. Dumas, Doctorate Thesis (2011)
Optimum energy
Optimum
FoM
The polarization distribution of generated positrons is dominated by low-energy events.
The positron energy at the optimum FoM (P2I) is about half of the electron beam energy.
Figure of Merit (Ee- = 60 MeV)
15
Producing highly polarized positron beams with intensities > 100 nA with typical injector energies (10-100 MeV) requires polarized electron beam intensities of >1-10 milliAmps

## Slide 16
  Superlattice Performance >1 mA Encouraging
Year
Intensity (mA)
SLAC: First GaAs photogun
JLAB: Low-P Bulk GaAs
JLAB: High-P GaAs/GaAsP
?
W. Liu et al., Appl. Phys. Lett. 109, 252104 (2016)

## Slide 17
Source Operation using GaAs/GaAsP >1 mA
  A electron source operating at 1 mA for one week produces 605 C.
  Recent tests demonstrate photocathode charge lifetimes 300-450 C for beam intensities > 1 mA.

## Slide 18
Polarized Positron Injector Concepts Abound
We have explored concepts with varying level of detail (theses, proposals, and yes…napkins).
The common denominator at JLab is leveraging our skills: Polarized Beams, SRF, Photoinjectors, High energy beams, etc).
A polarized e+ injector at Jlab would be novel in various ways:
  mA polarized e- source
  fast helicity reversal
  cw/short pulse bunches
  high power target > 10 kW
  srf acceleration

## Slide 19
High Power Target R&D
Stainless Steel Windows (0.25mm)
LBE (2mm)
Input (e-)
Output (e-,e+,γ)
Liquid Metal Target – lead-bismuth eutectic (LBE)
  High Z = 82, 83
  Low melting point: 124°C
  High boiling point: 1670°C
Multiple LBE targets tested on various accelerators
  Natural Circulation
  Mechanical Pumping
  Electromagnetic Pumping
Approaching 10 kW power level, CW

## Slide 20
Jefferson Lab ERL (LERF)
Powerful light source
IR and UV FEL
THz light
Search for Dark Matter
Fixed Target Options
500kV, 10mA HVPS
350kV Vent Bake Gun
GaAs (500C @ 5mA)
SRF Booster 10 MeV
HPC for mA current, nC bunch charge

## Slide 21
350kV Vent Bake Gun
Single photocathode material
4 weeks to replace photocathode
Repeated vacuum/HV conditioning
500kV, 10mA HVPS
Physically connected to gun SF6
2 days for each gun access
Repeated HV conditioning
LERF Vent Bake Gun
Slide Courtesy: C. Hernandez-Garcia

## Slide 22
GTS Magnetized Beam Photogun
Load-lock inverted insulator photogun (multiple photocathodes) like CEBAF
Cable connection from HVPS to gun
Over 1000 hours operating >300kV; HV conditioning about 1 week
Operating with CsKSb photocathodes at >10 mA average current
Slide Courtesy: C. Hernandez-Garcia

## Slide 23
Polarized Positron Source
Upgrading the LERF injector with a >350kV inverted photogun and dual photocathode (GaAs or multi-alkali) photo-gun provides capability to:
  achieve predicted lifetime scaling of spin polarized photocathodes
  demonstrate reliable operation of high power conversion targets
  supports on-going unpolarized beam operations at LERF
  opens door to new polarized beam operations
Next priority should be designing, building and testing a positron beam collection system to define and optimize the transverse & longitudinal phase space and spin polarization for RF acceleration.

## Slide 24
Integrated Positron Beams Program
Only scratching the surface…there are still many issues to consider related to the operation of positron beam in CEBAF (magnet reversal and reproducibility, managing beam loss and diagnostics of low current beams).
However, simulations of the various concepts to date suggest that a CW polarized positron source can be built to meet the CEBAF requirements.
The next most important questions to answer are, however, related to the technical aspects of the positron source:
  What is the e+ yield in an optimized CW target and captured system?
  What is the energy, emittance and phase filter design, and how well does it work?
  Demonstrate the resulting e+ beam is suitable for SRF acceleration.

## Slide 25
Outlook
Jefferson Lab Users are making the physics case to lab management for high energy polarized positron physics program at CEBAF.
PEPPo demonstrated high positron polarization from moderate energy polarized electrons with a small footprint (cost, energy, radioactivity)
Progress of mA-sources is promising for the development of polarized positron beams with intensity >100 nA (5 x 1011 e+/sec).
Next priority should be building and testing a collection system to define and optimize the transverse/longitudinal phase space for RF acceleration.
A comprehensive plan, supported by JLab Management, that can be successfully executed is essential for future success.