## Slide 1: Magnetized Electron Source
2018 Accelerator R&D PI Exchange Meeting
November 13-14, 2018
Riad Suleiman
This work is supported by the Department of Energy, Laboratory Directed Research and Development (LDRD) funding, under contract DE-AC05-06OR23177

## Slide 2: Outline
LDRD Goals, Budget, Deliverables and Schedule
Magnetized Bunched-Beam Electron Cooling at Jefferson Lab Electron Ion Collider (JLEIC)
LDRD Magnetized Electron Source:
  K2CsSb Photocathode and HV Chamber
  Cathode Solenoid
  Beamline
Characterization of Magnetized Beam:
  Beam Size and Shearing Angle
  Drift Emittance
  High Bunch Charge
  High Average Current and Charge Lifetime
Future Plans
Summary

## Slide 3: Jefferson Lab LDRD Goals
Project, “Generation and Characterization of Magnetized Bunched Electron Beam from DC Photogun for JLEIC Cooler”, was funded by Jefferson Lab LDRD program. This was three-year project concluded on September 30, 2018.
LDRD Goals:
  Generate magnetized electron beam from dc high voltage photogun and measure its properties
  Exploring impact of cathode solenoid on photogun operation
  Simulations and measurements will provide insights on ways to optimize JLEIC electron cooler and help design appropriate source
  Jefferson Lab will have direct experience on magnetizing electron beams at high currents
Jones report

## Slide 4: Budget
Materials and Supplies:
  Cathode solenoid magnet
  Beamline hardware: steering magnets and slits
  Laser components
Labor:
  Cathode solenoid design, mapping and installation
  Mechanical designer
  Beam simulations with A Space Charge Tracking Algorithm (ASTRA) and General Particle Tracer (GPT)
  Postdoc (FY17 and FY18)
FY16 | $339,211
FY17 | $264,979
FY18 | $211,449
Total | $815,639

## Slide 5: Deliverables and Schedule
FY16:
  HV condition gun to 350 kV and build K2CsSb preparation chamber
  Design beamline. Design and procure slits
  Design and procure cathode solenoid magnet
  Measure lifetime at 1 mA and 300 kV (non-magnetized)
  Install cathode solenoid magnet
FY17:
  Generate magnetized beam
  Measure mechanical angular momentum vs magnetic field and laser size at photocathode
  Benchmark simulation against measurements
  Measure lifetime at 5 mA and 300 kV
  Study beam halo and beam loss vs magnetic field at photocathode
FY18:
  Design TE011 cavity to measure beam magnetization (non-invasive)
  Change to HV Supply of 30 mA and 225 kV
  Measure photocathode lifetime at 30 mA
  Generate high bunch charge magnetized beam
  Commission TE011 cavity with beam
Explore these magnetized beam parameters:
= 0.1 – 1 mm, Bz = 0 – 1.5 kG
Bunch charge: up to 0.5 nC
Frequency: 1 – 15 Hz, 100 – 500 MHz
Average beam currents up to 30 mA
Gun high voltage: 200 – 350 kV

## Slide 6: JLEIC High Energy Electron Cooler
High Energy Electron Cooler
Circulator Cooler Ring
ERL Ring

## Slide 7: Magnetized Bunched-Beam Electron Cooling
Ion beam cooling in presence of magnetic field is much more efficient than cooling in a drift (no magnetic field):
  Electron beam helical motion in strong magnetic field increases electron-ion interaction time, thereby significantly improving cooling efficiency
  Electron-ion collisions that occur over many cyclotron oscillations and at distances larger than cyclotron radius are insensitive to electrons transverse velocity
Long cooling solenoid provides desired cooling effect:
  Counteracting emittance degradation induced by intra-beam scattering
  Maintaining ion beam emittance during collisions and extending luminosity lifetime
  Suppressing electron-ion recombination
  Putting electron beam into cooling solenoid represents a challenge

## Slide 8: Magnetized Cooling Schematics
Electron beam suffers an azimuthal kick at entrance of cooling solenoid. But this kick can be cancelled by an earlier kick at exit of photogun. That is the purpose of cathode solenoid.
Upon exit of Cathode Solenoid
Upon entering Cooling Solenoid
Electrons born in strong uniform Bz
v
Bz
v
Bz
v
Br
v
Br

## Slide 9: JLEIC Magnetized Source Requirements
Parameter | JLEIC Requirements | LDRD Demonstrated
Bunch length – Flat-top | 60 ps (2 cm) | 25 – 60 ps
Repetition rate | 43.3 MHz | 100 Hz – 374.3 MHz
Bunch charge | 3.2 nC | 0.7 nC (75 ps FWHM, 25 kHz, 225 kV, 0.76 kG)
Peak current | 53.9 A | 9.3 A
Average current | 140 mA (400 kV) | 28 mA (50 ps FWHM, 74.8 pC, 374.25 MHz, 100 kV, 0.57 kG)
Transverse normalized emittance | <19 microns | <2 microns
Normalized drift emittance | 36 microns | 26 microns
Cathode spot radius – Flat-top () | 3.14 mm | 1.70 mm
Solenoid field at cathode (Bz) | 0.50 kG | 1.51 kG
Parameter | JLEIC Requirements | LDRD Demonstrated
Bunch length – Flat-top | 60 ps (2 cm) | 25 – 60 ps
Repetition rate | 43.3 MHz | 100 Hz – 374.3 MHz
Bunch charge | 3.2 nC | 0.7 nC (75 ps FWHM, 25 kHz, 225 kV, 0.76 kG)
Peak current | 53.9 A | 9.3 A
Average current | 140 mA (400 kV) | 28 mA (50 ps FWHM, 74.8 pC, 374.25 MHz, 100 kV, 0.57 kG)
Transverse normalized emittance | <19 microns | <2 microns
Normalized drift emittance | 36 microns | 26 microns
 | 3.14 mm | 1.70 mm
Solenoid field at cathode (Bz) | 0.50 kG | 1.51 kG
Beam current was limited by laser power and power of high voltage
supply (30 mA/225 kV supply with 3 kW limit)

## Slide 10: Gun Test Stand with 300 kV Inverted Gun and K2CsSb Photocathode
Salvaged un-used beamline from old project
Designed and procured cathode solenoid that can provide magnetic field up to 1.5 kG at photocathode
Used CEBAF spare Dogleg magnet power supply (400 A, 80 V)
Cathode solenoid can trigger field emission but we have learned how to prevent this
Photogun operated at 300 kV with gun solenoid at 400 A
Chart: z, m
Magnetic Field at 400 A
Beamline
Focusing
Solenoid 1
Beamline
Focusing
Solenoid 2
Electrostatic Field at 300 kV
Gun Test Stand in October 2015
Gun Test Stand in September 2018

## Slide 11: Magnetized Source Schematics
Beamline
Cathode Solenoid
Photocathode
Preparation
Chamber
Gun HV Chamber
Slit
Viewer Screen
Shield Tube
Viewer 3 Screen
Beam Dump
Use slit and viewscreens to characterize magnetization:
: beam size on i -th viewer
θ: shearing angle

## Slide 12: Beam Size and Shearing Angle
Chart: Bz@cathode, G
| 0 | 7.57 | 18.925000000000001 | 30.28 | 37.85 | 56.775000000000006 | 75.7 | 94.625 | 113.55000000000001 | 151.4 | 189.25 | 227.10000000000002 | 264.95 | 302.8 | 340.65000000000003 | 378.5 | 416.35 | 454.20000000000005 | 492.05 | 529.9 | 567.75 | 605.6 | 643.45000000000005 | 662.375 | 681.30000000000007 | 719.15 | 757 | 794.85 | 832.7 | 870.55000000000007 | 908.40000000000009 | 946.25 | 984.1 | 1021.95 | 1059.8 | 1097.6500000000001 | 1135.5 | 1230.125 | 1324.75 | 1419.375 | 1514
σ (V2 data) | 4.5925 | 4.8449 | 4.8867 | 4.613 | 4.1973 | 3.6337 | 2.3706 | 1.3047 | 1.2439 | 4.0026 | 5.2902 | 4.5872 | 2.183 | 3.1807 | 5.1196 | 4.9853 | 2.8309 | 2.1399 | 2.9657 | 2.5657 | 1.3029 | 1.5463 | 1.7464 | 1.6518 | 1.9049 | 3.163 | 4.3091 | 4.5513 | 6.1355 | 7.5073 | 8.7252 | 8.3367 | 9.8913 | 12.6293 | 12.5157 | 12.7635 | 11.6239 | 14.0262 | 13.1802 | 11.6409 | 10.425
θ for S1-V2 (data) | 0 | -0.29794 | -0.60752 | -0.13751 | -0.27502 | -0.022918 | 0.32659 | 5.4775 | 10.3648 | 0.45837 | -0.68182 | -0.060349 | 4.8472 | 2.1601 | -0.911 | -1.1516 | 2.3205 | 9.3908 | 3.0997 | 6.2567 | 45.9397 | 45.9398 | 36.9271 | 55.8976 | 58.3384 | 18.2831 | 6.3885 | 3.5753 | -0.18259 | -2.4637 | -3.4377 | -3.7529 | -4.8071 | -5.7697 | -6.039 | -6.0603 | -5.8843 | -7.775 | -9.0413 | -9.3621 | -9.3335
Magnetic field at photocathode = 0 G
Beam and beamlet observed on successive viewers
300 kV, laser rms = 0.3 mm
Beam size and Shearing Angle: Experiment vs Simulation
V1
V1
V2
V2
S1-V2
S1-V2
S1-V3
S1-V3
Magnetic field at photocathode = 1514 G
Modelled apparatus using ASTRA & GPT
Focusing by cathode solenoid magnetic field causes mismatch oscillations resulting in repeated focusing inside cathode solenoid field which affects beam size at exit of solenoid field and resulted in varying beam expansion in field free region

## Slide 13: Drift Emittance
Used beamline solenoid and viewer screen to measure drift emittance for different laser sizes at 200 kV
GPT simulation and experimental results show good agreement
Chart: Bz@cathode, G
| 0 | 94.462500000000006 | 226.71 | 358.95750000000004 | 453.42 | 566.77499999999998 | 755.7 | 944.625 | 1133.55 | 1322.4750000000001 | 1511.4
0.44 mm | 0 | 0.3648 | 0.9 | 1.4729 | 1.8618 | 2.4096 | 3.3562 | 4.2718 | 5.0409 | 5.8738 | 6.5317
0.90 mm | 0.63065 | 1.885 | 4.3202 | 6.9325 | 11.3036 | 14.9175 | 19.3278
 | 26.7548
0.44 mm (GPT simulation) | 0.2811 | 0.51773 | 1.12 | 1.7092 | 2.1322 | 2.6533 | 3.3238 | 4.4138 | 5.0737 | 6.0372 | 6.5514
0.90 mm (GPT simulation) | 0.58128 | 2.0574 | 4.6321 | 7.2702 | 9.9725 | 12.025 | 14.128
Beam size too large to transport cleanly

## Slide 14: High Bunch Charge
Encountered space-charge-limited regime within 0.3 nC for different magnetized conditions
Need longer laser pulses, higher gun voltage and better beamline optics to get nC bunches
Chart: Pulse energy, nJ
| 0.80600000000000005 | 2.88 | 6.18 | 10.46 | 15.34 | 21 | 27 | 33.4 | 40.4 | 48 | 88 | 92 | 108 | 120 | 128.80000000000001 | 136.6 | 143 | 148.6 | 186.4 | 218 | 264 | 318.00000000000006 | 380 | 450 | 530
 | 0.0218 | 0.078 | 0.16 | 0.22 | 0.252 | 0.27 | 0.28 | 0.288 | 0.292 | 0.296 | 0.316 | 0.334 | 0.35 | 0.366 | 0.378 | 0.392 | 0.4 | 0.412 | 0.53 | 0.58 | 0.596 | 0.604 | 0.654 | 0.66 | 0.72
 | 6.3042 | 6.3127 | 6.0345 | 4.9023 | 3.829 | 2.9968 | 2.4172 | 2.0098 | 1.6847 | 1.4373 | 0.83698 | 0.84619 | 0.75536 | 0.7109 | 0.68405 | 0.66888 | 0.65198 | 0.64623 | 0.66274 | 0.62013 | 0.5262 | 0.44271 | 0.40115 | 0.34185 | 0.31664
225 kV, 757 G, 50 kHz , 75 ps (FWHM)
Irregular pattern due to beam-loss

## Slide 15: High Average Current: 14 mA
Magnetic field = 757 G
Laser rms = 0.9 mm, 303 MHz, 60 ps (FWHM)
Gun HV = 200 kV, Gun Solenoid = 200 A, Anode at + 1 kV
K2CsSb photocathode on molybdenum
Bunch charge = 46 pC
No quantum efficiency (QE) reduction over 90 hour run
Positive anode bias (+1 kV) effectively prevented ions in beamline from reaching gun and stopped micro-arcs and sudden QE loss (problem we struggled with)

## Slide 16: High Average Current: 20 mA
14 mA, 725 G, 90 h run
Laser rms =0.9 mm, 303 MHz, 60 ps
Gun Sol=200 A, HV=200 kV
No QE loss over 20 hours
Magnetic field = 568 G
Laser rms = 0.9 mm, 303 MHz, 60 ps (FWHM)
Gun HV = 100 kV, Gun Solenoid = 150 A, Anode at + 1 kV
K2CsSb photocathode on molybdenum
Bunch charge = 66 pC

## Slide 17: High Average Current: 28 mA
Magnetic field = 568 G
Laser rms = 1.4 mm, 374.25 MHz, 50 ps (FWHM)
Gun HV = 100 kV, Gun Solenoid = 150 A, Anode at + 1 kV
K2CsSb photocathode on molybdenum
Bunch Charge = 92 pC
Limited lifetime might be a result of heating and associated bandgap shift, or enhanced ion bombardment
Will increase anode bias voltage beyond 1kV
Radiation Control Group approval obtained

## Slide 18: Future Plans
Swap photogun for RF-pulsed thermionic gun built by Xelera Research LLC to demonstrate magnetized beam at 65 mA and 125 kV (will use LDRD cathode solenoid and beamline but with new HV supply): an SBIR Phase II funded project (DE-SC0015186)
Install two non-invasive magnetometer cavities – LDRD cavity and “Brock” cavity from Electrodynamic to measure beam magnetization: another SBIR Phase II funded project (DE-SC0017120)
Collaborate with Xelera, Electrodynamic, Brookhaven National Lab and others on more follow-up projects

## Slide 19: Summary
K2CsSb photocathode preparation chamber, gun, cathode solenoid and beamline - all operational
Photogun operated reliably up to 300 kV for >1000 h
Have successfully generated and characterized magnetized electron beams
Demonstrated high bunch charge up to 0.7 nC
Delivered 28 mA magnetized beam (568 G at photocathode) with RF structure (gain-switched drive laser, 374.25 MHz, 50 ps FWHM) at 100 kV using 30 mA/225 kV HV supply with 3 kW limit
Successfully fabricated bialkali antimonide photocathode with QE ~ 9% on molybdenum substrate that provided long charge lifetime
Positive bias on anode helps to prevent sudden QE loss from ion-induced micro-arcing events
Envisioned new non-invasive device to measure beam magnetization (TE011 cavity). Cavity was designed and now under construction.
Thanks to those involved in this team work:
P. Adderley, J. Benesch, B. Bullard, J. Delayen , J. Grames, J. Guo, F. Hannon, J. Hansknecht, C. Hernandez-Garcia, R. Kazimi, G. Krafft, M. A. Mamun, M. Poelker, M. Tiefenback, Y. Wang, S. Wijiethunga, S. Zhang.
Postdoc
Old Dominion University Ph.D. Students