## Slide 1: Bubble Chamber – Beam Requirements
January 5, 2018

## Slide 2: Bubble Chamber Experiment
Plan to be installed on March 26, 2018
April run plan:
  2 weeks of beam (2 shifts per day)
  Active liquid is C3F8
  Beam energy: 4.5 – 5.5 MeV
  Beam current: 1 nA – 100 µA
  Prefer to run with RF at 2K but willing to try 4K
Keep chamber installed at 5D line
Plan to run again in August: 2 weeks of beam

## Slide 3
5 MeV
Dipole
5D Spectrometer
Bubble
Chamber
location
Notes: Interior Page Design 2

## Slide 6: Schematics
Power deposited in radiator (100 µA and 8.5 MeV) :
  6 mm: Energy loss = 8.5 MeV, P = 850 W
Pure Copper and Aluminum (high neutron threshold):
  63C(g,n) threshold = 10.86 MeV
  27Al(g,n) threshold = 13.06 MeV
0.001 – 100 µA
Al Beam Pipe
Cu
Radiator/Dump
6 mm
Bubble Chamber
Superheated
Al Photon Dump
40 cm long
Cu Photon
Collimator
Ceramic
Insulator
Notes: Interior Page Design 2

## Slide 7: Beam Requirements
Beam Kinetic Energy, (MeV) | 4.5–5.5
Beam Current (µA) | 0.001–100
Absolute Beam Energy Uncertainty | <0.1%
Relative Beam Energy Uncertainty (0.1 MeV steps) | <0.02%
Energy Resolution (Spread), σT /T | <0.06%
Beam Size, σx,y (mm) | 1
Polarization | None
Electron Beam Requirements at Radiator
Notes: Interior Page Design 2

## Slide 8: Beam Energy Measurement
Beam Position Monitor (BPM)
5 MeV
Dipole
Electron Beam
Momentum
Notes: Interior Page Design 2

## Slide 10
  For Bubble Chamber experiment:
    Installed new higher field dipole with better uniformity
    Installed new Hall probe: 0.01% accuracy, resolution to 2 ppm, and a temperature stability of 10 ppm/°C
    Better shielding of Earth’s and other stray magnetic fields
    Implemented 5 MeV dipole precision DCCT current readback
  Relative beam energy uncertainty <0.02% is required
Parameter | Term | Before | Goal
Dipole – field map | δB/B | 0.20% | 0.02%
Dipole – power supply | δI/I | 0.20% | 0.02%
Position – surveys | δθ/θ | 0.01% | 0.01%
Position – BPM calibration | δθ/θ | 0.05% | 0.05%
Stray magnetic field | δθ/θ | 0.05% | 0.05%
Total | δP/P | 0.30% | <0.10%
Notes: Interior Page Design 2

## Slide 11: Beam Position Measurement
Keep beam centered on collimator
Measure beam position on radiator – use x-ray fluorescent screen
Survey 5D line (radiator and collimator)

## Slide 12
x-ray fluorescent screen was installed in front of radiator on Nov 2, 2015
This screen has a special coating that illuminates under x-rays and emits a green light

## Slide 13
0.5 μA centered on x-ray screen
Need to develop procedure to center beam on radiator using 5D line BPMs and viewers for different beam energies while accounting for earth’s magnetic field

## Slide 14: Beam Current Measurement
Approved to run 10 μA CW and total energy of 10 MeV – needs approval to run at 100 μA
Calibrate BCM and measure nA beam currents
Re-isolate radiator to measure beam current
Stop beam when chamber is unstable while quenching a bubble