## Slide 1: Injector Update
QWeak Collaboration Meeting
September 17, 2010
P. Adderley, J. Clark, S. Covert, J. Grames, J. Hansknecht,
R. Mammei, M. Poelker, M. Stutzman, R. Suleiman, K. Surles-Law

## Slide 2: Gun HV at CEBAF
CEBAF Inverted Gun (with Stainless Steel Cathode) delivered beam to Hall C at 130 kV on August 13, 2010
Conditioned to 150 kV with no FE in September 2010
Beam is being restored at 130 kV – This is the new Gun HV
Maximum possible Gun Voltage is 140 kV (limited by Safety System and HV Power Supplies)

## Slide 6: INJTWF Slow Helicity Reversal
Injector Two-Wien Flipper (INJTWF) commissioned during PREx
Will be re-calibrated at 130 kV

## Slide 7: 5 MeV Mott Polarimeter
New detectors to replace old ones:
Detectors are ready
Will be installed next week
Might improve response
to Mott electrons

## Slide 8: Quad Intensity Attenuator (QIA)
Installed for all 3 Halls
New 16-bit DAC (QIA, PC, WF HV)
Orange | CH 1 | Helicity
Blue | CH 2 | IA0
Violet | CH 3 | IA1
Green | CH 4 | Voltage

## Slide 9
Fast Pockels Cell (PC) Reversal:
New Helicity Board commissioned during PREx
Clock signal is 20 MHz. Is this OK for DAQ and FR?
More patterns: Toggle, Pair, Quartet, Octet, Hexo-Quad and Octo-Quad
Experiment | Rate | Clock | Pattern
HAPPEx III & PVDIS | 30 Hz | Free | Quartet
PREx | 120 Hz 240 Hz | Free Free | Quartet Octet
QWeak (Preliminary) | 1 kHz | Free | Quartet
Helicity Reversal

## Slide 10: Injector Team
Coordinator: Suleiman
Members: Poelker, Grames, Hansknecht, King, Carlini, Paschke, Dalton, Ramsay
A student

## Slide 11: Commissioning Plan
Heated & re-activated photocathode: Good QE & polarization 85%
Characterized RHWP
Studies Pockels Cell (PC) ringing
Devise a means to quantify ringing on once a week basis. An access to laser table can be made, but remote measurement preferable.
Measure Laser Spot-size asymmetries

## Slide 12
Rotate photocathode to reduce effect of vacuum window birefringence
Study beam phase-space when using Wien Flip. Quantify the difference between Vertical Wien and Solenoid method with beam to Hall and large position differences. Use the Solenoids, until someone makes definite measurements to use V-Wien
Zero vertical polarization using 5 MeV Mott Polarimeter in Injector – requirement: Py < 4%

## Slide 13
Spin dance to zero transverse polarization using Hall C Polarimeter – requirement: Px < 4%
Optimize Helicity Board settings: T_Settle, T_Stable, and Pattern. Need hydrogen target and Lumi
Commission Charge Feedback with the new QIA
Try 32 MHz beam for background studies and Moller Polarimeter in Hall C. Not Ready yet, QWeak must talk to Engineering if it is really needed.

## Slide 14: Maintaining Good Beam Quality
It is important to get to a stable beam delivery of 150 μA for days, without modifying the injector configuration (i.e., flipping spin direction, or going to nA beam, where we don't pay attention to beam loss, which must always be maintained small via steering magnets ...)
If things drift away from optimum and beam quality degrades, Operators need to learn which steering knobs to adjust to get back to acceptable injector configuration.
Need Online display in MCC of parity data (Injector and Hall C BPMs & BCMs)