## Slide 1: CEBAF Injector Overview
Reza Kazimi

## Slide 2: 12 GeV CEBAF
Injector
11.25% of
Linac Energy

## Slide 3: Beam quality and Injector
In CEBAF many of critical beam parameters are set in the injector and some remain unchanged through the accelerator. Therefore, the injector plays a significant role in setting the final beam qualities such as bunch structure, energy spread, current stability, etc.

## Slide 4: Brief description of the CEBAF Injector
Chopper
FC#1
FC#2
Buncher
Capture
Bunchlength
Cavity
Cryounit
Cryomodules
Synchrotron
Light Monitor
100/500 keV Mott
Polarimeter
5 MeV Mott
Polarimeter
Injection Chicane
45 MeV Dump/
Spectrometer
PreBuncher
Gun#2
Gun#3
V-Wien Filter
H-Wien Filter
Apertures
Polarized Electron Source
(130 kV)
Electron Spin Manipulation
Bunching & Acceleration
500 keV
SRF Acceleration
(<10 MeV)
SRF Acceleration
(<125 MeV)
Injection
Chicane
Spin Solenoids
Synchronous Injection
B
C
A

## Slide 5: Breaking down the problem
Chopper
PCup
FC#1
FC#2
Buncher
Capture
Bunchlength
Cavity
Cryounit
Cryomodules
Synchrotron Light Monitor
500 keV Dump
5 MeV Dump
Injection Chicane
4D Dump/Spectrometer
Prebuncher
Gun#2
Gun#3
V-Wien Filter
H-Wien Filter
Apertures
Beam Creation
Bunch Structure
Spin Angle
Space Charge Control
Bunching Process
Acceleration

## Slide 6: Beam Bunch and Pulse Structure
Four Lasers, creating four beams at 500 MHz or 250 MHz.
Viewer limited mode, 4 ms/60Hz pulses (very low power for viewers)
Tune mode, 250 ms/60Hz pulses for low power tune up (long enough to see BPM signals)
CW mode, infinite pulse
User defined pulse structure

## Slide 7: Beam Dumps
1D dump, ~ 500 keV, Spectrometer for beam setup, Beam parking place for safety system.
2D dump, ~ 5 MeV, Spectrometer for beam setup
3D dump, ~ 5 MeV, Mott measurement
5D dump, ~ 5 MeV, experimental line
4D dump, ~ 17 MeV to 125 MeV (Final injector energy) Spectrometer for beam setup, Potential experimental line

## Slide 8: PEPPo, Polarized Electrons for Polarized Positrons
Chopper
Faraday Cup
Buncher
Capture
Superconducting
Booster
Cryo-modules
500 keV Dump
5 MeV Dump, 2D
Injection Chicane
Spectrometer/Beam Dump
Prebuncher
Gun#2
Gun#3
V-Wien Filter
H-Wien Filter
Apertures
Faraday Cup
5D, PEPPO line

## Slide 9
Compton
Polarimeter
(DESY)
Collection
Magnets
(Princeton/SLAC)
Pair
Creation
Target
PEPPo measured the polarization transfer from 8.2 MeV/c longitudinal electrons to longitudinal positrons in the 3.1-6.2 MeV/c momentum range.
Polarized Electrons for Polarized Positrons

## Slide 10: PEPPo at CEBAF injector
1. We held a workshop in 2009 to get people involved
2. Then we submitted LOI to PAC, and recommended we submit full proposal following year
3. We submitted to PAC asking for 6 weeks, they rated experiment A, so...
4. Experiment scheduling committee recommended 6 weeks before 12 GeV upgrade
5. We pretty much followed the same readiness/reviews process of hall experiments
6. Arne was doing Beam Studies campaigns at that time, definitely benefitted being ready
7. Ran for ~6 weeks May-June 2012

## Slide 11
PEPPo (E12-11-105) @ CEBAF Injector
Compton
Polarimeter
(DESY/Cornell)
Positron
Spectrometer
(Princeton/SLAC)
Positron
Production
Target
Mott
Polarimeter
Lead
Shielding
Polarized
Electron Beam
(3-10 MeV)
Positron Annihilation Counters

## Slide 12: 2D, 3D, 5D Lines

## Slide 13: Bubble Chamber
This experiment will be staged in the exact place of the completed PEPPo experiment and will re-use the same beamline. The experiment will measure the 16O(γ,α)12C reaction with bremsstrahlung photons at 7 different electron beam kinetic energies ranging from 7.9 MeV to 8.5 MeV.

## Slide 14: Bubble 5D Line

## Slide 15: Bubble 5D Line

## Slide 16: Bubble 5D Line

## Slide 17
6.3 MeV Setup w/ SRF 0L02 @ 4K (beam to FC#2)
We have operated the injector cryounit (0L02) w/ SRF at 4K a few times over the past 2-3 years.
Our SRF setup steps have been essentially the same:
  Maintain JT flow greater than 70%
  Maintain LL greater than 90%
  Tune cavities (resonance different at 4K vs. 2K)
Last year we compared standard injector setup of 6.3 MeV beam (beam to FC#2) with SRF @ 4K vs. 2K, and found similar beam quality.
The momentum spread was determined to be somewhat larger at 4K, but still relatively small.
28th Linear Accelerator Conference, LINAC 16, East Lansing, Michigan, 25-30 September 2016

## Slide 18: 4D Spectrometer line 0.1% precision momentum measurement Typical Beam parameters: dE/E<1e-3 dE>50keV rms Bunch L.< 0.5ps

## Slide 19: Isotope Production 4D line

## Slide 20: 4D Isotope Production Quick Reference

## Slide 21: Current and Power Limits
4D Line

## Slide 25: Acknowledgments
Thanks to Matt Poelker, Riad Suleiman, Joe Grames, Joseph Gubeli and others for injector experiments’ slides

## Slide 26
End of Presentation
Thank You!