## Slide 1
Polarized Beams – A Tale of Two Leptons
The production of Highly Spin Polarized Positrons
using MeV Energy Spin Polarized Electrons
Joe Grames
Center for Injectors & Sources
Jefferson Laboratory
Notes: INJECTOR SCIENTIST AT JEFFERSON LAB
WOULD LIKE TO TELL YOU ABOUT A SMALL EXPERIMENT WE PERFORMED TO PRODUCE POLARIZED POSITRONS AT LOW ENERGY
WILL GET TO THIS COMMENT AT THE END

## Slide 2
• Deliver discovery-caliber research of the atomic nucleus, its constituents, and their interactions
• Apply advanced particle accelerator to develop new basic research capabilities
• Over 1500 Users from 230 Institutions and 30 Countries; over 1/3rd of U.S. Ph.D’s in Nucl. Phy.
Thomas Jefferson National Accelerator Facility is a U.S. Department of Energy Office of Science national laboratory located in Newport News, VA

## Slide 3
CEBAF Accelerator
CW electron beams to 4 Halls
Electron Polarization 85-90%
Max Energy: 11 GeV(ABC) / 12GeV(D)
Max Current: 85 mA
Still working on this graphic !!!

## Slide 4
  Positron physics motivation at Jefferson Lab
  CEBAF Injector PEPPo Experiment
  Polarized Positron R&D Opportunities
  Outlook
Outline

## Slide 5
Polarized Electrons have supported some of the highest impact results from the JLab program:
  The strangeness distribution in the nucleon (HAPPEX and G0)
  Precision Tests of the Standard Model (QWeak)
  Measurement of the neutron skin in 208Pb
  Polarization transfer measurement of GE/GM for the proton
Unpolarized positron beams provide a key tool for further pushing the precision of electron scattering experiments
  Comparison of e- with e+ tests our understanding of two photon effects
Polarized positrons beams provide essential tool
  Unraveling nucleon structure through the measurement of charge-sensitive General Parton Distributions
  Expand the nature of these tests (e.g. for GE/GM via polarization transfer)
Why Polarized Positrons at JLab?
Beam Quality | Electron Beam (Delivered) | Positron Beam (Desired)
Average Intensity | > 200 mA | > 100 nA (5 x 1011 e+/s)
Duty Factor | 100% (cw) | 100% (cw)
Bunch Frequency | 499 MHz (or sub-harmonic) | 499 MHz (or sub-harmonic)
Polarization (orientation) | > 89% (4p control) | > 50% (4p control)
Helicity Control | Rapid reversal (> 2 kHz) | Rapid reversal (> 30 Hz)

## Slide 6
A polarized positron injector suitable for the Jefferson Lab Electron Ion Collider (JLEIC) has been considered.
L ≥1033cm-2s-1 Pe+≥40%
Iave > 10 nA
e+
Polarized Positrons at an Electron Ion Collider
Challenge is accumulating high electron bunch charge prior to conversion.

## Slide 7
QE ~ 5%, 30 mA/W
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 mA/W
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Strained Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 mA/W
Pol ~ 89% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
Figure-of-Merit (P2I) has improved by a factor of 43
over the span of the CEBAF “6 GeV era”
Pe- 35% 35% 75% 75% 85% 89%
Ie- 30mA 100mA 50mA 100mA 150mA 200mA
1995 1998 1999 2000 2004 2012 2018
JLab’s e- Beams Provide the Basis for e+ Beams

## Slide 8
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
E.G. Bessonov, A.A. Mikhailichenko, EPAC (1996) A.P. Potylitsin, NIM A398 (1997) 395
Polarized Electrons for Polarized Positrons
Polarized Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Polarized Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)
Notes: THE PEPPO METHOD IS PRETTY STRAIGHT-FORWARD
FIRST STAGE IS POLARIZED BREMMSTRHALUNG
SECOND STAGE IS POLARIZED PAIR CREATION
THIS COULD BE DONE IN SEPARATE TARGETS, BUT CONVENIENTLY ALSO IN ONE SINGLE TARGET
WE LEARNED EARLY ON THE CALCULATIONS OF OLSON/MAXIMON WERE NOT CORRECT AT LOW ENERGY, ESPECIALLY PAIR CREATION
NEW CALCULATIONS WERE DONE, THAT AGREE W/ OM AT HIGHER ENERGIES
WE WERE NOT FIRST TO PROPOSE THIS IDEA, SO WHY NOT BEFORE…

## Slide 9
J. Grames, E. Voutier et al., JLab Experiment E12-11-105 (2011)
The purpose of the PEPPo (Polarized Electrons for Polarized Positrons) experiment at the CEBAF Injector was to demonstrate the feasibility of using bremsstrahlung radiation of MeV energy Polarized Electrons for the efficient production of Polarized Positrons.
PEPPo Demonstrated Efficient e+ Production

## Slide 10
1. BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
e+
2. PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
3. Phase Space Definition
The emittance of the positron beam is defined by slits and magnetic fields
S1
D
D
S2
Positron Transverse and Longitudinal Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
4. COMPTON TRANSMISSION POLARIMETER
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
PEPPo: Principle of Operation

## Slide 11
e+
Pe+
Polarized positrons incident on a target also produce polarized bremsstrahlung.
Positron polarization is related to the transmission of the bremsstrahlung through magnetic material by the spin dependent Compton cross-section.
μ1 - Compton absorption coefficient
L - target length
P3 - photon polarization (long.)
Pe - electron/positron polarization
PT - target polarization
Ae - analyzing power
g
Polarimeter Target (Densimet D17K) 90.5% W, 7%, 2.5% Cu
Compton Transmission Polarimetry
PT = 7.06% ± 0.05% (sys1) ± 0.07% (sys2)
Fe Core

## Slide 12
C
A
L
O
R
I
M
E
T
E
R
e+
g
Trigger Scintillator
10mil Al window
Reconversion
Target
Positrons are detected in coincidence between a thin trigger scintillator placed prior to the reconversion target and the central crystal and tagged by e- helicity.
Trigger Scintillator
Coincidence
Calorimeter
Compton Transmission Polarimeter
WITHOUT
Coincidence
WITH
Coincidence
Background

## Slide 13
PEPPo demonstrated efficient polarization transfer of 8.2 MeV/c polarized electrons to positrons, expanding polarized positron production using MeV electron beam energies.
(PEPPo Collaboration) D. Abbott et al. , Phys. Rev. Lett. 116 (2016) 214801
electron beam polarization
85.2 ± 0.6 ± 0.7 %
Whenever producing e+ from e-, polarization is coming for free, if initial electrons are polarized.
PEPPo Experiment Result

## Slide 14
P. Adderley1, A. Adeyemi4, P. Aguilera1, M. Ali1, H. Areti1, M. Baylac2, J. Benesch1, G. Bosson2,
B. Cade1, A. Camsonne1, L. Cardman1, J. Clark1, P. Cole5, S. Covert1, C. Cuevas1, O. Dadoun3,
D. Dale5, J. Dumas1,2, E. Fanchini2, T. Forest5, E. Forman1, A. Freyberger1, E. Froidefond2,
S. Golge6, J. Grames1, P. Guèye4, J. Hansknecht1, P. Harrell1, J. Hoskins8, C. Hyde7, R. Kazimi1,
Y. Kim1,5, D. Machie1, K. Mahoney1, R. Mammei1, M. Marton2, J. McCarter9, M. McCaughan1,
M. McHugh10, D. McNulty5, T. Michaelides1, R. Michaels1, C. Muñoz Camacho11, J.-F. Muraz2,
K. Myers12, A. Opper10, M. Poelker1, J.-S. Réal2, L. Richardson1, S. Setiniyazi5, M. Stutzman1,
R. Suleiman1, C. Tennant1, C.-Y. Tsai13, D. Turner1, A. Variola3, E. Voutier2,11, Y. Wang1, Y. Zhang12
1Jefferson Lab, Newport News, VA, US, 2 LPSC, Grenoble, France, 3LAL, Orsay, France
4 Hampton University, Hampton, VA, USA 5 Idaho State University & IAC, Pocatello, ID, USA
6 North Carolina University, Durham, NC, USA 7 Old Dominion University, Norfolk, VA, US
8 The College of William & Mary, Williamsburg, VA, USA 9 University of Virginia, Charlottesville, VA, USA 10 George Washington University, Washington, DC, USA 11 IPN, Orsay, France
12 Rutgers University, Piscataway, NJ, USA 13 Virginia Tech, Blacksburg, VA, USA
Many thanks for support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and Jefferson Science Associates
The PEPPo Collaboration

## Slide 15
Two NaI detectors measured coincidence of back-to-back photons emitted by annihilation of positrons in a viewscreen.
Positron Yield at MeV Energies
T1
T2
S1
S2
D
D
e+
e-
pe-= 8.2 MeV/c
e+
For these data we had a yield of ~10-5 e+/e-
A3
A1
A3
A1

## Slide 16
R. Dollan, K. Laihem, A. Schälicke, NIM A 559 (2006) 185,
J. Dumas, J. Grames, E. Voutier, JPos09, AIP 1160 (2009) 120
J. Dumas, Doctorate Thesis (2011)
Optimum energy
Optimum
FoM
The polarization distribution of generated positrons is dominated by low-energy events.
The positron energy at the optimum FoM (P2I) is about half of the electron beam energy.
Figure of Merit (Ee- = 60 MeV)
16
Producing highly polarized positron beams with intensities > 100 nA with typical injector energies (10-100 MeV) requires polarized electron beam intensities of >1-10 milliAmps

## Slide 17
Lifetime of GaAs/GaAsP at mA current
  Recent measurements demonstrate improved conditions to extend useful operational lifetime at mA beam intensity
  Charge lifetimes 300-450 C are now achieved beam intensity >1.0 mA

## Slide 18
  Superlattice Performance >1 mA Encouraging
Year
Intensity (mA)
SLAC: First GaAs photogun
JLAB: Low-P Bulk GaAs
JLAB: High-P GaAs/GaAsP
Chart: Electron Polarization (%)
| 1.67 | 10.4 | 50.5 | 100.5 | 250.5 | 504 | 755 | 1011 | 1.06
 | 85.6704 | 84.5218 | 84.3896 | 85.3479 | 84.9536 | 86.116 | 84.7714 | 85.9647 | 87.1486
?

## Slide 19
Polarized Positron Injector Concepts Abound
We’ve explored a number of concepts to varying degrees (PhD theses, proposals, intuitions, napkins).
The common denominator at JLab is making use of our skill sets: Polarized Beams, SRF, Photoinjectors, High energy beams, etc).
A polarized e+ injector is novel:
  mA polarized e- source
  fast helicity reversal
  cw operation
  high power target
  srf acceleration

## Slide 20
A new injector facility for research and design is coming on-line soon
Polarized electron beams
Beam energy up to 10 MeV
Beam intensity up to 100 mA (100 nA initial)
THIS AREA could be used to test key apparatus for a polarized positron source (target and collection).
Upgraded Injector Test Facility

## Slide 21
High Power Target R&D
Stainless Steel Windows (0.25mm)
LBE (2mm)
Input (e-)
Output (e-,e+,γ)
Liquid Metal Target – lead-bismuth eutectic (LBE)
  High Z = 82, 83
  Low melting point: 124°C
  High boiling point: 1670°C
Multiple LBE targets tested on various accelerators
  Natural Circulation
  Mechanical Pumping
  Electromagnetic Pumping
Approaching 10 kW power level, CW

## Slide 22
Summary and Outlook
Jefferson Lab Users are making a case to JLab Management to use polarized positron beams at CEBAF for high impact experiments.
With a relatively small footprint (cost, energy, radioactivity) the PEPPo experiment demonstrated highly spin-polarized positrons from moderate energy polarized electrons.
The progress of mA-sources and MeV-energy electron injectors is promising for the development of polarized positron beams with intensity >100 nA (5 x 1011 e+/sec).
Future work at JLab would focus on building and testing a collection system that defines the transverse, longitudinal and energy acceptance.
Synergistic collaboration can be fruitful, but a comprehensive plan supported by JLab Management that can be successfully executed is essential.

## Slide 23
Backup

## Slide 24
P(e+) = 73 ± 15(stat) ± 19(syst) %
Compton Backscattering (KEK)
T. Omori et al, PRL 96 (2006) 114801
Helical Undulator (SLAC E166)
G. Alexander et al, PRL 100 (2008) 210801
P(e+) = 80 ± 7(stat) ± 9(syst) %
47.7GeV
Polarized b+ Decay
L.A. Page & M. Heinberg. Phys. Rev.
106(6):1220-1224 (1957)
Polarized due to parity non-conservation in the weak interaction
P(e+) ~ 40 %
Sokolov-Ternov Effect
D. Barber , AIP Conf. Proc. 588, 338 (2001)
HERA 27.5 GeV e+/e-
P(e+) ~ 70 %
Methods for Generating Polarized Positrons
Notes: TO PROVIDE SOME CONTEXT, POLARIZED POSITRONS CAN BE COLLECTED IN A NUMBER OF WAYS
BETA DECAY – WEAK INTERACTION (NOT EFFICIENT FOR RF ACCEL)
ST – QUANTUM EMISSION OF SYNC. RAD. (NOT COMPATIBLE W/ CW BEAM)
PAIR PRODUCTION BY POLARIZED GAMMAS (PLAUSIBLE, BUT HIGH TECHNICAL CHALLENGE – INTENSE LASERS, HIGH ENERGY BEAMS)
WE WONDERED IF WE COULD SIMPLY USE OUR POLARIZED ELECTRON BEAM

## Slide 25
511 keV from e+ annihilation at rest
Bremsstrahlung
end-point
Energy (FADC units)
Energy Integrated Asymmetry
Accidentals
Time (TDC units)

## Slide 26
PEPPo Principle of Operation
S1
D
D
S2
Positron Transverse and Longitudinal Phase Space Selection
e+
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
Ee = 6.3 MeV
Ie = 1 µA
T1 = 1 mm W
Geant4
PEPPo
J. Dumas, PhD Thesis (2011)
PEPPo measured the longitudinal polarization transfer from 8.25 MeV/c e- to e+ in the 3.07-6.25 MeV/c momentum range.