## Slide 1: Magnetized Beam Simulations (LDRD)
Fay Hanon
March 29, 2016
Notes: Title Page

## Slide 2: Overview

## Slide 3: Goals
Produce a magnetized beam from a 350kV DC gun
Measure magnetization
Measure emittance
Demonstrate a round to flat transform

## Slide 4: Beamline
Gun
‘Magnetizing’ Magnet
Solenoid 0.6m
H slit/ Viewer
1m
H slit/Viewer
1.38m
Fcup/viewer 1.6m
Dump

## Slide 5: Beamline
Cathode prep chamber
Gun
solenoid
diagnostics

## Slide 6: Beam Evolution
Parameter | 
Cathode Bz | 0.2T
XY_rms, top-hat | 1.5mm
t rms, Gaussian | 23ps
Charge | 0 – 420pC
Gun voltage | 350kV

## Slide 7: Transverse rms beam size
20pC, 100pC, 210pC, 420pC
TRANSPORT THE SAME: DOMINATED by canonical angular momentum!
Ldrd.010
Location of solenoid
Big beam!

## Slide 8: Transverse normalize trace-space emittance
Ldrd.010
Angular momentum included in calculation of emittance

## Slide 9: Bunch length rms
Longitudinally we see space charge as usual.
Ldrd.010

## Slide 10: Measurements - Emittance

## Slide 11: Double slit emittance measurement

## Slide 12: Double slit virtual experiment
At the diagnostic, break the beam up into beamlets transversely to simulate the beam scanning over the slit
Let the beamlet particles drift to the second slit location (removing any that intercept the diagnostic)
Break the beamlet up into more beamlets
Count particles in each sub beamlet
Produce phase space

## Slide 13: Virtual result
Directly from simulation
Reconstructed via 2 slit method
Can change slit size and spacing to get best design

## Slide 14: Measurements - Magnetization

## Slide 15: Magnetization/Angular momentum
Insert a slit into the beamline to select an emittance-dominated beamlet.
Let the beamlet drift to a screen and image it.
  :
  D: drift between diagnostics, : angular rotation, pz : longitudinal momentum

## Slide 16: Fermilab experiment

## Slide 17: Example beam
Ldrd.014.001

## Slide 18: Movie

## Slide 19: Magnetization virtual experiment
Blue – beam at the slit (500k, 20um slit)
Red – particles selected by slit
Green – particles tracked to screen 0.26m away
Not linear!
Assumes a solenoid at cathode with 0.2T peak
0.07% particles through slit
Ldrd.009.0100.001
Nrad=70, Nlong_in=100
420pC

## Slide 20: Magnetization virtual experiment
The curve is still evident at 20pC.
Ldrd.009.0100.002
Ldrd.009.0100.004
Nrad=70, Nlong_in=100
210pC
20pC
This isn’t charge related.

## Slide 21: Phase space plots
This is what the slit cuts out in phase space
Ldrd.009.0100.001

## Slide 22: Why is there an ‘S’?
This is the solenoid field I used…
Could it be because the field isn’t uniform transversely over the emitting spot?

## Slide 23: Why is there an ‘S’?
This is what simulation assumes off axis
Slight variation
x
z
Bz

## Slide 24: Why is there an ‘S’?
Make fake Helmholz pair field
Cathode here!
Make fake field map.

## Slide 25: Compare
Ldrd.010.001
Ldrd.009.001
Both 420pC
Fake Helmholtz coil
Standard solenoid

## Slide 26: 4 real field maps, scaled to give ~0.2T
Chart: Options Combined

## Slide 27: Transverse beam size, emittance

## Slide 28: Magnetization virtual experiment
Can’t see ‘S’
– all seem linear… why is this…
At 1m
Ldrd.013.001-004

## Slide 29: Normal solenoid
Ldrd.014

## Slide 30: Normal solenoid
Ldrd.014

## Slide 31: Is the trick to keep beam small in beamline solenoids?
Trying not to have different B.dl over transverse direction.
Ldrd.017.0072.004

## Slide 32: Let beam get big and then focus
So even with good Helmholtz field it can become distorted!
Ldrd.020

## Slide 33: Measurements - Round to Flat Transform

## Slide 34: Modified beamline
Gun
‘Magnetizing’ Magnet
Solenoid 0.6m
Diagnostics
Dump
3 skew quads
x
y
x
y
Emittance splits into a large and small component

## Slide 35: Beam evolution

## Slide 36: Beam evolution

## Slide 37: Beam evolution

## Slide 38: Conclusions

## Slide 39
Simulations show we should be able to demonstrate measurement of angular momentum dominate beams
Space charge does not effect transverse transport much
Should try to keep transverse size small
Round to flat possible with low energy beam

## Slide 41: Increase gun voltage
CAM dominated
Ldrd.023

## Slide 42: So what does the emittance look like
Remove the contribution from angular momentum. Calculate the angular momentum from a correlation in the x, px phase space and subtract prior to the emittance calculation.
Ldrd.024

## Slide 43: Field calculation
In astra – off axis fields calculated from the on-axis field profile derivatives polynomial expansion
Bz(r)=Bz,0-(r^2/4*Bz’’)+(r^4/64*Bz’’’’)…etc
Br(r)=-r/2*Bz’+(r^3/16*Bz’’’)… etc
Flatter the profile, less variation in Bz off axis.