## Slide 1: Bubble Chamber Planning Meeting
24 July 2013

## Slide 2: Agenda
Schedule
Design of beamline, radiator and dump
Bubble Chamber work at Argonne
Simulation and Background
Absolute beam energy
Safety

## Slide 3: 12C(α, γ)16O S-Factor
Statistical Error: dominated by background subtraction from 18O(γ,α)14C (depletion = 5,000)
Systematic Error: dominated by absolute beam energy (= 0.2%)
SE1(300 keV) = 74±21 keV b

## Slide 4: Schedule
12GeV CEBAF Commissioning:
Bubble Chamber Activities:
  Install beamline, radiator and dump
  Commission beamline, radiator and dump
  Install Bubble Chamber
  Commission Bubble Chamber
  Physics run
 | Start | End
Period I | 2013-11-04 | 2013-12-20
SAD I | 2014-01-02 | 2014-02-05
Period II | 2014-02-05 | 2014-05-07
SAD II | 2014-05-07 | 2014-09-22
Period III | 2014-09-22 | 2014-12-19
SAD III | 2015-01-02 | 2015-02-13
Period IV | 2015-02-13 | 2015-06-12

## Slide 5: Design of beamline, Radiator & Dump
Need to design new beamline to replace PEPPo beamline and increase the distance between the two BPMs
Radiator: 0.02 mm and 0.1 mm Copper
Electron Dump: 2kW dump (10 MeV, 200 µA)
Photon Dump

## Slide 6
Electron Beam
3.0 – 8.5 MeV (K.E.)
0.01 – 100 µA
Al Beam Pipe
Cu Radiator
0.02 mm
Cu Electron Dump
Sweep Magnet
Bubble Chamber
Superheated N2O
3 cm long
15°C, 60 atm
Al Photon Dump
10 cm long
20 cm diameter
50 cm
50 cm
Cu Vacuum Window 10 mil
Cu Photon
Collimator
Cu Inner
Pipe

## Slide 7
BCM
5 MeV
Dipole
5 MeV
Spectrometer
PEPPo/Bubble
Chamber
Beamline
Bubble
Chamber
location
27’’

## Slide 8: Simulation
Two programs:
  GEANT4
  FLUKA
Both use models that calculate wrong cross sections. Both do not allow for user’s cross sections. Suggestion:
  Use GEANT4 and FLUKA to produce the photon spectrum impinging on the super heated liquid.
  Fold the above photon spectrum with our cross sections in stand-alone codes.
Both GEANT4 and FLUKA are good in neutron tracking. Still need to check the neutron cross sections.

## Slide 9: Background
Must measure:
  17O(γ,α)13C , enrichment=10%
  18O(γ,α)14C , enrichment=10%
Rates:
  17O(γ,α)13C, depletion=5,000
  18O(γ,α)14C, depletion=5,000
  14N(γ,p)13C, detection eff.= 10-8
  Natural Abundance:
    17O: 0.038%
    18O: 0.205%
Still need to study 17O(γ,n)16O, …

## Slide 10: Safety
High pressure system
Super heated liquid: N2O or CO2
Buffer liquid: Mercury

## Slide 11: Running in FEL?
Absolute Beam Energy: FEL can measure the energy with a precision of 0.4%. However, it could be very hard to improve (?)
Required Systems:
  Personnel Safety System (PSS)
  Liquid helium and RF
  Gun Laser
  Staff

## Slide 12: Planning Meeting
Do we want to meet every two weeks?
Wednesday 3:00 – 5:00 pm?