## Slide 1: CEBAF Injector Update PREX/CREX March 3-4, 2017
Joe Grames
Center for Injectors and Sources

## Slide 2: Outline
Operation
  Recent Source Performance
  Delivering Spin in the 12 GeV era
  Simultaneous 4-Hall Operation
Injector Upgrade
  Overview of planned work
  Status updates
  Near term plans 2017-2018
Parity Quality Beam Readiness

## Slide 3
3
Source Operation
Spring/Fall 2016
  SSL GaAs/GaAsP SVT #5756-4 (Polarization ~ 87%)
  No heat/activation over Summer 2016 / Winter 2017 SADS
Fall 2016
Gun2 operating at -130 kV without any problems
Charge lifetime >100C with average current 70-80 mA
Spring 2017
Delivering up to 3 halls at a time (either 249.5 or 499 MHz)
Hall A (Physics), Hall B (KPP), Hall C (KPP), Hall D (Physics)
Jun 2016
Sep 2016

## Slide 4
PSS High Voltage Interface Upgrade
Fall 2016
Historically Gun HV commensurate with PSS Beam Permit state => Off often!
Gun HV power supply now remains ON when PSS = Power Permit
Anticipate improved injector reliability and possibly increased charge lifetime
First 5 weeks of
Spring 2016 Run
(before upgrade)
First 5 weeks of
Fall 2016 Run
(after upgrade)

## Slide 5
Delivering Spin in 12 GeV era
Spring 2016
Synchrotron radiation energy losses become important for spin precession > 3rd pass
  (not an issue for CREX/PREX)
We are using Elegant to calculate evolving energy and post-processing spin calculation
Model vs. measured with Hall A @ 11 GeV agrees within couple degrees (<10-4 level)

## Slide 6
Condition | (D+2) | (D+3)
Maximum number of halls receiving beam | 3 halls | 4 halls
ABC Beam @ 5th pass (Hall D on) | 499 MHz | 249.5 MHz
ABC Beam @ 5th pass (Hall D off) | 499 MHz | 499 MHz
ABC Beam @ lower passes | 499 MHz | 499 MHz
  CEBAF 4-Hall Operations Begins Fall 2017
4 Hall Operations (also called D+3) begins this Fall
4 Hall Preparations Completed ….so far
  Rebuild laser table w/ 4th laser and 4-beam combination
  Two beams @ 249.5 MHz share one 499 MHz “RF Chopping Bucket”
  750 MHz separators for 5th pass ABC / D separation

## Slide 7
4-Hall Polarized Source Laser Table Rebuild
Summer 2016

## Slide 8
4-Beam Operations Punch list
Summer 2017 Shutdown
  New LLRF system to support 4 lasers and 499/249.5 MHz
  Improve => define, communicate, manage, archive 4-Hall Ops
      (4 lasers, 2 rep rates, 6 unique RF buckets, 5.5 passes, 4 halls)

## Slide 9
Poor Extinction
(dc HV)
Afterpulse
(old cell)
Tune Mode Generators
High bandwidth RTP electro-optic crystals used to shutter beam (Pulsed Mode)
New/simpler design implemented Summer 2016 => maintains dc voltage on crystal:
  Contrary to vendor claim RTP suffers from ion migration from electrode to RTP
  Returning to conventional configuration Summer 2017
Cells are mainly >10 years old, signs of degradation from long term use
  Asked management for additional funds ~$24k

## Slide 10
    AIP Injector Upgrade Project
(A. Freyberg Aug 2016 ECT’16)

## Slide 11
Injector Upgrade (what remains after R100)
Increase gun voltage and Wien filters for 200kV operation
Improve baked beam line vacuum so gun does not pump on beam line
Locate Wien filters (energy filter) upstream of pre-buncher cavity
New SRF booster eliminates warm capture, RF deflection and x/y coupling
Our new “1/4 cryomodule”:
2 cell capture section + 7 cell cavity,
should provide 10 MeV beam and introduce no x/y coupling, allow better matching, more adiabatic damping
200 kV

## Slide 12
Chart: Transmission Vs Gun Voltage
| 50.0 | 100.0 | 150.0 | 200.0
200KeV | 97.9 | 97.7 | 97 | 96.6
115KeV | 93.7 | 86.6 | 77.8 | 69.9
100KeV | 92.6 | 78.4 | 67.4 | 60.3
85KeV | 85.6 | 66.7 | 57.3 | 50.9
70KeV | 72.5 | 54.5 | 46.2 | 39.6
Chart: Transmission vs Gun Voltage
| 11.7 | 26.0 | 51.4 | 74.8 | 98.2 | 122.2 | 148.0 | 170.5 | 198.0
115kV | 96.5812 | 92.6923 | 82.4903 | 73.262 | 67.0061 | 61.784 | 57.6351 | 54.8974 | 51.3131
100kV | 99.0099 | 92.7419 | 77.8431 | 66.7553 | 59.2 | 52.7911 | 47.451 | 44.2153 | 40.5941
85kV | 93.8931 | 83.274 | 67.2761 | 56.2421 | 47.6465 | 40.9161 | 35.0449 | 30.9244 | 27.2059
70kV | 77.2727 | 61.6327 | 45.2479 | 35.9712 | 29.0608 | 23.7197 | 19.8027 | 17.2973 | 14.5238
Measured
Modeled
Parity Quality Beam improves with better transmission
  Space charge repulsion drops as beam becomes more relativistic
Why a higher voltage gun?
Parity Quality Beam improves with more uniform Quantum Efficiency
  Electron impact ionization cross-section falls with increasing beam energy

## Slide 13
CEBAF Upgrade Activities at the UITF
TEST MORE ROBUST (>300kV) INVERTED GUN
COMMISSION 2/7 CELL CRYOUNIT
TEST 200 kV WIEN FILTER

## Slide 14
Testing high voltage gun at UITF
8 MV/m
11 MV/m
Benefits of higher gun voltage will be tested
Doped insulator to bleed ceramic charge
Spherical electrode and shed to minimize gradient
Improvements to NEG pumps/geometry for pumping
450kV HVPS
Tested
HV Chamber
Baked ~2E-12 T
Prep Chamber ready for activation

## Slide 15
Testing 200 kV Wien filter at UITF
Will test the 200 kV Wien characterization
  Existing Wien filters limited to about 150 keV beam
  Believe we can modify for 200 keV beam
  Barrel polished electrodes, successfully tested HV feed thru to 20kV
  Shop is fabricating new 20A coils Jay proposed (JLAB-TN-15-032)
  Small modification to magnet completed to accept new coils
Wien Upgrade for 100 deg precession |  |  | 
Beam Voltage | keV | 200.00 | 350.00
Integrated BL | G-cm | 3993.86 | 6788.51
Magnet Current | A | 15.36 | 26.11
Electric Field | MV/m | 2.67 | 5.27
Electrode High Voltage | kV | 20.05 | 39.56

## Slide 16
Testing new CEBAF Cryounit at UITF
2016 Commissioning at Test Lab
  Summer 2016 – Cryostat assembled + cryo @ UITF
  Fall 2016 – SRF commissioned to 20 MV/m @ CMTF
  Winter 2017 – Moved to UITF

## Slide 17
UITF Today

## Slide 18
A. Freyberg Aug 2016 ECT’16 =>
PREX/CREX
timescale
Not likely if we test at UITF first

## Slide 19
Summer 2017 – Install/Test 200kV gun @ CEBAF
  Modify existing CEBAF/ILC 200 kV gun design
  Install 200 kV HV chamber and operate with higher voltage PS
  Run 200 keV beam and test functionality of existing beam line
Spare CEBAF/ILC Gun:
Operated at 200kV and up to 4mA at Test Cave
Upgrading Polarized Source / Beamline
Summer 2018 – Rebuild Two Wien Beam line
  Install 225 kV HVPS for routine operation (will run -130kV until new QCM)
  Modify INJTWF beam line layout and w/ 200kV Wien filters

## Slide 20
Scheduled Accelerator Down : Summer 2017

## Slide 21
Parity Quality Beam Readiness
PQB specs for PREX/CREX have been demonstrated
  QWeak achieved these with higher current for longer duration
  Recall we are now operating with essentially the QWeak injector today
Resume the same successful mindset from the 6 GeV era
  Careful control of source systematics (Pockels cell, laser spot size, QE)
  Optimizing injector transmission to minimize intensity asymmetry
  Matching across the cryo-unit to benefit from setup at the source
  Careful separation of the beam
On-going Injector upgrade activities benefit PREX/CREX
  Motivated to improved parity quality beam
  Improved two-Wien spin flipper will be ready for Fall 2018

## Slide 22
Summary
CEBAF Operations
  Source is operating well, providing high polarization at 11 GeV
  On track for 4-Beam operations in Fall 2017, time will tell how easy this is.
Injector Upgrade
  Deliver and test 200 kV beam at CEBAF injector Summer 2017 SAD
  Test of 200 kV Wien filter, new QCM and higher voltage polarized gun at UITF
  Rebuild baked beamline with 2-Wien spin flipper Summer 2018 SAD
Parity Quality Beam Readiness
  Required specifications have been demonstrated
  We are ready to return to setting up and delivering PQB beams