## Slide 1: CEBAF Polarized Electron Source
JLab Summer Lecture Series, July 11, 2017
Joe Grames
Center for Injectors and Sources
wiki.jlab.org/ciswiki

## Slide 2
Where do we find energetic electrons ?
Storage batteries, power generators, wall-plug power, Nature, movies and… in particle accelerators!!!

## Slide 3
7Li

## Slide 4
Energy scale to probe massive particles…
energy ~ 1/l ~ mass
M ~ 938 MeV/c2
m ~ 0.511 MeV/c2
E = mc2

## Slide 5: What to do?
Build a 5 mile long electron microscope!
Make electrons energetic enough (Ebeam) to peek inside proton or neutron (Mnucleon).
Neutron
Proton
Electron

## Slide 6: How to make the electrons “energetic” ?
?
?
Accelerating voltage
Decelerating voltage
Electrons gain energy on each crest!
Use oscillating voltage !!!
How about static voltage?
Air ~ 6 MV/m
Sulfur hexafluoride ~15 MV/m
Ceramic ~ 30 MV/m

## Slide 7: Photo Finish at 2 billionths of a second !!!
“DC” Electron Current
A B C
Short electron bunch
Short Pulse Electron Bunches
A
B
C
Bunch < 1ps
DC beam
500 MHz = 2 ns/revolution

## Slide 8: The “C” in CEBAF
1 Coulomb
1 Coulomb

## Slide 9: The CEBAF polarized source “Big Three”
High frequency
High power
Polarization
Laser
Very high voltage
Ultra high vacuum
No field emission
Gun
Photocathode
Many electrons/photon
High polarization
Fast response time

## Slide 10
-130kV
light in
electrons out
photocathode
DC High Voltage Electron Gun

## Slide 11
Vacuum conditions at CEBAF
Application | Pressure Range | Location | Vacuum Regime
Beamline to dumps | 10-5 Torr | Target to dump line | Medium
Insulating vacuum for cryogens | 10-4 Torr to 10-7 Torr | Cryomodules, transfer lines | Medium to high
Targets, Scattering Chambers | 10-6 to 10-7 Torr | Experimental Halls | High to very high
RF waveguide warm to cold windows | 10-7 to 10-9 Torr | Between warm and cold RF windows | High to very high
Warm beamline | 10-7 to 10-8 Torr | Arcs, Hall beamline, BSY, some injector | High to very high
Warm region girders | 10-9 Torr or better | Girders adjacent to cryomodules | Very high to ultrahigh
Differential pumps | Below 10-10 Torr | Ends of linacs, isolate cryomodules | Ultrahigh vacuum
Baked beamline | 10-10 to 10-11Torr | Y chamber, Wien filter, Pcup | Ultra high vacuum
Polarized guns | 10-11 to 10-12 Torr | Photoguns | Ultra to Extreme high vacuum
SRF cavity vacuum | < 10-12 Torr | Inside SRF cavities with walls at 2K | Extreme high vacuum
1 Atmosphere ~ 760 Torr

## Slide 12
Vacuum regimes
Low, Medium Vacuum (>10-3 Torr)
  Viscous flow
    interactions between particles are significant
  Mean free path less than 1 mm
High, Very High Vacuum (10-3 to 10-9 Torr)
  Transition region
Ultra High Vacuum (10-9 - 10-12 Torr)
  Molecular flow
    interactions between particles are negligible
    interactions primarily with chamber walls
  Mean free path 100-10,000 km
Extreme High (<10-12 Torr)
  Molecular flow
  Mean free path 100,000 km or greater
Air ~ 1016 / Torr-cm3

## Slide 13
Ultra High Vacuum
Avoid contamination by oils due to roughing pumps, fingerprints, machining.
Baking used to get pressures below 10-10 Torr
  250°C for 30 hours removes water vapor bonded to surface that otherwise limits pressure
Getter Pumps
  Chemically active surface
    Titanium sublimed from hot filament
    Non-Evaporative Getters
  Molecules stick when they hit
    Does not work well for inert gasses such as Argon, Helium or for methane
Ion Pumps
  Electric field to ionize gasses
  Magnetic field to direct gasses into cathodes where they are trapped
    Has some pumping capability for noble gasses
NEG pump array
Ion Pump

## Slide 14: The CEBAF polarized source “Big Three”
High frequency
High power
Define Polarization
Laser
Very high voltage
Ultra high vacuum
No field emission
Gun
Photocathode
Many electrons/photon
High polarization
Fast response time

## Slide 15: RF High Power Fiber Laser
1560 nm
780 nm
Master Oscillator
499 MHz
Low-Power (1 mW)
1560 nm Fiber Diode
Follows RF sine wave
Frequency-doubler
1560 nm to 780 nm
30% Efficiency (2 W)
High Power (6 W) 1560 nm Fiber Amplifier

## Slide 16
Continuous Electron Beam Accelerator Facility
A
B
C
A
B
C
RF Synchronous
Lasers
499 MHz,
ΔФ = 120
Pockels Cell
Gun
2 Linacs
1497 MHz
RF Separators
499 MHz
B
A
C
A B C A B C
100 ps
D
D

## Slide 17
Combine 4 lasers onto a single path !!!

## Slide 18: The CEBAF polarized source “Big Three”
High frequency
High power
Synchronous RF
Laser
Very high voltage
Ultra high vacuum
No field emission
Gun
Photocathode
Many electrons/photon
High polarization
Fast response time

## Slide 19: Accelerators need “freed” electrons ! How might get them?
Field Emission (electronic energy)
Thermionic Emission (thermal energy)
Photo Emission (optical energy)
All are manifestations of electromagnetism

## Slide 20: The Canonical Emission Equations (slide courtesy of Dr. K. Jensen, Naval Research Laboratory)
Field Emission Fowler Nordheim E.L. Murphy, and R.H. Good, Physical Review 102, 1464 (1956).
Thermal Emission Richardson-Laue-Dushman C. Herring, and M. Nichols, Reviews of Modern Physics 21, 185 (1949).
Photoemission Fowler-Dubridge L.A. DuBridge Physical Review 43, 0727 (1933).
Listed chronologically

## Slide 21: Field Emitter Sources
Explained by Fowler and Nordheim (1928): a quantum mechanical tunneling effect
Small emission area makes for a very “bright” beam, good for surface science
I = BV2 exp(-C/V)
Vacuum diode
60°
human hair

## Slide 22: Thermionic Emission
Studied since early 1800’s and perfected over 100 years
Thermionic emission from Tungsten filaments and metalloids like LaB6 operating at >1000K are common
>90% of consumed power simply generates heat
Edison’s patent,
Long-lasting filament
Melts 3695K

## Slide 23: Thermionic Emission
Used to make x-ray light….
1880s
X-rays are generated when a DC electron beam, typically a few mA, strikes a tungsten target at 60-200 keV. e-Beam quality is not a big concern
Rotating anode to distribute heat
1930’s
bias at high voltage

## Slide 24: Photo-Emission from bulk GaAs
Bare GaAs surface
Large Work Function
Positive Electron Affinity (PEA)
PEA=4.07 eV
Egap
Conduction
Band
Valence
Band
GaAs
Vacuum
Dipole layers of
Cesium + NF3
Reduces Work Function
Negative Electron Affinity (NEA)
+
-
-
χNEA ~ 0.2 eV
GaAs
Vacuum
Light
NEA Surface Activation
Quantum Efficiency ~ 10% (1e-/10 photons)

## Slide 25: What about the probing with spin ?
Target
You measure
an experimental
asymmetry

## Slide 26: Parity Violation Experiments at CEBAF
Experiment | Energy (GeV) | I (µA) | Target | Apv (ppb) | Maximum Charge Asym (ppb) | Maximum Position Diff (nm) | Maximum Angle Diff (nrad) | Maximum Size Diff (δσ/σ)
HAPPEx-II (Achieved) | 3.0 | 55 | 1H (20 cm) | 1400 | 400 | 1 | 0.2 | Was not specified
HAPPEx-III (Achieved) | 3.484 | 100 | 1H (25 cm) | 16900 | 200±100 | 3±3 | 0.5±0.1 | 10-3
PREx | 1.063 | 70 | 208Pb (0.5 mm) | 500 | 100±10 | 2±1 | 0.3±0.1 | 10-4
QWeak | 1.162 | 180 | 1H (35 cm) | 234 | 100±10 | 2±1 | 30±3 | 10-4
Møller | 11.0 | 75 | 1H (150 cm) | 35.6 | 10±10 | 0.5±0.5 | 0.05±0.05 | 10-4
PV experiments motivate polarized e-source R&D

## Slide 27: What does “234 ppb” even mean?
Target
1,000,000,000
A
B
A - B
1,000,000,000
A = 500,000,117
B = 499,999,883

## Slide 28
Electron Bunch Spin & Polarization
0% Polarization

v
50% Polarization

v

## Slide 29
Spin Polarized Photoemission from Bulk GaAs
Laser excitation from P3/2 to S1/2 : Egap < E < Egap+Δ
Electron Polarization:
Reverse electron polarization by reversing light polarization
σ+: Right circularly polarized light
σ- : Left circularly polarized light
mj
E
-1/2
+1/2
J
P1/2
-3/2
-1/2
+3/2
+1/2
P3/2
-1/2
+1/2
S1/2
σ+
σ-
3
1
S1/2
P3/2
P1/2
Egap=1.42 eV
Δ=0.34 eV
E
k
EF
3
1

## Slide 30: Practical polarized source requirements
Instead of wastefully chopping a DC beam, RF time structure.
A small beam size and divergence (think ”laser”), known in beam physics as a small emittance.
Probing with polarized beam requires fast helicity reversal to scatter both electron spin states from same target in short period of time.
Giant lasers, pounds of reactive alkali metal, hot and cold things near on another, strong magnetic fields, very high voltage, challenging vacuum issues can “kill” a concept. Must be feasible !
Once feasible, very high reliability and reproducibility - most accelerators operate 24 hours per day and want the same stable beam for weeks on end…

## Slide 31: Polarized Source Landscape 1970’s
Self-polarization via Sokolov-Ternov Effect
Electron Scattering (Mott)
Photo-ionization: Fano Effect
Photo-ionization of State Selected alkali atoms
Optically Pumped He Discharge
Field Emission from EuS
Photoemission from GaAs

## Slide 32: First Observation of Polarization from GaAs

## Slide 33
Built for SLAC parity-violation experiment E122
December 1977 - Polarized electrons accelerated at SLAC
June 1978 - E122 announces parity violation (Standard Model)
First HV GaAs photogun used on an accelerator
mA

## Slide 34: Breaking the 50% Barrier
The band gap of the substrate layer must be larger than surface layer
Lattice constants must differ enough to introduce suitable strain
Adjust lattice constant of substrate by varying concentration of third element
Lattice mismatch provides stress
Pablo Saez, PhD Thesis, SLAC Report 501, 1997
1% lattice mismatch provides equivalent force as hydraulic press!
Notes: Interior Page Design 2

## Slide 35
Strained layer GaAs
MOCVD-grown epitaxial spin-polarizer wafer
+3/2
mj = -1/2
+1/2
S1/2
P3/2
mj = -3/2
-1/2
+1/2
σ+
σ-
Strained GaAs
GaAs1-xPx (x=0.29)
p-type GaAs
substrate
600 μm
250 μm
250 μm
0.1 μm
GaAs1-xPx (0<x<0.29)
Strain relaxes in 0.1 mm layer
Not all electrons reach surface
Polarization 75% >> 50% 
QE 0.1% << 6% 

## Slide 36
Strained GaAs
GaAsP
Strained GaAs
GaAsP
Strained GaAs
GaAsP
30 A
30 A
GaAs Substrate
GaAs(1-x)Px Graded Layer
GaAs0.64P0.36
Buffer
Active Region
2.5mm
2.5mm
1000 A
From Aaron Moy, SVT Assoc and SLAC, PESP2002
Strained-Superlattice GaAs/GaAsP
D. Luh et al, SLAC, PESP2002
QE 1% and Polarization 85%

## Slide 37
P I
2
P I
2
sup.
str.
= 1.38
Experiment Figure of Merit
And, it really works!
QE ~ 0.2%
QE ~ 1.0%

## Slide 38
Benefits of Distributed Bragg Reflector
non-DBR Photocathode : absorption in the GaAs/GaAsP superlattice < 5%
  Most light passes into the substrate leading to unwanted heating
DBR photocathode : absorption in the GaAs/GaAsP superlattice >20%
  Less light required to make required beam, less light means less heat
Great for high current initiatives like polarized positrons at CEBAF and eRHIC
Non-DBR photocathode
DBR photocathode

## Slide 39
World Record QE from High Polarization Photocathode
6.4% QE & 84% polarization at 776 nm from strained GaAs/GaAsP superlattice photocathode with GaAsP/AlAsP Distributed Bragg Reflector (DBR)
The highest QE & FOM of any reported high polarization photocathode
Candidate photocathode for mA ops
SBIR partnership
W. Liu, S. Zhang, M. Stutzman, M. Poelker, Y. Chen, W. Lu, and A. Moy, Appl. Phys. Lett. 109, 252104 (2016)
DBR
Substrate
Photo-cathode

## Slide 40
Ion Bombardment

## Slide 41
“The woods were dark and foreboding, and Alice sensed that sinister eyes were watching her every step. Worst of all, she knew that Nature abhorred a vacuum” – Gary Larson
We understand Alice’s worry…
Air ~ 1016 / Torr-cm3
Gun ~ 10-12 Torr

## Slide 42: Ion back bombardment
Ion bombardment – with characteristic QE “trench” from laser spot to electrostatic center of photocathode – damages NEA of GaAs
High energy ions are focused to electrostatic center: create QE “hole”
  Don’t run beam from electrostatic center.
QE can be restored, but takes about 8 hours to heat and reactivate
Photocathode “QE scan”
  Active area = 5 mm
  Laser size = 0.35 mm

## Slide 43
Always Tweaking the Design
The endless (?) quest for perfection
1
2
3
4

## Slide 44
High Polarization from GaAs:
Trending toward higher current…
Year
Ave. Beam Current (mA)
First polarized beam from GaAs photogun
EIC
First low polarization, then high polarization at CEBAF
(Insert your name) breaks world record !!!
?