## Slide 1: Aperture Interception for Full Energy Injector Upgrade
Alicia Hofler
Reza Kazimi

## Slide 2: 200 kV gun and new (2-7) quarter injector
Space maintained for Capture section
Aperture locations unchanged
DC Gun
Solenoids
Prebuncher Cavity
Buncher
Cavity
Choppers
Apertures
INJECTOR LAYOUT
SC Booster Cavity
NA-PAC2011 WEP288
IPAC2012 TUPPR055
Aperture | z from cathode (m) | Diameter (mm) installed | Diameter (mm) modeled | Modeled extent (mm)
A1 | 5.37989 | 4.0 (2.0, 3.0, 4.0) | 3.0 | 10
A2 | 6.41519 | 6.0? (4.0, 6.0, 8.0) | 6.0 | 10
A3 | 10.69145 | 6.0 | 6.0 | 10
A4 | 11.44258 | 6.5 | 6.5 | 10

## Slide 3: Baseline: No initial momentum distributions (px=py=pz=0)
Space charge model | # particles | A1 | A2 | MS | A3 | A4
Point-to-point (tout) | 1000 | 2.6% | 0.0% | 0.0% | 1.6% | 0.0%
P-to-P (snapshot) | 1000 | 0.0% | 4.5% | 0.0% | 2.5% | 0.0%
mesh | 1000 | 0.0% | 0.0% | 0.0% | 17.9% | 0.0%
mesh | 10000 | 0.0% | 0.0% | 0.0% | 26.0% | 0.0%
100 μA
170 μA
Space charge model | # particles | A1 | A2 | MS | A3 | A4
Point-to-point (tout) | 1000 | 22.6% | 0.0% | 0.0% | 0.0% | 0.0%
P-to-P (snapshot) | 1000 | 0.0% | 0.0% | 0.3% | 0.5% | 0.0%
mesh | 1000 | 0.0% | 0.0% | 0.0% | 27.1% | 0.0%
mesh | 10000 | 0.0% | 0.0% | 0.0% | 32.2% | 0.0%

## Slide 4: No initial momentum distributions (px=py=pz=0) Override time step control during emission
100 μA
170 μA
Space charge model | # particles | A1 | A2 | MS | A3 | A4
Point-to-point (tout) | 1000 | 2.3% | 0.0% | 0.0% | 2.1% | 0.0%
P-to-P (snapshot) | 1000 | 0.0% | 0.0% | 0.0% | 7.5% | 0.0%
mesh | 1000 | 0.0% | 0.0% | 0.0% | 8.8% | 0.0%
mesh | 10000 | 0.0% | 0.0% | 0.0% | 26.4% | 0.0%
Space charge model | # particles | A1 | A2 | MS | A3 | A4
Point-to-point (tout) | 1000 | 22.4% | 0.0% | 0.0% | 0.1% | 0.0%
P-to-P (snapshot) | 1000 | 0.0% | 0.0% | 0.3% | 0.2% | 0.0%
mesh | 1000 | 0.0% | 0.0% | 0.0% | 7.1% | 0.0%
mesh | 10000 | 0.0% | 0.0% | 0.0% | 12.0% | 0.0%

## Slide 5: Initial transverse momentum distributions (px=py≠0; pz=0) Override time step control during emission
100 μA
170 μA
Space charge model | # particles | A1 | A2 | MS | A3 | A4
Point-to-point (tout) | 1000 | 0.00% | 0.00% | 0.0% | 0.00% | 0.00%
P-to-P (snapshot) | 1000 | 0.00% | 0.00% | 0.0% | 0.00% | 0.00%
mesh | 1000 | 0.00% | 0.00% | 0.0% | 0.00% | 0.00%
mesh | 10000 | 0.00% | 0.00% | 0.0% | 0.00% | 0.00%
Space charge model | # particles | A1 | A2 | MS | A3 | A4
Point-to-point (tout) | 1000 | 14.3% | 0.0% | 0.0% | 0.0% | 0.0%
P-to-P (snapshot) | 1000 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
mesh | 1000 | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
mesh | 10000 | 0.0% | 0.0% | 0.0% | 0.9% | 0.0%

## Slide 6: Thank You!

## Slide 8: Aperture ACCEPTANCES/TRANSMISSIONS

## Slide 9: Baseline: No initial momentum distributions (px=py=pz=0)
Space charge model | Number of macroparticles | A1 | A2 | A3 | A4
Point-to-point (tout) | 1000 | 974 (-26) | 974 (0) | 958 (-16) | 958 (0)
Point-to-point (snapshot) | 1000 | 1000 | 955 | 930 | 930
mesh | 1000 | 1000 | 1000 | 821 | 821
mesh | 10000 | 10000 | 10000 | 7402 | 7402
100 μA
Space charge model | Number of macroparticles | A1 | A2 | A3 | A4
Point-to-point (tout) | 1000 | 774 (-226) | 774 (0) | 774 (0) | 774 (0)
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 995 | 995
mesh | 1000 | 1000 | 1000 | 729 | 729
mesh | 10000 | 10000 | 10000 | 6776 | 6776
170 μA

## Slide 10: No initial momentum distributions (px=py=pz=0) Override time step control during emission
Space charge model | Number of macroparticles | A1 | A2 | A3 | A4
Point-to-point (tout) | 1000 | 977 (-23) | 977 (0) | 956 (-21) | 956 (0)
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 925 | 925
mesh | 1000 | 1000 | 1000 | 912 | 912
mesh | 10000 | 10000 | 10000 | 7359 | 7359
100 μA
Space charge model | Number of macroparticles | A1 | A2 | A3 | A4
Point-to-point (tout) | 1000 | 776 (-224) | 776 (0) | 775 (-1) | 775 (0)
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 998 | 998
mesh | 1000 | 1000 | 1000 | 929 | 929
mesh | 10000 | 10000 | 10000 | 8796 | 8796
170 μA

## Slide 11: Initial transverse momentum distributions (px=py≠0; pz=0) Override time step control during emission
Space charge model | Number of macroparticles | A1 | A2 | A3 | A4
Point-to-point (tout) | 1000 | 1000 (0) | 1000 (0) | 1000 (0) | 1000 (0)
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 1000 | 1000
mesh | 1000 | 1000 | 1000 | 1000 | 1000
mesh | 10000 | 10000 | 10000 | 10000 | 10000
100 μA
Space charge model | Number of macroparticles | A1 | A2 | A3 | A4
Point-to-point (tout) | 1000 | 857 (-143) | 857 (0) | 857 (0) | 857 (0)
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 1000 | 1000
mesh | 1000 | 1000 | 1000 | 999 | 999
mesh | 10000 | 10000 | 10000 | 9913 | 9913
170 μA

## Slide 12: Master slit ACCEPTANCES/TRANSMISSIONS

## Slide 13: Baseline: No initial momentum distributions (px=py=pz=0)
Space charge model | Initial number of macroparticles | Arriving at MS | Pass through MS (± 55 ps) | Pass through MS and A3
Point-to-point (tout) | 1000 | 974 | 974 | 958
Point-to-point (snapshot) | 1000 | 955 | 955 | 930
mesh | 1000 | 1000 | 1000 | 821
mesh | 10000 | 10000 | 10000 | 7402
100 μA
170 μA
Space charge model | Initial number of macroparticles | Arriving at MS | Pass through MS (± 55 ps) | Pass through MS and A3
Point-to-point (tout) | 1000 | 774 | 774 | 774
Point-to-point (snapshot) | 1000 | 1000 | 997 | 992
mesh | 1000 | 1000 | 1000 | 729
mesh | 10000 | 10000 | 10000 | 6776

## Slide 14: No initial momentum distributions (px=py=pz=0) Override time step control during emission
Space charge model | Initial number of macroparticles | Arriving at MS | Pass through MS (± 55 ps) | Pass through MS and A3
Point-to-point (tout) | 1000 | 977 | 977 | 956
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 925
mesh | 1000 | 1000 | 1000 | 912
mesh | 10000 | 10000 | 10000 | 7359
100 μA
170 μA
Space charge model | Initial number of macroparticles | Arriving at MS | Pass through MS (± 55 ps) | Pass through MS and A3
Point-to-point (tout) | 1000 | 776 | 776 | 775
Point-to-point (snapshot) | 1000 | 1000 | 997 | 995
mesh | 1000 | 1000 | 1000 | 929
mesh | 10000 | 10000 | 10000 | 8796

## Slide 15: Initial transverse momentum distributions (px=py≠0; pz=0) Override time step control during emission
Space charge model | Initial number of macroparticles | Arriving at MS | Pass through MS (± 55 ps) | Pass through MS and A3
Point-to-point (tout) | 1000 | 1000 | 1000 | 1000
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 1000
mesh | 1000 | 1000 | 1000 | 1000
mesh | 10000 | 10000 | 10000 | 10000
100 μA
170 μA
Space charge model | Initial number of macroparticles | Arriving at MS | Pass through MS (± 55 ps) | Pass through MS and A3
Point-to-point (tout) | 1000 | 857 | 857 | 857
Point-to-point (snapshot) | 1000 | 1000 | 1000 | 1000
mesh | 1000 | 1000 | 1000 | 999
mesh | 10000 | 10000 | 10000 | 9913