## Slide 1: Generation and Dynamics of Magnetized Beams for High-Energy Electron Cooling*
Northern Illinois Center for Accelerator
and Detector Development
Philippe Piot,
Department of Physics and Northern Illinois Center for Accelerator & Detector Development, Northern Illinois University, DeKalb IL 60115
Accelerator Physics Center, Fermi National Accelerator Laboratory, Batavia IL 60510
Yin-e Sun,
Advanced Photon Source, Argonne National Laboratory, Argonne IL 60439
*sponsored by the DOE awards DE-FG02-08ER41532 to Northern Illinois University and DE-AC02-07CH11359 to the Fermi Research Alliance LLC.
International Workshop on Accelerator Science & Technologies for future electron-ion colliders (EIC’14), Jefferson Lab, March 17-21, 2014

## Slide 2: Outline
Introduction
Features and parameterization of magnetized beams
Formation of magnetized bunches:
  methods and limitations,
  experiments in rf gun.
Transport and Manipulation:
  transverse matching,
  longitudinal manipulations,
  decoupling into flat beams.
Outlook

## Slide 3: Required Electron-Beam Parameters
Cooling interaction time
magnetized cooling less dependent on e- beam transverse emittance (to what extent?)
electron-cooling accelerator provides beam eventually matched to cooling-solenoid section
(magnetized)
(not magnetized)
(not magnetized)
(magnetized)

## Slide 4: Cooler configurations
low-energy coolers:
  lattice (bends) embed-ded in magnetic fields,
  based on DC electron sources,
  no further acceleration or bunching, needed.
high-energy coolers:
  medium energies required (50-100 MeV),
  acceleration in SCRF linac bunching
  lumped solenoidal fields matching
e.g. see S. Nagaitsev, et al, PRL96, 044801 (2006)
e.g. see I. Ben-Zvi, et al., Proc. PAC2001, p. 48 (2001)
300 keV, 3 A cooler produced by Budker INP for IMP, Lanzhou (China)
early concept for RHIC e-cooling

## Slide 5: High-energy coolers
magnetized- beam injector
cooling section
dump or energy recovery
matching
matching mode/converter
bunching
acceleration
debuncher
injector: produces bunched beam for RF acceleration
debuncher: matched electron bunch length to ion-beam’s,
matching + mode/converter sections: repartition “physical” emittances, match in cooling-solenoid section.

## Slide 6: Beam dynamics regimes (round beams)
space charge
emittance “pressure”
angular momentum
contribution
adapted from Y.-E Sun, Dissertation U. Chicago (2005)
: magnetization
: uncorrelated geometric emittance
: generalized perveance
Radial envelope (s ) equation in a drift (Lawson):

## Slide 7: Features & Parameterization
possible parameterization of coupled motion between 2 degrees of freedom has been extensively discussed; see:
  D.A. Edwards and L.C. Teng, IEEE Trans. Nucl. Sci. 20, 3, pp. 885-889 (1973).
  I. Borchardt, E. Karantzoulis, H. Mais, G. Ripken, DESY 87-161 (1987).
  V. Lebedev, S. A. Bogacz, ArXiV:1207.5526 (2007).
  A. Burov, S. Nagaitsev, A. Shemyakin, Ya. Derbenev, PRSTAB 3, 094002 (2000).
  A. Burov, S. Nagaitsev, Ya. Derbenev, PRE 66, 016503 (2002).
Simpler description that provides the necessary insights..

## Slide 8: A simple description of coupled motion
Consider the 4x4 beam matrix
Introduce the “correlation” matrix:
Beam matrix takes the form:
The correlation subjects to transforms as
C provides information on the coupling only.
where

## Slide 9: Beam matrix for a round magnetized beam
At a waist, the matrix of a magnetized (round) beam is
The eigen-emittances of this beam matrix are:
the eigen-emittances can be mapped into “physical” emittances using a skewed beamline
where
and the magnetization is
K.-J. Kim, PRSTAB 6, 104002 (2003)
D. A. Edwards, unpublished (2001)
where
decoupling when

## Slide 10: Formation of magnetized bunches
Cathode immersed in an axial B field
Sheet beams at birth (with subsequent flat-to-round beam converter)
  shaped cathode,
  line-laser focus
  Nonlinear optics (speculative)
mode converter
G. Florentini, et al., Proc. PAC95, p. 973 (1996)
Y. Derbenev, University of Michigan report UM-HE-98-04 (1998)

## Slide 11: Cathode in a magnetic field
electrons born in an axial B field CAM
upon exit of solenoid field ( ): CAM becomes purely kinetic.

## Slide 12: Emittance vs magnetization
“effective emittance”
magnetization
The emittance has a lower-bound value :
Practically, includes other contributions.
where is the excess in kinetic energy during emission

## Slide 13: Example of 3.2-nC magnetized bunch
high-charge bunch subject to emittance degradation
proper optimization (emittance compensation) 4-D emittance com- parable to round beams.
eigenemittances evolution in ASTA photoinjector
P. Piot et al. IPAC13; C-X. Wang, FEL06, 721 (2006)
X. Chang, I. Ben-Zvi, J. Kewisch AAC04 (2004)

## Slide 14: Measuring (kinetic) angular momentum
Kinetic angular momentum can be measured using a slit technique (similar to emittance)
The beam’s average angular momentum is given by
Y.-E Sun et al, PRSTAB 7, 123501 (2004)
: rms beam size at slit (1) and observation screen (2),
: axial momentum
: drift length between locations (1) and (2).
beam at slits
beam at observation point

## Slide 15: Experimental generation in a photoinjector
Fermilab A0 normal-conducting photoinjector (decommissioned),
15 MeV, charge up to 2 nC,~3-10 ps bunch
main focus was conversion to flat beams
Y.-E Sun et al, PRSTAB 7, 123501 (2004)

## Slide 16: Experimental generation in a photoinjector
rotation angle (deg)
magnetic field B0 on cathode (G)
Y.-E Sun et al, PRSTAB 7, 123501 (2004)
linear scaling with B field on photocathode

## Slide 17: Experimental generation in a photoinjector
Y.-E Sun et al, PRSTAB 7, 123501 (2004)
CAM from applied B field
measured kinetic angular momentum
weak dependence,
quadratic scaling with laser spot size on photocathode.

## Slide 18: Decoupling into flat (ex/ey≠1) beam
Transport of magnetized bunches while preserving is challenging,
Use of round-to-flat beam transformer to convert into uncoupled (flat) beam eigen-emittances maps into “physical” transverse emittances:
R. Brinkmann et al., PRSTAB 4, 053501 (2001)
Y. Derbenev, University of Michigan report UM-HE-98-04 (1998)

## Slide 19: Decoupling into flat beam: experiments (1)
Same experimental setup as used for generation of CAM-dominated beams
simulations
simulations
experiments
P. Piot, et al, PRSTAB 9 , 031001 (2006)
0.5 nC

## Slide 20: Decoupling into flat beam: experiments (2)
normal emittances map into the flat- beam emittance
large experimental uncertainties for smallest emittance meas.

## Slide 21: Outlook + open questions
magnetized beam from a SCRF gun:
  flux concentrator around cathode?
  flat beam at cathode [J. Rosenzweig, PAC93 showed ( , )=(95,4.5) mm]
needed and ? and limit on 4-D emittance?
planned future experiment at ASTA