## Slide 1: Helicity Decoder Board
Prevents mis-identification of real helicity of some of events in counting mode – needed with 2 kHz MOLLER Helicity Reversal
Paul King and Riad Suleiman

## Slide 2: CEBAF Helicity Controls
Gain-switched Diode Laser and Fiber Amplifier
Attenuator
PC WP LP
Shutter
Rotatable Strained
Superlattice GaAs
Photocathode
Vacuum
Window
15° Dipole
ge-2 Reversal
IHWP
RHWP
RTP
Cell
Delayed
Helicity Fiber
HV Supply
(0 – 4 kV)
HV Supply
(0 – 90 V)
CEBAF
Hall
T-Settle
Fiber
Charge and Position
Feedback s
Laser
Electron Beam
Com. Fiber
Controls
Helicity Fiber
Charge Feedback (IA)
LP HWP LP
IA
Target
BCMs
BPMs
5 MeV
Helicity Magnets
DAQ
nHelicity
Fiber
Position
Feedback
Helicity Generator
V-Wien Filter
H-Wien Filter
Spin Solenoids
11.0 GeV
200 keV
ISB

## Slide 3: Helicity Generator Signals to DAQ – What user gets
Example: Quarter Pattern
  +--+ or
  -++-
Pair Sync
Helicity Pattern
Reported or Delayed Helicity
T_Settle
or
T_Stable

## Slide 4: Helicity Generator Signals – Real time signals
Helicity Flip
nHelicity Flip
Reported or Delayed Helicity
8– window delay
To Pockels Cell (Real Time)
To Helicity Magnets (Real Time)
T_Settle
or
T_Stable

## Slide 5: Helicity Decoder Board
MOLLER fast helicity reversal (1920 Hz, 10 µsec settle time, 64-window pattern, 128-window delay) could cause mis-identification of real helicity of some of events in counting mode (these are random events), diluting measured asymmetry
Board to be developed by: MOLLER collaboration (Ohio University), Jefferson Lab Fast Electronics Group and Accelerator Division
Will be used by data acquisition systems running in counting mode: Hall B, Hall C, Møller Polarimeters and Mott Polarimeter in CEBAF Injector
Board will not reconstruct real helicity or real 30-Bit Shift Register
Board has four input signals: T_Settle, Delayed Helicity, Helicity Pattern, and Pair Sync
For each counting event:
  Now: Delayed Helicity and Pattern are recorded in Rings of helicity-gated SIS3801 Scaler. Offline analysis then attempts to construct real helicity, a complicated process due to delay and randomness of events.
  New Board: board will keep records of helicities spanning last 30 patterns – to be able to construct 30-bit shift register seed of pseudo-random helicity generator – and position within pattern. And for each event, these records are read along with event. Offline analysis (anytime>n-patterns) will calculate real helicity using helicity predictor. Will be able to correctly identify helicity of every event.

## Slide 6: Electron Beam Travel Time
With 10 µs T_Settle time, travel time from photocathode (Pockels Cell) to Hall target becomes relevant. Also, time it takes for helicity board signals to propagate to Laser Hut and to Halls.
It takes beam about 4.3 µs per pass to reach Hall.
Fiber length from Injector Service Building (ISB) IN01B05 to Hall C was measured to be 1705 ft using “20 MHz Clock” fiber. With n=1.45, it takes 2.5 µs for helicity signals to travel in fibers to Hall.
  All these travel times will be accounted for in this new Helicity Decoder Board such that recorded events have correct helicity at Physics Interaction Time

## Slide 7: Pseudo-Radom Helicity Generator
Determines helicity at start of pattern
Use 30-bit Shift Register
It is Pseudorandom, not “Random” because it is deterministic, once a sequence of 30 helicity states is known, next states can be predicted, and it repeats its cycle.
For any initial seed, there are 230 – 1 = 1,073,741,823 (maximal length) random bits before sequence repeats, 50 days for 1000 Hz helicity reversal rate and a Quartet.
1
30
29
28
27
…
7
…
1
Switch
Open: Pseudo-random Patterns
Closed: Toggle Pattern
30-Bit Shift Register
Pseudo-random Bit out
Pseudo-random Bit
(0 or 1)
Shift Left
OR
XOR
XOR
XOR

## Slide 8: Decoder Board I/O and Features
Input:
  T_Settle
  Delayed Helicity
  Helicity Pattern
  Pair Sync
  External 250 MHz FADC Clock (ECL) – Board has 250 MHz internal clock
  Trigger and Sync Signals
Output:
  Four NIM helicity outputs (T_Settle, Delayed, Pattern and Pair) after common delay for timing check
  20 Data words for each trigger event
Add programable common delay (0-30 µs) for input helicity signals:
  To fix time delays due to beam travel time and helicity signal distribution to Hall
  Will be measured for each board in a specific DAQ
  Will sync helicity of beam at Physics Interaction Time in Hall
NIM or Fiber, programmable

## Slide 9: Scheme Outline
New scheme to readout delayed helicity for Physics Event Trigger:
Running in background in Helicity Decoder Board:
  On Pattern Start:
    Increment pattern counter
    Grab delayed (or reported) helicity
    Push onto running Helicity Seed (32 bits)
    Clear pattern phase counter
  On T_Settle Transition:
    Increment pattern phase counter
    Increment T_Settle counter
Then, when a physics event triggers DAQ, report Data Word of:
    Current seed value – to find true helicity for first window in pattern
    Counter of pattern phase
    Counters of pattern and T_Settle
    Status of T_Settle at time of trigger – to be used to veto event
    Event Polarity: XOR of delayed helicity and delayed helicity on Pattern Start
Analysis will use last two delayed helicity windows to check 30-bit Shift Register

## Slide 10: Analysis – Realtime on Crate, Online, Offline
Use seed value to construct 30-Bit Shift Register – use first 30 bits
Note: No 1,0 vs 0,1 symmetry, i.e., these two registers generate different helicity sequence:
  110100011110010101010100011001
  001011100001101010101011100110
Predict last 30 bits to confirm valid data – generate delayed helicity shift register
Predict n-patterns (e.g., two patterns for 8-window delay with Quartet Pattern)
No realtime prediction on crate level, prediction can happen in analysis after event buffering and/or event transfer from crate
Use Pattern Phase Counter to find real helicity
Use status of T_Settle at time of trigger to accept or veto event
30
29
28
27
…
7
…
1

## Slide 11: Cross-Check
For cross-check, Decoder Board will report data words that have same info as Rings of helicity-gated SIS3801 Scaler:
  Latched delayed helicity for this event
  Latched pattern sync for this event
  Latched T_Settle for this event
  Time of trigger since start of T_Settle
  Time of trigger since end of T_Settle
  Duration of previous complete T_Settle interval
  Duration of previous complete inverse T_Settle interval
  Last 32 windows of Pattern Sync (Delayed Helicity at start of Pattern)
  Last 32 windows of Pair Sync
  Last 32 windows of Delayed Helicity
  Time of trigger since last trigger
Board will continuously check:
  Delayed helicity at start of Pattern is as expected from 30-bit Shift Register
  No three consecutive delayed helicity signals are same
  No two Pair Sync signals are same

## Slide 12: Board Programmable Common Delay
How to set input common time delay:
  Helicity Board: 60 Hz Line Sync
  Electron Beam: VL, 60 Hz Line Sync, 50 ns pulses
  First, check relative timing of electron VL Generator and Helicity signal on laser table
  Adjust board common delay to match relative timing at laser table
VL
Generator
RTP
Cell
Delayed
Helicity
Fiber
HV Supply
CEBAF
Hall
Target
DAQ
Helicity Generator
ISB
60 Hz Line Sync
Real
Helicity
Fiber
Check relative timing
Helicity Decoder Board
Check relative timing
Trigger
Board Common Input Delay (0-30 µs)

## Slide 13: Required No. of Boards – 20 Boards
Number of boards (20):
  Accelerator: CEBAF Mott, UITF Mott, Spare
  Hall A: Moller Pol, Compton Pol, HRS1, HRS2, 2-Spares
  Hall B: Moller Pol, CLAS, Spare
  Hall C: Moller Pol, Compton Pol, HMS, SHMS, 2-Spares
  Hall D: HD, Spare