## Slide 1: CEBAF Source/Injector Update PREX/CREX Collaboration Meeting February 26, 2018
Joe Grames
Center for Injectors and Sources

## Slide 2
CEBAF Polarized Source
  Simultaneous 4-Hall operation
  Source performance
Summer SAD 2018
  200 kV Gun
  350 kV HVPS
  NEG tube
Summer SAD 2019 and beyond…
  200 keV Wien filter
  Beamline Redesign
  Booster
Outline

## Slide 3
3
4-Hall Operations & D+3
  All lasers now operating at 250 MHz
  December : B (0-10 nA) + D (0-100 nA) sharing narrow B-slit
  January-Now : A (22.5 uA) + D (25-400 nA) sharing open A-slit
  Since January : D+3(ABC) at highest energy 5.5 + (555)
Recent CEBAF/Source Operation

## Slide 4
CEBAF Polarized Inverted Load Lock Gun (Spring 2017)
CEBAF Gun 2 (130kV)

## Slide 5
Photocathode
  Strained Superlattice GaAs/GaAsP #5756-4
  Polarization 85-87% typical (Mott and Hall B Moller)
  QE after activation typical (>1%), lifetime very good (>300 C)
Polarized source recent performance

## Slide 6
CEBAF Polarized Source
  Simultaneous 4-Hall operation
  Source performance
Summer SAD 2018
  200 kV Gun
  350 kV HVPS
  NEG tube
Summer SAD 2019 and beyond…
  200 keV Wien filter
  Beamline Redesign
  Booster
Outline

## Slide 7
Injector Upgrade
Increase gun voltage and Wien filters for 200kV operation
Locate Wien filters (energy filter) upstream of pre-buncher cavity
New SRF booster eliminates warm capture, RF deflection and x/y coupling
Our new “1/4 cryomodule”:
2 cell capture section + 7 cell cavity,
should provide 10 MeV beam and introduce no x/y coupling, allow better matching, more adiabatic damping
200 kV

## Slide 8
Modify spare CEBAF/ILC gun for reliable 200 kV operation
  Retain extreme high vacuum (XHV) 1E-12 Torr
  Reliable 200 kV operation w/o field emission
Work of G. Palacios, C.H. Garcia
200 kV Gun Design Goals

## Slide 9: COMSOL model of gun improvements
White Conductivity of 2E-14 S/m
4.83 [MV/m]
7.78 [MV/m]
6.66 [MV/m]
Black Conductivity of 2E-12 S/m
4.81 [MV/m]
7.75 [MV/m]
5.68 [MV/m]
Work of G. Palacios, C.H. Garcia
CEBAF Existing Gun @ 200 kV
CEBAF Upgrade Gun @ 200kV
Pure alumina insulator
No triple point shielding
Mildly conductive alumina insulator for charge dissipation
Triple point shielding to prevent arcing across HV plug

## Slide 10
Black Conductivity of 2E-12 S/m
|E|=1.16 [V/m]
Ey=-1.14 [V/m]
White Conductivity of 2E-14 S/m
|E|=146.9 [V/m]
Ey=-139 [V/m]
Work of G. Palacios, C.H. Garcia
CEBAF Existing Gun @ 200 kV
CEBAF Upgrade Gun @ 200kV
Triple point shielding minimizes E-field: important to prevent arcing along HV plug
COMSOL model of gun improvements

## Slide 11: Potential is more linear along the rubber plug-insulator interface to prevent arcing
Work of G. Palacios, C.H. Garcia
CEBAF exiting gun @ 200 kV
CEBAF upgrade gun @ 200kV
Notes: I would leave this slide for backup

## Slide 12
Gun assembled and baked successfully.
HV conditioned at the UITF using available with 225kV HVPS (Spellman) and SF6
Small, yet measurable on-set of field emission above 200kV – requires conditioning > 225kV to process
Conditioning the 200 kV gun at UITF (June 2017)
Chart: Ch. 2 (Top) Radiation vs. Voltage
| 210 | 200 | 180 | 150 | 130
23-Jun | 0.58934 | 0.2597 | 0.14107 | 0.12581 | 0.15827
30-Jun | 0.82728 | 0.27563 | 0.15534 | 0.14838 | 0.1289

## Slide 13
Conditioning w/ 350 kV HVPS (Nov-Dec 2017)
Moved HV chamber to gun table, baked and Kr gas conditioned to 227 kV (above the 225 kV Spellman!)
Reliable operation to 200 kV w/o signs of field emission.
Will move 200kV electrode to CEBAF HV chamber (better vacuum) in May 2018.

## Slide 14
Existing 150kV inadequate for upgraded gun
  SF6 pressure vessel delivered + plumbing/sensors ready
  Modifying stack for QE scans
  Major installation (safety systems, engineering, software)
New Spellman 350 kV HVPS

## Slide 15
Tunnel Penetration
Tunnel Floor
Gun
Little Oil Tank
ISB Rack
Bue Oil Tank
HV Interlocks
PSS/MPS
Bus Bar
Gun Switches (x3)
HV Switch
Ross Probe (1000:1)
Bias Switch
Bus Bar
Short
Resistor
Glassman (150kV)
Software
HV Enable
Knife Switch
Ross Probe DVM
Slow Lock (software)
Battery Bias (cathode)
QE scan
NOW
Tunnel Penetration
Tunnel Floor
Gun
ISB Rack
HV Interlocks
PSS/MPS
Glassman (Control)
Software
HV Enable
Knife Switch
Battery Bias (anode)
QE scan
350kV
HVPS
SF6 Tank
Resistor
SF6 Tank
Upgrade
New gun HV system simpler

## Slide 16
Replace NEG coated pipe w/ one including BPM’s
  Improve spot move
  S/H for PQB tests
  Explore 2nd moment
Upgrade NEG coated BPM beam pipe

## Slide 17
Modified M20
Plan A : Modify M20 spares on shelf (last year)
Plan A is happening, but repurposing existing M20’s w/ welded feedthroughs has proved cumbersome:
  Bake limited to 450C
  No fixture to repair leak
  Shield antennae from NEG coating
Status:
  Gabou mapping (J. Musson) in progress
  Vacuum assembly test follows

## Slide 18
Plan B : New XHV M20
Plan B = Achieve best vacuum
  Mini-CF antennae allow SS bake 900C and convenient to NEG coat surface
  Design is robust to leaks
  Machined tolerance to fixture antennae – yaw only
  Retains smaller pipe compatible w/ existing H/V correctors
Status
  ME model and field simulation complete
  Vacuum chamber out for bid
Work of D. Machie, K. Harding, F. Marhauser

## Slide 19
CEBAF Polarized Source
  Simultaneous 4-Hall operation
  Source performance
Summer SAD 2018
  200 kV Gun
  350 kV HVPS
  NEG tube
Summer SAD 2019 and beyond…
  200 keV Wien filter
  Beamline Redesign
  Booster
Outline

## Slide 20
Upgrade the existing 130 keV Wien filters for 200 keV operation
Barrel polished electrodes and successfully tested to 20kV
Replace 14 kV supplies with 30 kV power supplies
Replace 10 A coils with 20 A coils (J. Benesch, JLAB-TN-15-032)
Wien Upgrade for 100 deg precession |  | 
Beam Voltage | keV | 200.00
Integrated BL | G-cm | 3993.86
Magnet Current | A | 15.36
Electric Field | MV/m | 2.67
Electrode High Voltage | kV | 20.05
Upgrade 200 keV Wien filter

## Slide 21
Under vacuum and magnet tested at UITF
Prototype Wien filter installed at UITF
Successfully powered to 15A (200kV requirement)
Machine shop working on 6 more coil pairs (improved design)
Software is working on communication to +/- 30kV Matsusada HVPS’s
Working with safety group to assess x-ray potential (60keV)

## Slide 22
200 keV CEBAF : evaluating ME layout
200 kV Gun
NEG w/ BPM’s
New single gun Y-chamber
(delivered)
Repurpose INJTWF
(move bfore PB)
Retain Prebuncher
Simplify A1/A2 region

## Slide 23
Upgrade Cryounit Commissioning at Test Lab
  Nov 2017 – keV vacuum beam line connected
  Feb 2018 – 80K shield cooldown in progress
  March 2018 – application of klystron power
Testing new cryounit booster at UITF

## Slide 24
Preparing for MeV beam commissioning
  Fabricating/installing immediate “straight” MeV section
  Completing design of horizontal spectrometer
  Planning to accelerate beam to MeV by ~August 2018
Testing new cryounit booster at UITF
Now routinely running 200keV beam here
Installing MeV vacuum beam line
MeV spectrometer

## Slide 25
Testing CEBAF upgrade gun at 200 keV
Testing new UITF beam line with 200 keV beam
  Delivered beam to dumps (before MeV acceleration)
  Commissioned 1497 MHz chopper (~CEBAF 499 MHz)
  Fixing ~handful of PREP chamber issues, then ~100 uA

## Slide 26
Summer 2018 SAD Plan
April - May
  PQB studies (RTP, Wien flipper + time permitting Helicity Quad, PosDiff vs. CathPos)
  Test of spin resonant cavity
  Bubble chamber engineering run
May – June
  Replace Gun2 electrode one w/ shed + conductive insulator
  Install and commission 350 kV HVPS
  Replace existing NEG tube w/ one that has two BPM’s
June – July
  High voltage condition gun for 200 kV operation
  Make 200 keV beam, test beam line components and regulation of HVPS
  Quantify 200 keV beam (transmission/space charge, emittance, PQB)
July – August
  2nd Bubble run will use new gun+HVPS at 130 keV
  Any of the (electrode, HVPS, NEG tube) independently ‘backed out’ by Fall run
  Planning on success we operate new gun+HVPS at 130 keV for Fall run