## Slide 1
Generation and Characterization of Magnetized Bunched Electron Beam from DC Photogun for MEIC Cooler
MEIC bunched magnetized electron cooler is part of Collider Ring and aims to maintain ion beam emittance and extend luminosity lifetime
LDRD Scientific Goals:
  Generate magnetized electron beam and measure its properties
  Explore impact of cathode magnet on photogun operation
LDRD Benefits:
  Simulations and measurements will provide insights on ways to optimize MEIC electron cooler and help design appropriate electron source
  JLab will have direct experience magnetizing high current electron beam
PIs: Riad Suleiman and Matt Poelker

## Slide 2: Milestones and Costs
Materials and Supplies:
Cathode magnet
Three skew quadrupoles
Components for three diagnostics crosses
Labor:
Gun magnet design and installation
Mechanical designer for skew quad magnets and slits
ASTRA and GPT modeling
Postdoc
FY16 | $339,211
FY17 | $265,850
FY18 | $212,025
Total | $817,086
Year 1: Design, procure and install cathode magnet, skew quads and slits
Year 2: Generate magnetized beam, measure mechanical angular momentum and benchmark simulation
Year 3: Measure photocathode lifetime vs magnetization up to 32 mA , generate flat beam with three skew quads – RTFB Transformer – and measure horizontal and vertical emittances using slit method

## Slide 3
Generate magnetized beam:
  = 1 – 8 mm, Bz = 0 – 2 kG
  Bunch charge: 1 – 500 pC
  Frequency: 0 – 476 MHz
  Bunch length: 50 – 150 ps
  Average beam currents up to 32 mA
  Gun high voltage: 200 – 350 kV
Green
Laser
Cathode
Anode
K2CsSb
Photocathode
Cathode Solenoid or Helmholtz pair
(Bz=2 kG)
Diagnostic Cross 1
(Multislit + YAG Screen)
Three Skew Quads
(Round-to-Flat Beam Transformer)
Diagnostic Cross 2
(H,V slit + YAG Screen)
Diagnostic Cross 3
(YAG Screen)
Injector Focusing Solenoids
Experimental Overview: GTS