## Slide 1
Generation and Characterization of Magnetized Bunched Electron Beam from a DC High Voltage Photogun
R. Suleiman, M. Poelker, J. Benesch, F. Hannon, C. Hernandez-Garcia, Y. Wang (Jefferson Lab)
Jefferson Lab Electron Ion Collider (JLEIC) bunched magnetized electron cooler is part of Collider Ring and aims to counteract emittance degradation induced by intra-beam scattering, to maintain ion beam emittance during collisions and extend luminosity lifetime
Acknowledgement: This work is supported by the Department of Energy, Laboratory Directed Research and Development funding, under contract DE-AC05-06OR23177
Generate magnetized electron beam and measure its properties starting fall 2016
Explore impact of cathode solenoid on photogun operation
Simulations and measurements will provide insights on ways to optimize JLEIC electron cooler and help design appropriate source
Jefferson Lab will have direct experience magnetizing high current electron beam
Motivation
Electron beam is being used inside cooling solenoid where it suffers an azimuthal kick when it enters. This kick is cancelled by an earlier kick at exit of cathode solenoid.
Plans and Summary
Cathode Solenoid
Experimental Overview
Simulations
Magnetized Cooling
Electrons helical motion in strong magnetic field increases electron-ion interaction time, thereby significantly improving cooling efficiency. Electron-ion collisions that occur over many cyclotron oscillations and at distances larger than cyclotron radius are insensitive to electrons transverse velocity.
Cooling rates are determined by electron longitudinal energy spread rather than electron beam transverse emittance as transverse motion of electrons is quenched by magnetic field.
This cyclotron motion also provides suppression of electron-ion recombination.
Upon exit of Cathode Solenoid
Upon entering Cooling Solenoid
re= 1.4 mm
Bcool = 2 T
Electrons born in strong uniform Bz
= Rlaser = 4.4 mm
Bz = 2 kG
= 284 µm
Bunch length | 60 ps (2 cm)
Repetition rate | 476.3 MHz
Bunch charge | 420 pC
Peak current | 7.0 A
Average current | 200 mA
Transverse normalized emittance | 10s mm mrad
Cathode spot radius – top-hat () | 4.4 mm
Solenoid field at cathode (Bz) | 2 kG
Bunch length | 60 ps (2 cm)
Repetition rate | 476.3 MHz
Bunch charge | 420 pC
Peak current | 7.0 A
Average current | 200 mA
Transverse normalized emittance | 10s mm mrad
 | 4.4 mm
Solenoid field at cathode (Bz) | 2 kG
Generate magnetized beam:
  = 1 – 5 mm, Bz = 0 – 2 kG
  Bunch charge: 1 – 500 pC
  Frequency: 15 Hz – 476.3 MHz
  Bunch length: 10 – 100 ps
  Average currents up to 32 mA
  Gun high voltage: 200 – 350 kV
Measure mechanical angular momentum
Measure photocathode lifetime versus solenoid field at high currents (up to 32 mA) and high voltages (200 – 350 kV) limited by in-house HV supplies
Study beam halo and beam loss versus magnetization
Use skew quads – Round-to-Flat Beam (RTFB) Transformer – to generate flat beam and measure horizontal and vertical emittances using slit method
Generate very high currents magnetized beam and study beam transport and RTFB versus electron bunch charge
Provides 1.4 kG at cathode with standard molybdenum puck
Moly and carbon steel hybrid puck designed to enhance field to 2 kG at cathode
Carbon
Steel
Stainless
Steel
2 mm
10 mm
4 mm
Molybdenum
Insert slit into beamline to select an emittance-dominated beamlet
Let beamlet drift to screen and image it
beam radius measured at Diagnostic Cross 1
beam radius measured at Diagnostic Cross 2
D drift between two crosses
pz beam longitudinal momentum
Cathode Preparation Chamber
Gun
Solenoid
Diagnostics
Parameter | 
Cathode Bz | 2 kG
Radius, top-hat () | 3 mm
t rms, Gaussian | 23 ps
Bunch Charge | 420 pC
Gun HV | 350 kV
Parameter | 
Cathode Bz | 2 kG
 | 3 mm
t rms, Gaussian | 23 ps
Bunch Charge | 420 pC
Gun HV | 350 kV
Green
Laser
Cathode
Anode
K2CsSb
Photocathode
Cathode
Solenoid
Diagnostic Cross 1
(Slit + YAG Screen)
Three Skew Quads
(Round-to-Flat Beam Transformer)
Diagnostic Cross 2
(Slit + YAG Screen)
Diagnostic Cross 3
(YAG Screen)
Injector
Focusing
Solenoid
Hybrid Puck
Cathode
Solenoid
Magnet
ion
electron
Cathode Solenoid
Cooling Solenoid
SRF LINAC
9 cm