## Specs
Type | Name | Function | Specifications | LCW | Iron | Energy | Available | Jobs | Design BL | Design I | Trim I | Trim V | R | HiPot | B profile | B v. I
dipole | MDS01 | 15 deg bend | DWG# 32709-C-0358 Tested 2.5A | no | no | 350 keV | DS001 (first design) DS002 (spare) DS004 (test cave) | Test spare @ 4.2 A Build new w/ AWG16 on DS001 fixture | 603 G-cm | 4.187 A | 10 A
dipole | MWF01 | 0 deg Wien filter | Wien filter DWG package | no | yes | 350 keV | Assembly #3 | Assemble magnet Measure at MMF Cut electrodes Assemble
dipole | MDI02 | 45 deg spectrometer | Need to find | no | yes | 350 keV | Assemble | Pull from tunnel Locate old field map Decide if MMF
dipole | MBV? | MeV spectrometer | Need to find | no | yes | 10 MeV | 2 spares? | Pull from ISB Determine type Measure MMF
dipole | MDL | Vertical chicane 1 | Need to find | no | yes | 10 MeV | Spare at MMF | Ready
dipole | MDL | Vertical chicane 2 | Need to find | no | yes | 10 MeV | Fabricate $10k | Test Measure MMF
dipole | ? | ALT Vertical chicane 1 | Need to find | yes | yes | 10 MeV | At ISB | Test Measure MMF
dipole | ? | ALT Vertical chicane 2 | Need to find | yes | yes | 10 MeV | At ISB | Test Measure MMF
solenoid | MFH01 | SW focus to 15 deg bend | L=3.0", ID=2.5", OD=6.875", N=742 8.62E4 G2-m/A, BL<>0 Tested to 2A | no | yes | 350 keV | At UITF | Cut off NEG tube Test and measure at new Imax | F=50cm 4.3E5 G2-cm | 2.22 A
solenoid | MFB02 | SW focus to Wien filter | L=3.0", ID=2.0", OD=6.875", N=742 1.0E5 G2-m/A, BL<>0 Tested 3.5 A | no | yes | 350 keV | At UITF | Test | F=50cm 4.3E5 G2-cm | 2.07 A
solenoid | CAV1 | CW focussing element | L=2.62", ID=1.5", OD=6.25", N=520 Thin central plate B2L=1.11E5 G2-cm/A, BL=0 Tested 1.5A | no | yes | 350 keV | On chopper 1 | Test and measure at new Imax | F=50cm 4.3E5 G2-cm | 1.96 A
solenoid | CAV2 | CW focussing element | L=2.62", ID=1.5", OD=6.25", N=520 Thin central plate B2L=1.11E5 G2-cm/A, BL=0 Tested 1.5A | no | yes | 350 keV | MFA0I05 @ ISB | Test and measure at new Imax | F=50cm 4.3E5 G2-cm | 1.96 A
solenoid | CHOP1 | CW chopping lens | Steel DWG# Coils DWGE 39200-D-0067 | no | yes | 350 keV | Coils @ ISB | Fabricate steel Fabricate spare coils
solenoid | CHOP2 | CW chopping lens | Steel DWG# Coils DWGE 39200-D-0067 | no | yes | 350 keV | Coils @ ISB | Fabricate steel Fabricate steel coils
solenoid | MFQ02 | CW focus to QCM | L=2.62", ID=1.5", OD=6.25", N=573 Thick central plate B2L=1.34E5 G2-cm/A, BL=0 Tested 2.0A | no | yes | 350 keV | At ISB | Test | F=50cm 4.3E5 G2-cm | 1.78 A
quad | MQU01 | quad Wien astigmatism |  | yes | no | 350 keV | Spare at ISB | Verify MMF map
quad | MQU02 | quad Wien astigmatism |  | yes | no | 350 keV | Locate | Verify MMF map
quad | ? | ALT quad Wien astigmatism | n/a | no | yes | 350 keV | Spare at ISB | Test Measure MMF
quad | ? | ALT quad Wien astigmatism | n/a | no | yes | 350 keV | Spare at ISB | Test Measure MMF
quad | MQDxx | 12 transport quads |  | yes | yes | 10 MeV | No | Fabricate 13 QA Measure MMF |  |  | 10 A | 20 V