## Slide 1: 200 kV guns comparison using CST Microwave studio + GPT
Gabriel Palacios
gabrielp@jlab.org 03/04/18

## Slide 2: Summary
For T-cathode, Mushroom, small mushroom, sphere (3 anode configurations). All @200 [kV] bias and grounded anode.
GPT: SC-ON, 10000 particles, Gaussian laser, Qbunch -4E-14 [C], XYrms 0.32E-3 [m], Trms 20E-12 [s], MTE 0.0166 [eV]
Solidworks
Field maps
E-field color maps
Surface E-field color maps
Emittance
Standard deviation

## Slide 3: Models: T-cathode

## Slide 4: Models: Mushroom

## Slide 5: Models: Small mushroom

## Slide 6: Models: Sphere, 6cm gap, short anode

## Slide 7: Models: Sphere, 9cm gap, large anode

## Slide 8: Models: Sphere, 6cm gap, large anode

## Slide 9: Cathode-anode gap:
The data for the following plots was probed along a horizontal line on the cathode-anode gap as a function of vertical position on the photocathode surface (varying from y=-6mm to 6mm.)

## Slide 10: CST results: Transverse electric field – T-shape
Chart: No shield
The different colors show how the transverse electric field changes as a function of height on the photocathode in the interval -6mm<y<6mm along a horizontal line in the cathode-anode gap
0.252 gap between 0.21 and -0.042
Note: offset in z due to CST model photocathode not in 0,0 coordinates

## Slide 11: CST results: Transverse electric field – Mushroom
The different colors show how the transverse electric field changes as a function of height on the photocathode in the interval -6mm<y<6mm along a horizontal line in the cathode-anode gap
Chart: Original shield
0.191 gap between 0.27 and 0.079
Note: offset in z due to CST model photocathode not in 0,0 coordinates

## Slide 12: CST results: Transverse electric field – Small mushroom
Chart: Shield 8
The different colors show how the transverse electric field changes as a function of height on the photocathode in the interval -6mm<y<6mm along a horizontal line in the cathode-anode gap
0.257 gap between 0.22 and -0.037
Note: offset in z due to CST model photocathode not in 0,0 coordinates

## Slide 13: CST results: Transverse electric field – Sphere, 6 cm gap, short anode
Chart: Sphere, 6 cm gap, short anode
The different colors show how the transverse electric field changes as a function of height on the photocathode in the interval -6mm<y<6mm along a horizontal line in the cathode-anode gap
0.014 gap between 0.10 and 0.086
Note: offset in z due to CST model photocathode not in 0,0 coordinates

## Slide 14: CST results: Transverse electric field – Sphere, 9 cm gap, large anode
Chart: Sphere, 9cm gap, long anode
The different colors show how the transverse electric field changes as a function of height on the photocathode in the interval -6mm<y<6mm along a horizontal line in the cathode-anode gap
0.25 gap between 0.39 and 0.14
Note: offset in z due to CST model photocathode not in 0,0 coordinates

## Slide 15: CST results: Transverse electric field – Sphere, 6 cm gap, large anode
Chart: Sphere, 6cm gap, long anode
The different colors show how the transverse electric field changes as a function of height on the photocathode in the interval -6mm<y<6mm along a horizontal line in the cathode-anode gap
0.01 gap between 0.06 and 0.05
Note: offset in z due to CST model photocathode not in 0,0 coordinates

## Slide 16: Comparing all models at the c-a gap only for the y=0 electric field line

## Slide 17: CST results: Transverse electric field at C-a gap axis
Chart: z (m)
All the data sets correspond to the center line in the cathode-anode gap. Different colors represent different shields.
~12% difference between 0.17 and 0.15
~53% difference between 0.17 and 0.08

## Slide 18: CST model at 200 kV T-electrode on R28 white insulator vs spherical electrode on R30 insulator 6 cm anode-cathode gap and CEBAF anode
4.87 MV/m
7.9MV/m
6.5MV/m
29MV/m at cusp
4.6 MV/m
7.2MV/m
6.3MV/m
5.5MV/m

## Slide 19: CST results 200 kV T-electrode on white insulator: Electric field norm– No shield
4.87 MV/m
7.9MV/m
6.5MV/m
29MV/m at cusp
Triple points:
Upper flange:5MV/m
Triple points:
Cathode: 3.6MV/m

## Slide 20: CST results 200 kV UITF gun: Electric field norm– Sphere 6cm gap CEBAF-type anode
4.6 MV/m
7.2MV/m
6.3MV/m
5.5MV/m
Triple points:
Upper flange:9.7MV/m
Triple points:
Cathode: 0.3MV/m

## Slide 21: CST results: Electric field norm– original shield
4.85 MV/m
7.9MV/m
5.6MV/m
7.2MV/m
Triple points:
Upper flange:10MV/m
Triple points:
Cathode: 0.6MV/m

## Slide 22: CST results: Electric field norm– Shield 8
4.86 MV/m
8.08MV/m
6.5MV/m
7.9MV/m
Triple points:
Upper flange:11MV/m
Triple points:
Cathode: 1.2MV/m

## Slide 23: CST results: Electric field norm– Sphere 6cm gap large anode
4.6 MV/m
7.8MV/m
6.9MV/m
5.8MV/m
Triple points:
Upper flange:10MV/m
Triple points:
Cathode: 0.3MV/m

## Slide 24: CST results GTS gun: Electric field norm– Sphere 9 cm gap large anode
4.5 MV/m
6.4MV/m
5.2MV/m
5.5MV/m
Triple points:
Upper flange:10MV/m
Triple points:
Cathode: 0.3MV/m

## Slide 25: Electric field norm:
On the metallic surface
Pics are sadly not to scale, in all of them the cathode (horizontal cylinder) size is the same.

## Slide 26: CST results: Electric field norm– T-shape

## Slide 27: CST results: Electric field norm– Mushroom

## Slide 28: CST results: Electric field norm– Shield 8

## Slide 29: CST results: Electric field norm– Sphere 6cm gap short anode

## Slide 30: CST results: Electric field norm– Sphere 9cm gap large anode

## Slide 31: CST results: Electric field norm– Sphere 6cm gap large anode

## Slide 32: GPT
Important note!
  The plots contain all electrodes, but the apples-to apples-comparison is not *entirely* valid between T-cathode-like shapes and Sphere-cathode-like shapes, since the vacuum chambers are also different.

## Slide 33: GPT: Transverse horizontal Normalized emittance
Chart: z [cm]

## Slide 34: GPT: Transverse vertical Normalized emittance
Chart: z [cm]
~37%
~29%
~7%
Difference with T-cathode at red line:
~52%
~71%

## Slide 35: GPT: Longitudinal Normalized emittance
Chart: z [cm]

## Slide 36: Standard deviation X
Chart: z [cm]

## Slide 37: Standard deviation Y
Chart: z [cm]

## Slide 38: Fin.

## Slide 39: CST frame of reference:
y
z
x
X goes into the page.