## Slide 1
Polarized Beams – A Tale of Two Leptons
The production of Highly Spin Polarized Positrons
using MeV Energy Spin Polarized Electrons
(…or why polarized electrons may be like Red-Billed Oxpeckers)
Joe Grames
Center for Injectors & Sources
Jefferson Laboratory

## Slide 2
• Deliver discovery-caliber research of the atomic nucleus, its constituents, and their interactions
• Apply advanced particle accelerator to develop new basic research capabilities
• Over 1500 Users from 230 Institutions and 30 Countries; over 1/3rd of U.S. Ph.D’s in Nucl. Phy.
Thomas Jefferson National Accelerator Facility is a U.S. Department of Energy Office of Science national laboratory located in Newport News, VA

## Slide 3
CEBAF Accelerator
Multiplicity: 4 Halls Simultaneously
Electron Polarization: 85-90%
Max Energy: 11 GeV(ABC) / 12 GeV(D)
Max Power: 1 MW => 85 mA @ 11 GeV
CHL: Two 4.5kW plants @ 2.1 K
C100: 17.5 MV/m
GaAs/GaAsP

## Slide 4
  Positron physics motivation at Jefferson Lab
  CEBAF Injector PEPPo Experiment
  Polarized Positron R&D Opportunities
  Outlook
Outline

## Slide 5
Polarized Electrons have supported some of the highest impact results from the JLab program:
  The strangeness distribution in the nucleon (HAPPEX and G0)
  Precision Tests of the Standard Model (QWeak)
  Measurement of the neutron skin in 208Pb
  Polarization transfer measurement of GE/GM for the proton
Unpolarized positron beams provide a key tool for further pushing the precision of electron scattering experiments
  Comparison of e- with e+ tests our understanding of two photon effects
Polarized positrons beams provide essential tool
  Unraveling nucleon structure through the measurement of charge-sensitive General Parton Distributions
  Expand the nature of these tests (e.g. for GE/GM via polarization transfer)
Why Polarized Positrons at JLab?
Beam Quality | Electron Beam (Delivered) | Positron Beam (Desired)
Average Intensity | > 200 mA | > 100 nA (5 x 1011 e+/s)
Duty Factor | 100% (cw) | 100% (cw)
Bunch Frequency | 499 MHz (or sub-harmonic) | 499 MHz (or sub-harmonic)
Polarization (orientation) | > 85% (4p control) | > 50% (4p control)
Helicity Control | Rapid reversal (> 30 Hz) | Rapid reversal (> 30 Hz)

## Slide 6
A polarized positron injector suitable for the Jefferson Lab Electron Ion Collider (JLEIC) has also been considered.
L ≥1033cm-2s-1 Pe+≥40%
Iave > 10 nA (~1010 e+/s)
Ipeak > 4 mA (~1013 e+/s)
e+
Polarized Positrons at an Electron Ion Collider
Challenge is accumulating high positron bunch charge with high rep rate.

## Slide 7
P(e+) = 73 ± 15(stat) ± 19(syst) %
Compton Backscattering (KEK)
T. Omori et al, PRL 96 (2006) 114801
Helical Undulator (SLAC E166)
G. Alexander et al, PRL 100 (2008) 210801
P(e+) = 80 ± 7(stat) ± 9(syst) %
SLAC 47.7GeV
Polarized b+ Decay
L.A. Page & M. Heinberg. Phys. Rev.
106(6):1220-1224 (1957)
Polarized due to parity non-conservation in the weak interaction
P(e+) ~ 40 %
Sokolov-Ternov Effect
D. Barber , AIP Conf. Proc. 588, 338 (2001)
P(e+) ~ 70 %
HERA 27.5 GeV e+/e-
Methods for Generating Polarized Positrons
KEK 1.28 GeV

## Slide 8: Photo-Emission from GaAs
Bare GaAs surface
Large Work Function
Positive Electron Affinity (PEA)
PEA=4.07 eV
Egap
Conduction
Band
Valence
Band
GaAs
Vacuum
Dipole layers of
Cesium + NF3
Reduce Work Function
Negative Electron Affinity (NEA)
+
-
-
χNEA ~ 0.2 eV
GaAs
Vacuum
Light
NEA Surface Activation

## Slide 9
Spin Polarized Photoemission from Bulk GaAs
Laser excitation from P3/2 to S1/2 : Egap < E < Egap+Δ
Electron Polarization:
Reverse electron polarization by reversing light polarization
σ+: Right circularly polarized light
σ- : Left circularly polarized light
mj
E
-1/2
+1/2
J
P1/2
-3/2
-1/2
+3/2
+1/2
P3/2
-1/2
+1/2
S1/2
σ+
σ-
3
1
S1/2
P3/2
P1/2
Egap=1.42 eV
Δ=0.34 eV
E
k
EF
3
1

## Slide 10
QE ~ 5%, 30 mA/W
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 mA/W
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Strained Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 mA/W
Pol ~ 89% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
Figure-of-Merit (P2I) has improved by a factor of 43
over the span of the CEBAF “6 GeV era”
Pe- 35% 35% 75% 75% 85% 89%
Ie- 30mA 100mA 50mA 100mA 150mA 200mA
1995 1998 1999 2000 2004 2012 2018
JLab’s e- Beams Provide the Basis for e+ Beams

## Slide 11
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
E.G. Bessonov, A.A. Mikhailichenko, EPAC (1996) A.P. Potylitsin, NIM A398 (1997) 395
Polarized Electrons for Polarized Positrons
Polarized Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Polarized Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)

## Slide 12
P. Adderley1, A. Adeyemi4, P. Aguilera1, M. Ali1, H. Areti1, M. Baylac2, J. Benesch1, G. Bosson2,
B. Cade1, A. Camsonne1, L. Cardman1, J. Clark1, P. Cole5, S. Covert1, C. Cuevas1, O. Dadoun3,
D. Dale5, J. Dumas1,2, E. Fanchini2, T. Forest5, E. Forman1, A. Freyberger1, E. Froidefond2,
S. Golge6, J. Grames1, P. Guèye4, J. Hansknecht1, P. Harrell1, J. Hoskins8, C. Hyde7, R. Kazimi1,
Y. Kim1,5, D. Machie1, K. Mahoney1, R. Mammei1, M. Marton2, J. McCarter9, M. McCaughan1,
M. McHugh10, D. McNulty5, T. Michaelides1, R. Michaels1, C. Muñoz Camacho11, J.-F. Muraz2,
K. Myers12, A. Opper10, M. Poelker1, J.-S. Réal2, L. Richardson1, S. Setiniyazi5, M. Stutzman1,
R. Suleiman1, C. Tennant1, C.-Y. Tsai13, D. Turner1, A. Variola3, E. Voutier2,11, Y. Wang1, Y. Zhang12
1Jefferson Lab, Newport News, VA, US, 2 LPSC, Grenoble, France, 3LAL, Orsay, France
4 Hampton University, Hampton, VA, USA 5 Idaho State University & IAC, Pocatello, ID, USA
6 North Carolina University, Durham, NC, USA 7 Old Dominion University, Norfolk, VA, US
8 The College of William & Mary, Williamsburg, VA, USA 9 University of Virginia, Charlottesville, VA, USA 10 George Washington University, Washington, DC, USA 11 IPN, Orsay, France
12 Rutgers University, Piscataway, NJ, USA 13 Virginia Tech, Blacksburg, VA, USA
PEPPo possible due to support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and the Jefferson Science Associates
The PEPPo Collaboration

## Slide 13
J. Grames, E. Voutier et al., JLab Experiment E12-11-105 (2011)
The purpose of the PEPPo (Polarized Electrons for Polarized Positrons) experiment at the CEBAF Injector was to demonstrate the feasibility of using bremsstrahlung radiation of MeV energy Polarized Electrons for the efficient production of Polarized Positrons.
PEPPo Demonstrated Efficient e+ Production

## Slide 14
1. BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
e-
e+
2. PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
3. Phase Space Definition
The emittance of the positron beam is defined by slits and magnetic fields
S1
D
D
S2
Positron Transverse and Longitudinal Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
4. COMPTON TRANSMISSION POLARIMETER
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
PEPPo: Principle of Operation

## Slide 15
e+
Pe+
Polarized positrons incident on a target produce polarized bremsstrahlung, which is then analyzed via the Compton scattering transmission asymmetry through a magnetized target.
μ1 - Compton absorption coefficient
L - target length
P3 - photon polarization (long.)
Pe - electron/positron polarization
PT - target polarization
Ae - analyzing power
g
Target (Densimet D17K) 90.5% W, 7%, 2.5% Cu
Compton Transmission Polarimetry
PT = 7.06% ± 0.05% (sys1) ± 0.07% (sys2)
Fe Core

## Slide 16
C
A
L
O
R
I
M
E
T
E
R
e+
g
Trigger Scintillator
10mil Al window
Reconversion
Target
Positrons are detected by coincidence between a thin charge sensitive scintillator in front of the reconversion target and the central polarimeter crystal.
Trigger Scintillator
Coincidence
Calorimeter
Compton Transmission Polarimeter
WITHOUT
Coincidence
WITH
Coincidence
Background

## Slide 17
511 keV from e+ annihilation at rest
Bremsstrahlung
end-point
Energy (FADC units)
Energy Integrated Asymmetry
Accidentals
Time (TDC units)

## Slide 18
PEPPo demonstrated efficient polarization transfer of 8.2 MeV/c polarized electrons to positrons, expanding polarized positron production using MeV electron beam energies.
(PEPPo Collaboration) D. Abbott et al. , Phys. Rev. Lett. 116 (2016) 214801
electron beam polarization
85.2 ± 0.6 ± 0.7 %
Whenever producing e+ from e-, polarization is coming for free, if initial electrons are polarized.
PEPPo Experiment Result

## Slide 19
Two NaI detectors measured coincidence of back-to-back photons emitted by annihilation of positrons in a viewscreen.
Positron Yield at MeV Energies
T1
T2
S1
S2
D
D
e+
e-
pe-= 8.2 MeV/c
e+
For these data we had a yield of ~10-5 e+/e-
A3
A1
A3
A1
Viewscreen 0.011 thick @ 45 deg to beam line
99.5% aluminum oxide Al2O3
0.5% chromium doped Al2O3/Al2O3Cr2O3
pe+= 4 MeV/c

## Slide 20
R. Dollan, K. Laihem, A. Schälicke, NIM A 559 (2006) 185,
J. Dumas, J. Grames, E. Voutier, JPos09, AIP 1160 (2009) 120
J. Dumas, Doctorate Thesis (2011)
Optimum energy
Optimum
FoM
The polarization distribution of generated positrons is dominated by low-energy events.
The positron energy at the optimum FoM (P2I) is about half of the electron beam energy.
Figure of Merit (Ee- = 60 MeV)
20
Producing highly polarized positron beams with intensities > 100 nA with typical injector energies (10-100 MeV) requires polarized electron beam intensities of >1-10 milliAmps

## Slide 21
  Superlattice Performance >1 mA Encouraging
Year
Intensity (mA)
SLAC: First GaAs photogun
JLAB: Low-P Bulk GaAs
JLAB: High-P GaAs/GaAsP
Chart: Electron Polarization (%)
| 1.67 | 10.4 | 50.5 | 100.5 | 250.5 | 504 | 755 | 1011 | 1.06
 | 85.6704 | 84.5218 | 84.3896 | 85.3479 | 84.9536 | 86.116 | 84.7714 | 85.9647 | 87.1486
?
W. Liu et al., Appl. Phys. Lett. 109, 252104 (2016)

## Slide 22
Source Operation using GaAs/GaAsP >1 mA
  A electron source operating at 1 mA for one week produces 605 C.
  Recent tests demonstrate photocathode charge lifetimes 300-450 C for beam intensities > 1 mA.

## Slide 23
Polarized Positron Injector Concepts Abound
We have explored concepts with varying level of detail (theses, proposals, and yes…napkins).
The common denominator at JLab is leveraging our skills: Polarized Beams, SRF, Photoinjectors, High energy beams, etc).
A polarized e+ injector at Jlab would be novel in various ways:
  mA polarized e- source
  fast helicity reversal
  cw/short pulse bunches
  high power target > 10 kW
  srf acceleration

## Slide 24
A new injector facility for research and design is coming on-line soon
Polarized electron beams
Beam energy up to 10 MeV
Beam intensity up to 100 mA (100 nA initially)
THIS AREA could be used to test key apparatus for a polarized positron source (target and collection).
Upgraded Injector Test Facility

## Slide 25
High Power Target R&D
Stainless Steel Windows (0.25mm)
LBE (2mm)
Input (e-)
Output (e-,e+,γ)
Liquid Metal Target – lead-bismuth eutectic (LBE)
  High Z = 82, 83
  Low melting point: 124°C
  High boiling point: 1670°C
Multiple LBE targets tested on various accelerators
  Natural Circulation
  Mechanical Pumping
  Electromagnetic Pumping
Approaching 10 kW power level, CW

## Slide 26
Summary and Outlook
Jefferson Lab Users are making the physics case to lab management for high energy polarized positron physics program at CEBAF.
PEPPo demonstrated high positron polarization from moderate energy polarized electrons with a small footprint (cost, energy, radioactivity)
Progress of mA-sources is promising for the development of polarized positron beams with intensity >100 nA (5 x 1011 e+/sec).
Next priority goal is building and testing a collection system to define and optimize the transverse/longitudinal phase space for RF acceleration.
A comprehensive plan, supported by JLab Management, that can be successfully executed is essential for large-scale positron program at JLab.
Collaboration of synergistic technological R&D is possible, especially leveraging JLab skills, provided labor and funding are identified.

## Slide 27
Synergy
The Hippopotamus and Red-Billed Oxpecker share a positive and synergistic relationship.