## Slide 1: Booster Test at UITF
Test of the New Injector Booster at UITF:
RF tests (done!)
Basic Beam Tests and Setup
Exploring the limits and Capabilities
Reza Kazimi, Alicia Hofler, Yan Wang (June 2021)

## Slide 2: Upgraded Injector Test Facility - UITF
TEST NEW PHOTOGUNS
COMMISSION NEW QUARTER CRYOMODULE
TEST 200 kV WIEN FILTER
TEST HDIce

## Slide 3
Why the new booster
New SRF booster
1) Eliminates need for warm capture
2) Reduces RF deflection
3) Has no x/y coupling
4) Provides more adiabatic damping
Our new Booster (“1/4 cryomodule”, or QCM):
2 cell capture section + 7 cell cavity,
should provide 10 MeV beam and introduce no x/y coupling, allow better matching, more adiabatic damping

## Slide 4: Does it do all that? We have to test it!
The beam based studies include the following: 1. x/y kicks 2. x/y coupling 3. Energy spread 4. Energy gain 5. Adiabatic damping 6. Beam stability 7. Bunch length measurements
8. Setup different solutions from GPT

## Slide 5: Beam Study
Using 1. x/y kicks (<1 mrad) (Viewers & BPMs) ~1 shift
2. x/y coupling (<5%) (Correctors + Viewers & BPMs) ~2 shift
3. Energy spread (<10keV) (Spectrometer + Harp) ~2 shift
4. Energy gain (setup) (Spectrometer) ~2 shift
5. Adiabatic damping (depends) (Emittance Measurements, could be tricky) ~2 shift
6. Beam stability (<<s) (BPMs and viewers especially @ high dispersion.
Stability during HDIce) ~? shift
7. Bunch length (0.15 mm) (Need working choppers and bunch length
diagnostics hardware to do this at UITF) ~6 shift
Adds up to ~15 shift + ~ 5 shifts for setup = ~20 shifts

## Slide 6: Exploring the limits and Capabilities
Find minimum and maximum beam energy possible.
Stability: RF stability, Beam energy stability, bunchlength stability, …
Off-axis behavior,
Robustness with respect phase, amplitude, beam position, beam focusing, …
Current and space charge effects.
Try different gun voltages.
4K operation.

## Slide 7
Thank You!
Supporting Materials

## Slide 9: 200 kV gun and new (2-7) quarter injector
Particle distribution at cathode Gaussian distributions for t, x, y, px, and py:
  100 uA 1000 macroparticles
  Beam size 0.213 mm
  Laser pulse length 21.3 ps
  Transverse emittance 0.061 mm mrad
DC Gun
Solenoids
Prebuncher Cavity
Buncher
Cavity
Choppers
Apertures
INJECTOR LAYOUT
SC Booster Cavity
NA-PAC2011 WEP288
IPAC2012 TUPPR055
Cavity | Center distance from cathode (m)
Buncher | 8.875078
2-cell | 12.2337
7-cell | 13.0643
0L03-1 (omitted) | ~29.25 m
1D profiles for DC gun, RF elements, and solenoids

## Slide 10: 3D Mesh Space Charge

## Slide 11: UITF 1 nA front end optimization
2 x 10
-4
3 x 10
-4
4 x 10
-4
5 x 10
-4
6 x 10
-4
7 x 10
-4
8 x 10
-4
9 x 10
-4
1 x 10
-3
0
0.2
0.4
0.6
0.8
1
1.2
1.4
s
E
k
/
E
k
s
t
(ps)
A
B
C

## Slide 12: Phases relative to crest for 1 nA optimization
-140
-120
-100
-80
-60
-40
-20
0
20
0
5
10
15
20
25
30
35
40
45
p
h
a
s
e
o
f
f
s
e
t
r
e
l
a
t
i
v
e
t
o
c
r
e
s
t
(
d
e
g
r
e
e
s
)
simulation run id
Buncher
2-cell
7-cell
CB A
+
X*
0o crest
-90o zero-crossing
Vertical color-coded lines for A, B, and C example cases

## Slide 13: Basic Beam Tests and Setup:
Drift through with both 2 and 7 cells off, checking basic beamline.
Set the phase and amplitude for 2-cell and 7-cell independently.
Check concerns such as alignments, possible tilt effects of cavities,etc.
Check bunchlength, delta E, beam size, …
Try different solutions from GPT simulations

## Slide 14: Results – checked with two codes
Bunch length for different currents. This accelerator has to work for both low and high beam currents at the same time!
The currents are for 499Mhz cw beam structure.