## Slide 1: PQB Meeting
July 2016

## Slide 2: Linewidth Test Cell Setup
laser
Polarizer
(horizontal)
Analyzer
(rotate)
Photodiode
/Power meter
QWP
RTP crystal (45deg)
Depolarized
Light

## Slide 3: Laser Table
Goal - Determine line width is >1nm
When – After August 7
Materials - 5-10mW beam, 2 linear polarizers, QWP, photodiode, scope, power meter, 1 RTP crystal, IR card, IR viewer
Short Procedure summary – ~1hour
Optics Alignment - 30min - align polarizer, analyzer, QWP, RTP crystal, photodiode
Examine Scope to get rms fluctuations- 10min -Take 4 scope shots of pk-pk noise and mean on 1ms time scale and 100ms timescale for QWP in /out and analyzer at 90deg
Measure powers to get % depolarization- 10min - Take 8 power measurements at different analyzer angles for QWP in/out and before/after optical elements
Calculate: Convert pk-pk transmission noise to wavelength fluctuations via
  linewidth=RMST *0.108nm/sin(acos(1-2<T>)) [sensitive to <0.169nm]
Calculate: Convert % depolarization to intrinsic line width via calibration plot already calculated [sensitive to <1nm]

## Slide 4: Injector Measurements
Goal – Compare presummer(old laser) to postsummer(new laser) injector measurements
When – After Aug10, Bob Michaels – injector server
Need – 40-70uA stable beam, control of helicity settings, beam through bpm0R05, autogaining on bpms off, PC HV controls, PC translation controls, RHWP controls
Procedure summary – (previously took ~5-6hours)
1 BCM calibration – current calibration run (for bcm0L02)
1 BPM calibration – autogains off, current run
2 PITA scans for IHWP in/IHWP out
4 RHWP scans for IWHPin/IHWP out at 2 HV settings
1 longer run for RHWP and PITAV chosen settings
(PC translation scan in X/Y)

## Slide 5: BPM 0L02 ym wire channel
Needs checking out
(Pete Francis?)