## Slide 1
e+ mature for Ce+BAF
LERF 123 MeV e+ injector
(start 5-6 year earlier)
LERF e- 650 MeV ready
LERF e- source (> 5 mA) and target tests (10 MeV)
David Dean’s slide to 22 GeV workshop …
I guess would be proposed at the NSAC LRP meeting
Me, working backwards…

## Slide 2: 123 MeV e+ injector for 12 GeV positrons
#6 – SRF accelerate e+ to 123 MeV
#4 - Produce e+ accelerate to 50-70 MeV
#2 - SRF accelerate >100 MeV
#1A – FEL style compact e- injector 10 MeV
#3 – Extract e- to target
#7 – Transport e+ at 123 MeV to exit LERF
#5 – Injector e+ to linac

## Slide 3
Stage | When ? | Electron Driver Capability | Options ? | Final Positron or Electron LERF Beam Capability | Options ?
1 | 2024 – 2026 | Accelerate to ~10 MeV, at least 1 mA but higher currents 5-10 mA desired | CEBAF or FEL QCM Bunche& Laser RF | Test high power targets, but no e+ collection yet… | N/A
2 | 2025 – 2028 | Add one CM, single-pass, reliable highest energy, current >3 mA | ? | Add warm-capture, 1.5 GHz, maybe single-cell cavities | S2E sims are now “done”, ready to start talking…?
3 | 2027 – 203? | Hopefully done…or add second e- CM for energy | ? | Add CM to reach 123 MeV, (up to 100 uA for e- or e+) | C100 ?
Full e+ injector ready by 203?

## Slide 4: 650 MeV e- injector for FFA >22 GeV
Vertically stacked return lines to save floor space
#1 – CEBAF style polarized e- injector 10 MeV
#3 – 3-pass SRF acceleration to 650 MeV
#4 – Extract 650 MeV from linac
#5 – Transport e- at 650 MeV to exit LERF
#2 – Inject 10 MeV e- to linac