## Slide 1: Momentum Measurement Analysis
A. Hofler

## Slide 2: Measurement
Design p (MeV/c) | Design K.E. (MeV) | 2D line dipole setting (G cm) | 5D (Bubble) line dipole setting (G cm)
5.84 | 5.35 | -9937.637 | 8168.800
5.74 | 5.25 | -9865.500 | 8099.000
5.64 | 5.15 | -9632.300 | 7909.200
5.54 | 5.05 | -9468.500 | 7771.400
5.44 | 4.95 | -9320.700 | 7646.800
5.34 | 4.85 | -9135.993 | 7490.000
5.24 | 4.75 | -8957.675 | 7338.900
Dipole
2D
-30o
5D
25o
BPM
BPM
BPM
BPM
BPM=Beam Position Monitor
Procedure:
A priori, center beam in quadrupole closest to BPM and note positions (except 2D).
Turn OFF and cycle all unnecessary magnets around hysteresis loop.
Degauss dipole.
Establish straight ahead orbit with restricted corrector magnet set.
Adjust dipole setting (and cycle) for zero orbit in each dump BPM.

## Slide 3: Analysis
EPICS dipole setpoints provide
Dipole setpoints must be converted to account for beam orbit through dipole
For = ,
-
Accelerator coordinate system is LH

## Slide 4: Fit 2D vs. 5D dipole settings for each set up
Assume there is some unaccounted for field integral ,
then,
correcting for vs. with -30o and 25o
G cm

## Slide 5: Refit accounting for angle error
Assume there is some unaccounted for angle error and field integral
then
G cm

## Slide 6: Measured momenta
Design p (MeV/c) | Design K.E. (MeV) | Measured p (MeV/c)
5.84 | 5.35 | 5.88
5.74 | 5.25 | 5.84
5.64 | 5.15 | 5.70
5.54 | 5.05 | 5.60
5.44 | 4.95 | 5.51
5.34 | 4.85 | 5.40
5.24 | 4.75 | 5.30

## Slide 7: Questions?
A. Hofler
Thank you.
Thanks to
  J. Grames
  R. Kazimi
  D. Moser