## Slide 1: Center for Injectors and Sources
Scientists: M. Poelker, J. Grames, C. Hernandez-Garcia, R. Suleiman, M. Stutzman, and S. Zhang
Postdoc: M. A. Mamun
Technical Staff: P. Adderley, B. Bullard, J. Hansknecht,
Graduate Students: Gabriel Palacios, Y. Wang, S. Wijiethunga, J. Yoskovitz, M. Stefani
Frequently work with others: F. Hannon, R. Kazimi, A. Hofler

## Slide 2: CIS Responsibilities
CEBAF polarized electron source and injector upgrade
LERF photogun and drive laser
Gun Test Stand: magnetized beam for JLIEC (pgun and tgun)
UITF: a compact 10 MeV accelerator at bldg 58

## Slide 3: Skill Set
Photocathode
  High Polarization
  High QE (photoemission yield)
  Long Lifetime
Vacuum
  Static Vacuum
  Dynamic Vacuum
High Voltage
  Eliminating field emission
Drive Laser
  Reliable, phase locked to machine
  Adequate Power
  Wavelength Tunable
Notes: Interior Page Design 2

## Slide 4
Injector Upgrade
Increase gun voltage, modify Wien filters for 200kV operation
Improve baked beam line vacuum so gun does not pump on beam line
Locate H-Wien (energy filter) upstream of pre-buncher cavity
New SRF booster eliminates warm capture, RF deflection and x/y coupling
Our new “1/4 cryomodule”, or QCM:
2 cell capture section + 7 cell cavity,
should provide 10 MeV beam and introduce no x/y coupling, allow better matching, more adiabatic damping
200 kV
4
Accelerator Division All Hands Meeting

## Slide 5: JLab Energy Recovery Linac
Powerful light source
IR and UV FEL
THz light
Search for Dark Matter
Fixed Target Options
Beam accelerated from 5 to 100 MeV and then decelerated back to 5 MeV, to recover the energy
Notes: Interior Page Design 2

## Slide 6: The injection line - DC photogun NCRF buncher + SRF booster and dog-leg merger
0.35 MeV
DC photogun
10 MeV
SRF booster
NCRF buncher
Solenoid
Quadrupoles
Dog-leg
Beam to linac
Solenoid
2.5 m

## Slide 7: Vent-Bake FEL gun
Electrodes
Vacuum chamber
Ceramic stand-offs
Corona shield
High voltage feed
(3) 1000 l/s NEG pumps
RGA, extractor gauge
and leak valve
Photocathode
Photocathode retractor mechanism
80 cm
End flange
End flange
Anode

## Slide 8: JLEIC High Energy Electron Cooler
High Energy Electron Cooler
ion beam
cooling solenoid (B>0)
Magnetization flip
cooling solenoid (B<0)
injector
beam dump
linac
fast extraction kicker
fast injection kicker
dechirper
rechirper
circulating bunches
extracted bunches
injected bunches
exchange
septum
vertical
bend
into ERL
vertical
bend
to CCR
ion beam
Circulator Cooler Ring
ERL Ring

## Slide 9: JLEIC Magnetized Source Requirements
Bunch length | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Peak current | 33.3 A
Average current | 120 mA
Transverse normalized emittance | <19 microns
Cathode spot radius – Flat-top () | 3.14 mm
Solenoid field at cathode (Bz) | 0.5 kG
Bunch length | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Peak current | 33.3 A
Average current | 120 mA
Transverse normalized emittance | <19 microns
 | 3.14 mm
Solenoid field at cathode (Bz) | 0.5 kG
Cornell University demonstrated 65 mA and 2 nC, but not at same time, and non-magnetized
Fermilab Magnetized Photoinjector Laboratory:
Pulsed NCRF gun with Cs2Te photocathode and UV laser (λ=263 nm)
Bunch charge: 0.5 nC and bunch length: 3 ps
0.5% duty factor (average current: 7.5 μA)
  Bunch frequency: 3 MHz
  Macropulse duration: 1 ms
  Number of bunches per macropulse: 3000
  Macropulse frequency: 5 Hz

## Slide 10: Magnetized Source Schematics
Beamline
Gun Solenoid
Photocathode
Preparation
Chamber
Gun HV Chamber
Slit
Viewer Screen
Shield Tube
Viewer 3 Screen
Beam Dump
Use slit and viewscreens to measure mechanical angular momentum:
: solenoid field at photocathode
: laser rms size
φ: rotation (sheering) angle

## Slide 11: 300 kV Inverted Gun and CsK2Sb Photocathode

## Slide 12: Upgraded Injector Test Facility - UITF
TEST NEW PHOTOGUNS
COMMISSION NEW QUARTER CRYOMODULE
TEST 200 kV WIEN FILTER
TEST HDIce
12
New equipment for CEBAF: photoguns, Wien filter, QCM
mA polarized beam R&D
NbSn-coated cavities
Polarimetry (SBIR-sponsored)
Fast Kicking (SBIR-sponsored)

## Slide 13: Upgraded Injector Test Facility
Demonstrated 200 keV beam delivery
QCM cooled to 2K
HDIce cryostat to be installed soon
Need to build MeV beamline
Need klystrons
Need to design/build current-limiting safety device