## Slide 1
UITF Noteworthy developments
(1/11/2021)
HDIce Run3 ended successfully December 18, 2020, as planned
  We accomplished all our intended HDIce tasks
  Andy to describe target performance after my presentation
  I submitted a summary of the 6-year long UITF/HDIce effort
Covid Task Force has approved continued operation of UITF for booster tests
  We did not finish characterization of booster performance: we restarted the “booster characterization” program yesterday. Remember, the booster was promised to improve beam quality for Moeller experiment (FY25?)
  We have LHe at UITF through mid-March, here are the tasks:
    Improve RF stability: The booster rf stays in “GDR mode” for only ~ five minutes before tripping to “SEL mode”. In SEL mode, we can’t accelerate beam. For the HDIce tests we masked numerous fault nodes, but this is unacceptable for CEBAF
    Optics measurements, to characterize beam quality, beam accelerated through booster at CEBAF momentum 6.3 MeV/c. Would prefer to validate performance at CEBAF currents, but still limited to 1.7uA macropulse, 25nA average current. More concrete arrives in ~ May, but still only 8uA macropulse, 100nA average current
    BPM troubleshooting: the stripline BPMs report beam when there’s no beam, and report different orbits in CW and Tune Mode

## Slide 2
UITF program through mid-March, and then through June
Task 1, Improve RF stability (Curt Hovater, Tomasz Plawski, Rama B., Clyde Mounts, others) Matt and Yan to support
Task 2, optics measurements (Yan, Matt, Dennis Turner, Max Bruker)
Task 3, BPM trouble shooting (John Musson, Brian Bevins, Kyle Hesse, Keith Cole), Matt and Yan to support
Task4?, talk of HDIce run4?
When helium is redirected to CMTF for C75-1 testing in mid-March, we will modify the beamline to prepare for the LDRD water irradiation tests which we believe could start in May (?) (G. Ciovati, Hannes Vennekate, Xi Li, Shaun Gregory)
Mike McCaughn, Crew Chief from CEBAF Operations, volunteered to serve as Work Coordinator and Facility Manager for this LDRD project, I will school him