## Slide 1: R30-4 gun S&A during electrode assembly installation and laser retro-reflection evaluation with various pucks Including CMM on Puck #35
C. Hernandez-Garcia, G. Palacios-Serrano, M. Stutzman, S. Zhang,
B. Mares, C. Gould, S. Hardisty, R. Ammons, E. Mosby
May 8, 2024

## Slide 2
R30-4 back end zoomed in showing orientation of puck retainer assembly to be used for installing puck with ear (tab) up
Up
Puck keys horizontal
Puck tab vertical at 12 o’clock orientation
Puck retainer spring at 6 o’clock orientation
R30-4 gun puck retainer assembly orientation
R30-4 gun electrode assembled on April 25, 2024 with 16/30 front end

## Slide 3
D = 1380 mm
Y reflected laser spot displacement (mm)
Reflected laser spot measuring plane (card with pinhole)
Puck plane
(mirror or GaAs)
Reflected light angle is 2 X electrode angle
The electrode z-axis is tilted down 0.124 deg with respect to chamber z-axis
S&A reports that the electrode z-axis is 0.124 deg pointing down wrt to the gun HVC z-axis
532 nm laser beam path
S&A setup to evaluate laser retro-reflection with R30-4 electrode installed to gun high voltage chamber

## Slide 4
First with the laser launch colinear with R30-4 gun high voltage chamber z-axis
Mirror puck ear up
GaAs wafer on Moly puck # 35 ear up
Mirror puck 𝜃=
Y = 6 mm
D = 1380 mm
Reflection 𝜃 = 0.249∘
Electrode z-axis angle = 𝜃/2 = 0.124∘
Agrees with S&A measurement
GaAs on Moly puck # 35. 𝜃=
Y = 15 mm
D = 1380 mm
Reflection 𝜃 = 0.624∘
GaAs puck # 35 z-axis angle = 𝜃/2 = 0.312∘
𝜃 = 0.124 ∘
High voltage chamber
Electrode & mirror puck
High voltage chamber
Electrode & puck # 35
𝜃 = 0.312 ∘
Is the Moly puck z-axis tilted?
Or is the GaAs wafer plane tilted wrt to the moly puck z-axis?

## Slide 5
Ear to the left
Ear up
Ear to the right
Next, and for the rest of measurements, the laser launch was made colinear with R30-4 gun electrode z-axis
Mirror Puck
Y = 1.5 mm
D = 1380 mm
Reflection 𝜃 = 0.062∘
Mirror puck z-axis
angle = 𝜃/2 = 0.031∘

## Slide 6
Laser colinear with R30-4 gun electrode z-axis
Bulk GaAs on Puck # 35
Ear to the left
Ear up
Ear to the right
Y = 10 mm
D = 1380 mm
Reflection 𝜃 = 0.416∘
Bulk GaAs on puck # 35 z-axis angle = 𝜃/2 = 0.208∘

## Slide 7
Laser colinear with R30-4 gun electrode z-axis
SSL GaAs on Puck # 31
Ear to the left
Ear up
Ear to the right
Y = 7 mm
D = 1380 mm
Reflection 𝜃 = 0.290∘
SSL GaAs on puck # 31 z-axis angle = 𝜃/2 = 0.145∘

## Slide 8
Laser colinear with R30-4 gun electrode z-axis
SSL GaAs on Puck # 10
Ear to the left
Ear up
Inadvertently I missed taking the picture with the ear to the right
Y = 13 mm
D = 1380 mm
Reflection 𝜃 = 0.540∘
SSL GaAs on puck # 10 z-axis angle = 𝜃/2 = 0.270∘

## Slide 9
𝜃 = 0.124 ∘
𝛽 = 0.312 ∘
𝛼 = 0.312- 0.124 ∘
𝛼 = 0.188 ∘
𝛼 = 0.188 ∘
Y= 15 mm
X = Y∙tan (0.188 ∘) = 0.048 mm or ~ 50 microns
Indium foil is 50 microns thick
Based solely on laser retro-reflection spot displacement measurements.
the GaAs wafer plane seems to be tilted 0.188∘ down wrt to the puck z-axis

## Slide 10: Puck # 35 with bulk GaAs was sent to SRF Coordinate Measuring Machine (CMM)
z
x
y

## Slide 11
The CMM results show that:
The crown plane is tilted up wrt the puck z-axis by 0.0574∘
The wafer plane is tilted down wrt the puck z-axis by 0.1729∘