## Slide 1: Magnetized Electron Source, LDRD
M. Poelker and R. Suleiman

## Slide 2: Outline
Magnetized Bunched-Beam Electron Cooling
LDRD Magnetized Electron Source
  K2CsSb Photocathode and HV Chambers
  Gun Solenoid
  Beamline
Generation of Magnetized Electron Beam
Measuring Electron Beam Magnetization
  Slit and Viewscreens
  TE011 Cavity: new method
Outlook
Summary

## Slide 3: JLEIC High Energy Electron Cooler
High Energy Electron Cooler
ion beam
cooling solenoid (B>0)
Magnetization flip
cooling solenoid (B<0)
injector
beam dump
linac
fast extraction kicker
fast injection kicker
dechirper
rechirper
circulating bunches
extracted bunches
injected bunches
exchange
septum
vertical
bend
into ERL
vertical
bend
to CCR
ion beam
Circulator Cooler Ring
ERL Ring

## Slide 4: Magnetized Bunched-Beam Electron Cooling
Ion beam cooling in presence of magnetic field is much more efficient than cooling in a drift (no magnetic field):
  Electron beam helical motion in strong magnetic field increases electron-ion interaction time, thereby significantly improving cooling efficiency
  Electron-ion collisions that occur over many cyclotron oscillations and at distances larger than cyclotron radius are insensitive to electrons transverse velocity
Long cooling solenoid provides desired cooling effect:
  Counteracting emittance degradation induced by intra-beam scattering
  Maintaining ion beam emittance during collisions and extending luminosity lifetime
  Suppressing electron-ion recombination
  but putting electron beam into cooling solenoid represents a challenge
Solution: Beam rotation in cooling solenoid is compensated by creating electrons inside a longitudinal magnet field

## Slide 5: Magnetized Cooling Schematics
Electron beam suffers an azimuthal kick at entrance of cooling solenoid. But this kick can be cancelled by an earlier kick at exit of photogun. That is purpose of cathode solenoid
Upon exit of Cathode Solenoid
Upon entering Cooling Solenoid
re= 0.7 mm
Bcool = 1 T
Electrons born in strong uniform Bz
= Rlaser = 3.14 mm
Bz = 0.5 kG
= 36 µm

## Slide 6: JLEIC Magnetized Source Requirements
Bunch length | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Average current | 140 mA
Transverse normalized emittance | <19 microns
Cathode spot radius – Flat-top () | 3.14 mm
Solenoid field at cathode (Bz) | 0.5 kG
Bunch length | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Average current | 140 mA
Transverse normalized emittance | <19 microns
 | 3.14 mm
Solenoid field at cathode (Bz) | 0.5 kG
Cornell University demonstrated 65 mA and 2 nC, but not at same time, and non-magnetized
Fermilab Magnetized Photoinjector Laboratory:
Pulsed NCRF gun with Cs2Te photocathode and UV laser (λ=263 nm)
Bunch charge: 0.5 nC and bunch length: 3 ps
0.5% duty factor (average current: 7.5 μA)
  Bunch frequency: 3 MHz
  Macropulse duration: 1 ms
  Number of bunches per macropulse: 3000
  Macropulse frequency: 5 Hz

## Slide 7: Magnetized Beam LDRD
Three-year project (FY16 – FY18):
  Generate magnetized electron beam from dc high voltage photogun and measure its properties
  Explore impact of cathode solenoid on photogun operation
  Simulations and measurements will provide insights on ways to optimize JLEIC electron cooler and help design appropriate source
  JLab will have direct experience magnetizing electron beams at high current

## Slide 8: LDRD Magnetized Electron Source
K2CsSb Photocathode Preparation Chamber, Gun, Solenoid and Beamline are all operational

## Slide 9: Magnetized Source Schematics
Beamline
Gun Solenoid
Photocathode
Preparation
Chamber
Gun HV Chamber
Slit
Viewer Screen
Shield Tube
Viewer 3 Screen
Beam Dump

## Slide 10: Photocathode Preparation Chamber
K2CsSb grown with a mask – limit photocathode active area (3 mm diameter) to reduce beam halo, minimize vacuum excursions and high voltage arcing, prolong photogun operating lifetime
Active area can be offset from electrostatic center
5 mm active area also available
Entire photocathode can be activated too

## Slide 11: Gun HV Chamber
Upgraded HV Chamber with new doped-alumina inverted insulator and newly designed screening electrode (triple point junction shield) to lower gradient from 12 MV/m to 10 MV/m at 350 kV
Photogun now operating at 300 kV with gun solenoid at 400 A

## Slide 12: Gun Solenoid
Using spare CEBAF Dogleg magnet power supply (500 A, 80 V)
Learned that gun solenoid can influence field emission
First trials with gun at high voltage and solenoid ON resulted in new field emission and vacuum activity
Procedure to energize solenoid without exciting new field emitters
Size | 11.811" ID, 27.559" OD, 6.242" Z
Conductor | L=500 m, A=0.53 cm2 16 layers by 20 turns
Coil Weight | 254 kg (560 lbs)
Resistance | 0.198 Ω
Field at Photocathode | 1.4 kG
Voltage | 79 V
Current | 400 A

## Slide 13: New Steel Photocathode Holders
New steel holders (pucks) to enhance field to 2.0 kG at photocathode. Two types:
  Molybdenum and carbon steel hybrid puck
  Carbon steel puck
Molybdenum
Steel
Steel

## Slide 14: Non-magnetized Beam
Commissioned beamline
Measured beam emittance, typical thermal angle (thn) value of 0.5 mm mrad/mm(rms), consistent with published data
Delivered 1.0 mA dc

## Slide 15: High Current Magnetized Beam
1450 G
Delivered 0.5 mA dc
Plan for 5 mA by end of summer – installed dc ion-clearing electrodes to stop ions in beamline from reaching gun and causing HV arcs

## Slide 16: Measuring Electron Beam Magnetization
Use slit and viewscreens to measure mechanical angular momentum:
: solenoid field at photocathode
: laser rms size
φ: rotation (sheering) angle

## Slide 17: Slit and Viewscreen Measurement
0 G at photocathode
1450 G at photocathode

## Slide 18: TE011 Cavity: Non-invasive Technique
New non-invasive technique to measure electron beam magnetization
Filed inventor disclosure entitled “Non-invasive RF Cavity to Measure Beam Magnetization”
E-field: only in azimuthal direction
H-field: only in longitudinal and radial direction
Copper cavity in progress
Waveguide-coax out-coupler

## Slide 19: Outlook
Continue to characterize magnetized beam and cross check measurements with simulation
Test magnetic puck (i.e., steel photocathode holder), which should enhance beam magnetization for given solenoid current
Install RF pulsed laser
Build and install TE011 cavity to measure beam magnetization in collaboration with JLab SRF Institute and Brock Roberts (Electrodynamics LLC)
Demonstrate 32 mA magnetized beam
Next: Funded Phase-II SBIR with Xelera, to develop rf-pulsed dc high voltage thermionic gun to be installed at Gun Test Stand (GTS) in FY19 – will use LDRD beamline

## Slide 20: Summary
K2CsSb Photocathode Preparation Chamber, Gun, Solenoid and Beamline are all operational
Photogun operates reliably at 300 kV
Cathode solenoid can trigger field emission but we have learned how to prevent this
Have successfully magnetized electron beam and measured rotation angle
Thanks to: P. Adderley, J. Benesch, B. Bullard, J. Grames, J. Guo, F. Hannon, J. Hansknecht, C. Hernandez-Garcia, R. Kazimi, G. Krafft, M. A. Mamun, Y. Wang, S. Wijiethunga, J. Yoskovitz, S. Zhang
ODU Graduate Students
Postdoc