## Slide 1
Magnetized Electron Beam for Ion Cooling at JLEIC
Y. Wang, P. Adderley, B. Bullard, J. Benesch, G. Krafft, F. Hannon, C. Hernandez-Garcia, J. Hansknecht,
M. Poelker, M. A. Mamun, R. Suleiman, S. Wijiethunga, J. Yoskovitz, S. Zhang
Jefferson Lab Users Group Annual Meeting June 19, 2017
Acknowledgement: This work is supported by the Department of Energy, Laboratory Directed Research and Development funding, under contract DE-AC05-06OR23177
Photogun operates reliably at 300 kV
Cathode solenoid can trigger field emission but we have learned how to prevent this
Have successfully magnetized electron beam and measured rotation angle of magnetized beam
Continue to characterize magnetized beam
- Different laser sizes
- Impact on beam emittance
- High beam current run, 5mA
Cross check beam-based measurements with simulation
Install an RF-pulsed laser
Use magnetic puck to increase beam magnetization
Gun Test Stand
Cathode Solenoid
Power supply voltage 72 V
Maximum current 400 A
Field at photocathode 1.4 kG
Long solenoid of cooling ring provides desired cooling effect, containing ion beams and enhancing cooling efficiency, suppressing electron-ion recombination, and counteracting emittance degradation induced by intra-beam scattering, but putting electron beam into cooling solenoid represents a challenge.
Upon entering Cooling Solenoid
re= 0.7 mm
Bcool = 1 T
Electrons born in strong uniform Bz
= Rlaser = 1.56 mm
Bz = 2 kG
= 36 µm
Bunch length | 60 ps (2 cm)
Repetition rate | 476.3 MHz
Bunch charge | 420 pC
Peak current | 7.0 A
Average current | 200 mA
Transverse normalized emittance | 10s mm mrad
Cathode spot radius – Flat-top () | 1.56 mm
Solenoid field at cathode (Bz) | 2 kG
Bunch length | 60 ps (2 cm)
Repetition rate | 476.3 MHz
Bunch charge | 420 pC
Peak current | 7.0 A
Average current | 200 mA
Transverse normalized emittance | 10s mm mrad
 | 1.56 mm
Solenoid field at cathode (Bz) | 2 kG
Six meter beamline consist of photocathode pre-paration chamber, gun chamber, cathode solenoid to magnetize beam, four lenses, three viewers and two slits, vacuum pumps and beam dump
Electron beam suffers an azimuthal kick at entrance of cooling solenoid. But this kick can be cancelled by an earlier kick at exit of photocathode. That is
the purpose of large solenoid near the photogun.
Upon exit of Cathode Solenoid
ion
electron
Cathode Solenoid
Cooling Solenoid
SRF LINAC
New Photocathode Holder
Enhance the magnetic field at cathode to 2.0 kG
Steel
Molybdenum
Beam on viewers
Cathode Solenoid Off
Cathode Solenoid On
Electron Cooler
JLEIC
(Jefferson Lab Electron Ion Collider)
Cooling With
Magnetized Electron Beam
Summary & Plan
K2CsSb photocathodes provide
stable QE and lifetime
One hour run with cathode solenoid at 400 A
Electron Cooling
To achieve required luminosity of 1034 cm-2 s-1, ion beams at JLEIC must be cooled. In general, this is accomplished when an electron beam co-propagates with ion beam moving at same average velocity, but different temperatures (𝑇𝑒≪𝑇i), where energy of chaotic motion of the ion beam is transferred to cold electron beam.
JLEIC proposal relies on
Magnetized Beam Cooling
slit
ion bunch
electron bunch
Cooling Solenoid
SRF Linac
dump
injector
energy recovery
Utilizes Energy-Recovery-Linac (ERL) (11MW)
Cooling Uses a Bunched Electron Beam
: field at photocathode
: laser rms size
Φ: rotation (sheering) angle
Use slit and viewscreens to measure mechanical angular momentum