## Slide 1
Simulation Study of the Magnetized Electron Beam
ABSTRACT
The proposed Jefferson Lab Electron Ion Collider (JLEIC) must provide ultra-high collision luminosity to achieve promised physics goals. Small transverse emittance at the ion-electron collision point is one of the key requirements of the collider design. Emittance growth that results from electron-ion collisions will be controlled by electron cooling of the ion beam and cooling can be enhanced using a magnetized electron beam, where the cooling process occurs inside a solenoid field. The radial fringe magnetic field at the entrance of the solenoid creates a large additional rotational motion which adversely affects the cooling process. At the electron source, we create the electron beam inside a similar field but inducing rotational motion in the opposite direction to compensate this effect. Beam-based magnetization measurements have been performed and this presentation provides a comparison to predictions based on simulations using ASTRA and GPT software, as a function of beam size variations and rotation angle variations along the beamline, for different solenoid currents and other parameters.
Sajini A. K. Wijethunga1, J. R. Delayen1, G. A. Krafft2, F. E. Hannon2, R. Suleiman2,
M. Poelker2, J. Benesch2, M. A. Mamun2
1Department of Physics, Old Dominion University, Norfolk, Virginia 23529, USA
2Thomas Jefferson National Accelerator Facility, Newport News, Virginia 23606, USA
Acknowledgement: This work is supported by the Department of Energy, Laboratory Directed Research and Development funding, under contract DE-AC05-06OR23177
Beam Line
Modelling
sajini@jlab.org
: beam radius at slit 1
: beam radius at slit 2
: solenoid field at photocathode
: laser rms size
: rotation angle
= 693 keV/c
General formula to find
When beam converging
When beam is at waist 0
When beam diverging 0
Green
Laser
Cathode
Anode
K2CsSb
Photocathode
Cathode
Solenoid
Diagnostic Cross 1
(Slit + YAG Screen)
Diagnostic Cross 2
(Slit + YAG Screen)
Diagnostic Cross 3
(YAG Screen)
Injector Focusing
Solenoid
Mismatch Oscillations
Rotation Angle Variations with the Gun Solenoid Currents
Chart: Beam Size vs Gun Solenoid Current on Three Viewers
| 0 | 2 | 5 | 8 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 175 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 325 | 350 | 375 | 400
σ (V1) | 4.2187 | 4.1365 | 4.0356 | 3.5672 | 3.4484 | 2.7941 | 1.9864 | 1.1014 | 0.85912 | 2.7442 | 3.9267 | 3.3982 | 1.8134 | 2.1099 | 3.6258 | 3.7659 | 2.3538 | 1.7027 | 2.4811 | 2.3046 | 1.4525 | 1.0398 | 1.191 | 0.99283 | 0.88574 | 1.3713 | 1.9517 | 2.3174 | 3.1994 | 4.0307 | 4.4818 | 4.7415 | 5.8149 | 6.6285 | 7.398 | 7.0897 | 6.9298 | 8.3442 | 8.2379 | 8.4421 | 7.8597
σ (V2) | 4.5925 | 4.8449 | 4.8867 | 4.613 | 4.1973 | 3.6337 | 2.3706 | 1.3047 | 1.2439 | 4.0026 | 5.2902 | 4.5872 | 2.183 | 3.1807 | 5.1196 | 4.9853 | 2.8309 | 2.1399 | 2.9657 | 2.5657 | 1.3029 | 1.5463 | 1.7464 | 1.6518 | 1.9049 | 3.163 | 4.3091 | 4.5513 | 6.1355 | 7.5073 | 8.7252 | 8.3367 | 9.8913 | 12.6293 | 12.5157 | 12.7635 | 11.6239 | 14.0262 | 13.1802 | 11.6409 | 10.425
σ (V3) | 8.2711 | 8.1582 | 7.9486 | 7.4899 | 7.0536 | 5.6187 | 3.681 | 1.7613 | 2.5215 | 7.3594 | 9.8289 | 7.7033 | 3.3171 | 5.9178 | 8.9017 | 7.6277 | 3.9011 | 3.6677 | 4.8102 | 3.0628 | 2.3942 | 4.0379 | 4.3015 | 4.6495 | 5.6595 | 8.7479 | 10.5377 | 10.9501 | 14.4948 | 13.9034 | 14.2003 | 15.6104 | 14.5324 | 14.8272 | 15.0506 | 14.6523 | 14.9129 | 16.0503 | 14.5189 | 13.6736 | 12.7048
σ (V1)_Sim | 2.0005 | 1.998 | 1.9832 | 1.9482 | 1.9087 | 1.7305 | 1.4197 | 1.022 | 0.81119 | 1.7936 | 2.3842 | 2.7895 | 2.7652 | 1.7747 | 1.5407 | 2.6527 | 3.0539 | 2.4058 | 1.5439 | 1.7104 | 1.9383 | 1.5177 | 0.95919 | 0.91955 | 0.86285 | 1.4798 | 1.8584 | 2.1714 | 2.9138 | 2.4891 | 3.7195 | 4.0438 | 4.1642 | 4.8299 | 5.7999 | 6.2813 | 6.2252 | 6.2108 | 6.3247 | 7.1753 | 7.4565 | 7.3968 | 7.3508 | 7.2155 | 7.0058 | 6.9078 | 6.7007
σ (V2)_Sim | 2.7173 | 2.7132 | 2.6892 | 2.6345 | 2.5742 | 2.3106 | 1.8654 | 1.327 | 1.1461 | 2.6377 | 3.4383 | 3.9567 | 3.7951 | 2.3482 | 2.2329 | 3.7417 | 4.0997 | 3.0393 | 1.9333 | 2.2674 | 2.3519 | 1.5881 | 1.1649 | 1.4672 | 1.5491 | 3.1979 | 3.7131 | 4.2265 | 5.4967 | 4.7844 | 6.7338 | 7.091 | 7.169 | 8.1876 | 9.612 | 10.1771 | 9.9086 | 9.8138 | 9.9187 | 10.9346 | 11.1299 | 10.8296 | 10.6589 | 9.8795 | 9.3295 | 9.0568 | 8.4706
σ (V3)_Sim | 5.2845 | 5.2747 | 5.2178 | 5.0929 | 4.9586 | 4.3911 | 3.471 | 2.4571 | 2.42 | 5.6681 | 7.2147 | 8.1358 | 7.4833 | 4.4365 | 4.764 | 7.6444 | 7.842 | 5.3366 | 3.521 | 4.3918 | 3.9716 | 2.4573 | 3.2938 | 4.2748 | 4.8483 | 9.442 | 10.3918 | 11.5852 | 14.6816 | 12.9719 | 17.4225 | 17.8702 | 17.7818 | 20.0289 | 22.9892 | 23.7902 | 22.8034 | 22.4272 | 22.5254 | 24.6224 | 25.0019 | 23.839 | 23.1915 | 19.8622 | 17.86 | 16.882 | 14.7399
Summary and Outlook
Measurements vs Simulations
Beam Profile
GPT
ASTRA
Beam Size Variations with the Gun Solenoid Currents
2D Electric Field
1D Magnetic Field
 | JLEIC
Bunch length | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Peak current | 53.9 A
Average current | 140 mA
Transverse normalized emittance | <19 microns
Cathode spot radius – Flat-top () | 3.14 mm
Solenoid field at cathode (Bz) | 0.5 kG
 | JLEIC
Bunch length | 60 ps (2 cm)
Repetition rate | 43.3 MHz
Bunch charge | 3.2 nC
Peak current | 53.9 A
Average current | 140 mA
Transverse normalized emittance | <19 microns
 | 3.14 mm
Solenoid field at cathode (Bz) | 0.5 kG
Max Bz at the cathode | 0.1511 T
xy_rms, top-hat | 0.301 mm
t_rms, Gaussian | 24 ps
Charge | 1 nC
Gun voltage | 300 kV
x_off | 0 mm
y_off | 0.5 mm
Emittance | 0.56 pi mm mrad/ mm
Rotation angle variation of a diverging beam
Rotation angle variation of a converging and diverging beam
1D Electric Field
1D Magnetic Field
Simulation Parameters