## Slide 1: General Particle Tracer (GPT) Simplified Simulations
A. Hofler
May 24, 2017

## Slide 2: Summary of Elegant Model
Beam characteristics
  pcentral= 1.732 mec ⇒ Ek=507.7 keV
  Q=0.65 nC ⇒ 325 mA at 499 MHz
  𝛔x,y=7 mm
  𝛔t=1.16 ps
  𝛆n(x,y)=1 mm mrad
Beam line element | Length (cm) | Setting | Center location (m)
Solenoid | 5 | 0.0293 T | 0.1860
Permanent Magnet Quadrupole (PMQ)* | 0.6* | K1=-133333 1/m2 ⇒ -400 T/m* | 1.0029
Solenoid | 5 | 0.0293 T | 1.8198
Solenoid | 5 | 0.0293 T | 2.1918
PMQ | 0.6* | K1=133333 1/m2 ⇒ 400 T/m* | 3.0087
Solenoid | 5 | 0.0293 T | 3.8256
*R. K. Li and P. Musumeci, Phys. Rev. Applied 2 024003 (2014)

## Slide 3: Summary of GPT Model
Analytical magnet models
  Solenoid
    does not remove particles
    setpoint in nI (A turns/m)
  Quadrupole
    no fringe fields
    does not remove particles
    Horizontally defocussing quad in first cell
Beam characteristics
  ϒ=2
  Line of charge
    21 particles
    Evenly distributed
    1 mm long in +x direction
    (0,0,0) to (1,0,0) mm
Space charge off
Beam line element | Length (cm) | Aperture (cm) | Attempted Setting | Center location (m)
Solenoid (S1) | 5 | 5.4 | 0.0293 T ⇒ 34363 A turns/m | 1.1
PMQ (Q1) | 0.6* | 0.3* | 400 T/m* | 1.9169
Solenoid (S2) | 5 | 5.4 | 0.0293 T ⇒ 34363 A turns/m | 2.7338
Solenoid (S3) | 5 | 5.4 | 0.0293 T ⇒ 34363 A | 3.1058
PMQ (Q2) | 0.6* | 0.3* | -400 T/m* | 3.9227
Solenoid (S4) | 5 | 5.4 | 0.0293 T ⇒ 34363 A turns/m | 4.7396
*R. K. Li and P. Musumeci, Phys. Rev. Applied 2 024003 (2014)

## Slide 4: Solitary Quad Q1 On
Without focusing the beam at the quad location, particles on the edge of beam will be driven into the beam pipe and not transport through the quad.

## Slide 5: Process
For canned and fieldmap singlewound solenoid models:
Find solenoid setting to focus beam at center of quad
  All solenoids have same setting with quads off
With quads on, find a solenoid setting for all solenoids that restores the exit orbit
With quads on and focus setting for the outer solenoids, adjust center solenoid setting to restore exit orbit
With quads on, the solenoid setting from step 2 t for the outer solenoids, adjust center solenoid setting to restore exit orbit
Optional, with the quads on, find outer and center solenoid settings that maintains the orbit at the entrance and exit of all cells

## Slide 6: Canned Solenoid Field Extent
The solenoid is 5 cm long, but the residual field extends much further.
Solenoid S1 Only
Solenoid S1 Only
1 Cell (S1 and S2)
2 Cells (S1, S2, S3, S4)

## Slide 7: Solenoid Focused at Quad (Quads Off)
1 Cell
1 Cell
S1=S2=S3=S4=Sfocus
2 Cells
Step 1
Adjusted solenoid S1
to focus at center of Q1
Sdesign=0.0293 T
Sfocus=1.020171918Sdesign

## Slide 8: Solenoid Focused at Quad (Quads On)
1 Cell
1 Cell
Same solenoid setting as previous slide, Sfocus.
2 Cells
S1=S2=S3=S4=Sfocus

## Slide 9: Solenoid Adjusted rinitial=rmiddle (Quads On)
1 Cell
1 Cell
2 Cells
S1=S2=S3=S4=SCell1
Step 2
Adjusted solenoid setting to make rinitial=rmiddle with quad on.
Sdesign=0.0293 T
SCell1=1.0199975Sdesign

## Slide 10: Solenoid Focused at Quad (Quads On)
2 Cells
2 Cells
Step 3
S1=S4=Sfocus
S2=S3=𝛂focusSfocus
𝛂focus=1.000323
Step 4
S1=S4=SCell1
S2=S3=𝛂Cell1SCell1
𝛂Cell1=1.000047
Adjusted middle solenoid settings (𝛂) to make rinitial=rfinal with quad on.

## Slide 11: Solenoid Focused at Quad (Quads On)
2 Cells
2 Cells
Adjusted outer (SOuteri) and middle solenoid settings (𝛂Outeri) to make rinitial=rmiddle=rfinal with quad on.
Step 5
Sdesign=0.0293 T
SOuter1=1.0199925Sdesign
S1=S4=SOuter1
S2=S3=𝛂Outer1SOuter1
𝛂outer1=1.000048
Step 5
Sdesign=0.0293 T
SOuter1=1.0208109375Sdesign
S1=S4=SOuter2
S2=S3=𝛂Outer2SOuter2
𝛂Outer2=0.9987236

## Slide 12: 2.5D Fieldmap Solenoid Field Extent
Field extent is finite but overlaps between S2 and S3.
Solenoid S1 Only
Solenoid S1 Only
1 Cell (S1 and S2)
2 Cells (S1, S2, S3, S4)

## Slide 13: 2.5D Fieldmap Solenoid Field Extent
Shifted Cell 2 0.1 m downstream.
Cell 2 is shifted 0.1 m in following slides.
2 Cells (S1, S2, S3, S4)

## Slide 14: 2.5D Fieldmap Solenoid Focused at Quad (Quads Off)
1 Cell
1 Cell
S1=S2=S3=S4=Sfocus
2 Cells
Step 1
Adjusted solenoid S1
to focus at center of Q1
Sdesign=0.0293 T
Sfocus=1.02276Sdesign

## Slide 15: 2.5D Fieldmap Solenoid Focused at Quad (Quads On)
1 Cell
1 Cell
Same solenoid setting as previous slide, Sfocus.
2 Cells
S1=S2=S3=S4=Sfocus

## Slide 16: 2.5D Fieldmap Solenoid Adjusted rinitial=rmiddle (Quads On)
1 Cell
1 Cell
2 Cells
S1=S2=S3=S4=SCell1a
Step 2
Adjusted solenoid setting to make rinitial=rmiddle with quad on.
First of 2 Solutions
Sdesign=0.0293 T
SCell1a=1.02251Sdesign

## Slide 17: 2.5D Fieldmap Solenoid Adjusted rinitial=rmiddle (Quads On)
1 Cell
1 Cell
2 Cells
S1=S2=S3=S4=SCell1b
Step 2
Adjusted solenoid setting to make rinitial=rmiddle with quad on.
Second of 2 Solutions
Sdesign=0.0293 T
SCell1b=1.0233199Sdesign

## Slide 18: 2.5D Fieldmap Solenoid Focused at Quad (Quads On)
2 Cells
2 Cells
Step 3
S1=S4=Sfocus
S2=S3=𝛂focusaSfocus
𝛂focusa=0.99996
Step 3
S1=S4=Sfocus
S2=S3=𝛂focusbSfocus
𝛂focusb=1.001465
Step 3: Two solutions for Sfocus

## Slide 19: 2.5D Fieldmap Solenoid Focused at Quad (Quads On)
2 Cells
2 Cells
Step 4
S1=S4=SCell1a
S2=S3=𝛂Cell1aSCell1a
𝛂Cell1a=1.000214
Step 4
S1=S4=SCell1b
S2=S3=𝛂Cell1bSCell1b
𝛂Cell1b=0.99911
Step 4: One solution each for SCell1a and SCell1b

## Slide 20: Conclusion
GPT canned quad and solenoid models behave correctly
Canned single-wound solenoid model residual field problematic
  Crosstalk between solenoids and quads
  Shifting Cell 2 not viable
More realistic cylindrically symmetric single-wound solenoid model exhibits same set up sensitivities despite having finite field extent
  Shifting Cell 2 to remove crosstalk did not appreciably change results (unshifted results not provided here)
Attempted to using 3D counter-wound solenoid model (not provided here)
  20% increase in solenoid setting to focus beam at quad
  Multi-cell set ups did not converge (perhaps with more effort?)
Multi-cell system set up is very sensitive to solenoid settings.
  Single-wound or counter-wound solenoids?
    Beam will have net change in orbit with single-wound solenoids

## Slide 21: Conclusion/Questions
GPT canned quad and solenoid models behave correctly
Multi-cell system set up is very sensitive to solenoid settings.
  Canned single-wound solenoid model residual field problematic
    Crosstalk between solenoids and quads
    Shifting Cell 2 not viable
  More realistic cylindrically symmetric single-wound solenoid model exhibits same set up sensitivities despite having finite field extent
    Shifting Cell 2 to remove crosstalk did not appreciably change results (unshifted results not provided here)
Single-wound or counter-wound solenoids?
  Beam will have net change in orbit with single-wound solenoids
  Attempted to use 3D counter-wound solenoid model (not provided here)
    20% increase in solenoid setting to focus beam at quad
    Multi-cell set ups did not converge (perhaps with more effort?)
  CEBAF single- and counter-wound solenoids believed to be capable of focusing 500 keV beam