## Slide 1: Measurement of 16O(g,a)12C with Bubble Chamber and Bremsstrahlung Beam at Jefferson Lab Injector
Riad Suleiman
June 04, 2014
Notes: Title Page

## Slide 2
B. DiGiovine
D. Henderson
R. J. Holt
K. E. Rehm
A. Sonnenschein
A. Robinson
C. Ugalde
J. Benesch
P. Degtiarenko
A. Freyberger
J. Grames
G. Kharashvili
D. Meekins
M. Poelker
Y. Roblin
R. Suleiman
C. Tennant
V. Vylet
https://wiki.jlab.org/ciswiki/index.php/Bubble_Chamber
Notes: Interior Page Design 2

## Slide 3: Outline
Nucleosynthesis and the 12C(a,g)16O Reaction
Time Reversal Reaction: 16O(g,a)12C
The Bubble Chamber
Experimental Setup at Jefferson Lab Injector
Bremsstrahlung Beam and Penfold-Leiss Unfolding
Statistical and Systematic Errors
Backgrounds and Ion Energy Distributions
Summary and Outlook
Notes: Interior Page Design 1

## Slide 4: Relative Abundance of Elements by Weight
Chart: Universe
| Hydrogen | Helium | Oxygen | Carbon | Other
Universe | 73 | 23 | 1 | 0.5 | 0.6
Chart: Human Body
| Oxygen | Carbon | Hydrogen | Nitrogen | Calcium | Phosphorus | Other
Human Body | 61 | 23 | 10 | 2.6 | 1.4 | 1.1 | 0.9
This region is bypassed by 3a process
Notes: http://en.wikipedia.org/wiki/Nucleosynthesis

## Slide 5: Nucleosynthesis
Big Bang Nucleosynthesis: quark ̶ gluon plasma → p, n, He
Stellar Nucleosynthesis: H burning, He burning, NCO cycle
Supernovae Nucleosynthesis: Si burning
Cosmic Ray Spallation
Notes: http://en.wikipedia.org/wiki/Nucleosynthesis

## Slide 6: Stellar Helium Burning
Helium Reactions:
  a + a ↔ 8Be
  (Q = -0.092 MeV, T½ ≈ 10-16 s)
  a + 8Be → 12C + g (Q = +7.367 MeV, Hoyle State = 7.654 MeV)
  a + 12C → 16O + g (Q = +7.162 MeV)
  (slow, otherwise no 12C remains)
  a + 16O → 20Ne + g (very slow – due to parity conservation)
a + 12C burns at very small cross section s ≈ 10-17 barn (10-41 cm2)
Currently, reaction rate error is large (±35%)
Thermonuclear reaction rate involving two nuclei is:
Only narrow energy range is relevant (Gamow Peak)
Goal <±10%
Notes: Notes:
1- Simultaneous fusion of 3-alpha particles has very small probability, the process has to go through 8Be.

## Slide 7: The 12C(a,g)16O Reaction
The holy grail of nuclear astrophysics
S. Woosley, A. Heger, Phys. Rep. 442 (2007) 269
Affects the synthesis of most of the elements of the periodic table
Sets the N(12C)/N(16O) (≈0.4) ratio in the universe
Determines the minimum mass a star requires to become a supernova
Notes: Interior Page Design 2

## Slide 8: The Gamow Peak (Window)
Narrow energy range where thermonuclear reactions is most likely to occur in stellar plasma is a product of two distributions:
  Maxwell-Boltzmann energy distribution with e-E/kBT
  Penetration through Coulomb barrier with e-b/E½
For a + 12C, and stellar T=200 106 K:
  Gamow Peak, E0 ≈ 300 keV, Width ≈ 50 keV
  (in Center-of-Mass (CM) of a + 12C system)
  Maximum of Maxwell–Boltzmann
  energy distribution, kBT = 17 keV

## Slide 9: a+12C Reaction
    a (Jp=0+) + 12C (Jp=0+) cross section, s(E0), is dominated by p–wave (E1) and d–wave (E2) radiative capture to 16O ground state (Jp=0+)
Two bound states, at 6.92 MeV (Jp=2+) and 7.12 MeV (Jp=1–), with sub–threshold resonances at ER=-0.245 and -0.045 MeV, provide most of s(E0) through their finite widths
Distinguish E1 and E2 by measuring g–angular distributions
Notes: Gammas from E1 and E2 transitions have the same energy (7.162+0.3 MeV).

## Slide 10: Heroic efforts in search of 12C(a,g)16O
Previous Experiments:
  Direct Measurements:
    Helium ions on carbon target: 12C(a,g)16O
    Carbon ions on helium gas: 4He(12C, g)16O or 4He(12C,16O)g (Schürmann)
  Indirect Measurements:
    b–delayed a decay of 16N (Jp=2–, T½=7.13 s, BR=0.12%)
    16N → b– + 16O* (Jp=1–) → a + 12C
Experiment | Beam Current (mA) | Target (nuclei/cm2) | Time (h)
Redder | 0.7 | 12C, 3 1018 | 900
Ouellet | 0.03 | 12C, 5 1018 | 1950
Roters | 0.02 | 4He, 1 1019 | 5000
Kunz | 0.5 | 12C, 3 1018 | 700
EUROGAM | 0.34 | 12C, 1 1019 | 2100
GANDI | 0.6 (?) | 12C, 2 1018 | ?
Schürmann | 0.01 | 4He, 4 1017 | ?
Plag | 0.005 | 12C, 6 1018 | 278
Notes: GANDI is written in German, the reference is on the wiki. Also I put the references to all previous experiments on the wiki.

## Slide 11: Astrophysical S-Factor 12C(a,g)16O
R-matrix Extrapolation to stellar helium burning at E = 300 keV
Define S-Factor to remove both 1/E dependence of nuclear cross sections and Coulomb barrier transmission probability:
Author | Stot(300) (keV b)
Hammer (2005) | 162±39
Kunz (2001) | 165±50
Notes: What do you think about the table shown in this slide? See Schurmann data on slide 44. How did he come up with this small error?

## Slide 12: Time Reversal Reaction
12C
a
16O
g
Stellar helium burning at E = 300 keV
Notes: If we use linearly polarized gammas, we need also to measure the alpha-carbon angular distributions to separate E1 and E2 contributes.
What about right-handed or left-handed circularly polarized gammas? Circularly polarized light is a linear combination of linearly polarized light with a phase phi=90 deg. This is to say we cannot separate E1 and E2 with circularly polarized gammas.
At JLab Injector we can produce left-handed or right-handed gammas (our electron beam in linearly polarized).
To produce linear polarized gammas, we need to use a crystal radiator.
See paper: Y. Xu et al. on the wiki.

## Slide 13
A(a, g)B:
σ(g,a) is over two orders of magnitude larger than σ(a, g)
MeV
MeV
Reciprocity Relation: (g,a) and (a,g)
Notes: Interior Page Design 2

## Slide 14: New Approach: Reversal Reaction + Bubble Chamber
 + 16O → 12C + 
beam
target
signal
Extra gain (factor of 100) by measuring time reversal reaction
Target density up to 104 higher than conventional targets. Number of 16O nuclei = 3.5 1022 /cm2 (3.0 cm cell)
Measures total cross section stot (or Stot)
Solid Angle and Detector Efficiency = 100%
Electromagnetic debris (electrons and gammas, or positrons) do NOT trigger nucleation (detector is insensitive to g-rays by at least 1 part in 1011).
Monochromatic g beam at HIGS ≈ 107–8 g/s
Bremsstrahlung at JLab ≈ 109 g/s (top 250 keV)
Notes: Looking at the number of gammas we will have (slide 37), we will need to be insensitive to gamma-rays by at least 1 part in 10^15. I will keep using the factor of 10^11?

## Slide 15: The Bubble Chamber
Donald Glaser won Nobel Prize for inventing chamber to detect particles (1960)
Now being used in Dark Matter Search Experiments: COUPP, PICASSO, SIMPLE
Superheat Preparation:
  Liquid is pressurized at ambient temperature (1 to 2)
  Then pressure is kept constant while temperature is
  increased to above boiling point (2 to 3)
  Finally pressure is slowly released while keeping
  temperature constant (3 to 4)
  At this point (4), still liquid but now superheated
Bubble Formation:
  Particle energy loss will induce vaporization
  Resultant vapor bubble is observable either visibly or audibly
  Bubble growth is captured by a digital camera
  Pressure is increased (4 to 3) to quench bubble. It takes
  about a second for liquid to return to a stable state
  Superheat is restored by releasing pressure again (3 to 4), and cycle is repeated for each bubble event
Superheat
Notes: Do we have a similar figure for N2O?
The superheat is changed by changing the pressure not the temperature.

## Slide 16: Bubble Growth and Quenching
100 Hz Digital Camera: Dt = 10 ms
19F(g,a)15N event in C4F10 at HIGS
3.0 cm
Notes: That is writing on the glass.

## Slide 17: Acoustic Signal Discrimination
COUPP, FNAL, courtesy of A. Sonnenschein
Suppress neutron events by 100 using acoustic signal
Higher Pitch
Bubble growth produces an audible click which is recorded by piezo-electric transducers
Neutron Events:
  17O(g,n)16O
  Neutron–nucleus elastic scattering: 16O(n,n), 14N(n,n)
  Ions 16O or 14N will generate a single bubble
Alpha Events:
  16O(g,a)12C
  17O(g,a)13C
  18O(g,a)14C
  Ions 12C+a or 13C+a or 14C+a will generate a combined multi-bubble
Notes: The audio files are from http://www-coupp.fnal.gov/public/publications/publication.html
Proton events, i.e, (g,p), should be similar to alphas because it is about the energy loss per length in the target.
When we talk about neutrons, we only worry about elastic scattering. What about inelastic scattering or neutron absorption?
Neutron inelastic or capture radiative capture reactions are usually smaller than elastic scattering by orders of magnitude.
These neutrons are fast, i.e., energy range of few MeV.

## Slide 18: Bubble Chamber at HIGS
High Intensity Gamma Source (HIGS) at Duke University
g-rays generated by Compton backscattering of free-electron-laser (FEL) light from high-energy electron beam bunches
Chamber location

## Slide 19: Measuring 19F(g,a)15N at HIGS
C4F10 Bubble Chamber
  T = 30˚C
  P = 3 atm
2 Fast Digital Cameras
Notes: Interior Page Design 2

## Slide 20
Notes: That is a wire in the background of the bubble photo on the left. It was a wire attached to a piezoelectric on
the bottom of the glass for the acoustic signal. If not this, it was just a thermocouple wire.

## Slide 21: Bremsstrahlung Background at HIGS
Electron Beam Energy: 400 MeV
Electron Beam Current: 41 mA
Interaction Length: 35 m
Vacuum: 2x10-10 Torr
Residual Gas: Z = 10
Strong Bremsstrahlung
Background
(when coupled with large
cross sections at high energies)
Notes: If it is neutron background that we worry about at HIGS then we can the acoustic signal. At HIGS, we can get more than (g,n) produced by the bremsstrahlung. All photo breakup reactions are possible because of the high energy bremsstrahlung.

## Slide 22: N2O (Laughing Gas) Bubble Chamber
First g+O→α+C bubble
HIGS, April 2013
  T = -5˚C
  P = 60 atm
Notes: Why the bubble in N2O rises? But not in C4F10. And why the liquid is cloudy for N2O? What was the buffer liquid?
The bubble is far more buoyant in N2O than C4F10 and rises faster. The buffer liquid is water and we had water absorbed in the N2O, but not in C4F10.

## Slide 23: Bubble Chamber Principle
For bubble formation, particle must be over thresholds in both E and dE/dx
Only bubbles with r > Rc grow to be macroscopic
  s: Surface tension
Bubble requires minimum deposited energy (Ec) within minimum distance Lc (=aRc , 10s of nm to a few µm)
  a: free parameter (to determined experimentally)

## Slide 24: Efficiency Curve
g+14N and g+16O
g+16O
N2O efficiency curve,
HIGS April 2013,
Eg = 9.7 MeV
N2O thresholds
Superheat = 3.3˚C

## Slide 25: Experimental Setup at JLab Injector
BCM
5 MeV
Dipole
2D
Spectrometer
5D Spectrometer
Bubble
Chamber
location
Mott Polarimeter
Notes: Interior Page Design 2

## Slide 27: Beamline
Bubble Chamber at
HIGS April 2013
Photon Beam
Entrance
Beam Kinetic Energy, (MeV) | 7.9–8.5
Beam Current (µA) | 0.01–100
Absolute Beam Energy Uncertainty | <0.1%
Relative Beam Energy Uncertainty | <0.02%
Energy Resolution (Spread), σT /T | <0.06%
Beam Size, σx,y (mm) | 1–2
Electron Beam Requirements at Radiator
Notes: Interior Page Design 2

## Slide 28: Schematics
Electron K.E.
3.0 – 8.5 MeV
0.01 – 100 µA
Al Beam Pipe
Cu Radiator
0.02 mm
Cu Electron Dump
2 kW (200 µA and 10 MeV)
Sweep Magnet
Bubble Chamber
Superheated N2O
3 cm long
-5°C, 60 atm
Al Photon Dump
10 cm long
20 cm diameter
Cu Vacuum Window 10 mil
Cu Photon
Collimator
Cu Inner
Pipe
Power deposited in radiator (100 µA and 8.5 MeV) :
  0.02 mm: Energy loss = 21 keV, P = 2.1 W
Pure Copper and Aluminum (high neutron threshold):
  63C(g,n) threshold = 10.86 MeV
  27Al(g,n) threshold = 13.06 MeV
Use GEANT4 to design this region
Notes: Interior Page Design 2

## Slide 29: Measuring Absolute Beam Energy
BPM
5 MeV
Dipole
Electron Beam
Momentum
Notes: Interior Page Design 2

## Slide 30
  Jay Benesch designed and is now working with Engineering to fabricate a more uniform and higher field dipole
  New Hall Probe: 0.01% accuracy, resolution to 2 ppm, and a temperature stability of 10 ppm/°C
  Better shielding of Earth’s and other stray magnetic fields
  Additional goal: Relative beam energy uncertainty <0.02%
Parameter | Term | Now | Goal
Dipole – linearity | δB/B | 0.25% | 0.02%
Dipole – spatial | δBL/BL | 0.10% | 0.02%
Dipole – reproduce | δB/B | 0.10% | 0.02%
Dipole – power supply | δI/I | 0.20% | 0.02%
Position – surveys | δθ/θ | 0.01% | 0.01%
Position – BPM calibration | δθ/θ | 0.05% | 0.05%
Stray magnetic field | δθ/θ | 0.05% | 0.05%
Total | δP/P | 0.36% | <0.10%
Notes: Interior Page Design 2

## Slide 31: Bremsstrahlung Beam
Use both GEANT4 and FLUKA to calculate Bremsstrahlung spectra (we will not measure Bremsstrahlung spectra)
Monte Carlo simulation of Bremsstrahlung at radiotherapy energies is well studied, accuracy: ±5%
Bremsstrahlung Peaks
16O(g,a)12C is ideal case for Bremsstrahlung beam and Penfold–Leiss Unfolding :
  Very steep; only photons near endpoint contribute to yield
  No-structure (resonances)

## Slide 32: GEANT4 Simulation
Both GEANT4 and FLUKA use models that calculate wrong photo–nuclear cross sections. Both do not allow for user’s cross sections. What to do?
  Use GEANT4 and FLUKA to produce the photon spectra impinging on the superheated liquid.
  Fold the above photon spectra with our cross sections in stand-alone codes.
Use GEANT4 to design radiator, collimator, and dumps
Geometry in GEANT4:

## Slide 33: Penfold-Leiss Cross Section Unfolding
Measure yields at: where,
The solution can be written in two forms:
Or, Matrix form:
Method of Quadratures: numerical solution of integral equation based on replacement of integral by finite sum
Volterra Integral Equation of First Kind

## Slide 34: Statistical Error Propagation
With:
Then:
Note:
In case of background Subtraction

## Slide 35
Where:
For mono-chromatic photon beam
Although,

## Slide 36: Results
Radiator thickness = 0.02 mm
Bubble Chamber thickness = 3.0 cm, number of 16O nuclei = 3.474 1022 /cm2
Background subtraction of 18O(g,a)14C
Electron Beam K. E. | Beam Current (µA) | Time (hour) | yi | dyi (no bg) | dyi/yi (no bg, %) | dyi (with bg) | dyi/yi (with bg, %)
7.9 | 100 | 100 | 545 | 23 | 4.2 | 134 | 24.6
8.0 | 100 | 20 | 581 | 24 | 4.1 | 77 | 13.3
8.1 | 80 | 10 | 852 | 29 | 3.4 | 60 | 7.0
8.2 | 20 | 10 | 634 | 25 | 3.9 | 40 | 6.3
8.3 | 10 | 10 | 812 | 28 | 3.4 | 39 | 4.8
8.4 | 4 | 10 | 746 | 27 | 3.6 | 36 | 4.8
8.5 | 2 | 10 | 763 | 28 | 3.7 | 32 | 4.2
Notes: Interior Page Design 2

## Slide 37: Systematic Error Propagation
For absolute beam energy uncertainty of δE (= 0.1%) and zero relative beam energy uncertainty:
Ei (MeV) | dyi/yi (%) | dσi/σi (%)
7.9 | 12.5 | 12.6
8.0 | 10.8 | 10.5
8.1 | 9.3 | 9.1
8.2 | 8.0 | 7.1
8.3 | 7.0 | 6.3
8.4 | 6.3 | 5.8
8.5 | 5.6 | 5.2
This is the cross section dependence on energy
Accounted for dNij due to energy error when calculating dyi

## Slide 38
With:
Then:

## Slide 39
Where:
Note: Correlation Coefficient (rij) =1
No energy-to-energy change in systematic error

## Slide 40: Systematic Error Propagation
No energy-to-energy change in systematic error

## Slide 41: Other Systematic Errors
Then:
Simulation
Beam Current, δI/I | 3%
Photon Flux, δφ/φ | 5%
Radiator Thickness, δR/R | 3%
Bubble Chamber Thickness, δT/T | 3%
Bubble Chamber Efficiency, ε | 5%

## Slide 42
Electron Beam K. E. | Cross Section (nb) | Stat Error (no bg, %) | Stat Error (with bg, %)
7.9 | 0.046 | 4.4 | 24.5
8.0 | 0.185 | 6.0 | 20.7
8.1 | 0.58 | 6.3 | 14.7
8.2 | 1.53 | 8.2 | 13.8
8.3 | 3.49 | 9.1 | 13.3
8.4 | 7.2 | 10.6 | 13.8
8.5 | 13.6 | 12.2 | 14.8
Electron Beam K. E. | Cross Section (nb) | Sys Error (Energy, %) | Sys Error (Total, %)
7.9 | 0.046 | 12.5 | 15.3
8.0 | 0.185 | 10.2 | 13.5
8.1 | 0.58 | 8.3 | 12.2
8.2 | 1.53 | 7.0 | 11.4
8.3 | 3.49 | 6.0 | 10.7
8.4 | 7.2 | 5.3 | 10.5
8.5 | 13.6 | 4.7 | 10.1
Note: Absolute systematic errors do not get magnified in PL Unfolding

## Slide 43: JLab Projected 12C(a,g)16O S-Factor
Statistical Error: dominated by background subtraction from 18O(g,a)14C (depletion = 5,000)
Electron Beam K. E. | Gamma Energy (MeV) | ECM (MeV) | Cross Section (nb) | Stot Factor (keV b) | Stat Error (%) | Sys Error (Total, %)
7.9 | 7.85 | 0.69 | 0.046 | 62.2 | 24.5 | 15.3
8.0 | 7.95 | 0.79 | 0.185 | 48.7 | 20.7 | 13.5
8.1 | 8.05 | 0.89 | 0.58 | 41.8 | 14.7 | 12.2
8.2 | 8.15 | 0.99 | 1.53 | 35.5 | 13.8 | 11.4
8.3 | 8.25 | 1.09 | 3.49 | 32.0 | 13.3 | 10.7
8.4 | 8.35 | 1.19 | 7.2 | 28.8 | 13.8 | 10.5
8.5 | 8.45 | 1.29 | 13.6 | 26.3 | 14.8 | 10.1
Bubble Chamber experiment measures total S-Factor, SE1 + SE2
Notes: Notes:
1- Schurmann at low energy is limited by 16O contamination of 12C ion beam.

## Slide 44: Backgrounds
Background from oxygen
isotopes and nitrogen in N2O:
  18O(g,a)14C
  17O(g,a)13C
  14N(g,p)13C
Natural Abundance:
    17O: 0.038%
    18O: 0.205%
Expected Rates:
  17O(g,a)13C, depletion=5,000
  18O(g,a)14C, depletion=5,000
  14N(g,p)13C, Chamber eff.= 10-8
Notes: Interior Page Design 2

## Slide 45
Background from:
  17O(g,n)16O and secondary (n,n)
  neutron–nucleus elastic scattering
Background from Chamber glass:
  Neutron–nucleus elastic scattering from
  29Si(g,n)28Si
Cosmic–ray background:
  µ±–nuclear
  neutron–nuclear elastic scattering
Reject neutron events using
acoustic signal (100 suppression factor)
Notes: Interior Page Design 2

## Slide 46: Ion Energy Distributions
Use depleted N2O:
  17O depletion = 5,000
  18O depletion = 5,000
Suppress background with
Bubble Chamber thresholds
Threshold Efficiency (function
of superheat):
Particle | Efficiency
e± | <10-11
g | <10-11
14N(g,p)13C | <10-8
No acoustic cut
Notes: Interior Page Design 2

## Slide 47: Superheated Targets
List of superheated liquids to be used in experiment:
Readout:
  Fast Digital Camera
  Acoustic Signal to discriminate between neutron and alpha events
N2O Targets | 16O | 17O | 18O
Natural Target | 99.757% | 0.038% | 0.205%
16O Target |  | Depleted > 5,000 | Depleted > 5,000
17O Target |  | Enriched > 80% | <1.0%
18O Target |  | <1.0% | Enriched > 80%
Physics
Measure
Backgrounds
Notes: (g,p) events have acoustic signal similar to (g,a).

## Slide 48: Summary and Outlook
Test N2O Bubble Chamber at HIGS (Summer 2014)
Measure cross sections of 18O(g,a)14C and 17O(g,a)13C at HIGS (Fall 2014)
Test Bubble Chamber at JLab (October 2014, January 2015)
Run depleted N2O bubble chamber at JLab to measure 16O(g,a)12C
Beam issues:
  Design radiator, collimator, and dumps with GEANT4
  Simulate photon spectra with GEANT4 and FLUKA
  Deliver 8.5 MeV K.E. beam to 5D Spectrometer with <0.1% absolute energy uncertainty
Bubble Chamber issues:
  Study acoustic signal and measure neutron events suppression factor
  Deadtime measurements: use laser shutter to stop beam while chamber is not ready
  Measure O-isotopes depletion
Background tests:
  Measure cosmic–ray background
  Study chamber thresholds efficiency vs. superheat and measure g-rays suppression factor

## Slide 49: Backup Slides
Notes: Interior Page Design 1

## Slide 50: CO2 Superheated Liquid?
Similar Bubble Chamber operational
parameters as N2O
Natural Abundance: 13C: 1.07%
Depletion: 13C depletion=1,000
13C(g,n)12C Background
For comparison, 17O(g,n)16O
12C(g,2a)a Background
Notes: What is the expected background from 3-alpha?

## Slide 51: Water Superheated Liquid?
Etching of glass vessel by superheated H2O
  T = 250˚C
  P = 75 atm
Background from secondary neutron–nucleus elastic scattering by neutrons from d(g,n)p

## Slide 52
Rolfs and Rodney, 1988