## Slide 1: Cooler e-source Magnetized Beam LDRD Progress Report
June 1, 2017

## Slide 2
Magnetized Electron Source at GTS
Beamline
Gun Solenoid
Photocathode
Preparation
Chamber
Gun HV Chamber
Slit
Viewer Screen
Shield Tube
Viewer 3 Screen
Beam Dump

## Slide 4
Measuring Beam Magnetization
Use slit and viewscreens to measure mechanical angular momentum:
: solenoid field at photocathode
: laser rms size
Φ: rotation (sheering) angle

## Slide 5
0 G
at photocathode
1088 G
at photocathode

## Slide 6
Magnetized Beam Sizes
Solenoid Current (A) | Field (G) | σ1 (mm) | σ2 (mm) | σ3 (mm)
0 | 0 | 1.66 | 2.18 | 4.84
25 | 91 | 0.35 | 0.44 | 0.71
50 | 181 | 1.39 | 2.10 | 4.09
75 | 272 | 1.82 | 0.67 | 1.46
100 | 363 | 4.36 | 1.43 | 2.40
150 | 544 | 0.35 | 0.49 | 1.02
200 | 725 | 0.46 | 0.95 | 4.22
250 | 907 | 1.08 | 2.02 | 6.54
300 | 1088 | 1.88 | 3.28 | 7.11
All beamline solenoids are off

## Slide 7
Magnetized Beam Rotation Angles
Solenoid Current (A) | Field (G) | ɸ2 (deg) | ɸ3 (deg) | ɸ2- ɸ3 (deg)
0 | 0 | 0 | 0 | 0
25 | 91 | 3.6 | 18.9 | 15.3
50 | 181 | -1.7 | -5.7 | -4.0
75 | 272 | 5.8 | 11.7 | 5.9
100 | 363 | -3.6 | -7.5 | -3.9
150 | 544 | -30.1 | -54.1 | -24.0
200 | 725 | 5.7 | 8.8 | 3.1
250 | 907 | -4.1 | -8.5 | -4.4
300 | 1088 | -7.6 | -18.8 | -11.2

## Slide 8
High Current Magnetized Beam
1450 G
Delivered 0.5 mA
Plan for 5 mA by end of summer

## Slide 9
Summary of Progress
Submitted LDRD proposal for 3rd year funding
Delivered 0.5 mA magnetized beam with 1450 G on photocathode
Measured beam sizes and rotations with magnetic fields up to 1088 G on photocathode
Filed patent disclosure entitled “Non-invasive RF Cavity to Measure Beam Magnetization”

## Slide 10
Outlook: June – September
Measure beam sizes and rotations with magnetic fields up to 1450 G on photocathode
Simulation of magnetized beam sizes and rotation angles
Run 5 mA magnetized beam
Build and install a TE011 cavity at GTS to measure beam magnetization in collaboration with Brock and SRF Institute