## Slide 1: Measurement of 16O(g,a)12C with a Bubble Chamber and a Bremsstrahlung Beam at Jefferson Lab Injector
Riad Suleiman
January 9, 2014
Notes: Title Page

## Slide 2
B. DiGiovine
D. Henderson
R. J. Holt
K. E. Rehm
A. Sonnenschein
A. Robinson
C. Ugalde
J. Benesch
P. Degtiarenko
A. Freyberger
J. Grames
R. Kazimi
G. Kharashvili
D. Meekins
M. Poelker
Y. Roblin
R. Suleiman
V. Vylet
Notes: Interior Page Design 2

## Slide 3: Outline
Nucleosynthesis and the 12C(a,g)16O Reaction
Time-reversal Reaction: 16O(g,a)12C
Bubble Chamber Theory and Design
Work at HIGS
Experimental Setup at Jefferson Lab Injector
Bremsstrahlung Beam and Penfold-Leiss Unfolding
Statistical and Systematic Errors
Backgrounds and Ion Energy Distributions
Safety
Summary and Outlook
Notes: Interior Page Design 1

## Slide 4: Relative Abundance of Elements by Weight
Chart: Universe
| Hydrogen | Helium | Oxygen | Carbon | Other
Universe | 73.9 | 24 | 1 | 0.5 | 0.6
Chart: Human Body
| Oxygen | Carbon | Hydrogen | Nitrogen | Calcium | Phosphorus | Other
Human Body | 61 | 23 | 10 | 2.6 | 1.4 | 1.1 | 0.9
Notes: Interior Page Design 2

## Slide 5: Stellar Helium Burning
Rolfs and Rodney, 1988
Gamow window
Notes: Interior Page Design 2

## Slide 6: The 12C(a,g)16O Reaction
The “holy grail” of nuclear astrophysics
S. Woosley, A. Heger, Phys. Rep. 442 (2007) 269
Affects the synthesis of most of the elements of the periodic table
Sets the C to O ratio in the universe
Determines the minimum mass a star requires to become a supernova
Notes: Interior Page Design 2

## Slide 7: Stellar Carbon Burning
Helium burning stage of stellar evolution occurs at T=109 K
Most effective stellar energy, ECM = 0.3 MeV
He burning at cross section s ~ 10-17 barn
0.3
Stellar Energy
Notes: Interior Page Design 2

## Slide 8: Energy Level-diagram of 16O
No Resonances but interferences
Notes: Interior Page Design 2

## Slide 9
S(300)
Kunz 2001, Matei 2006

## Slide 10: Heroic efforts in search of the holy grail of astrophysics: 12C(a,g)16O
Expt | Beam current (mA) | Detector Effic. (%) | Target | Meas. Time (h)
Redder | 0.7 | Ge, 35 | 12C, ~3E18 | 900
Ouellet | 0.03 | Ge, 30 | 12C, 5E18 | 1950
Roters | 0.02 | BGO, 270 | 4He, 1E19 | 5000
Kunz | 0.45 | Ge, 100 | 12C, 3E18 | 700
EUROGAM | 0.34 | Ge, 70 | 1E19 | 2100
Luminosity ~ 1E34 cm-2s-1
Efficiency ~ 1E-3
16O(g,a)12C
Lum(HIgS) ~ 4E30 cm-2s-1
Lum(JLab) ~ 8E31 cm-2s-1
10 mA , top 100 keV
lg2/la2 ~ 60
Bubble chamber: solid angle x efficiency = 100%
4He(12C, 16O)g
12C(a,g)16O
Notes: Interior Page Design 2

## Slide 11: Astrophysical S-Factor 12C(a,g)16O
Author | S(300keV) (keV-b)
Buchmann (2005) | 102-198
Caughlan and Fowler (1988) | 120-220
Hammer (2005) | 162+-39
Stellar helium burning at E=300 keV
Notes: Interior Page Design 2

## Slide 12: Time Reversal Reaction
12C
a
16O
g
Notes: Interior Page Design 2

## Slide 13: (g,a) and (a,g) – Reciprocity Relation
A(α, γ)B:
σ(γ,α) is over two orders of magnitude larger than σ(α, γ)
Notes: Interior Page Design 2

## Slide 14: New Approach: Inverse Reaction + Bubble Chamber
 + 16O → 12C + 
beam
target
signal
Monochromatic g beam at HIgS
~ 107-8 g/s
Bremsstrahlung at JLab
~ 4x109 g/s (top 250 keV)
Extra gain (x100) by measuring time inverse reaction
Target density up to x106 higher than conventional targets
Superheated liquid will nucleate from a and 12C recoils
Electromagnetic debris (degraded electrons and gammas, or positrons) that escape the collimator/electron beam do NOT trigger nucleation (detector is insensitive to g-rays by at least 1 part in 1011).
Notes: Interior Page Design 2

## Slide 15: Bubble Chamber Theory and Design
Donald Glaser, 86, won Nobel for inventing chamber to detect subatomic particles (1960)
Dark Matter Search
COUPP PRL106,021203(2011)
PICASSO PLB,682,185(2009)
SIMPLE PRL105, 211301(2010)
Superheat
Notes: Interior Page Design 2

## Slide 16: Bubble Growth and Quenching
Dt = 10 ms
19F(g,a)15N in R134a
Notes: Interior Page Design 2

## Slide 17: Acoustic Signal: Particle ID
COUPP, FNAL, courtesy of A. Sonnenschein
Suppress neutron events by x500 from acoustic signal – FNAL dark matter bubble chambers
Notes: What about proton events, i.e, (g,p)?

## Slide 18
N2O thresholds, Superheat = 3.3 OC, Eg=8.5 MeV

## Slide 19: Efficiency Curve
N2O efficiency curve, HIGS April 2013. Eg = 9.7 MeV
g+14N and g+16O
g+16O
Notes: Interior Page Design 2

## Slide 20: Bubble Chamber at HIGS
High Intensity Gamma Source (HIGS) at Duke University
g-rays generated by Compton backscattering of free-electron-laser (FEL) light from high-energy electron beam bunches

## Slide 21: Measuring 19F(g,a)15N at HIGS
C4F10 Bubble Chamber
  T = 310 K
  P = 160 kPa – 900 kPa
2 Fast Cameras
Notes: Interior Page Design 2

## Slide 22
Notes: Interior Page Design 2

## Slide 23: Bremsstrahlung Background at HIGS
Vacuum: 2x10-10 Torr
Residual Gas: Z = 10
Electron Beam Energy: 400 MeV
Electron Beam Current: 41 mA
Interaction Length: 35 m
Strong Bremsstrahlung
Background
Notes: Calculate the Bremsstrahlung spectrum for HIGS beam using GEANT4

## Slide 24: Recent Work
N2O Bubble Chamber
First g+O→α+C bubble
April 2013
Notes: Interior Page Design 2

## Slide 25: Superheated Targets
List of superheated liquids to be used in the experiment:
Readout:
  Optical Camera
  Acoustic Signal to discriminate between (g,a) and (g,n) events
N2O Targets | 16O | 17O | 18O
Natural Target | 99.757% | 0.038% | 0.205%
16O Target |  | Depleted > 5,000 | Depleted > 5,000
17O Target |  | Enriched > 80% | <1.0%
18O Target |  | <1.0% | Enriched > 80%
Notes: Interior Page Design 2

## Slide 26: Experimental Setup
BCM
5 MeV
Dipole
2D
Spectrometer
5D Spectrometer
Bubble
Chamber
location
Mott Polarimeter
Notes: Interior Page Design 2

## Slide 27
5D Spectrometer
Bubble Chamber at HIGS
Photon Beam
Entrance
Notes: Interior Page Design 2

## Slide 28: Beamline
2 Superharps to measure beam profile and absolute beam position
New Fast Valve to protect from vacuum failure in front of ¼ Cryo-unit
Replace Dipole
Magnet
Notes: Interior Page Design 2

## Slide 29: Schematics
Electron K.E.
3.0 – 8.5 MeV
0.01 – 100 µA
Al Beam Pipe
Cu Radiator
0.02 mm
Cu Electron Dump
Sweep Magnet
Bubble Chamber
Superheated N2O
3 cm long
15°C, 60 atm
Al Photon Dump
10 cm long
20 cm diameter
20 cm
50 cm
Cu Vacuum Window 10 mil
Cu Photon
Collimator
Cu Inner
Pipe
Radiator motion and Sweep Dipole current must be in FSD
BCM0L02 and Electron Dump in Beam Loss Accounting (BLA)
Power deposited in radiator (100 µA and 8.5 MeV) :
  0.02 mm: Energy loss = 21 keV, P = 2.1 W
  0.10 mm: Energy loss = 112 keV, P = 11 W
Pure Copper and Aluminum (high neutron threshold):
  63C(g,n) threshold = 10.86 MeV
  27Al(g,n) threshold = 13.06 MeV
Notes: Interior Page Design 2

## Slide 30: Beam Requirements
Beam Properties at Radiator:
PEPPo achieved p=8.25 MeV/c or K.E.=7.75 MeV. Maximum stable ¼- cryounit cavity gradients achieved: 8.4 MV/m and 6.1 MV/m (7.25 MV/m average). Vacuum in the beam line indicates that field emission and desorbed gas are the most problematic, but improve with processing.
Helium process the ¼-cryounit
Beam Kinetic Energy, (MeV) | 7.9 – 8.5
Beam Current (µA) | 0.01 – 100
Absolute Beam Energy | <0.1%
Relative Beam Energy | <0.02%
Energy Resolution (Spread), σT /T | 0.06%
Beam Size, σx,y (mm) | 1 – 2
Notes: Interior Page Design 2

## Slide 31: Absolute Beam Energy
BPM
5 MeV
Dipole
25°
Electron Beam
Momentum
Notes: Interior Page Design 2

## Slide 32
Goal:
  Jay Benesch designed and now fabricating higher quality dipole (more uniformity, higher field)
  New Hall Probe: 0.01% accuracy, resolution to 2 ppm, and a temperature stability of 10 ppm/°C
  Relative beam energy error: <0.02%
Parameter | Term | Now | Goal
Dipole – linearity | δB/B | 0.25% | 0.02%
Dipole – spatial | δBL/BL | 0.10% | 0.02%
Dipole – reproduce | δB/B | 0.10% | 0.02%
Dipole – power supply | δI/I | 0.20% | 0.02%
Position – surveys | δθ/θ | 0.01% | 0.01%
Position – BPM calibration | δθ/θ | 0.05% | 0.05%
Stray magnetic field | δθ/θ | 0.05% | 0.05%
TOTAL | δP/P | 0.36% | <0.10%
Notes: Interior Page Design 2

## Slide 34: Bremsstrahlung Beam
Use both GEANT4 and FLUKA to calculate Bremsstrahlung spectra
Monte Carlo simulation of bremsstrahlung at radiotherapy energies is well studied, accuracy: 5%
Bremsstrahlung Peaks
16O(g,a)12C is ideal case for Bremsstrahlung beam and Penfold – Leiss Unfolding :
  Very steep; only photons near endpoint contribute to yield
  No-structure (resonances)

## Slide 35: GEANT4 Simulation
Both GEANT4 and FLUKA use models that calculate wrong photo–nuclear cross sections. Both do not allow for user’s cross sections.
  Use GEANT4 and FLUKA to produce the photon spectrum impinging on the super heated liquid.
  Fold the above photon spectrum with our cross sections in stand-alone codes.
Use GEANT4 to design Radiator/Collimator/Dump
Geometry in GEANT4:
Notes: Interior Page Design 2

## Slide 36: Penfold-Leiss Cross Section Unfolding
Measure Yields at: where,
The solution can be written in two forms:
Or, Matrix form:

## Slide 37: Statistical Error Propagation
With:
Then:
Note:
In case of background Subtraction

## Slide 38
Where:
For mono-chromatic beam
Although,

## Slide 39: Results
Radiator Thickness = 0.02 mm
Bubble Chamber Thickness = 3.0 cm. Number of 16O nuclei = 3.474e22 /cm2
Background subtraction of 18O(γ,α)14C . 17O(γ,n)16O: Still to do
Electron Beam K. E. | Beam Current (µA) | Time (hour) | yi | dyi (no bg) | dyi/yi (no bg, %) | dyi (with bg) | dyi/yi (with bg, %)
7.9 | 100 | 100 | 545 | 23 | 4.2 | 134 | 24.6
8.0 | 100 | 20 | 581 | 24 | 4.1 | 77 | 13.3
8.1 | 80 | 10 | 852 | 29 | 3.4 | 60 | 7.0
8.2 | 20 | 10 | 634 | 25 | 3.9 | 40 | 6.3
8.3 | 10 | 10 | 812 | 28 | 3.4 | 39 | 4.8
8.4 | 4 | 10 | 746 | 27 | 3.6 | 36 | 4.8
8.5 | 2 | 10 | 763 | 28 | 3.7 | 32 | 4.2
Notes: Interior Page Design 2

## Slide 40: Systematic Error Propagation
For absolute beam energy uncertainty of δE (= 0.1%) and zero relative beam energy uncertainty:
Ei (MeV) | dyi/yi (%) | dσi/σi (%)
7.9 | 12.5 | 12.6
8.0 | 10.8 | 10.5
8.1 | 9.3 | 9.1
8.2 | 8.0 | 7.1
8.3 | 7.0 | 6.3
8.4 | 6.3 | 5.8
8.5 | 5.6 | 5.2
This is the cross section dependence on energy
Accounted for dNij due to energy error when calculating dyi

## Slide 41
With:
Then:

## Slide 42
Where:
Note: Correlation Coefficient =1
No point-to-point systematic

## Slide 43: Systematic Error Propagation
No point-to-point systematic

## Slide 44: Other Relative Systematic Errors
Then:
Simulation
Beam Current, δI/I | 3%
Photon Flux, δφ/φ | 5%
Radiator Thickness, δR/R | 3%
Bubble Chamber Thickness, δT/T | 3%
Bubble Chamber Efficiency, ε | 5%

## Slide 45
Electron Beam K. E. | Cross Section (nb) | Stat Error (no bg, %) | Stat Error (with bg, %)
7.9 | 0.046 | 4.4 | 24.5
8.0 | 0.185 | 6.0 | 20.7
8.1 | 0.58 | 6.3 | 14.7
8.2 | 1.53 | 8.2 | 13.8
8.3 | 3.49 | 9.1 | 13.3
8.4 | 7.2 | 10.6 | 13.8
8.5 | 13.6 | 12.2 | 14.8
Electron Beam K. E. | Cross Section (nb) | Sys Error (Energy, %) | Sys Error (Total, %)
7.9 | 0.046 | 12.5 | 15.3
8.0 | 0.185 | 10.2 | 13.5
8.1 | 0.58 | 8.3 | 12.2
8.2 | 1.53 | 7.0 | 11.4
8.3 | 3.49 | 6.0 | 10.7
8.4 | 7.2 | 5.3 | 10.5
8.5 | 13.6 | 4.7 | 10.1
Note: Relative systematic errors do not get amplified in PL Unfolding
Notes: Get the right figure.

## Slide 46: 12C(α, γ)16O S-Factor
Statistical Error: dominated by background subtraction from 18O(γ,α)14C (depletion = 5,000)
SE1(300 keV) = 74±21 keV b
Electron Beam K. E. | Gamma Energy (MeV) | ECM (MeV) | Cross Section (nb) | SE1 Factor (keV b) | Stat Error (%) | Sys Error (Total, %)
7.9 | 7.85 | 0.69 | 0.046 | 62.2 | 24.5 | 15.3
8.0 | 7.95 | 0.79 | 0.185 | 48.7 | 20.7 | 13.5
8.1 | 8.05 | 0.89 | 0.58 | 41.8 | 14.7 | 12.2
8.2 | 8.15 | 0.99 | 1.53 | 35.5 | 13.8 | 11.4
8.3 | 8.25 | 1.09 | 3.49 | 32.0 | 13.3 | 10.7
8.4 | 8.35 | 1.19 | 7.2 | 28.8 | 13.8 | 10.5
8.5 | 8.45 | 1.29 | 13.6 | 26.3 | 14.8 | 10.1

## Slide 47: Backgrounds
Background from oxygen
isotopes and nitrogen in N2O:
  18O(g,a)14C
  17O(g,a)13C
  14N(g,p)13C
Natural Abundance:
    17O: 0.038%
    18O: 0.205%
Expected Rates:
  17O(g,a)13C, depletion=5,000
  18O(g,a)14C, depletion=5,000
  14N(g,p)13C, detection eff.= 10-8
Notes: Interior Page Design 2

## Slide 48
Background from:
  17O(g,n)16O and secondary (n,n)
  neutron–nucleus elastic scattering
Cosmic–ray background:
  µ±–nuclear
  neutron–nuclear elastic scattering
Reject neutron background using
the acoustic signal (500 factor)
Notes: Interior Page Design 2

## Slide 49: Ion Energy Distributions
Suppress background
with Bubble Chamber threshold
Calculated with Depletion:
  17O depletion = 5,000
  18O depletion = 5,000
Threshold Efficiency (function
of superheat):
Particle | Efficiency
e± | <10-11
g | <10-11
(g,n) | 2x10-3
Notes: Interior Page Design 2

## Slide 50
Notes: Interior Page Design 2

## Slide 51
COUPP exp. FNAL
Gamma suppression

## Slide 52: Bubble chamber basics

## Slide 54: C4F10 bubble chamber for JLab
Target cell
C4F10
180 psi max
Pressure amplifier
Accumulator
Fast CCD camera housing
Buffer fluid fill valve
Target fill port
Buffer fluid
Photon beam
entrance window
Secondary
containment vessel
N2 pressure inlet
Courtesy of B. DiGiovine
Instrumentation and
Relief valve manifold

## Slide 55: Safety
Super heated liquid N2O, Nitrous oxide (laughing gas)
  At room temperature, it is a colorless, non-flammable gas, with a slightly sweet odor and taste
High pressure system:
  Design Authority: Dave Meekins
  T =
  P =
  Stored energy (N2O is a gas)
Buffer liquid: Mercury
  Closed system
  Volume: 135 mL
0
OX
0
2
0
0
3
Notes: Interior Page Design 2

## Slide 56: Summary and Outlook
Test N2O Bubble Chamber at HIGS (February 2014)
Perform 18O(g,a)14C and 17O(g,a)13C experiments at HIGS (Summer 2014)
Test Bubble Chamber at JLab with Bremsstrahlung beam (October 2014)
If successful, run depleted N2O bubble chamber at JLab 16O(g,a)12C
Bubble Chamber issues:
  Piezo–electric acoustical signal
  Deadtime study (now t ± dt = 10.0 ± 0.9 s)
  Measure O-isotope depletion
Background tests:
  Measure cosmic–ray background
  Study chamber efficiency vs. superheat
Notes: Interior Page Design 1

## Slide 57: Backup Slides
Notes: Interior Page Design 1

## Slide 58: Cost Estimate
New beamline components:
  New Dipole Magnet and Hall Probe
  2 Super Harps
  Fast Valve
Summary of labor cost by group:
Group | Labor
Survey & Alignment | 3 wks x 2
Magnet Test | 1 wk x 2
Engineering Design | 16 wks
Software | 3 wks x 2
EES | 6 wk x 2
EH&Q | 4 wks
Notes: Interior Page Design 1

## Slide 59
Item | Material Procurement | Shop | Labor
New Dipole Magnet | Dipole Magnet ($8,000) Hall Probe System ($10,000) |  | Design (2 week) Mapping (1 week) EESDC (1 week) Alignment (2 days)
New Beamline | 2 Super Harps (20,000) Fast Valve ($23,000) | Pipes + Pedestals ($20,000) | Design (6 weeks) Alignment (1 week) Software (6 weeks) EES (6 weeks)
Radiator (cooled ladder, FSD) | 0.02 and 0.10 mm Cu foils ($2,000) | $4,000 | Design (2 week) Alignment (2 days)
Sweep Dipole |  |  | 
Electron Dump | Pure Cu ($5,000) | Dump + Pipes ($15,000) | Design (4 weeks) Alignment (1 day)
Cu Collimator | Pure Cu ($5,000) | Collimator + Stand ($5,000) | Design (1 week) Alignment (1 day)
Photon Dump & Stand | Pure Al ($3,000) | $4,000 | Design (1 week) Alignment (1 day)
Safety Review |  |  | 4 weeks
Install |  |  | 6 weeks
Bubble Chamber |  |  | Alignment (1 week)
Total | $76,000 | $48,000 | $80,000
Indirect G&A (55.65%) | $42,300 | $26,400 | $42,500
Indirect Stat & Fringe (57.15%) |  |  | $45,700
Total | $118,300 | $74,400 | $168,200
Notes: Accelerator is paying for magnet and Hall Probe System.
Accelerator will pay for Fast Valve and its electronics.

## Slide 60: CO2 Superheated Liquid?
Natural Abundance: 13C: 1.07%
Depletion: 13C depletion=1,000
13C(g,n)12C Background
For comparison, 17O(g,n)16O
12C(g,2a)a Background
Notes: The acoustic signal will suppress neutron events (?). What is the expected background from 3-alpha?

## Slide 61: Water Superheated Liquid?
etching of glass due to HF.
With the Mercury as a buffer liquid, can we go back to water?