## Slide 1: Measurement of 16O(g,a)12C with a Bubble Chamber and a Bremsstrahlung Beam at Jefferson Lab Injector
Riad Suleiman
January 9, 2014
Notes: Title Page

## Slide 2
B. DiGiovine
D. Henderson
R. J. Holt
K. E. Rehm
A. Sonnenschein
A. Robinson
C. Ugalde
J. Benesch
P. Degtiarenko
A. Freyberger
J. Grames
G. Kharashvili
D. Meekins
M. Poelker
Y. Roblin
R. Suleiman
C. Tennant
V. Vylet
https://wiki.jlab.org/ciswiki/index.php/Bubble_Chamber
Notes: Interior Page Design 2

## Slide 3: Outline
Nucleosynthesis and the 12C(a,g)16O Reaction
Time-reversal Reaction: 16O(g,a)12C
Bubble Chamber Theory and Design
Work at HIGS
Experimental Setup at Jefferson Lab Injector
Bremsstrahlung Beam and Penfold-Leiss Unfolding
Statistical and Systematic Errors
Backgrounds and Ion Energy Distributions
Safety
Summary and Outlook
Notes: Interior Page Design 1

## Slide 4: Relative Abundance of Elements by Weight
Chart: Universe
| Hydrogen | Helium | Oxygen | Carbon | Other
Universe | 73 | 23 | 1 | 0.5 | 0.6
Chart: Human Body
| Oxygen | Carbon | Hydrogen | Nitrogen | Calcium | Phosphorus | Other
Human Body | 61 | 23 | 10 | 2.6 | 1.4 | 1.1 | 0.9
Notes: The Pie Chart of “Universe” is not taking decimal numbers.

## Slide 5: Stellar Helium Burning
Helium Reactions:
  a + a ↔ 8Be (T½ ≈ 10-16 s)
  a + 8Be → 12C + g
  a + 12C → 16O +g
  (slow, otherwise no 12C remains)
  a + 16O → 20Ne + g (very slow)
a + 12C burning at very small cross section s ≈ 10-17 barn
Currently, reaction rate error is large (±35%)
Thermonuclear reaction rate involving two nuclei is:
Only narrow energy range is important (Gamow Peak)
Goal <±10%
Notes: Explain the Be dip and C/O ratio.

## Slide 6: The 12C(a,g)16O Reaction
The holy grail of nuclear astrophysics
S. Woosley, A. Heger, Phys. Rep. 442 (2007) 269
Affects the synthesis of most of the elements of the periodic table
Sets the N(12C)/N(16O) (≈0.4) ratio in the universe
Determines the minimum mass a star requires to become a supernova
Notes: Interior Page Design 2

## Slide 7: The Gamow Peak
Narrow energy range where thermonuclear reactions is most likely to occur in stellar plasma is a product of two distributions:
  Maxwell-Boltzmann energy distribution with e-E/kBT
  Penetration through Coulomb barrier with e-b/E½
For a + 12C (Z1=2, Z2=6, A=3),
and stellar T=200 106 K:
  Gamow Peak, E0 ≈ 300 keV, W ≈ 50 keV
  Maximum of Maxwell–Boltzmann
  energy distribution, kBT = 17 keV
keV
keV

## Slide 8: a + 12C Radiative Capture
Transition → 0 (E1) | SE1(300) = 1–288 keV b
Transition → 0 (E2) | SE2(300) = 7–120 keV b
Total | Stot(300) = 40–430 keV b
s(E0) is dominated by p–wave (E1) and d–wave (E2) radiative capture to (Jp=0+) 16O ground state
Two bound states, at 6.92 MeV (Jp=2+) and 7.12 MeV (Jp=1–), with sub–threshold resonances at ER=-0.245 and -0.045 MeV, provide most of s(E0) through their finite widths
Distinguish E1 and E2 by measuring g angular distributions
E1
E2
Notes: Interior Page Design 2

## Slide 9: Heroic efforts in search of 12C(a,g)16O
Previous Experiments:
  Direct Techniques:
    Helium ions on carbon target: 12C(a,g)16O
    Carbon ions on helium gas: 4He(12C,16O)g
  Indirect Methods:
    b–delayed a decay of 16N (Jp=2–, T½=7.13 s, BR=0.12%)
    16N → b– + 16O* (Jp=1–) → a + 12C
    Elastic a – 12C scattering
Experiment | Beam Current (mA) | Target (nuclei/cm2) | Time (h)
Redder | 0.7 | 12C, 3 1018 | 900
Ouellet | 0.03 | 12C, 5 1018 | 1950
Roters | 0.02 | 4He, 1 1019 | 5000
Kunz | 0.5 | 12C, 3 1018 | 700
EUROGAM | 0.34 | 12C, 1 1019 | 2100
GANDI | 0.6 (?) | 12C, 2 1018 | ?
Schürmann | 0.01 | 4He, 4 1017 | ?
Plag | 0.005 | 12C, 6 1018 | 278
Notes: GANDI is written in German, the reference is on the wiki.

## Slide 10: Astrophysical S-Factor 12C(a,g)16O
R-matrix Extrapolation to stellar helium burning at E = 300 keV
Define S-Factor to remove both 1/E dependence of nuclear cross sections and Coulomb barrier transmission probability:
Author | S(300) (keV b)
Schürmann (2012) | 161±19+8-2
Hammer (2005) | 162±39
Kunz (2001) | 165±50

## Slide 11
A(a, g)B:
σ(g,a) is over two orders of magnitude larger than σ(a, g)
MeV
MeV
Reciprocity Relation: (g,a) and (a,g)
Notes: Interior Page Design 2

## Slide 12: Time Reversal Reaction
12C
a
16O
g
Bubble Chamber experiment measures total cross section, E1 + E2.
We can separate E1 and E2 if we use linearly polarized g but cannot measure a and 12C angular distribution
Stellar helium burning at E = 300 keV
Notes: Is the statement in green correct?

## Slide 13: New Approach: Reversal Reaction + Bubble Chamber
 + 16O → 12C + 
beam
target
signal
Monochromatic g beam at HIGS ≈ 107-8 g/s
Bremsstrahlung at
JLab ≈ 109 g/s (top 250 keV)
Extra gain (factor of 100) by measuring time reversal reaction
Target density up to 104 higher than conventional targets. Number of 16O nuclei = 3.5 1022 /cm2 (3.0 cm cell)
Solid Angle and Detector Efficiency = 100%
Superheated liquid will nucleate from a and 12C recoils
Electromagnetic debris (electrons and gammas, or positrons) do NOT trigger nucleation (detector is insensitive to g-rays by at least 1 part in 1011).
Notes: Interior Page Design 2

## Slide 14: The Bubble Chamber
Donald Glaser won Nobel Prize for inventing chamber to detect particles (1960)
Now being used in Dark Matter Search Experiments: COUPP, PICASSO, SIMPLE
Superheat Preparation:
  Liquid is pressurized at ambient temperature (1 to 2)
  Then pressure is kept constant while temperature is
  increased to above boiling point (2 to 3)
  Finally pressure is slowly released while keeping
  temperature constant (3 to 4)
  At this point (4), water is still liquid but now superheated
Bubble Growth and Quenching:
  A small disturbance will induce vaporization
  When this happens , bubble growth process needs to be
  controlled by increasing pressure (4 to 3). It takes
  about 10 seconds for liquid to return to a stable state
  Superheat is then returned into system by releasing
  pressure again (3 to 4), and cycle is repeated for each bubble event
Superheat
Notes: The superheat is changed by changing the pressure not the temperature.

## Slide 15: Bubble Growth and Quenching
Fast Camera: Dt = 10 ms
19F(g,a)15N event in C4F10
Notes: Is that a writing on the glass?

## Slide 16: Bubble Chamber Principle
Gamma suppression of 1011
Nuclear recoil threshold

## Slide 17: Acoustic Signal: Particle ID
COUPP, FNAL, courtesy of A. Sonnenschein
Suppress neutron events by x500 from acoustic signal
a should be louder
Notes: What about proton events, i.e, (g,p)?

## Slide 18: Efficiency Curve
g+14N and g+16O
g+16O
N2O efficiency curve,
HIGS April 2013,
Eg = 9.7 MeV
N2O thresholds, Superheat = 3.3˚C, Eg=8.5 MeV
Notes: Interior Page Design 2

## Slide 19: Bubble Chamber at HIGS
High Intensity Gamma Source (HIGS) at Duke University
g-rays generated by Compton backscattering of free-electron-laser (FEL) light from high-energy electron beam bunches

## Slide 20: Measuring 19F(g,a)15N at HIGS
C4F10 Bubble Chamber
  T = 30˚C
  P = 3 atm
2 Fast Cameras
Notes: Interior Page Design 2

## Slide 21
Notes: Is that a wire in the background of the bubble photo on the left?

## Slide 22: Bremsstrahlung Background at HIGS
Vacuum: 2x10-10 Torr
Residual Gas: Z = 10
Electron Beam Energy: 400 MeV
Electron Beam Current: 41 mA
Interaction Length: 35 m
Strong Bremsstrahlung
Background
Notes: Calculate the Bremsstrahlung spectrum for HIGS beam using GEANT4

## Slide 23: Recent Work
N2O Bubble Chamber:
first g+O→α+C bubble
April 2013
Notes: Why the bubble in N2O rises? But not in C4F10. And why the liquid is cloudy for N2O? What was the buffer liquid?

## Slide 24: Superheated Targets
List of superheated liquids to be used in the experiment:
Readout:
  Optical Camera
  Acoustic Signal to discriminate between (g,a) and (g,n) events
N2O Targets | 16O | 17O | 18O
Natural Target | 99.757% | 0.038% | 0.205%
16O Target |  | Depleted > 5,000 | Depleted > 5,000
17O Target |  | Enriched > 80% | <1.0%
18O Target |  | <1.0% | Enriched > 80%
Notes: What about (g,p) events?

## Slide 25: Experimental Setup at JLab Injector
BCM
5 MeV
Dipole
2D
Spectrometer
5D Spectrometer
Bubble
Chamber
location
Mott Polarimeter
Notes: Interior Page Design 2

## Slide 26
5D Spectrometer
Bubble Chamber at HIGS
Photon Beam
Entrance
Notes: Interior Page Design 2

## Slide 27: Beamline
2 Superharps to measure beam profile and absolute beam position
New Fast Valve to protect from vacuum failure in front of ¼ Cryo-unit
Replace Dipole
Magnet
Notes: Interior Page Design 2

## Slide 28: Schematics
Electron K.E.
3.0 – 8.5 MeV
0.01 – 100 µA
Al Beam Pipe
Cu Radiator
0.02 mm
Cu Electron Dump
Sweep Magnet
Bubble Chamber
Superheated N2O
3 cm long
15°C, 60 atm
Al Photon Dump
10 cm long
20 cm diameter
20 cm
50 cm
Cu Vacuum Window 10 mil
Cu Photon
Collimator
Cu Inner
Pipe
Radiator motion and Sweep Dipole current must be in FSD
BCM0L02 and Electron Dump in Beam Loss Accounting (BLA)
Power deposited in radiator (100 µA and 8.5 MeV) :
  0.02 mm: Energy loss = 21 keV, P = 2.1 W
  0.10 mm: Energy loss = 112 keV, P = 11 W
Pure Copper and Aluminum (high neutron threshold):
  63C(g,n) threshold = 10.86 MeV
  27Al(g,n) threshold = 13.06 MeV
Use GEANT4 to optimize this region
Notes: Interior Page Design 2

## Slide 29: Beam Requirements
Beam Properties at Radiator:
PEPPo achieved p=8.25 MeV/c or K.E.=7.75 MeV. Maximum stable ¼- cryounit cavity gradients achieved: 8.4 MV/m and 6.1 MV/m (7.25 MV/m average). Vacuum in the beam line indicates that field emission and desorbed gas are the most problematic, but improve with processing.
Helium process the ¼-cryounit
Beam Kinetic Energy, (MeV) | 7.9 – 8.5
Beam Current (µA) | 0.01 – 100
Absolute Beam Energy | <0.1%
Relative Beam Energy | <0.02%
Energy Resolution (Spread), σT /T | 0.06%
Beam Size, σx,y (mm) | 1 – 2
Notes: Interior Page Design 2

## Slide 30: Absolute Beam Energy
BPM
5 MeV
Dipole
Electron Beam
Momentum
Notes: Interior Page Design 2

## Slide 31
Goal:
  Jay Benesch designed and now fabricating higher quality dipole (more uniformity, higher field)
  New Hall Probe: 0.01% accuracy, resolution to 2 ppm, and a temperature stability of 10 ppm/°C
  Relative beam energy error: <0.02%
Parameter | Term | Now | Goal
Dipole – linearity | δB/B | 0.25% | 0.02%
Dipole – spatial | δBL/BL | 0.10% | 0.02%
Dipole – reproduce | δB/B | 0.10% | 0.02%
Dipole – power supply | δI/I | 0.20% | 0.02%
Position – surveys | δθ/θ | 0.01% | 0.01%
Position – BPM calibration | δθ/θ | 0.05% | 0.05%
Stray magnetic field | δθ/θ | 0.05% | 0.05%
TOTAL | δP/P | 0.36% | <0.10%
Notes: Interior Page Design 2

## Slide 32: Bremsstrahlung Beam
Use both GEANT4 and FLUKA to calculate Bremsstrahlung spectra
Monte Carlo simulation of bremsstrahlung at radiotherapy energies is well studied, accuracy: 5%
Bremsstrahlung Peaks
16O(g,a)12C is ideal case for Bremsstrahlung beam and Penfold – Leiss Unfolding :
  Very steep; only photons near endpoint contribute to yield
  No-structure (resonances)

## Slide 33: GEANT4 Simulation
Both GEANT4 and FLUKA use models that calculate wrong photo–nuclear cross sections. Both do not allow for user’s cross sections.
  Use GEANT4 and FLUKA to produce the photon spectrum impinging on the superheated liquid.
  Fold the above photon spectrum with our cross sections in stand-alone codes.
Use GEANT4 to design radiator, collimator, and dumps
Geometry in GEANT4:
Notes: Add GEANT4 geometry figure.

## Slide 34: Penfold-Leiss Cross Section Unfolding
Measure Yields at: where,
The solution can be written in two forms:
Or, Matrix form:

## Slide 35: Statistical Error Propagation
With:
Then:
Note:
In case of background Subtraction

## Slide 36
Where:
For mono-chromatic beam
Although,

## Slide 37: Results
Radiator Thickness = 0.02 mm
Bubble Chamber Thickness = 3.0 cm. Number of 16O nuclei = 3.474e22 /cm2
Background subtraction of 18O(γ,α)14C . 17O(γ,n)16O: Still to do
Electron Beam K. E. | Beam Current (µA) | Time (hour) | yi | dyi (no bg) | dyi/yi (no bg, %) | dyi (with bg) | dyi/yi (with bg, %)
7.9 | 100 | 100 | 545 | 23 | 4.2 | 134 | 24.6
8.0 | 100 | 20 | 581 | 24 | 4.1 | 77 | 13.3
8.1 | 80 | 10 | 852 | 29 | 3.4 | 60 | 7.0
8.2 | 20 | 10 | 634 | 25 | 3.9 | 40 | 6.3
8.3 | 10 | 10 | 812 | 28 | 3.4 | 39 | 4.8
8.4 | 4 | 10 | 746 | 27 | 3.6 | 36 | 4.8
8.5 | 2 | 10 | 763 | 28 | 3.7 | 32 | 4.2
Notes: Interior Page Design 2

## Slide 38: Systematic Error Propagation
For absolute beam energy uncertainty of δE (= 0.1%) and zero relative beam energy uncertainty:
Ei (MeV) | dyi/yi (%) | dσi/σi (%)
7.9 | 12.5 | 12.6
8.0 | 10.8 | 10.5
8.1 | 9.3 | 9.1
8.2 | 8.0 | 7.1
8.3 | 7.0 | 6.3
8.4 | 6.3 | 5.8
8.5 | 5.6 | 5.2
This is the cross section dependence on energy
Accounted for dNij due to energy error when calculating dyi

## Slide 39
With:
Then:

## Slide 40
Where:
Note: Correlation Coefficient =1
No point-to-point systematic

## Slide 41: Systematic Error Propagation
No point-to-point systematic

## Slide 42: Other Systematic Errors
Then:
Simulation
Beam Current, δI/I | 3%
Photon Flux, δφ/φ | 5%
Radiator Thickness, δR/R | 3%
Bubble Chamber Thickness, δT/T | 3%
Bubble Chamber Efficiency, ε | 5%

## Slide 43
Electron Beam K. E. | Cross Section (nb) | Stat Error (no bg, %) | Stat Error (with bg, %)
7.9 | 0.046 | 4.4 | 24.5
8.0 | 0.185 | 6.0 | 20.7
8.1 | 0.58 | 6.3 | 14.7
8.2 | 1.53 | 8.2 | 13.8
8.3 | 3.49 | 9.1 | 13.3
8.4 | 7.2 | 10.6 | 13.8
8.5 | 13.6 | 12.2 | 14.8
Electron Beam K. E. | Cross Section (nb) | Sys Error (Energy, %) | Sys Error (Total, %)
7.9 | 0.046 | 12.5 | 15.3
8.0 | 0.185 | 10.2 | 13.5
8.1 | 0.58 | 8.3 | 12.2
8.2 | 1.53 | 7.0 | 11.4
8.3 | 3.49 | 6.0 | 10.7
8.4 | 7.2 | 5.3 | 10.5
8.5 | 13.6 | 4.7 | 10.1
Note: Relative systematic errors do not get amplified in PL Unfolding

## Slide 44: JLab Projected 12C(a,g)16O S-Factor
Statistical Error: dominated by background subtraction from 18O(g,a)14C (depletion = 5,000)
Electron Beam K. E. | Gamma Energy (MeV) | ECM (MeV) | Cross Section (nb) | Stot Factor (keV b) | Stat Error (%) | Sys Error (Total, %)
7.9 | 7.85 | 0.69 | 0.046 | 62.2 | 24.5 | 15.3
8.0 | 7.95 | 0.79 | 0.185 | 48.7 | 20.7 | 13.5
8.1 | 8.05 | 0.89 | 0.58 | 41.8 | 14.7 | 12.2
8.2 | 8.15 | 0.99 | 1.53 | 35.5 | 13.8 | 11.4
8.3 | 8.25 | 1.09 | 3.49 | 32.0 | 13.3 | 10.7
8.4 | 8.35 | 1.19 | 7.2 | 28.8 | 13.8 | 10.5
8.5 | 8.45 | 1.29 | 13.6 | 26.3 | 14.8 | 10.1
Bubble Chamber experiment measures total S-Factor, SE1 + SE2

## Slide 45: Backgrounds
Background from oxygen
isotopes and nitrogen in N2O:
  18O(g,a)14C
  17O(g,a)13C
  14N(g,p)13C
Natural Abundance:
    17O: 0.038%
    18O: 0.205%
Expected Rates:
  17O(g,a)13C, depletion=5,000
  18O(g,a)14C, depletion=5,000
  14N(g,p)13C, detection eff.= 10-8
Notes: Interior Page Design 2

## Slide 46
Background from:
  17O(g,n)16O and secondary (n,n)
  neutron–nucleus elastic scattering
Cosmic–ray background:
  µ±–nuclear
  neutron–nuclear elastic scattering
Reject neutron background using
the acoustic signal (500 factor)
Notes: Interior Page Design 2

## Slide 47: Ion Energy Distributions
Suppress background
with Bubble Chamber threshold
Calculated with Depletion:
  17O depletion = 5,000
  18O depletion = 5,000
Threshold Efficiency (function
of superheat):
Particle | Efficiency
e± | <10-11
g | <10-11
(g,n) | 2x10-3
Notes: Interior Page Design 2

## Slide 48
Notes: Interior Page Design 2

## Slide 49: Safety
Super heated liquid N2O, Nitrous oxide (laughing gas)
  At room temperature, it is a colorless, non-flammable gas, with a slightly sweet odor and taste
High pressure system:
  Design Authority: Dave Meekins
  T = 5˚C
  P = 5 atm
Buffer liquid: Mercury
  Closed system
  Volume: 135 mL
0
OX
0
2
0
0
3
Notes: Interior Page Design 2

## Slide 50: Summary and Outlook
Test N2O Bubble Chamber at HIGS (February 2014)
Measure cross sections of 18O(g,a)14C and 17O(g,a)13C at HIGS (Summer 2014)
Test Bubble Chamber at JLab with Bremsstrahlung beam (October 2014)
If successful, run depleted N2O bubble chamber at JLab 16O(g,a)12C
Beam issues:
  Design radiator, collimator, and dumps with GEANT4
  Simulate Photon Spectrum
  Deliver 8.5 MeV K.E. electron beam to 5D Spectrometer with <0.1% energy error
Bubble Chamber issues:
  Study acoustic signal
  Deadtime measurement (now t ± dt = 10.0 ± 0.9 sec)
  Measure O-isotopes depletion
Background tests:
  Measure cosmic–ray background
  Study chamber efficiency vs. superheat
Notes: Interior Page Design 1

## Slide 51: Backup Slides
Notes: Interior Page Design 1

## Slide 52: Cost Estimate
New beamline components:
  New Dipole Magnet and Hall Probe
  2 Super Harps
  Fast Valve
Summary of labor cost by group:
Group | Labor
Survey & Alignment | 3 wks x 2
Magnet Test | 1 wk x 2
Engineering Design | 16 wks
Software | 3 wks x 2
EES | 6 wk x 2
EH&Q | 4 wks
Notes: Interior Page Design 1

## Slide 53
Item | Material Procurement | Shop | Labor
New Dipole Magnet | Dipole Magnet ($8,000) Hall Probe System ($10,000) |  | Design (2 week) Mapping (1 week) EESDC (1 week) Alignment (2 days)
New Beamline | 2 Super Harps (20,000) Fast Valve ($23,000) | Pipes + Pedestals ($20,000) | Design (6 weeks) Alignment (1 week) Software (6 weeks) EES (6 weeks)
Radiator (cooled ladder, FSD) | 0.02 and 0.10 mm Cu foils ($2,000) | $4,000 | Design (2 week) Alignment (2 days)
Sweep Dipole |  |  | 
Electron Dump | Pure Cu ($5,000) | Dump + Pipes ($15,000) | Design (4 weeks) Alignment (1 day)
Cu Collimator | Pure Cu ($5,000) | Collimator + Stand ($5,000) | Design (1 week) Alignment (1 day)
Photon Dump & Stand | Pure Al ($3,000) | $4,000 | Design (1 week) Alignment (1 day)
Safety Review |  |  | 4 weeks
Install |  |  | 6 weeks
Bubble Chamber |  |  | Alignment (1 week)
Total | $76,000 | $48,000 | $80,000
Indirect G&A (55.65%) | $42,300 | $26,400 | $42,500
Indirect Stat & Fringe (57.15%) |  |  | $45,700
Total | $118,300 | $74,400 | $168,200
Notes: Accelerator is paying for magnet and Hall Probe System.
Accelerator will pay for Fast Valve and its electronics.

## Slide 54: CO2 Superheated Liquid?
Similar Bubble Chamber operational
parameters as N2O
Natural Abundance: 13C: 1.07%
Depletion: 13C depletion=1,000
13C(g,n)12C Background
For comparison, 17O(g,n)16O
12C(g,2a)a Background
Notes: The acoustic signal will suppress neutron events (?). What is the expected background from 3-alpha?

## Slide 55: Water Superheated Liquid?
Etching of glass vessel by superheated H2O
T = 250˚C
P = 75 atm
Background from secondary neutron–nucleus elastic scattering by neutrons from d(g,n)p

## Slide 58
Rolfs and Rodney, 1988