## Slide 1: Measurement of 16O(g,a)12C with a Bubble Chamber and a Bremsstrahlung Beam at Jefferson Lab Injector
Riad Suleiman
January 23, 2014
Notes: Title Page

## Slide 2
B. DiGiovine
D. Henderson
R. J. Holt
K. E. Rehm
A. Sonnenschein
A. Robinson
C. Ugalde
J. Benesch
P. Degtiarenko
A. Freyberger
J. Grames
G. Kharashvili
D. Meekins
M. Poelker
Y. Roblin
R. Suleiman
C. Tennant
V. Vylet
https://wiki.jlab.org/ciswiki/index.php/Bubble_Chamber
Notes: Interior Page Design 2

## Slide 3: Outline
Nucleosynthesis and the 12C(a,g)16O Reaction
Time Reversal Reaction: 16O(g,a)12C
The Bubble Chamber
Work at HIGS
Experimental Setup at Jefferson Lab Injector
Bremsstrahlung Beam and Penfold-Leiss Unfolding
Statistical and Systematic Errors
Backgrounds and Ion Energy Distributions
Safety
Summary and Outlook
Notes: Interior Page Design 1

## Slide 4: Relative Abundance of Elements by Weight
Chart: Universe
| Hydrogen | Helium | Oxygen | Carbon | Other
Universe | 73 | 23 | 1 | 0.5 | 0.6
Chart: Human Body
| Oxygen | Carbon | Hydrogen | Nitrogen | Calcium | Phosphorus | Other
Human Body | 61 | 23 | 10 | 2.6 | 1.4 | 1.1 | 0.9
This region is bypassed by 3a process

## Slide 5: Stellar Helium Burning
Helium Reactions:
  a + a ↔ 8Be
  (Q = -0.092 MeV, T½ ≈ 10-16 s)
  a + 8Be → 12C + g (Q = +7.367 MeV, Hoyle State = 7.654 MeV)
  a + 12C → 16O + g (Q = +7.162 MeV)
  (slow, otherwise no 12C remains)
  a + 16O → 20Ne + g (very slow)
a + 12C burning at very small cross section s ≈ 10-17 barn
Currently, reaction rate error is large (±35%)
Thermonuclear reaction rate involving two nuclei is:
Only narrow energy range is important (Gamow Peak)
Goal <±10%
Notes: Notes:
1- Simultaneous fusion of 3-alpha particles has very small probability, the process has to go through 8Be.

## Slide 6: The 12C(a,g)16O Reaction
The holy grail of nuclear astrophysics
S. Woosley, A. Heger, Phys. Rep. 442 (2007) 269
Affects the synthesis of most of the elements of the periodic table
Sets the N(12C)/N(16O) (≈0.4) ratio in the universe
Determines the minimum mass a star requires to become a supernova
Notes: Interior Page Design 2

## Slide 7: The Gamow Peak (Window)
Narrow energy range where thermonuclear reactions is most likely to occur in stellar plasma is a product of two distributions:
  Maxwell-Boltzmann energy distribution with e-E/kBT
  Penetration through Coulomb barrier with e-b/E½
For a + 12C (Z1=2, Z2=6, A=3),
and stellar T=200 106 K:
  Gamow Peak, E0 ≈ 300 keV, W ≈ 50 keV
  (in Center-of-Mass (CM) of a + 12C system)
  Maximum of Maxwell–Boltzmann
  energy distribution, kBT = 17 keV
keV
keV

## Slide 8: a+12C Reaction
Transition 1– → 0+ (E1) | SE1(300) = 1–288 keV b
Transition 2+ → 0+ (E2) | SE2(300) = 7–120 keV b
Total | Stot(300) = 40–430 keV b
    a (Jp=0+) + 12C (Jp=0+) cross section, s(E0), is dominated by p–wave (E1) and d–wave (E2) radiative capture to 16O ground state (Jp=0+)
Two bound states, at 6.92 MeV (Jp=2+) and 7.12 MeV (Jp=1–), with sub–threshold resonances at ER=-0.245 and -0.045 MeV, provide most of s(E0) through their finite widths
Distinguish E1 and E2 by measuring g–angular distributions
Notes: Gammas from E1 and E2 transitions have the same energy (7.162+0.3 MeV).

## Slide 9: Heroic efforts in search of 12C(a,g)16O
Previous Experiments:
  Direct Measurements:
    Helium ions on carbon target: 12C(a,g)16O
    Carbon ions on helium gas: 4He(12C, g)16O or 4He(12C,16O)g (Schürmann)
  Indirect Measurements:
    b–delayed a decay of 16N (Jp=2–, T½=7.13 s, BR=0.12%)
    16N → b– + 16O* (Jp=1–) → a + 12C
Experiment | Beam Current (mA) | Target (nuclei/cm2) | Time (h)
Redder | 0.7 | 12C, 3 1018 | 900
Ouellet | 0.03 | 12C, 5 1018 | 1950
Roters | 0.02 | 4He, 1 1019 | 5000
Kunz | 0.5 | 12C, 3 1018 | 700
EUROGAM | 0.34 | 12C, 1 1019 | 2100
GANDI | 0.6 (?) | 12C, 2 1018 | ?
Schürmann | 0.01 | 4He, 4 1017 | ?
Plag | 0.005 | 12C, 6 1018 | 278
Notes: GANDI is written in German, the reference is on the wiki. Also I put the references to all previous experiments on the wiki.

## Slide 10: Astrophysical S-Factor 12C(a,g)16O
R-matrix Extrapolation to stellar helium burning at E = 300 keV
Define S-Factor to remove both 1/E dependence of nuclear cross sections and Coulomb barrier transmission probability:
Author | Stot(300) (keV b)
Hammer (2005) | 162±39
Kunz (2001) | 165±50
Notes: What do you think about the table shown in this slide? See Schurmann data on slide 44. How did he come up with this small error?

## Slide 11
A(a, g)B:
σ(g,a) is over two orders of magnitude larger than σ(a, g)
MeV
MeV
Reciprocity Relation: (g,a) and (a,g)
Notes: Interior Page Design 2

## Slide 12: Time Reversal Reaction
12C
a
16O
g
Bubble Chamber experiment measures total cross section, E1 + E2
We can separate E1 and E2 if we use linearly polarized g but cannot measure a and 12C angular distribution
Stellar helium burning at E = 300 keV
Notes: If we use linearly polarized gammas, we need also to measure the alpha-carbon angular distributions to separate E1 and E2 contributes.
What about right-handed or left-handed circularly polarized gammas? Circularly polarized light is a linear combination of linearly polarized light with a phase phi=90 deg. This is to say we cannot separate E1 and E2 with circularly polarized gammas.
At JLab Injector we can produce left-handed or right-handed gammas (our electron beam in linearly polarized).
To produce linear polarized gammas, we need to use a crystal radiator.
See paper: Y. Xu et al. on the wiki.

## Slide 13: New Approach: Reversal Reaction + Bubble Chamber
 + 16O → 12C + 
beam
target
signal
Monochromatic g beam at HIGS ≈ 107–8 g/s
Bremsstrahlung at
JLab ≈ 109 g/s (top 250 keV)
Extra gain (factor of 100) by measuring time reversal reaction
Target density up to 104 higher than conventional targets. Number of 16O nuclei = 3.5 1022 /cm2 (3.0 cm cell)
Measures total cross section stot (or Stot)
Solid Angle and Detector Efficiency = 100%
Electromagnetic debris (electrons and gammas, or positrons) do NOT trigger nucleation (detector is insensitive to g-rays by at least 1 part in 1011).
Notes: Looking at the number of gammas we will have (slide 37), we will need to be insensitive to gamma-rays by at least 1 part in 10^15. I will keep using the factor of 10^11?

## Slide 14: The Bubble Chamber
Donald Glaser won Nobel Prize for inventing chamber to detect particles (1960)
Now being used in Dark Matter Search Experiments: COUPP, PICASSO, SIMPLE
Superheat Preparation:
  Liquid is pressurized at ambient temperature (1 to 2)
  Then pressure is kept constant while temperature is
  increased to above boiling point (2 to 3)
  Finally pressure is slowly released while keeping
  temperature constant (3 to 4)
  At this point (4), still liquid but now superheated
Bubble Formation:
  Particle energy loss will induce vaporization
  Resultant vapor bubble is observable either visibly or audibly
  Bubble growth is captured by a digital camera
  Pressure is increased (4 to 3) to quench bubble. It takes
  about few seconds for liquid to return to a stable state
  Superheat is restored by releasing pressure again (3 to 4), and cycle is repeated for each bubble event
Superheat
Notes: Do we have a similar figure for N2O?
The superheat is changed by changing the pressure not the temperature.

## Slide 15: Bubble Growth and Quenching
100 Hz Digital Camera: Dt = 10 ms
19F(g,a)15N event in C4F10
3.0 cm
Notes: That is writing on the glass.

## Slide 16: Bubble Chamber Principle
Particle must be over thresholds in both E and dE/dx
Only bubbles with r > Rc grow to be macroscopic
  s: Surface tension
Bubble requires minimum deposited energy (Ec) within minimum distance Lc (=aRc , 10s of nm to a few µm)
  a: free parameter (to determined experimentally)
Notes: Do we have a similar figure for N2O?
Are we going to allow alphas to generate bubbles or only heavier ions? This may affect the acoustic discrimination, see next slide.

## Slide 17: Efficiency Curve
g+14N and g+16O
g+16O
N2O efficiency curve,
HIGS April 2013,
Eg = 9.7 MeV
N2O thresholds
Superheat = 3.3˚C
Notes: Is it possible to get the Thresholds calculated at Eg=9.7 MeV. Is possible to get the efficiency figure updated and remove the number on the right.

## Slide 18: Acoustic Signal Discrimination
COUPP, FNAL, courtesy of A. Sonnenschein
Suppress neutron events by 100 using acoustic signal
Higher Pitch
Bubble growth produces an audible click which is recorded by piezo-electric transducers
Neutron Events:
  17O(g,n)16O
  Neutron–nucleus elastic scattering: 16O(n,n), 14N(n,n)
  Ions 16O or 14N will generate a single bubble
Alpha Events:
  16O(g,a)12C
  17O(g,a)13C
  18O(g,a)14C
  Ions 12C+a or 13C+a or 14C+a will generate a combined multi-bubble
Notes: The audio files are from http://www-coupp.fnal.gov/public/publications/publication.html
Proton events, i.e, (g,p), should be similar to alphas because it is about the energy loss per length in the target.
When we talk about neutrons, we only worry about elastic scattering. What about inelastic scattering or neutron absorption?
Neutron inelastic or capture radiative capture reactions are usually smaller than elastic scattering by orders of magnitude.
These neutrons are fast, i.e., energy range of few MeV.

## Slide 19: Bubble Chamber at HIGS
High Intensity Gamma Source (HIGS) at Duke University
g-rays generated by Compton backscattering of free-electron-laser (FEL) light from high-energy electron beam bunches
Chamber location

## Slide 20: Measuring 19F(g,a)15N at HIGS
C4F10 Bubble Chamber
  T = 30˚C
  P = 3 atm
2 Fast Digital Cameras
Notes: Interior Page Design 2

## Slide 21
Notes: That is a wire in the background of the bubble photo on the left. It was a wire attached to a piezoelectric on
the bottom of the glass for the acoustic signal. If not this, it was just a thermocouple wire.

## Slide 22: Bremsstrahlung Background at HIGS
Vacuum: 2x10-10 Torr
Residual Gas: Z = 10
Electron Beam Energy: 400 MeV
Electron Beam Current: 41 mA
Interaction Length: 35 m
Strong Bremsstrahlung
Background
(when coupled with large
cross sections at high energies)
Notes: Need to simulate the Bremsstrahlung spectrum for HIGS beam using GEANT4
If it is neutron background that we worry about at HIGS then we can the acoustic signal. At HIGS, we can get more than (g,n) produced by the bremsstrahlung. All photo breakup reactions are possible because of the high energy bremsstrahlung.

## Slide 23: Recent Work
First g+O→α+C bubble
April 2013
N2O Bubble Chamber
  T = 5˚C
  P = 60 atm
Notes: Why the bubble in N2O rises? But not in C4F10. And why the liquid is cloudy for N2O? What was the buffer liquid?
The bubble is far more buoyant in N2O than C4F10 and rises faster. The buffer liquid is water and we had water absorbed in the N2O, but not in C4F10.

## Slide 24: Superheated Targets
List of superheated liquids to be used in experiment:
Readout:
  Fast Digital Camera
  Acoustic Signal to discriminate between neutron and alpha events
N2O Targets | 16O | 17O | 18O
Natural Target | 99.757% | 0.038% | 0.205%
16O Target |  | Depleted > 5,000 | Depleted > 5,000
17O Target |  | Enriched > 80% | <1.0%
18O Target |  | <1.0% | Enriched > 80%
Physics
Measure
Backgrounds
Notes: (g,p) events have acoustic signal similar to (g,a).

## Slide 25: Experimental Setup at JLab Injector
BCM
5 MeV
Dipole
2D
Spectrometer
5D Spectrometer
Bubble
Chamber
location
Mott Polarimeter
Notes: Interior Page Design 2

## Slide 26
5D Spectrometer
Bubble Chamber at HIGS
April 2013
Photon Beam
Entrance
Notes: Interior Page Design 2

## Slide 27: Beamline
2 Superharps to measure beam profile and absolute beam position
New Fast Valve to protect from vacuum failure in front of ¼ Cryo-unit
Replace Dipole
Magnet
Notes: Interior Page Design 2

## Slide 28: Schematics
Electron K.E.
3.0 – 8.5 MeV
0.01 – 100 µA
Al Beam Pipe
Cu Radiator
0.02 mm
Cu Electron Dump
Sweep Magnet
Bubble Chamber
Superheated N2O
3 cm long
5°C, 60 atm
Al Photon Dump
10 cm long
20 cm diameter
Cu Vacuum Window 10 mil
Cu Photon
Collimator
Cu Inner
Pipe
Radiator motion and Sweep Dipole current must be in FSD
BCM0L02 and Electron Dump in Beam Loss Accounting (BLA)
Power deposited in radiator (100 µA and 8.5 MeV) :
  0.02 mm: Energy loss = 21 keV, P = 2.1 W
  0.10 mm: Energy loss = 112 keV, P = 11 W
Pure Copper and Aluminum (high neutron threshold):
  63C(g,n) threshold = 10.86 MeV
  27Al(g,n) threshold = 13.06 MeV
Use GEANT4 to design this region
Notes: Interior Page Design 2

## Slide 29: Beam Requirements
Beam Properties at Radiator:
PEPPo achieved p=8.25 MeV/c or K.E.=7.75 MeV
January 2014, achieved p=9.1 MeV/c or K.E.=8.6 MeV for one hour. Still, suffer from trips due to wave guide vacuum faults; may improve with more processing.
We may also need to helium process the ¼-cryounit
Beam Kinetic Energy, (MeV) | 7.9–8.5
Beam Current (µA) | 0.01–100
Absolute Beam Energy Uncertainty | <0.1%
Relative Beam Energy Uncertainty | <0.02%
Energy Resolution (Spread), σT /T | <0.06%
Beam Size, σx,y (mm) | 1–2
Notes: Interior Page Design 2

## Slide 30: Measuring Absolute Beam Energy
BPM
5 MeV
Dipole
Electron Beam
Momentum
Notes: Interior Page Design 2

## Slide 31
  Jay Benesch designed and is now working with Engineering to fabricate a more uniform and higher field dipole
  New Hall Probe: 0.01% accuracy, resolution to 2 ppm, and a temperature stability of 10 ppm/°C
  Better shielding of stray magnetic fields
  Additional goal: Relative beam energy uncertainty <0.02%
Parameter | Term | Now | Goal
Dipole – linearity | δB/B | 0.25% | 0.02%
Dipole – spatial | δBL/BL | 0.10% | 0.02%
Dipole – reproduce | δB/B | 0.10% | 0.02%
Dipole – power supply | δI/I | 0.20% | 0.02%
Position – surveys | δθ/θ | 0.01% | 0.01%
Position – BPM calibration | δθ/θ | 0.05% | 0.05%
Stray magnetic field | δθ/θ | 0.05% | 0.05%
Total | δP/P | 0.36% | <0.10%
Notes: Interior Page Design 2

## Slide 32: Bremsstrahlung Beam
Use both GEANT4 and FLUKA to calculate Bremsstrahlung spectra
Monte Carlo simulation of Bremsstrahlung at radiotherapy energies is well studied, accuracy: ±5%
Bremsstrahlung Peaks
16O(g,a)12C is ideal case for Bremsstrahlung beam and Penfold–Leiss Unfolding :
  Very steep; only photons near endpoint contribute to yield
  No-structure (resonances)

## Slide 33: GEANT4 Simulation
Both GEANT4 and FLUKA use models that calculate wrong photo–nuclear cross sections. Both do not allow for user’s cross sections. What to do?
  Use GEANT4 and FLUKA to produce the photon spectra impinging on the superheated liquid.
  Fold the above photon spectra with our cross sections in stand-alone codes.
Use GEANT4 to design radiator, collimator, and dumps
Geometry in GEANT4:
Notes: I need to add a better GEANT4 geometry figure.

## Slide 34: Penfold-Leiss Cross Section Unfolding
Measure yields at: where,
The solution can be written in two forms:
Or, Matrix form:
Method of Quadratures: numerical solution of integral equation based on replacement of integral by finite sum
Volterra Integral Equation of First Kind

## Slide 35: Statistical Error Propagation
With:
Then:
Note:
In case of background Subtraction

## Slide 36
Where:
For mono-chromatic photon beam
Although,

## Slide 37: Results
Radiator thickness = 0.02 mm
Bubble Chamber thickness = 3.0 cm, number of 16O nuclei = 3.474 1022 /cm2
Background subtraction of 18O(g,a)14C
Electron Beam K. E. | Beam Current (µA) | Time (hour) | yi | dyi (no bg) | dyi/yi (no bg, %) | dyi (with bg) | dyi/yi (with bg, %)
7.9 | 100 | 100 | 545 | 23 | 4.2 | 134 | 24.6
8.0 | 100 | 20 | 581 | 24 | 4.1 | 77 | 13.3
8.1 | 80 | 10 | 852 | 29 | 3.4 | 60 | 7.0
8.2 | 20 | 10 | 634 | 25 | 3.9 | 40 | 6.3
8.3 | 10 | 10 | 812 | 28 | 3.4 | 39 | 4.8
8.4 | 4 | 10 | 746 | 27 | 3.6 | 36 | 4.8
8.5 | 2 | 10 | 763 | 28 | 3.7 | 32 | 4.2
Notes: Interior Page Design 2

## Slide 38: Systematic Error Propagation
For absolute beam energy uncertainty of δE (= 0.1%) and zero relative beam energy uncertainty:
Ei (MeV) | dyi/yi (%) | dσi/σi (%)
7.9 | 12.5 | 12.6
8.0 | 10.8 | 10.5
8.1 | 9.3 | 9.1
8.2 | 8.0 | 7.1
8.3 | 7.0 | 6.3
8.4 | 6.3 | 5.8
8.5 | 5.6 | 5.2
This is the cross section dependence on energy
Accounted for dNij due to energy error when calculating dyi

## Slide 39
With:
Then:

## Slide 40
Where:
Note: Correlation Coefficient (rij) =1
No energy-to-energy change in systematic error

## Slide 41: Systematic Error Propagation
No energy-to-energy change in systematic error

## Slide 42: Other Systematic Errors
Then:
Simulation
Beam Current, δI/I | 3%
Photon Flux, δφ/φ | 5%
Radiator Thickness, δR/R | 3%
Bubble Chamber Thickness, δT/T | 3%
Bubble Chamber Efficiency, ε | 5%

## Slide 43
Electron Beam K. E. | Cross Section (nb) | Stat Error (no bg, %) | Stat Error (with bg, %)
7.9 | 0.046 | 4.4 | 24.5
8.0 | 0.185 | 6.0 | 20.7
8.1 | 0.58 | 6.3 | 14.7
8.2 | 1.53 | 8.2 | 13.8
8.3 | 3.49 | 9.1 | 13.3
8.4 | 7.2 | 10.6 | 13.8
8.5 | 13.6 | 12.2 | 14.8
Electron Beam K. E. | Cross Section (nb) | Sys Error (Energy, %) | Sys Error (Total, %)
7.9 | 0.046 | 12.5 | 15.3
8.0 | 0.185 | 10.2 | 13.5
8.1 | 0.58 | 8.3 | 12.2
8.2 | 1.53 | 7.0 | 11.4
8.3 | 3.49 | 6.0 | 10.7
8.4 | 7.2 | 5.3 | 10.5
8.5 | 13.6 | 4.7 | 10.1
Note: Relative systematic errors do not get magnified in PL Unfolding

## Slide 44: JLab Projected 12C(a,g)16O S-Factor
Statistical Error: dominated by background subtraction from 18O(g,a)14C (depletion = 5,000)
Electron Beam K. E. | Gamma Energy (MeV) | ECM (MeV) | Cross Section (nb) | Stot Factor (keV b) | Stat Error (%) | Sys Error (Total, %)
7.9 | 7.85 | 0.69 | 0.046 | 62.2 | 24.5 | 15.3
8.0 | 7.95 | 0.79 | 0.185 | 48.7 | 20.7 | 13.5
8.1 | 8.05 | 0.89 | 0.58 | 41.8 | 14.7 | 12.2
8.2 | 8.15 | 0.99 | 1.53 | 35.5 | 13.8 | 11.4
8.3 | 8.25 | 1.09 | 3.49 | 32.0 | 13.3 | 10.7
8.4 | 8.35 | 1.19 | 7.2 | 28.8 | 13.8 | 10.5
8.5 | 8.45 | 1.29 | 13.6 | 26.3 | 14.8 | 10.1
Bubble Chamber experiment measures total S-Factor, SE1 + SE2
Notes: Notes:
1- Schurmann at low energy is limited by 16O contamination of 12C ion beam.

## Slide 45: Backgrounds
Background from oxygen
isotopes and nitrogen in N2O:
  18O(g,a)14C
  17O(g,a)13C
  14N(g,p)13C
Natural Abundance:
    17O: 0.038%
    18O: 0.205%
Expected Rates:
  17O(g,a)13C, depletion=5,000
  18O(g,a)14C, depletion=5,000
  14N(g,p)13C, Chamber eff.= 10-8
Notes: Interior Page Design 2

## Slide 46
Background from:
  17O(g,n)16O and secondary (n,n)
  neutron–nucleus elastic scattering
Background from Chamber glass:
  Neutron–nucleus elastic scattering from
  29Si(g,n)28Si
Cosmic–ray background:
  µ±–nuclear
  neutron–nuclear elastic scattering
Reject neutron events using
acoustic signal (100 suppression factor)
Notes: Interior Page Design 2

## Slide 47: Ion Energy Distributions
Use depleted N2O:
  17O depletion = 5,000
  18O depletion = 5,000
Suppress background with
Bubble Chamber thresholds
Threshold Efficiency (function
of superheat):
Particle | Efficiency
e± | <10-11
g | <10-11
14N(g,p)13C | <10-8
No acoustic cut
Notes: Interior Page Design 2

## Slide 48: Safety
Superheated liquid: N2O, Nitrous oxide (laughing gas)
  At room temperature, it is colorless, non-flammable gas, with slightly sweet odor and taste
High pressure system:
  Design Authority: Dave Meekins
  T = 5˚C
  P = 60 atm
Buffer liquid: Mercury
  Closed system
  Volume: 135 mL
0
OX
0
2
0
0
3
Notes: Are these the correct T and P for N2O? The pressure is about correct, but we may go lower in temperature, say
-10C or so. This will depend on tests.

## Slide 49: Summary and Outlook
More testing of N2O Bubble Chamber at HIGS (March 2014)
Measure cross sections of 18O(g,a)14C and 17O(g,a)13C at HIGS (Summer 2014)
Test Bubble Chamber at JLab with Bremsstrahlung beam (October 2014)
If successful, run depleted N2O bubble chamber at JLab to measure 16O(g,a)12C
Beam issues:
  Design radiator, collimator, and dumps with GEANT4
  Simulate photon spectra with GEANT4 and FLUKA
  Deliver 8.5 MeV K.E. beam to 5D Spectrometer with <0.1% absolute energy uncertainty
Bubble Chamber issues:
  Study acoustic signal and measure neutron events suppression factor
  Deadtime measurements (now t ± dt = 10.0 ± 0.9 sec)
  Measure O-isotopes depletion
Background tests:
  Measure cosmic–ray background
  Study chamber thresholds efficiency vs. superheat and measure g-rays suppression factor
Notes: Is the schedule too aggressive? I need a realistic timeline.

## Slide 50: Backup Slides
Notes: Interior Page Design 1

## Slide 51: Cost Estimate
New beamline components:
  New Dipole Magnet and Hall Probe
  2 Super Harps
  Fast Valve
Summary of labor cost by group:
Group | Labor
Survey & Alignment | 3 wks x 2
Magnet Test | 1 wk x 2
Engineering Design | 16 wks
Software | 3 wks x 2
EES | 6 wk x 2
EH&Q | 4 wks
Notes: Interior Page Design 1

## Slide 52
Item | Material Procurement | Shop | Labor
New Dipole Magnet | Dipole Magnet ($8,000) Hall Probe System ($10,000) |  | Design (2 week) Mapping (1 week) EESDC (1 week) Alignment (2 days)
New Beamline | 2 Super Harps (20,000) Fast Valve ($23,000) | Pipes + Pedestals ($20,000) | Design (6 weeks) Alignment (1 week) Software (6 weeks) EES (6 weeks)
Radiator (cooled ladder, FSD) | 0.02 and 0.10 mm Cu foils ($2,000) | $4,000 | Design (2 week) Alignment (2 days)
Sweep Dipole |  |  | 
Electron Dump | Pure Cu ($5,000) | Dump + Pipes ($15,000) | Design (4 weeks) Alignment (1 day)
Cu Collimator | Pure Cu ($5,000) | Collimator + Stand ($5,000) | Design (1 week) Alignment (1 day)
Photon Dump & Stand | Pure Al ($3,000) | $4,000 | Design (1 week) Alignment (1 day)
Safety Review |  |  | 4 weeks
Install |  |  | 6 weeks
Bubble Chamber |  |  | Alignment (1 week)
Total | $76,000 | $48,000 | $80,000
Indirect G&A (55.65%) | $42,300 | $26,400 | $42,500
Indirect Stat & Fringe (57.15%) |  |  | $45,700
Total | $118,300 | $74,400 | $168,200
Notes: Accelerator is paying for magnet and Hall Probe System.
Accelerator will pay for Fast Valve and its electronics.

## Slide 53: CO2 Superheated Liquid?
Similar Bubble Chamber operational
parameters as N2O
Natural Abundance: 13C: 1.07%
Depletion: 13C depletion=1,000
13C(g,n)12C Background
For comparison, 17O(g,n)16O
12C(g,2a)a Background
Notes: What is the expected background from 3-alpha? I will need the 3-alpha cross section.

## Slide 54: Water Superheated Liquid?
Etching of glass vessel by superheated H2O
T = 250˚C
P = 75 atm
Background from secondary neutron–nucleus elastic scattering by neutrons from d(g,n)p

## Slide 59
Rolfs and Rodney, 1988